| Input Contribution |
| --- |
| Meeting ID* | TST 28 |
| Title:* | TS-0019-Abstract Test Method – Definition of Upper Tester Trigger Control Message |
| Source:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr JaeYoung Hwang, Sejong University, forest62590@sju.ac.kr Abdullah Aziz, Sejong University, G2016FFM082@sju.ac.kr Miguel Angel Reina Ortega, ETSI CTI, miguelangel.reinaortega@etsi.org |
| Uploaded Date:* | 2017-03-28 |
| Document(s) Impacted* | TS-0019 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution defines abstract service primitives and formats for AE triggering control message. Protocol and serialization are also clarified for transportation of AE triggering control message.

## -----------------------Start of change 1--------------------------------------------

# 5	Abstract Test Method (ATM)

### 5.4.2 utPort

#### 5.4.2.2 Upper Tester Control Primitives

#### 5.4.2.2.1 Introduction

The upper tester triggering message is used to transport control commands between Test System and the Upper Tester Application. The control command will contain essential parameters that are required for certain testcase.

The upper tester triggering message type maps to particular message formats for exchanging data and those message formats are defined by TTCN-3 primitive as shown at table 5.4.2.2.1-1, UtTrigger and UtTriggerAck primitive.

Table 5.4.2.2.1-1 Mapping of TTCN-3 Primitives to oneM2M Service Primitives

| Upper TesterControl Message Type | TTCN-3 Primitives | Direction |
| --- | --- | --- |
|  |  | TS | UT |
| Trigger | UtTrigger Primitive | ( |
| Trigger Acknowledgement | UtTriggerAck Primitive | ( |

5.4.2.2.2 UtTrigger and UtTriggerAck Primitives

The UtTrigger primitive is initialized by the Test System to send triggering message to the target IUT as depicted in Figure 5.4.2.2.2-1. The IUT will send acknowledgement message back to the Test System using UtTriggerAck primitive if trigger message is successfully transported to the IUT. Then IUT starts interaction with Test System through oneM2M request and response primitives.

Figure 5.4.2.2.2-1 Trigger message flow

| Table 5.4.2.2.2-2 defines UtTrigger and UtTriggerAck primitives including oneM2M data types to which are mapped as well as examples to show how to implmenet UtTrigger and UtTriggerAck primitives. |  |  |  |
| --- | --- | --- | --- |

Table 5.4.2.2.2-2 UtTrigger and UtTriggerAck Primitive

| Ut Control Primitive | Mapping to oneM2M data types | Description | Reference | Example in oneM2M Primitive Level | HTTP Example |
| --- | --- | --- | --- | --- | --- |
| UtTrigger Primitive | requestPrimtive | ONLY essential parameters included for certain testcase* NOTE: Additional rules defined in Table 5.4.2.2.2-3 are also applied. | TS-0004 [ ] | Example-A: Test System triggers IUT to execute a testcase for creation of <AE> with labels attribute under a CSEBase resource. The requestPrimitive will be serialized into JSON as following: { "rsp" :{ "op": 1, "ty": 2, "to": {CSE_ADDRESS}, "pc":{ "m2m:ae": { "lbl": ["UNINITIALIZED"] } } } } The upper tester needs to set following attributes in the requestPrimitive operation, resource type parameters, an accpetable labels attribute value Example-B: Test System triggers IUT to execute a testcase for delete of <AE> resource. The requestPrimitive will be serialized into JSON as following: { "rsp" :{ "op": 4, "ty": 2 } } The upper tester needs to set following attributes in the requestPrimitive operation, resource type parameters, | Example-A: POST {CSE_ADDRESS} HTTP/1.1 Host: {SUT_IP_ADDRESS:PORT} Content-Length: {PAYLOAD_LENGTH} Content-Type: application/vnd.onem2m-res+json;ty=2 { "m2m:ae": { "lbl":["UNINITIALIZED"] } } Example-B: DELETE HTTP/1.1 Host: {SUT_IP_ADDRESS:PORT} |
| UtTriggerAck Primitive | responsePrimitive | ONLY responseStatusCode attribute included Note: Attribute response status code is defined at Table 5.4.2.2.2-3. | TS-0004 [ ] | { "rsp" :{ "rsc": 2000 } } | HTTP/1.1 200 OK X-M2M-RSC: 2000 |

Table 5.4.2.2.2-3 Rules for defining UtTrigger and UtTriggerAck primitives

UtTrigger primitive is represented in requestPrimitive serialized in JSON format.

Parameters that are required within UtTrigger are listed as following: Operation: operation type (m2m:operation) that IUT is triggered to perform. resourceType: resource type (m2m:resourceType) of a target resource against which IUT is triggered to perform certain operation If the UtTrigger contains following parameters, IUT shall include them in the requestPrimitive: to: target resource against which IUT is triggered to perform certain operation. Default value is the AE_RESOURCE_ADDRESS. primitiveContent: represents the resource attributes that shall be included in the requestPrimitive.

If the UtTrigger contains parameters or resource attributes set to "UNINITIALIZED", IUT shall include such parameters or attributes with a valid value.

Table 5.4.2.2.2-3 Definition of ResponseStatusCode for UtTriggerAck primitive

| Response Status Code Description | Response Status Code Value | Interpretation |
| --- | --- | --- |
| OK | 2000 | The SUT receives successfully the triggering message from Test System |
| BAD_REQUEST | 4000 | The SUT does not interpret correctly the UtTrigger primitive |
| Note: Only above two response status codes are allowed to use in UtTriggerAck primitive. |

## -----------------------End of change 1--------------------------------------------

## -----------------------Start of change 2--------------------------------------------

#### 5.4.2.2.2 Control Communication Protocol

Protocol used for proceeding communications between TS and Upper Tester Application is designated to the Hypertext Transfer Protocol (HTTP) protocol owning it is an application protocol that is widely supported by most all IoT devices and various intrinsic features such as persistent connection, ease of programming, flexibility etc.

#### 5.4.2.2.3 Control Message Serialization

Control commands that are wrapped within a request body of HTTP message shall be serialized into JavaScript Object Notation (JSON) because it is very lightweight and easy to parse and generate for machines.

|  |  |  | Create <container> with maxNrOfInstances |
| --- | --- | --- | --- |
|  |  |  | Create <container> with maxInstanceAge |
|  |  |  | Create <contentInstance> with resourceName |
|  |  |  | Create <contentInstance> with expirationTime |
|  |  |  | Create <contentInstance> with labels |
|  |  |  | Create <contentInstance> with creator |
|  |  |  | Create <contentInstance> with contentInfo |
|  |  |  | Create <contentInstance> with contentRef |
|  |  | At least one |  |
|  |  | AE/GEN/00002/00001 | Support Create request targeting one resource |
|  |  | AE/REG/00002/00001 | Create <AE> with mandatory attributes |
|  |  | AE/REG/00002/00006 |  |
|  |  | AE/SUB/00001/00001 | Create <subscription> with mandatory attributes |
|  |  | At least one |  |
|  |  | AE/GEN/00002/00001 |  |
|  |  | AE/REG/00002/00001 |  |
|  |  | AE/DMR/00001/00001 |  |
|  |  | AE/DMR/00002/00001 |  |

## -----------------------End of change 2--------------------------------------------