| Input Contribution |
| --- |
| Meeting ID* | TST 26.2 |
| Title:* | TS-0028-Security Test Purposes contribution ESPrim (Rel2) |
| Source:* | Easy Global Market |
| Uploaded Date:* | 2017-03-28 |
| Document(s) Impacted* | TS-0028 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some additional TPs for the TS-0028 – Security Test Suite Structure and Test Purposes, Release 2.

Proposal

================ Start of  1st  Part: Test Purposes ==================

| TP Id | TP/oneM2M/CSE/SEC/BV/004 |
| --- | --- |
| Test objective | Check that the IUT responds with a valid ESPrim object |
| Reference | TS-0003 8.4.2 – step C10, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a sessionESPrimKey with AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from AE containing To set to CSE-IDENTIFIER and From set to AE-IDENTIFIER and Content containing securityInfo element containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute } | IUT  AE |
|  | then { the IUT sends a valid NOTIFY Response containing Response Status Code set to 2000 (OK) and Content containing securityInfo element containing securityInfoType attribute set to 5 and valid esprimObject attribute } | IUT  AE |

| TP Id | TP/oneM2M/CSE/SEC/BV/005 |
| --- | --- |
| Test objective | Check that the IUT responds with a valid ESPrim object, but with expired session values |
| Reference | TS-0003 8.4.2 – step C11, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a sessionESPrimKey with AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY request from AE containing To set to CSE-IDENTIFIER and From set to AE-IDIDENTIFIER and Content containing securityInfo resource containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute | IUT  AE |
|  | then { the IUT sends a valid NOTIFY Response containing Response Status Code set to 2000 (OK) and Content containing securityInfo resource containing securityInfoType attribute set to 5 and valid esprimObject attribute containing JWE Protected Header containing expired ATTRIBUTE } | IUT  AE |

| TP Id | Reference | ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BV/005_01 | TS-0003 8.4.3.2 | pairwiseESPrimKeyID |
| TP/oneM2M/CSE/SEC/BV/005_02 | TS-0003 8.4.3.2 | originatorESPrimRandObject |
| TP/oneM2M/CSE/SEC/BV/005_03 | TS-0003 8.4.3.2 | receiverESPrimRandObject |

================ End of  1st  Part: Test Purposes ==================