| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST29 |
| Source:* | Martin Bauer, NEC, martin.bauer@neclab.eu |
| Date:* | 2017-05-22 |
| Reason for Change/s:* | This contribution provides the content to complete TR-0045. Clause 8 on the semantic modelling is completed and Clauses 9 and 10 on Procedure and Implementation are added. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0054 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0045 |
| Clauses * | Clauses 8, 9, 10, Annex A |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | - |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the content to complete TR-0045. Clause 8 on the semantic modelling is completed and Clauses 9 and 10 on Procedure and Implementation are added.

### -----------------------Start of change 1-------------------------------------------

# 8	Semantic Modelling

The semantic modelling is typically based on an ontology that specifies classes and properties, i.e. the ontology defines the vocabulary to be used for the semantic description. In Figure 8-1, a simple ontology for the semantic annotation and discovery use case is visualized. The Table 8-1 shows the actual OWL ontology in an RDF representation.

Figure 8-1: Simple ontology for the semantic annotation and discovery use case

Table 8-1: OWL/RDF representation of the simple ontology for the semantic annotation and discovery use case

<?xml version="1.0"?> <rdf:RDF xmlns="http://www.onem2m.org/ontology/temperature_example#" xml:base="http://www.onem2m.org/ontology/temperature_example" xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#" xmlns:owl="http://www.w3.org/2002/07/owl#" xmlns:xml="http://www.w3.org/XML/1998/namespace" xmlns:xsd="http://www.w3.org/2001/XMLSchema#" xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#"> <owl:Ontology rdf:about="http://www.onem2m.org/ontology/temperature_example"/> <!-- Classes --> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#Fridge"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#House"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/> <!-- Object Properties --> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasFridgeTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#Fridge"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasIndoorTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasOutdoorTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasTemperatureMeasuringFunction"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#measuresTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <!-- Data properties --> <owl:DatatypeProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasDatatype"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <rdfs:range rdf:resource="http://www.w3.org/2001/XMLSchema#string"/> </owl:DatatypeProperty> <owl:DatatypeProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasUnit"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <rdfs:range rdf:resource="http://www.w3.org/2001/XMLSchema#string"/> </owl:DatatypeProperty> <owl:DatatypeProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#valueIsStoredIn"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <rdfs:range rdf:resource="http://www.w3.org/2001/XMLSchema#anyURI"/> </owl:DatatypeProperty> </rdf:RDF>

In Annex A, it is shown how the simple ontology for the semantic annotation and discovery use case can be mapped to the oneM2M Base Ontology [i.3] and thus be semantically integrated with the core concepts that have been identified for oneM2M itself. Such a mapping may be helpful to semantically relate to other parts of the oneM2M system, but is not required, i.e. depending on what is to be achieved, the above ontology can be used “stand-alone” as the basis for supporting semantic annotation and discovery in a particular use case as shown in this developer guide.

Figure 8-2: Semantic description of the scenario according to the ontology

Figure 8-2 shows all the instances needed for modelling the semantic annotation and discovery use case, their respective types and their relations (without annotations). Each sensor will be represented by an AE and all the semantic instances related to the given sensor will be contained in the semantic descriptor. For example, IndoorTempSensor1 models the sensor, which has a function called TempFunction1, which measures IndoorProperty1, which in turn describes the indoor temperature of House 1. In addition there are some datatype properties like the unit of measurement, which are not shown in this figure.

# 9	Procedures

## 9.1	Introduction

In order to implement the presented use case based on oneM2M, procedures are required that are classified as shown below. The focus is on the core semantic aspects, i.e. typical common aspects like the creation of appropriate access control policies are not shown and the interested reader is referred to other developer guides, e.g. TR-0025 [i.5].

- Application Registration: The current procedure contains sensor application registration and smartphone application registration.

- Initial resource creation: The current procedure contains container resources creation and content instance resources creation.

- Semantic descriptor resource creation:The procedure shows the creation of semantic descriptor resources by a smartphone application that is annotating the resources created earlier by the sensor applications.

- Semantic discovery of relevant sensor reources: The procdure shows how all sensor applications that fit the semantic filter criteria specified in SPARQL are discovered by a smartphone application.

- Retrieval of semantic descriptor and sensor information: The procedure shows how the smartphone application first retrieves the semantic descriptor resources of the discovered resource and then, based on the information contained in the semantic descriptor, retrieves the contentInstance resource containing the latest sensor reading.

## 9.2	Call Flows

### 9.2.1 	Application registration

Figure 9.2.1-1 depicts how the applications register with oneM2M and can be described as follows:

- Sensor applications (ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4) register with the oneM2M service platform (IN-CSE).

- Smartphone application (ADN-AE5 and ADN-AE6) register with the oneM2M service platform (IN-CSE).

Figure 9.2.1-1: Registration phase call flows

### 9.2.2 	Initial resource creation

Call flows regarding the initial resource creation phase depicted in figure 9.2.2-1 can be described as follows:

- Four container resources are created in the oneM2M service platform (IN-CSE) to store the the temperature values measured by Sensor#1, Sensor#2, Sensor#3 and Sensor#4 under the registered application ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4, respectively (in figure 9.2.2-1 this is only shown for ADN-AE1 and ADN-AE2, ADN-AE3 and ADN-AE4 are handled in exactly the same way).

- Content Instance resources are created by the applications (ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4) under each created container and represent the measured temperatures (in figure 9.2.2-1 this is only shown for the respective first contentInstances of ADN-AE1 and ADN-AE2, ADN-A3 and ADN-AE4 are handled in exactly the same way and contentInstances are created continuously).

Figure 9.2.2-1: Initial resource creation phase call flows

### 9.2.3	Semantic descriptor resource creation

Call flows regarding the semantic descriptor resource creation phase are depicted in figure 9.2.3-1 and can be described as follows:

- ADN-AE5 creates a semantic descriptor resource under each of the ADN resources representing a sensor application instance (i.e ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4).The semantic information has been provided by a human user using the smartphone application. It provides information about the sensor, the sensor measurements (e.g. unit of measurement) and what is being measured. In the given example these are the information measured by the sensor (temperature), the unit of measurement (Celsius or Fahrenheit), and the relaton to the Thing for which the value is being measured (house or fridge).

Figure 9.2.3-1: Semantic descriptor resource creation phase call flows

### 9.2.4		Semantic discovery of relevant sensor reources

Call flows regarding the discovery are depicted in figure 9.2.4-1 and can be described as follows:

- Smartphone application (ADN-AE6) sends a RETRIEVE request including the parameter  filterUsage and specific semantic filter criteria condition(s) provided in SPARQL for discovery of sensor application resources stored in the oneM2M service platform (IN-CSE)

- The oneM2M service platform (IN-CSE) responds with URIs of the discovered sensor resources, if any, to the smartphone application (ADN-AE6) according to the filter criteria.

Figure 9.2.4-1: Semantic discovery phase call flows

### 9.2.5 		Retrieval of semantic descriptor and sensor information

Call flows regarding the retrieval of the semantic descriptor and the contentInstance resources are depicted in figure 9.2.5-1 and can be described as follows:

- The smartphone application (ADN-AE6) sends GET requests for retrieval of the semantic descriptor child resources of the discovered sensor resources.

- The oneM2M service platform (IN-CSE) returns the requested semantic descriptor child resource(s)

- Based on the respective information contained in the retrieved semantic descriptor, the smartphone application (ADN-AE6)  requests the (latest) content instance provided by the sensor application containing the sensor measurement.

- The oneM2M service platform (IN-CSE) returns the requested content instance containing the sensor information.

Figure 9.2.5-1: Retrieval of semantic descriptor and sensor information phase call flows

# 10		Implementation

## 10.1 	Introduction

Clause 10 presents necessary procedures required for the implementation of the semantic annotation and discovery use case, including conditions that must be met for the correct implementation of the current use case, and resource tree etc.

## 10.2 	Assumptions

Assumptions are presented as below in order to ensure the semantic annotation and discovery use case can be correctly implemented.

- Security is not considered in the current use case;

- HTTP binding of oneM2M primitives is used in the current use case;

- XML serializations of oneM2M primitives are used in the current use case;

- All mandatory HTTP headers are presented in the HTTP requests while optional headers are selectively used in the current use case;

- All mandatory resource attributes for resources presented in the current use case are presented in the HTTP requests while optional resource attributes are selectively used in the current use case;

- All AEs in the current use case are initially registered with the IN-CSEs and the identifier of the AEs are assigned by it acting as the Registrar CSE of the AE;

- All resources created in the current use case are addressable with the oneM2M Resource Identifier form of Hierarchical address;

- Short names for the representation of the resources and attributes are used in the current use case;

- Default access control policy has already been created under IN-CSE

- All request originators send Blocking Requests for accessing resources located in CSEs.

## 10.3 	Resource Structure

### 10.3.1 	Introduction

The development of an oneM2M application includes the design of the resource trees of service capability layers i.e. the IN-CSE in the current use case. The resource tree is constructed with child resources created according to the high level procedures presented in clause 9. All the child resources shown in the resource trees are mandatorily required in order to correctly implement the semantic annotation and discovery use case.

### 10.3.2 	Resource Structure of IN-CSE

The resource tree of IN-CSE starts with a CSEBase named server depicted in figure 10.3.2-1.

The root CSEBase has four direct child resources directly relevant for the semantic annotation and discovery use case, the tempsensorae1, tempsensorae2, tempsensorae3 and tempsensorae4 resources which represent ADN-AE1, ADN-AE2, ADN-AE3, ADN-AE4 respectively. Each AE will have a container named temperature in which the content instances are stored and a semantic descriptor named SD1. As the substructure of each AE resource is exactly the same, only the substructure of tempsensorae1 is shown, the visualization of the substructure of the others is omitted.

Figure 10.3.2-1: IN-CSE resource structure

## 10.4	Role of Entities

### 10.4.1 	oneM2M service platform (IN-CSE)

The oneM2M service platform is modelled as an IN-CSE and is responsible for

- handling the registration requests from all ADN-AEs in the use case

- creating and managing the resource structures for storing sensor information and semantic annotations

- executing semantic resource discovery

### 10.4.2 	Temperature sensor applications (ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4)

Each of the temperature sensor applications are modelled as an ADN-AE and are responsible for

- measuring the sensor information

- registering the temperature sensors with the IN-CSE,

- creating container resources named “temperature”

- creating content instance resources under the container “temperature” that contain the temperature measurements.

### 10.4.3 	Semantic Annotation Application (ADN-AE5)

The semantic annotation application, which is expected to run on a smartphone or other device with user interface is responsible for the following

- enable the user to create semantic annotations for resources representing senors

- create semantic descriptor resources as child resources of sensor AE resources that contain the semantic annotations.

### 10.4.4 	Semantic Discovery Application (ADN-AE6)

The semantic discovery application, which is ecpected to run on a user device, is responsible for the following:

- Enable the user to formulate the semantic filter for the semantic discovery (in SPARQL)

- Retrieve the semantic annotation for discovered resources

- Retrieve sensor measurements based on the semantic annoations

## 10.5	Implementation Procedures

### 10.5.1 	Introduction

The implementation procedures in the current use case are mapped into HTTP bindings with XML serializations of oneM2M primitives according to the standard APIs describing the reference points Mca and Mcc, as defined in oneM2M TS-0001 [i.6], oneM2M TS-0004 [i.7], the HTTP binding TS-0009 [i.8].

In addition, short names for the representation of the resources and attributes are used in the implementation procedures.

### 10.5.2	Application registration

The following example shows how the tempsensorae1 (ADN-AE) is registered with the IN-CSE. The same is done for tempsensorae2, tempsensorae3 and tempsensorae4, which is not explicitly shown here.

HTTP Request:

POST /server HTTP/1.1

Host: http://in.provider.com:7579

Accept: application/xml

X-M2M-RI: 12345

X-M2M-Origin: SOrigin

Content-Type: application/vnd.onem2m-res+xml; ty=2

nmtype: short

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae mlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" rn="tempsensorae1">

<api>0.2.481.2.0001.001.000111</api>

<lbl>semanticallyAnnotated tempSensor</lbl>

<rr>true</rr>

</m2m:ae>

HTTP Response:

201 Created

Accept: application/xml

X-M2M-RI: 12345

X-M2M-RSC: 2001

Content-Location: /server/tempsensorae1

### 10.5.3 	Initial resource creation

The following example shows how the temperature container child resource of tempsensorae1 is created, which will hold the content instances with the measured sensor values. The same is done for the temperature container child resources of tempsensorae2, tempsensorae3 and tempsensorae4, which is not explicitly shown here.

HTTP Request:

POST /server/tempsensorae1 HTTP/1.1

Host: http://in.provider.com:7579

Accept:application/xml

X-M2M-RI:12345

X-M2M-Origin:SOrigin

Content-Type:application/vnd.onem2m-res+xml; ty=3

nmtype:short

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" rn="temperature">

<lbl>container</lbl>

</m2m:cnt>

HTTP Response:

201 Created

Accept: application/xml

X-M2M-RI: 12345

X-M2M-RSC: 2001

Content-Location: /server/tempsensorae1/temperature

Content-Type: application/vnd.onem2m-res+xml; ty=3

The example below shows how a content instance holding a temperature value is created in the temperature container.

HTTP Request:

POST /server/tempsensorae1/temperature HTTP/1.1

Host: http://in.provider.com:7579

Accept:application/xml

X-M2M-RI:12345

X-M2M-Origin:SOrigin

Content-Type:application/vnd.onem2m-res+xml; ty=4

nmtype:short

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<con>75</con>

</m2m:cin>

HTTP Response:

201 Created

Accept: application/xml

X-M2M-RI: 12345

X-M2M-RSC: 2001

Content-Location: /server/tempsensorae1/temperature/ci-234523664

Content-Type: application/vnd.onem2m-res+xml; ty=4

### 10.5.4 	Semantic descriptor resource creation

In the semantic annotation and discovery use case, a semantic annotation user application, e.g. running on a smartphone, is used for semantically annotating a given resource. For this purpose, the semantic annotation application (ADN-AE5) creates a semantic descriptor child resource of the resource to be semantically annotated. The actual semantic description is represented in base64-encoded RDF/XML and can be found in the descriptor attribute of the semantic descriptor resource.

According to the scenario, there is one AE representing each temperature sensor. In the semantic description, all relevant information regarding the sensor and what it is measuring is represented, e.g. that the unit of measurement is Celsius, the temperature value is represented as an integer, the value represents the indoor temperature of a particular house and how the latest value can be retrieved. Figure 8-2 shows the complete semantic information of the scenario combined, the semantic annotations listed below each contain the relevant information for one temperature sensor. In base64-encoded form they are stored in the descriptor attributes of the respective semantic descriptor resources.

Semantic descriptor of indoor temperature sensor 1:

<?xml version="1.0"?>

<rdf:RDF xmlns="http://www.onem2m.org/ontology/houses_temperature_example#"

xml:base="http://www.onem2m.org/ontology/houses_temperature_example"

xmlns:temperature_example="http://www.onem2m.org/ontology/temperature_example#"

xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#"

xmlns:owl="http://www.w3.org/2002/07/owl#"

xmlns:xml="http://www.w3.org/XML/1998/namespace"

xmlns:xsd="http://www.w3.org/2001/XMLSchema#"

xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#">

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#House1">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/>

<temperature_example:hasIndoorTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempProperty1"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempProperty1">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/>

<temperature_example:hasDatatype>xsd:int</temperature_example:hasDatatype>

<temperature_example:hasUnit rdf:datatype="http://www.w3.org/2001/XMLSchema#string">Fahrenheit</temperature_example:hasUnit>

<temperature_example:valueIsStoredIn>http:// in.provider.com:7579/server/tempsensorae1/temperature/latest</temperature_example:valueIsStoredIn>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempSensor1">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/>

<temperature_example:hasTemperatureMeasuringFunction rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction1"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction1">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/>

<temperature_example:measuresTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempProperty1"/>

</owl:NamedIndividual>

</rdf:RDF>

Semantic descriptor of outdoor temperature sensor:

<?xml version="1.0"?>

<rdf:RDF xmlns="http://www.onem2m.org/ontology/houses_temperature_example#"

xml:base="http://www.onem2m.org/ontology/houses_temperature_example"

xmlns:temperature_example="http://www.onem2m.org/ontology/temperature_example#"

xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#"

xmlns:owl="http://www.w3.org/2002/07/owl#"

xmlns:xml="http://www.w3.org/XML/1998/namespace"

xmlns:xsd="http://www.w3.org/2001/XMLSchema#"

xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#">

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#House1">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/>

<temperature_example:hasOutdoorTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#OutdoorTempProperty"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#OutdoorTempProperty">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/>

<temperature_example:hasDatatype>xsd:int</temperature_example:hasDatatype>

<temperature_example:hasUnit rdf:datatype="http://www.w3.org/2001/XMLSchema#string">Celsius</temperature_example:hasUnit>

<temperature_example:valueIsStoredIn>http://in.provider.com:7578/server/tempsensorae2/temperature/latest</temperature_example:valueIsStoredIn>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#OutdoorTempSensor">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/>

<temperature_example:hasTemperatureMeasuringFunction rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction2"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction2">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/>

<temperature_example:measuresTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#OutdoorTempProperty"/>

</owl:NamedIndividual>

</rdf:RDF>

Semantic descriptor of indoor temperature sensor 2:

<?xml version="1.0"?>

<rdf:RDF xmlns="http://www.onem2m.org/ontology/houses_temperature_example#"

xml:base="http://www.onem2m.org/ontology/houses_temperature_example"

xmlns:temperature_example="http://www.onem2m.org/ontology/temperature_example#"

xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#"

xmlns:owl="http://www.w3.org/2002/07/owl#"

xmlns:xml="http://www.w3.org/XML/1998/namespace"

xmlns:xsd="http://www.w3.org/2001/XMLSchema#"

xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#">

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#House2">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/>

<temperature_example:hasIndoorTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempProperty2"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempProperty2">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/>

<temperature_example:hasDatatype>xsd:double</temperature_example:hasDatatype>	         <temperature_example:hasUnit rdf:datatype="http://www.w3.org/2001/XMLSchema#string">Celsius</temperature_example:hasUnit>

<temperature_example:valueIsStoredIn>http://in.provider.com:7579/server/tempsensorae3/temperature/latest</temperature_example:valueIsStoredIn>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempSensor2">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/>

<temperature_example:hasTemperatureMeasuringFunction rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction3"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction3">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/>

<temperature_example:measuresTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#IndoorTempProperty2"/>

</owl:NamedIndividual>

</rdf:RDF>

Semantic descriptor of fridge temperature sensor 1:

<?xml version="1.0"?>

<rdf:RDF xmlns="http://www.onem2m.org/ontology/houses_temperature_example#"

xml:base="http://www.onem2m.org/ontology/houses_temperature_example"

xmlns:temperature_example="http://www.onem2m.org/ontology/temperature_example#"

xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#"

xmlns:owl="http://www.w3.org/2002/07/owl#"

xmlns:xml="http://www.w3.org/XML/1998/namespace"

xmlns:xsd="http://www.w3.org/2001/XMLSchema#"

xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#">

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#Fridge1">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#Fridge"/>

<temperature_example:hasFridgeTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#FridgeTempProperty"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#FridgeTempProperty">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/>

<temperature_example:hasDatatype>xsd:double</temperature_example:hasDatatype>

<temperature_example:hasUnit rdf:datatype="http://www.w3.org/2001/XMLSchema#string">Celsius</temperature_example:hasUnit>

<temperature_example:valueIsStoredIn>http://in.provider.com:7579/server/tempsensorae4/temperature/latest</temperature_example:valueIsStoredIn>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#FridgeTempSensor">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/>

<temperature_example:hasTemperatureMeasuringFunction rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction4"/>

</owl:NamedIndividual>

<owl:NamedIndividual rdf:about="http://www.onem2m.org/ontology/houses_temperature_example#TempFunction4">

<rdf:type rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/>

<temperature_example:measuresTemperature rdf:resource="http://www.onem2m.org/ontology/houses_temperature_example#FridgeTempProperty"/>

</owl:NamedIndividual>

</rdf:RDF>

The following example shows how the semantic descriptor child resource of the tempsensorae1 (ADN-AE1) is created. The semantic descriptors of tempsensorae2, tempsensorae3 and tempsensorae4 are created in the same way. Please note that the content of the descriptor attribute first needs to be base64-enoded.

HTTP Request:

POST /server/tempsensorae1 HTTP/1.1

Host: http://in.provider.com:7579

Accept:application/xml

X-M2M-RI:12345

X-M2M-Origin:SOrigin

Content-Type:application/vnd.onem2m-res+xml; ty=24

nmtype:short

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sd

xmlns:m2m="http://www.onem2m.org/xml/protocols"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

rn=SD1>

<dspt> PD94bWwgdmVyc2lvbj0iMS4wIj8+DQo8cmRmOlJERiB4bWxucz0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlIyINCiAgICAgeG1sOmJhc2U9Imh0dHA6Ly93d3cub25lbTJtLm9yZy9vbnRvbG9neS9ob3VzZXNfdGVtcGVyYXR1cmVfZXhhbXBsZSINCiAgICAgeG1sbnM6dGVtcGVyYXR1cmVfZXhhbXBsZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L3RlbXBlcmF0dXJlX2V4YW1wbGUjIg0KICAgICB4bWxuczpyZGY9Imh0dHA6Ly93d3cudzMub3JnLzE5OTkvMDIvMjItcmRmLXN5bnRheC1ucyMiDQogICAgIHhtbG5zOm93bD0iaHR0cDovL3d3dy53My5vcmcvMjAwMi8wNy9vd2wjIg0KICAgICB4bWxuczp4bWw9Imh0dHA6Ly93d3cudzMub3JnL1hNTC8xOTk4L25hbWVzcGFjZSINCiAgICAgeG1sbnM6eHNkPSJodHRwOi8vd3d3LnczLm9yZy8yMDAxL1hNTFNjaGVtYSMiDQogICAgIHhtbG5zOnJkZnM9Imh0dHA6Ly93d3cudzMub3JnLzIwMDAvMDEvcmRmLXNjaGVtYSMiPg0KDQogICAgPG93bDpOYW1lZEluZGl2aWR1YWwgcmRmOmFib3V0PSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvaG91c2VzX3RlbXBlcmF0dXJlX2V4YW1wbGUjSG91c2UxIj4NCiAgICAgICAgPHJkZjp0eXBlIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L3RlbXBlcmF0dXJlX2V4YW1wbGUjSG91c2UiLz4NCiAgICAgICAgPHRlbXBlcmF0dXJlX2V4YW1wbGU6aGFzSW5kb29yVGVtcGVyYXR1cmUgcmRmOnJlc291cmNlPSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvaG91c2VzX3RlbXBlcmF0dXJlX2V4YW1wbGUjSW5kb29yVGVtcFByb3BlcnR5MSIvPg0KICAgIDwvb3dsOk5hbWVkSW5kaXZpZHVhbD4NCg0KICAgIDxvd2w6TmFtZWRJbmRpdmlkdWFsIHJkZjphYm91dD0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlI0luZG9vclRlbXBQcm9wZXJ0eTEiPg0KICAgICAgICA8cmRmOnR5cGUgcmRmOnJlc291cmNlPSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvdGVtcGVyYXR1cmVfZXhhbXBsZSNUZW1wZXJhdHVyZVByb3BlcnR5Ii8+DQogICAgICAgIDx0ZW1wZXJhdHVyZV9leGFtcGxlOmhhc0RhdGF0eXBlPnhzZDppbnQ8L3RlbXBlcmF0dXJlX2V4YW1wbGU6aGFzRGF0YXR5cGU+DQogICAgICAgIDx0ZW1wZXJhdHVyZV9leGFtcGxlOmhhc1VuaXQ+RmFocmVuaGVpdDwvdGVtcGVyYXR1cmVfZXhhbXBsZTpoYXNVbml0Pg0KICAgICAgICA8dGVtcGVyYXR1cmVfZXhhbXBsZTp2YWx1ZUlzU3RvcmVkSW4+aHR0cDovL2luLnByb3ZpZGVyLmNvbTo3NTc5L3NlcnZlci90ZW1wc2Vuc29yYWUxL3RlbXBlcmF0dXJlL2xhdGVzdDwvdGVtcGVyYXR1cmVfZXhhbXBsZTp2YWx1ZUlzU3RvcmVkSW4+DQogICAgPC9vd2w6TmFtZWRJbmRpdmlkdWFsPg0KDQogICAgPG93bDpOYW1lZEluZGl2aWR1YWwgcmRmOmFib3V0PSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvaG91c2VzX3RlbXBlcmF0dXJlX2V4YW1wbGUjSW5kb29yVGVtcFNlbnNvcjEiPg0KICAgICAgICA8cmRmOnR5cGUgcmRmOnJlc291cmNlPSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvdGVtcGVyYXR1cmVfZXhhbXBsZSNUZW1wZXJhdHVyZVNlbnNvciIvPg0KICAgICAgICA8dGVtcGVyYXR1cmVfZXhhbXBsZTpoYXNUZW1wZXJhdHVyZU1lYXN1cmluZ0Z1bmN0aW9uIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlI1RlbXBGdW5jdGlvbjEiLz4NCiAgICA8L293bDpOYW1lZEluZGl2aWR1YWw+DQoNCiAgICA8b3dsOk5hbWVkSW5kaXZpZHVhbCByZGY6YWJvdXQ9Imh0dHA6Ly93d3cub25lbTJtLm9yZy9vbnRvbG9neS9ob3VzZXNfdGVtcGVyYXR1cmVfZXhhbXBsZSNUZW1wRnVuY3Rpb24xIj4NCiAgICAgICAgPHJkZjp0eXBlIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L3RlbXBlcmF0dXJlX2V4YW1wbGUjVGVtcGVyYXR1cmVNZWFzdXJpbmdGdW5jdGlvbiIvPg0KICAgICAgICA8dGVtcGVyYXR1cmVfZXhhbXBsZTptZWFzdXJlc1RlbXBlcmF0dXJlIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlI0luZG9vclRlbXBQcm9wZXJ0eTEiLz4NCiAgICA8L293bDpOYW1lZEluZGl2aWR1YWw+ICAgDQo8L3JkZjpSREY+DQo=</dspt>

<or>http://www.onem2m.org/ontology/temperature_example</or>

</m2m:sd>

HTTP Response:

201 Created

Accept: application/xml

Content-Location: /server/tempsensorae1/SD1

Content-Type: application/vnd.onem2m-res+xml; ty=24

X-M2M-RI: 12345

X-M2M-RSC: 2001

### 10.5.5 	Semantic discovery of relevant sensor reources

For the semantic discovery, a semantic filter has to be specified. The semantic filter is formulated as a SPARQL query. For all child resources that themselves have semantic descriptor child resources, the SPARQL query is executed on the content of the descriptor attribute of each of the semantic descriptor resources. If the SPARQL query returns a valid result on one of the semantic descriptor child resources, the parent resource is included in the result list, otherwise not.  There are also options for linking additional semantic content to be considered together with the semantic content of the descriptor for evaluating the SPARQL query – either through the relatedSemantics attribute of the semantic descriptor resource, or through the onem2m:resourceDescriptorLink annotation property in the RDF description in the descriptor attribute itself – but this is beyond the scope of this developer guide. Details for this can be found in TS-0001 [i.6] and [i.7].

In the following, a number of different semantic filters formulated in SPARQL are provided together with the results that would be returned, thus determining which (parent) resources would be included in the result of the discovery. Then a complete request is shown. For this purpose the SPARQL request has to be URI encoded as it is used as the value of the smf (semantic filter) parameter.

Query 1:

Natural language query: “Give me all the sensor related resources that measure the temperature in the unit Celsius.”

PREFIX temp: <http://www.onem2m.org/ontology/temperature_example#>

SELECT ?sensor

WHERE {

?sensor temp:hasTemperatureMeasuringFunction ?tempFunction .

?tempFunction temp:measuresTemperature ?property .

?property temp:hasUnit

"Celsius"^^<http://www.w3.org/2001/XMLSchema#string>

}

?sensor	does not match	temp:IndoorTempSensor1 ( tempsensorae1 is not included in the result
?sensor	matches	 		temp:OutdoorTempSensor ( tempsensorae2 is included in the result
?sensor	matches 			temp:IndoorTempSensor2 ( tempsensorae3 is included in the result
?sensor	matches			temp:FridgeTempSensor  ( tempsensorae4 is included in the result

Query 2:

Natural language query: “Give me all the sensor related resources that measure the indoor temperature of a house.”

PREFIX temp: <http://www.onem2m.org/ontology/temperature_example#>

SELECT ?sensor

WHERE { ?thing temp:hasIndoorTemperature ?property .

?tempFunction temp:measuresTemperature ?property .

?sensor temp:hasTemperatureMeasuringFunction ?tempFunction

}

?sensor	matches 	 		temp:IndoorTempSensor1 ( tempsensorae1 is included in the result
		?sensor	does not match 	temp:OutdoorTempSensor ( tempsensorae2 is not included in the result
 		?sensor	matches 	 		temp:IndoorTempSensor2 ( tempsensorae3 is included in the result
		?sensor	does not match 	temp:FridgeTempSensor  ( tempsensorae4 is not included in the result

Query 3:

Natural language query: “Give me all the sensor related resources that measure the indoor temperature of a house and provide the measurement in the unit Fahrenheit.”

PREFIX temp: <http://www.onem2m.org/ontology/temperature_example#>

SELECT ?sensor

WHERE { ?thing temp:hasIndoorTemperature ?property .

?property temp:hasUnit 
                             "Fahrenheit"^^<http://www.w3.org/2001/XMLSchema#string> .

?tempFunction temp:measuresTemperature ?property .

?sensor temp:hasTemperatureMeasuringFunction ?tempFunction

}

?sensor	matches 	 		temp:IndoorTempSensor1 ( tempsensorae1 is included in the result
			?sensor	does not match 	temp:OutdoorTempSensor ( tempsensorae2 is not included in the result
 			?sensor	does not match 	temp:IndoorTempSensor2 ( tempsensorae3 is not included in the result
			?sensor	does not match 	temp:FridgeTempSensor  ( tempsensorae4 is not included in the result

The following example shows how the semantic discovery application (ADN-AE6) on the user device can perform the complete HTTP request for Query 2, where the semantic filter in SPARQL is URI-encoded.

HTTP Request:

GET /server?fu=1&amp;smf= PREFIX%20temp%3A%20%3Chttp%3A%2F%2Fwww.onem2m.org%2Fontology%2Ftemperature_example%23%3E%20SELECT%20%3Fsensor%20WHERE%20%7B%20%3Fthing%20temp%3AhasIndoorTemperature%20%3Fproperty%20.%20%3FtempFunction%20temp%3AmeasuresTemperature%20%3Fproperty%20.%20%3Fsensor%20temp%3AhasTemperatureMeasuringFunction%20%3FtempFunction%7D HTTP/1.1

Host: http://in.provider.com:7579

Accept: application/xml

X-M2M-RI: 12345

X-M2M-Origin: SOrigin

nmtype: short

HTTP Response:

200 OK

Accept: application/xml

X-M2M-RI: 12345

X-M2M-RSC: 2000

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:uril xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

/server/tempsensorae1

/server/tempsensorae3

</m2m:uril>

As expected the two AEs tempsensorae1 (ADN-AE1) and tempsensorae3 (ADN-AE3)  are returned.

### 10.5.6 	Retrieval of semantic descriptor and sensor information

As the final step, the semantic discovery application (ADN-AE6) on the user device can now retrieve the semantic descriptor itself and find out how to access the latest sensor measurement (under the assumption that the convention of using the name SD1 for the semantic descriptor was used, otherwise it needs to get the information about the semantic descriptor child resource(s) first).

HTTP Request:

GET /server/tempsensorae1/SD1 HTTP/1.1

Host: http://in.provider.com:7579

Accept: application/xml

X-M2M-RI: 12345

X-M2M-Origin: SOrigin

nmtype: short

HTTP Result:

200 OK

Accept: application/xml

X-M2M-RI: 12345

X-M2M-RSC: 2000

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sd

xmlns:m2m="http://www.onem2m.org/xml/protocols"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

rn=SD1>

<pi>/server</pi>

<ty>24</ty>

<ct>20170519T064158</ct>

<ri>/sensor/tempsensorae1/SD1</ri>

<lt>20170519T064158</lt>

<aei>SOrigin</aei>

<dspt>PD94bWwgdmVyc2lvbj0iMS4wIj8+DQo8cmRmOlJERiB4bWxucz0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlIyINCiAgICAgeG1sOmJhc2U9Imh0dHA6Ly93d3cub25lbTJtLm9yZy9vbnRvbG9neS9ob3VzZXNfdGVtcGVyYXR1cmVfZXhhbXBsZSINCiAgICAgeG1sbnM6dGVtcGVyYXR1cmVfZXhhbXBsZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L3RlbXBlcmF0dXJlX2V4YW1wbGUjIg0KICAgICB4bWxuczpyZGY9Imh0dHA6Ly93d3cudzMub3JnLzE5OTkvMDIvMjItcmRmLXN5bnRheC1ucyMiDQogICAgIHhtbG5zOm93bD0iaHR0cDovL3d3dy53My5vcmcvMjAwMi8wNy9vd2wjIg0KICAgICB4bWxuczp4bWw9Imh0dHA6Ly93d3cudzMub3JnL1hNTC8xOTk4L25hbWVzcGFjZSINCiAgICAgeG1sbnM6eHNkPSJodHRwOi8vd3d3LnczLm9yZy8yMDAxL1hNTFNjaGVtYSMiDQogICAgIHhtbG5zOnJkZnM9Imh0dHA6Ly93d3cudzMub3JnLzIwMDAvMDEvcmRmLXNjaGVtYSMiPg0KDQogICAgPG93bDpOYW1lZEluZGl2aWR1YWwgcmRmOmFib3V0PSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvaG91c2VzX3RlbXBlcmF0dXJlX2V4YW1wbGUjSG91c2UxIj4NCiAgICAgICAgPHJkZjp0eXBlIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L3RlbXBlcmF0dXJlX2V4YW1wbGUjSG91c2UiLz4NCiAgICAgICAgPHRlbXBlcmF0dXJlX2V4YW1wbGU6aGFzSW5kb29yVGVtcGVyYXR1cmUgcmRmOnJlc291cmNlPSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvaG91c2VzX3RlbXBlcmF0dXJlX2V4YW1wbGUjSW5kb29yVGVtcFByb3BlcnR5MSIvPg0KICAgIDwvb3dsOk5hbWVkSW5kaXZpZHVhbD4NCg0KICAgIDxvd2w6TmFtZWRJbmRpdmlkdWFsIHJkZjphYm91dD0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlI0luZG9vclRlbXBQcm9wZXJ0eTEiPg0KICAgICAgICA8cmRmOnR5cGUgcmRmOnJlc291cmNlPSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvdGVtcGVyYXR1cmVfZXhhbXBsZSNUZW1wZXJhdHVyZVByb3BlcnR5Ii8+DQogICAgICAgIDx0ZW1wZXJhdHVyZV9leGFtcGxlOmhhc0RhdGF0eXBlPnhzZDppbnQ8L3RlbXBlcmF0dXJlX2V4YW1wbGU6aGFzRGF0YXR5cGU+DQogICAgICAgIDx0ZW1wZXJhdHVyZV9leGFtcGxlOmhhc1VuaXQ+RmFocmVuaGVpdDwvdGVtcGVyYXR1cmVfZXhhbXBsZTpoYXNVbml0Pg0KICAgICAgICA8dGVtcGVyYXR1cmVfZXhhbXBsZTp2YWx1ZUlzU3RvcmVkSW4+aHR0cDovL2luLnByb3ZpZGVyLmNvbTo3NTc5L3NlcnZlci90ZW1wc2Vuc29yYWUxL3RlbXBlcmF0dXJlL2xhdGVzdDwvdGVtcGVyYXR1cmVfZXhhbXBsZTp2YWx1ZUlzU3RvcmVkSW4+DQogICAgPC9vd2w6TmFtZWRJbmRpdmlkdWFsPg0KDQogICAgPG93bDpOYW1lZEluZGl2aWR1YWwgcmRmOmFib3V0PSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvaG91c2VzX3RlbXBlcmF0dXJlX2V4YW1wbGUjSW5kb29yVGVtcFNlbnNvcjEiPg0KICAgICAgICA8cmRmOnR5cGUgcmRmOnJlc291cmNlPSJodHRwOi8vd3d3Lm9uZW0ybS5vcmcvb250b2xvZ3kvdGVtcGVyYXR1cmVfZXhhbXBsZSNUZW1wZXJhdHVyZVNlbnNvciIvPg0KICAgICAgICA8dGVtcGVyYXR1cmVfZXhhbXBsZTpoYXNUZW1wZXJhdHVyZU1lYXN1cmluZ0Z1bmN0aW9uIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlI1RlbXBGdW5jdGlvbjEiLz4NCiAgICA8L293bDpOYW1lZEluZGl2aWR1YWw+DQoNCiAgICA8b3dsOk5hbWVkSW5kaXZpZHVhbCByZGY6YWJvdXQ9Imh0dHA6Ly93d3cub25lbTJtLm9yZy9vbnRvbG9neS9ob3VzZXNfdGVtcGVyYXR1cmVfZXhhbXBsZSNUZW1wRnVuY3Rpb24xIj4NCiAgICAgICAgPHJkZjp0eXBlIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L3RlbXBlcmF0dXJlX2V4YW1wbGUjVGVtcGVyYXR1cmVNZWFzdXJpbmdGdW5jdGlvbiIvPg0KICAgICAgICA8dGVtcGVyYXR1cmVfZXhhbXBsZTptZWFzdXJlc1RlbXBlcmF0dXJlIHJkZjpyZXNvdXJjZT0iaHR0cDovL3d3dy5vbmVtMm0ub3JnL29udG9sb2d5L2hvdXNlc190ZW1wZXJhdHVyZV9leGFtcGxlI0luZG9vclRlbXBQcm9wZXJ0eTEiLz4NCiAgICA8L293bDpOYW1lZEluZGl2aWR1YWw+ICAgDQo8L3JkZjpSREY+DQo=</dspt>

<or>http://www.onem2m.org/ontology/temperature_example</or>

</m2m:sd>

### Decoding the base64 encoded descriptor attribute and extracting the valueIsStoredIn data property of  TempProperty1, yields the URI for accessing the latest content instance storing with the most recently measured temperature value: http://in.provider.com:7579/server/tempsensorae1/temperature/latest

HTTP Request:

GET /server/tempsensorae1/temperature/latest HTTP/1.1

Host: http://in.provider.com:7579

Accept: application/xml

X-M2M-RI: 12345

X-M2M-Origin: SOrigin

nmtype: short

HTTP Result:

200 OK

Accept: application/xml

X-M2M-RI: 12345

X-M2M-RSC: 2000

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m=http://www.onem2m.org/xml/protocols xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<pi>/server</pi>

<ty>4</ty>

<ct>20170519T064023</ct>

<ri>/sensor/tempsensorae1/ci-234523664</ri>

<lt>20170519T064023</lt>

<aei>SOrigin</aei>
 <con>75</con>
</m2m:cin>

So the content 75 is retrieved by the semantic discovery application – which it knows to be the indoor temperature of House#1 in Fahrenheit according to the semantic descriptor.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Annex A:
Mapping to oneM2M Base Ontology

Figure A-1 shows the mapping of the specific concepts of the simple ontology for the semantic annotation and discovery use case to the more general concepts of the oneM2M Base Ontology [i.3]. Thus the semantic integration with the concepts identified for oneM2M itself is achieved.

Figure A-1: Mapping of the introduced concepts to the oneM2M Base Ontology

When comparing to the concepts available in the complete oneM2M Base Ontology, it can be seen that the focus of the modelling here has been on the semantic aspects,  It is assumed that the functional aspects sre implemented by oneM2M AEs using the Mca interface. In the case of using non-oneM2M technologies and applications for the sensors, an interworking proxy would be needed that translates between oneM2M and the native technology. Using Generic Interworking as described in [i.4] with a complete modelling of the functionality according to the oneM2M Base Ontology (or an ontology that has been mapped to the oneM2M Base Ontology in a similar way as shown in Figure A-1) would allow the automatic creation of a oneM2M resource structure for the case and enable tool-support for the partially automated creation of the required interworking proxy.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of Changes to References Section -------------

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]	oneM2M TS-0011: "Common Terminology".

[i.3]	oneM2M TS-0012: "Base Ontology"

[i.4]	oneM2M TS-0030: “Generic Interworking”

[i.5]	oneM2M TR-0025: “Application Developer Guide”

[i.6]	oneM2M TS-0001:  “Functional Architecture”

[i.7]	oneM2M TS-0004: “Service Layer Core Protocol”

[i.8] 	oneM2M TS-0009: “HTTP Protocol Binding”

### -----------------------End of Changes to References Section -------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?