| Input Contribution |
| --- |
| Meeting ID* | TST#29 |
| Title:* | Missing TPs REG |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., yinjiaxin@huawei.com |
| Date:* | 2017-05-17 |
| Input related to* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0018 v0.1.9 |
| Decision requested or recommendation:* | Incorporate the contribution if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

##### 7.2.3.2.6	CE/REG/00002/00003

TP/oneM2M/CSE/REG/BV/011

| TP Id | TP/oneM2M/CSE/REG/BV/011 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration with the optional attribute OPTIONAL_ATTRIBUTE provided |
| Reference | TS-0001 10.1.1.2.2, 9.6.5-2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_IN_PROFILE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) and From set to AE_ID and Content containing AE resource containing OPTIONAL_ATTRIBUTE attribute } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/REG/BV/011_01 | TS-0001 9.6.5-2 | labels | AE |
| TP/oneM2M/CSE/REG/BV/011_02 | TS-0001 9.6.5-2 | AppName | AE |
| TP/oneM2M/CSE/REG/BV/011_03 | TS-0001 9.6.5-2 | pointOfAccess | AE |

##### 7.2.3.2.9	CE/REG/00002/00006

TP/oneM2M/CSE/REG/CRE/BV/009

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/009 |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 and provided preprovisioned SP_relative_ AE_ID. |
| Reference | TS-0001 10.1.1.2.2 case b, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_ CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having preconfigured AE_ID_stem } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to CSEBASE_RESOURCE_ADDRESS and From set to SP_RELATIVE_CSE_ID and Resource Type set to 2(AE) and Content containing AE resource representation } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing AE resource representation } | IUT ( AE |

##### 7.2.3.2.22	CE/REG/00004/00001

TP/oneM2M/CSE/REG/CRE/BV/0xx

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/011 |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <remoteCSE> resource with OPTIONAL_ATTRIBUTES. |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.4.2.1, TS-0001 9.6.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16(remoteCSE) and Content containing remoteCSE resource representation containing OPTIONAL_ATTRIBUTE attribute } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing remoteCSE resource representation } | IUT ( CSE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/REG/CRE/BV/0xx_01 | TS-0001 9.6.4 | labels | remoteCSE |
| TP/oneM2M/CSE/REG/CRE/BV/0xx_02 | TS-0001 9.6.4 | cseType | remoteCSE |
| TP/oneM2M/CSE/REG/CRE/BV/0xx_03 | TS-0001 9.6.4 | pointOfAccess | remoteCSE |
| TP/oneM2M/CSE/REG/CRE/BV/0xx_04 | TS-0001 9.6.4 | nodeLink | remoteCSE |

7.2.3.2.23	CE/REG/00004/00002

TP/oneM2M/CSE/REG/CRE/BV/0xx_01

7.2.3.2.24	CE/REG/00004/00003

TP/oneM2M/CSE/REG/CRE/BV/0xx_02

##### 7.2.3.2.25	CE/REG/00004/00004

TP/oneM2M/CSE/REG/CRE/BV/0xx_03

##### 7.2.3.2.26	CE/REG/00004/00005

TP/oneM2M/CSE/REG/CRE/BV/0xx_04