| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#29 |
| Source:* | Bob Flynn, Convida , Flynn.Bob@convidawireless.com |
| Date:* | 2017-05-21 |
| Reason for Change/s:* | To provide TPs for RemoteCSE requirements |
| CR against: Release* | 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 |
| Clauses * | 7.2.3.3.1, 7.2.3.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

| CE/REG/00004/00001 | Support <remoteCSE> resource with attributes multiplicity equals 1[1] | REQ-0001-09067 REQ-0001-09083 REQ-0001-09084 REQ-0001-09085 REQ-0001-09086 REQ-0001-09089 | TP/oneM2M/CSE/REG/RET/BV/006 TP/oneM2M/CSE/REG/CRE/BV/011 TP/oneM2M/CSE/REG/DEL/BV/002 |
| --- | --- | --- | --- |

| TS-0001_remoteCSE_006 | REQ-0001-09062 | 9.6.4 | General description. Perhaps not a good requirement. Describes end state of CSE registration process. |  |
| --- | --- | --- | --- | --- |
| TS-0001_remoteCSE_007 | REQ-0001-09063 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_008 | REQ-0001-09064 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_009 | REQ-0001-09065 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_010 | REQ-0001-09066 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_011 | REQ-0001-09067 | 9.6.4-1 | <subscription> at remoteCSE | TP/oneM2M/CSE/DMR/CRE/BV/001_xx |
| TS-0001_remoteCSE_012 | REQ-0001-09068 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_013 | REQ-0001-09069 | 9.6.4-1 | <schedule> at remoteCSE | TP/oneM2M/CSE/DMR/CRE/BV/001_xx |
| TS-0001_remoteCSE_014 | REQ-0001-09070 | 9.6.4-1 | <nodeAnnc> at remoteCSE |  |
| TS-0001_remoteCSE_015 | REQ-0001-09071 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_016 | REQ-0001-09072 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_017 | REQ-0001-09073 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_018 | REQ-0001-09074 | 9.6.4-1 | <containerAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_019 | REQ-0001-09075 | 9.6.4-1 | <group> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_020 | REQ-0001-09076 | 9.6.4-1 | <groupAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_021 | REQ-0001-09077 | 9.6.4-1 | <accessControlPolicy> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_022 | REQ-0001-09078 | 9.6.4-1 | <accessControlPolicyAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_023 | REQ-0001-09079 | 9.6.4-1 | <subscription> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_025 | REQ-0001-09080 | 9.6.4-1 | <scheduleAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_026 | REQ-0001-09081 | 9.6.4-1 | <nodeAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_027 | REQ-0001-09082 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_028 | REQ-0001-09083 | 9.6.4-3 | cseType. IN (M) MN/ASN (O) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_029 | REQ-0001-09084 | 9.6.4-3 | pointOfAccess. (O) M if rr=true | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_030 | REQ-0001-09085 | 9.6.4-3 | CSEBase (M)(WO) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_031 | REQ-0001-09086 | 9.6.4-3 | CSE-ID (M)(WO) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_032 | REQ-0001-09087 | 9.6.4-3 | M2M-Ext-ID (O) |  |
| TS-0001_remoteCSE_033 | REQ-0001-09088 | 9.6.4-3 | Trigger-Recipient-ID (O) |  |
| TS-0001_remoteCSE_034 | REQ-0001-09089 | 9.6.4-3 | RequestReachability (M) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_035 | REQ-0001-09090 | 9.6.4-3 | nodeLink (O) |  |

- Change old req id’s to new requirement ids.

- Identify TP’s for this list. There is a lot of overlap with existing tests, so I cross reference them to existing testcases. This can be entered in the tracking spreadsheet.

### -----------------------Start of change 0-------------------------------------------

### Resource Type remoteCSE

A <remoteCSE> resource shall represent a Registree CSE that is registered to the Registrar CSE. <remoteCSE> resources shall be located directly under the <CSEBase> resource of Registrar CSE.

Similarly <remoteCSE> resource shall also represent a Registrar CSE. <remoteCSE> resource shall be located directly under the <CSEBase> resource of Registree CSE.

For example, when CSE1 (Registree CSE) registers with CSE2 (Registrar CSE), there will be two <remoteCSE> resources created: one in CSE1: <CSEBase1>/<remoteCSE2> and one in CSE2: <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> does not mean CSE2 registered with CSE1 in the example above.

Figure 9.6.4-1: Structure of <remoteCSE> resource

The <remoteCSE> resource shall contain the child resources specified in table 9.6.4-1. The <remoteCSE> resource may contain <remoteCSEAnnc> child resources.

Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resources of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> |
| [variable] | <containerAnnc> | 0..n | Announced variant of <container>. See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> |
| [variable] | <groupAnnc> | 0..n | Announced variant of <group>. See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> |
| [variable] | <accessControlPolicyAnnc> | 0..n | Announced variant of <accessControlPolicy>. See clause 9.6.2 | <accessControlPolicy> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <pollingChannel> | 0..1 | See clause 9.6.21. If requestReachability is FALSE, the CSE that created this <remoteCSE> resource should create a <pollingChannel> resource and perform long polling. The <pollingChannel> shall be utilized by the parent resource. | None |
| [variable] | <schedule> | 0..1 | This resource defines the reachability schedule information of the CSE represented by the parent <remoteCSE> resource. See clause 9.6.9 for <schedule>. | <scheduleAnnc> |
| [variable] | <remoteCSEAnnc> | 0..n | Announced variant of <remoteCSEAnnc> defined in the present clause 9.6.4. | <remoteCSEAnnc> |
| [variable] | <nodeAnnc> | 0..n | Announced variant of <node>. This announced resource is assoiated with a <node> resource that is hosted on a CSE which is represented by the parent <remoteCSE> or <remoteCSEAnnc> resource. See clause 9.6.18 for <node>. | <nodeAnnc> |
| [variable] | <AEAnnc> | 0..n | Announced variant of <AE>. See clause 9.6.5 | <AEAnnc> |
| [variable] | <locationPolicyAnnc> | 0..n | Announced variant of <locationPolicy>. See clause 9.6.10 | <locationPolicyAnnc> |

The <remoteCSE> resource shall contain the attributes specified in table 9.6.4-2.

Table 9.6.4-2: Attributes of <remoteCSE> resource

| Attributes of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| cseType | 0..1 | WO | Indicates the type of CSE represented by the created resource. Mandatory for an IN-CSE, hence multiplicity (1). Its presence is subject to SP configuration in case of an ASN-CSE or a MN-CSE. | OA |
| pointOfAccess | 0..1 (L) | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. If this information is not provided, the CSE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the CSE without using the PoA. | OA |
| CSEBase | 1 | WO | The address of the <CSEBase> resource represented by this <remoteCSE> resource. | OA |
| CSE-ID | 1 | WO | The CSE identifier of the remote CSE represented by this <remoteCSE> resource in SP-relative CSE-ID format (clause 7.2). | OA |
| M2M-Ext-ID | 0..1 | RW | Supported when Registrar is IN-CSE. See clause 7.1.8 where this attribute is described. This attribute is used only for the case of dynamic association of M2M-Ext-ID and CSE-ID. | NA |
| Trigger-Recipient-ID | 0..1 | RW | Supported when Registrar is IN-CSE. See clause 7.1.10 where this attribute is described. This attribute is used only for the case of dynamic association of M2M-Ext-ID and CSE-ID. | NA |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> resource can receive a request from other AE/CSE(s), this attribute is set to "TRUE" otherwise "FALSE" (see note) | OA |
| nodeLink | 0..1 | RW | The resource identifierof a <node> resource that stores the node specific information of the node on which the CSE represented by this <remoteCSE> resource resides. | OA |
| NOTE: Even if this attribute is set to "FALSE", it does not mean it AE/CSE is always unreachable by all entities. E.g. the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. |

### -----------------------End of change 0-------------------------------------------

### -----------------------Start of change 1-------------------------------------------

##### CE/DMR/00001/00001

Support <container> resource with attributes multiplicity equals 1[1]

###### CREATE OPERATION

TP/oneM2M/CSE/DMR/CRE/BV/001

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/001 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource on the TARGET_RESOURCE_ADDRESS of type PARENT_RESOURCE_TYPE with resource name not provided |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the Originator having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to RESOURCE_TYPE and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing RESOURCE_TYPE resource containing no resourceName attribute } | IUT ( AE |
|  | then { the IUT creates the RESOURCE_TYPE resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing RESOURCE_TYPE resource containing Valid resourceName attribute } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | PARENT_RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/001_01 | TS-0001 10.2.4.1 | 3 (container) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_02 | TS-0001 10.2.4.1 | 3 (container) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_03 | TS-0001 10.2.4.1 | 3 (container) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_04 | TS-0001 10.2.7.2 | 9 (group) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_05 | TS-0001 10.2.7.2 | 9 (group) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_06 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_07 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_08 |  | 18 (schedule) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_09 |  | 18 (schedule) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_10 |  | 18 (schedule) | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_11 | TS-0001 10.2.13.2 | 15 (pollingChannel) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_12 | TS-0001 10.2.11.2 | 23 (subscription) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_13 | TS-0001 10.2.11.2 | 23 (subscription) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_14 | TS-0001 10.2.11.2 | 23 (subscription) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_15 | TS-0001 10.2.11.2 | 23 (subscription) | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_16 | TS-0001 10.2.11.2 | 23 (subscription) | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_17 | TS-0001 10.2.11.2 | 23 (subscription) | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_xx | TS-0001 9.6.4-1 | 23 (subscription) | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/BV/001_xx | TS-0001 9.6.4-1 | 18 (schedule) | 16 (remoteCSE) |

TP/oneM2M/CSE/DMR/CRE/BV/001_01

TP/oneM2M/CSE/DMR/CRE/BV/002_01

TP/oneM2M/CSE/DMR/CRE/BV/003

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation of a RESOURCE_TYPE resource with an existing resource name provided by AE |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS and the AE containing a child resource containing resourceName attribute set to NAME } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to AE_RESOURCE_ADDRESS and Resource Type set to RESOURCE_TYPE and From set to AE-ID and Content containing RESOURCE_TYPE resource containing resourceName attribute set to NAME } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 5106 (ALREADY_EXISTS) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/003_01 | TS-0001 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_02 | TS-0001 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_03 | TS-0001 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_05 | TS-0001 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/BV/003_06 | TS-0001 10.2.11.2 | 23 (subscription) |

TP/oneM2M/CSE/DMR/CRE/BV/003_01

TP/oneM2M/CSE/DMR/CRE/BV/009

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/009 |
| --- | --- |
| Test objective | Check that the IUT increaments and then copies the field value of attribute stateTag in parent container resource when contentInstance resource is created as the direct child of the parent container |
| Reference | TS-0001 9.6.1.3.2, TS-0004 7.4.7.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing a container resource CONTAINER_RESOURCE_ADDRESS containing stateTag attribute and the AE having privileges to perform CREATE operation on the resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to CONTAINER_RESOURCE_ADDRESS and From set to AE_ID and Resource Type set to 4 (contentInstance) and no Content } | IUT ( AE |
|  | then { the IUT increments stateTag attribute of CONTAINER_RESOURCE_ADDRESS resource andthe IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/DMR/CRE/BV/015

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/015 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource with the optional attribute OPTIONAL_ATTRIBUTE provided |
| Reference | TS-0001 10.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_IN_PROFILE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to AE_RESOURCE_ADDRESS and From set to AE-ID and Content containing RESOURCE_TYPE resource containing valid OPTIONAL_ATTRIBUTE attribute } | IUT ( AE |
|  | then { the IUT creates the RESOURCE_TYPE resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/015_01 | TS-0001 9.6.1.3.2-1 | accessControlPolicyIDs | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_02 | TS-0001 9.6.1.3.1-1 | expirationTime | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_03 | TS-0001 9.6.1.3.2-1 | labels | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_04 | TS-0001 9.6.6-2 | maxNrOfInstances | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_05 | TS-0001 9.6.6-2 | maxByteSize | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_06 | TS-0001 9.6.6-2 | maxInstanceAge | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_07 | TS-0001 9.6.6-2 | ontologyRef | container |
| TP/oneM2M/CSE/DMR/CRE/BV/015_08 | TS-0001 9.6.1.3.1-1 | expirationTime | contentInstance |
| TP/oneM2M/CSE/DMR/CRE/BV/015_09 | TS-0001 9.6.1.3.2-1 | labels | contentInstance |
| TP/oneM2M/CSE/DMR/CRE/BV/015_10 | TS-0001 9.6.7-2 | creator | contentInstance |
| TP/oneM2M/CSE/DMR/CRE/BV/015_11 | TS-0001 9.6.7-2 | contentInfo | contentInstance |
| TP/oneM2M/CSE/DMR/CRE/BV/015_12 | TS-0001 9.6.7-2 | ontologyRef | contentInstance |
| TP/oneM2M/CSE/DMR/CRE/BV/015_13 | TS-0001 9.6.1.3.1-1 | expirationTime | accessControlPolicy |
| TP/oneM2M/CSE/DMR/CRE/BV/015_14 | TS-0001 9.6.1.3.2-1 | labels | accessControlPolicy |
| TP/oneM2M/CSE/DMR/CRE/BV/015_15 | TS-0001 9.6.1.3.2-1 | accessControlPolicyIDs | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_16 | TS-0001 9.6.1.3.1-1 | expirationTime | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_17 | TS-0001 9.6.1.3.2-1 | labels | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_18 | TS-0001 9.6.8-2 | eventNotificationCriteria | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_19 | TS-0001 9.6.8-2 | expirationCounter | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_20 | TS-0001 9.6.8-2 | groupID | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_21 | TS-0001 9.6.8-2 | notificationForwardingURI | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_22 | TS-0001 9.6.8-2 | batchNotify | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_23 | TS-0001 9.6.8-2 | rateLimit | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_24 | TS-0001 9.6.8-2 | preSubscriptionNotify | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_25 | TS-0001 9.6.8-2 | pendingNotification | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_26 | TS-0001 9.6.8-2 | notificationStoragePriority | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_27 | TS-0001 9.6.8-2 | latestNotify | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_28 | TS-0001 9.6.8-2 | notificationContentType | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_29 | TS-0001 9.6.8-2 | notificationEventCat | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_30 | TS-0001 9.6.8-2 | creator | subscription |
| TP/oneM2M/CSE/DMR/CRE/BV/015_31 | TS-0001 9.6.8-2 | subscriberURI | subscription |

TP/oneM2M/CSE/DMR/CRE/BV/015_02

###### RETRIEVE OPERATION

TP/oneM2M/CSE/DMR/RET/BV/013_03

###### UPDATE OPERATION

TP/oneM2M/CSE/DMR/UPD/BV/010

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/010 |
| --- | --- |
| Test objective | Check that the stateTag attribute of a container resource is increased when an update operation has been performed on its child resource |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a container resource containing CHILD_RESOURCE_TYPE resource containing valid ATTRIBUTE_NAME attribute set to VALUE_1 and the AE having privileges to perform UPDATE operation on the TARGET_CHILD_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_CHILD_RESOURCE_ADDRESS and From set to AE_ID Content containing CHILD_RESOURCE_TYPE resource containing valid ATTRIBUTE_NAME attribute set to VALUE_2 } | IUT  AE |
|  | then { the IUT increments the stateTag attribute of container resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) } | IUT  AE |

TP/oneM2M/CSE/DMR/UPD/BV/014

| TP Id | TP/oneM2M/CSE/DMR/UPD/BV/014 |
| --- | --- |
| Test objective | Check that the IUT updates successfully the value of the optional attribute OPTIONAL_ATTRIBUTE of the RESOURCE_TYPE resource. |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_IN_PROFILE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created the RESOURCE_TYPE resource and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing RESOURCE_TYPE resource containing OPTIONAL_ATTRIBUTE attribute set to VALUE } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing RESOURCE_TYPE resource containing OPTIONAL_ATTRIBUTE attribute set to VALUE } | IUT ( AE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/BV/014_01 | TS-0001 9.6.1.3.2-1 | accessControlPolicyIDs | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_02 | TS-0001 9.6.1.3.1-1 | expirationTime | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_03 | TS-0001 9.6.1.3.2-1 | labels | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_04 | TS-0001 9.6.6-2 | maxNrOfInstances | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_05 | TS-0001 9.6.6-2 | maxByteSize | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_06 | TS-0001 9.6.6-2 | maxInstanceAge | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_07 | TS-0001 9.6.6-2 | ontologyRef | container |
| TP/oneM2M/CSE/DMR/UPD/BV/014_08 | TS-0001 9.6.1.3.1-1 | expirationTime | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/BV/014_09 | TS-0001 9.6.1.3.2-1 | labels | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/BV/014_10 | TS-0001 9.6.2-2 | Privileges | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/BV/014_11 | TS-0001 9.6.2-2 | selfPriviliges | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/BV/014_12 | TS-0001 9.6.1.3.2-1 | accessControlPolicyIDs | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_13 | TS-0001 9.6.1.3.1-1 | expirationTime | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_14 | TS-0001 9.6.1.3.2-1 | labels | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_15 | TS-0001 9.6.8-2 | eventNotificationCriteria | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_16 | TS-0001 9.6.8-2 | expirationCounter | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_17 | TS-0001 9.6.8-2 | groupID | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_18 | TS-0001 9.6.8-2 | notificationForwardingURI | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_19 | TS-0001 9.6.8-2 | batchNotify | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_20 | TS-0001 9.6.8-2 | rateLimit | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_21 | TS-0001 9.6.8-2 | pendingNotification | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_22 | TS-0001 9.6.8-2 | notificationStoragePriority | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_23 | TS-0001 9.6.8-2 | latestNotify | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_24 | TS-0001 9.6.8-2 | notificationContentType | subscription |
| TP/oneM2M/CSE/DMR/UPD/BV/014_25 | TS-0001 9.6.8-2 | notificationEventCat | subscription |

TP/oneM2M/CSE/DMR/UPD/BV/014_02

TP/oneM2M/CSE/DMR/UPD/BV/018_07

###### DELETE OPERATION

TP/oneM2M/CSE/DMR/DEL/BV/001

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/001 |
| --- | --- |
| Test objective | Check that the IUT accepts the deletion of a RESOURCE_TYPE resource |
| Reference | TS-0001 10.1.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE and the AE having privileges to perform DELETE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID } | IUT  AE |
|  | then { the IUT deletes the TARGET_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 2002 (DELETED) } | IUT  AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/BV/001_01 | TS-0001 10.2.4.4 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/BV/001_02 | TS-0001 10.2.7.5 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/BV/001_03 | TS-0001 10.2.21.4 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/BV/001_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/BV/001_05 | TS-0001 10.2.13.5 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/DEL/BV/001_06 | TS-0001 10.2.11.5 | 23 (subscription) |

TP/oneM2M/CSE/DMR/DEL/BV/001_01

TP/oneM2M/CSE/DMR/DEL/BV/003

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/003 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to delete the resource TARGET_RESOURCE_ADDRESS which does not exist |
| Reference | TS-0001 10.1.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having not yet created a resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID } | IUT ( AE |
|  | then { the IUT does not delete the TARGET_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

Editor’s Note: permutations need to be added here.

TP/oneM2M/CSE/DMR/DEL/BV/004

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/004 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when AE tries to delete a child resource of a RESOURCE_TYPE resource when this resource has been already deleted |
| Reference | TS-0001 10.1.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing a child resource and the AE having privileges to perform DELETE operation on the resource TARGET_RESOURCE_ADDRESS and the AE having deleted the TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_CHILD_RESOURCE_ADDRESS and From set to AE_ID } | IUT  AE |
|  | then { the IUT does not delete the TARGET_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/BV/004_01 | TS-0001 10.2.4.4 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/BV/004_02 | TS-0001 10.2.7.5 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/BV/004_03 | TS-0001 10.2.21.4 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/BV/004_04 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/BV/004_05 | TS-0001 10.2.13.5 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/DEL/BV/004_06 | TS-0001 10.2.11.5 | 23 (subscription) |

TP/oneM2M/CSE/DMR/DEL/BV/004_01

TP/oneM2M/CSE/DMR/DEL/BV/005

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/005 |
| --- | --- |
| Test objective | Check that the stateTag attribute of a container resource is increased when a child resource is deleted |
| Reference | TS-0001 10.1.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a container resource containing a child resource and the AE having privileges to perform DELETE operation on the TARGET_CHILD_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_CHILD_RESOURCE_ADDRESS and From set to AE_ID } | IUT  AE |
|  | then { the IUT increments the stateTag attribute of the container resource and the IUT sends a valid Response containing Response Status Code set to 2002 (DELETED) } | IUT  AE |

TP/oneM2M/CSE/DMR/DEL/BV/006

| TP Id | TP/oneM2M/CSE/DMR/DEL/BV/006 |
| --- | --- |
| Test objective | Check that the IUT decreases the field value of attribute currentNrOfInstances and currentByteSize of parent container when a latest contentInstance resource is deleted successfully |
| Reference | TS-0001 10.2.19.5, TS-0004 7.4.8.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a container resource containing currentNrOfInstances attribute set to NR_OF_INSTANCES and currentByteSize attribute set to BYTE_SIZE_OF_DATA and a contentInstance resource TARGET_RESOURCE_ADDRESS and the AE having privileges to perform DELETE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID } | IUT ( AE |
|  | then { the IUT decreases the currentNrOfInstances attribute of container resource and the IUT decreases the currentByteSize attribute of container resource and the IUT sends a valid Response containing Response Status Code set to 2002 (DELETED) and } | IUT ( AE |

Editor’s Note: Need to clarify if needed to split into two separate test purposes.

### -----------------------End of change 1---------------------------------------------

# Comments

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-09062

REQ-0001-09074

REQ-0001-09075

REQ-0001-09076

REQ-0001-09077

REQ-0001-09078

REQ-0001-09067

REQ-0001-09079

REQ-0001-09069

REQ-0001-09080

REQ-0001-09070

REQ-0001-09081

REQ-0001-09083

REQ-0001-09084

REQ-0001-09085

REQ-0001-09086

REQ-0001-09087

REQ-0001-09088

REQ-0001-09089

REQ-0001-09090

Should add to the initial conditions that the IUT supports RESOURCE_TYPE.