| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#29.1 |
| Source:* | Ting Martin MIAO, KETI, martin.miao@keti.re.kr SeungMyeong JEONG, KETI, sm.jeong@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.re.kr |
| Date:* | 2017-06-07 |
| Reason for Change/s:* | Clarification of Implementation Procedures |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0035 v0.1.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TR-0035 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clarification implementation procedures in TR-0035 Device management user guide.

Changes includes:

- Resource ID format

- CoAP request message

- Update informative reference list

- Typo correction

- Etc.

### -----------------------Start of change 1-------------------------------------------

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

As a Technical Report (TR) is entirely informative it shall not list normative references.

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

[i.2]     oneM2M TS-0001: "Functional Architecture".

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 5	Device management over the service layer

## 5.1	Introduction

oneM2M uses <mgmtObj> resource for device management. For device management  over the service layer, the <mgmtObj> that is used for the management of the managed entity is located at different places in case of the characteristic of the managed entity. In either of the case, there exists one driver or client on the managed entity that observes the update of the <mgmtObj> resource to perform management operation.

For ASN, MN and IN which has CSE, the <mgmtObj> is hosted on the corresponding ASN-CSE, MN-CSE and IN-CSE as child resource of the <node> resource that represents the ASN, MN and IN. The managed entity observes the <mgmtObj> directly to perform the management operation.

For ADN, the <mgmtObj> resource is hosted on the registrar CSE of the ADN-AE as child resource of the <node> resource that represents the ADN. The ADN-AE in this case should subscribe the <mgmtObj> resources under the corresponding <node> resource to receive notifications on any update of the <mgmtObj> resource. The ADN which is the managed entity in this case further perform the management operation based on the notifications received.

For NoDN, the <mgmtObj> resource is hosted on the CSE which is NoDN is connected to. As NoDN is not an oneM2M defined entity, the connection between NoDN and the CSE is out of scope of oneM2M and is implementation specific. In this case, the <mgmtObj> resource on the CSE under the corresponding <node> resource should be monitored to determine if any management operation need to be performed. This part is implementation specific and is out of scope of oneM2M as well.

## 5.2	Use case

An application want to retrieve the current  avaiable memory of the device. In this case, the specialization of <mgmtObj> memory is used Annex D.4 of [2]. In the memory specialization, memAvailable is the attribute that contains the required information. The application can get to know the available memory by retrieving the resource.

Figure: 5.2-1: Use case for management

## 5.3	Architecture

### 5.3.1	Management of ASN, MN and IN

Figure: 5.3.1-1: Architecture for management of IN,MN,ASN

In the architecture for management of IN, MN and ASN. As those Managed Entities have their own CSEBase resource, they have the capability to host oneM2M resources. When using device management over the service layer, the [memory] resource is directly hosting under the <node> resource of the CSEBase. In this case, the <node> resource represents the IN, MN, ASN themselves.

The Driver is the software that interacts with the memory of the device that acquires the total memory and available memory from the system.

In this case, the [memory] specialization is modified by Driver using internal interface. The modification may be done periodically or some other policies which is out of scope of oneM2M standard.

Whenever the AE issues a RETRIEVE request to the [memory] specialization, the value from the resource is returned.

### 5.3.2	Management of ADN

Figure: 5.3.2-1: Architecture for management of ADN

In the architecture of management of ADN, the [memory] specialization is hosted on the Registrar CSE of the ADN. According to the supported configuration of oneM2M architecture, the Registrar CSE could be IN-CSE or MN-CSE.

In this case, the <node> resource hosted under the CSEBase of the Registrar CSE represents the ADN which is the managed entity. The driver gets the memory information using internal interfaces and make the ADN-AE updates the memory value to the [memory] specialization over the Mca reference point. The update over Mca is triggered periodically or based on the policy of the ADN which is implementation specific.

### 5.3.3	Management of NoDN

Figure: 5.3.3-1: Architecture for management of NoDN

In the architecture of management of NoDN, the [memory] specialization is hosted on the connection point of NoDN. The connection point is the entity that the NoDN is connected to. The entity has the adaptor that shares the same network protocol with NoDN.

In this case, the <node> resource hosted under the CSEBase represents the NoDN. And the connection between Driver and the CSE is out of scope of oneM2M. It may be Bluetooth, ZigBee or even proprietary.

The update of the memory information happens over the interface between driver and CSE which is out of scope of oneM2M.

## 5.4	Procedures

### 5.4.1	Management of ASN, MN and IN

Figure: 5.4.1-1: Procedures for management of IN, MN, ASN

001: The AE send an oneM2M Retrieve request primitive to the ResourceID of [memory] resource.

002: The CSE receives the Retrieve primitive and triggers the Driver to acquire the current available memory value, update the [memory] resource.

003: The CSE responds the AE with the representation of the [memory] resource.

Note: The AE could also subscribe the [memory] resource to get the notification on the update of the [memory] resource.

The [memory] resource is this case is locally created before hand by the Hosting CSE using internal interfaces.

### 5.4.2	Management of ADN

Figure: 5.4.2-1: Procedures for management of ADN

001: The AE sends Retrieve request to Registrar CSE of ADN-AE. Requesting the [memory] resource.

003: The Registrar CSE responds with the representation of the [memory] resource.

002: The ADN internally acquires the available memory information.

004: The ADN-AE updateds the [memory] resource using Mca reference point.

005: Update successful

Note that 001, 003 and 002, 004 don’t have a specific order. The ADN is updating the [memory] resource periodically. In 003, the Registrar CSE is responding always the current resource.

Subscritpion and notification could also be used by the AE to monitor the current status of the [memory] resource.

The [memory] resource in this case is created by ADN-AE.

### 5.4.3	Management of NoDN

Figure: 5.4.3-1: Procedures for management of NoDN

001: The AE sends Retrieve request to connecton point of NoDN. Requesting the [memory] resource.

003: The CSE of the connection point responds with the representation of the [memory] resource.

002: The NoDN internally acquires the available memory information.

004: The NoDN updateds the [memory] resource using protocol that is non-oneM2M.

Note that 001, 003 and 002, 004 don’t have a specific order. The NoDN is updating the [memory] resource periodically. In 003, the Registrar CSE is responding always the current resource.

The [memory] resource in this case is created by NoDN via non oneM2M interface.

## 5.5	Implementation

### 5.5.1	Introduction

In this implementation,  the current document is using HTTP binding and JSON serialization as examples, and SP-relative-structured resource addressing format is used.

Following resource ID and/or entity ID is used:

- Memory Resource

  - Resource Name "memory001"

  - Resource ID "m343245334adf" represented in CSE-relative Unstructured-Resource-ID of the [memory] resource

  - Parent Resource ID "n893051036jdg"

- AE-ID "C324352841DAS" of the managed entity

- Registrar/Hosting CSE

  - SP-relative CSE-ID "/CSE0034234"

  - CSE Resource Name "server"

- Host name of the Registrar/Hosting CSE "in.management.server.com".

### 5.5.2	Management of ASN, MN and IN

| Step | Message Example |
| --- | --- |
| 001 | HTTP Request GET /~/CSE0034234/server/memory001 HTTP/1.1 Host : in.management.server.com X-M2M-RI : 1234 X-M2M-Origin: C324352841DAS Accept : application/json |
| 002 | HTTP Response 200 OK X-M2M-RI : 1234 X-M2M-RSC : 2000 { "m2m:mgo" : { "ri":"m343245334adf", "pi":"n893051036jdg", "ct":"20161129T121550", "et":"20181231T235959", "lt":"20161130T152341", "ty":13, "rn":"memory001", "mgd":1003, "mma":800, "mmt":1024 } } |

### 5.5.3	Management of ADN

| Step | Message Example |
| --- | --- |
| 001 | Same as 001 in 5.5.2 |
| 002 | Same as 002 in 5.5.2 |
| 004 | HTTP Request PUT /~/CSE0034234/server/memory001?rcn=0 HTTP/1.1 Host : in.management.server.com X-M2M-RI : 1235 Content-Type: application/json X-M2M-Origin: C324352841DAS { "m2m:mgo":{ "mma":600 } } |
| 005 | HTTP Response 200 OK X-M2M-RI : 1235 X-M2M-RSC : 2004 |

### 5.5.4	Management of NoDN

001 and 003 is the same as in clause 5.5.2.

002 and 004 is protocol specific and even proprietary, thus it’s out of scope of oneM2M.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

# 6	Device management using external management technologies

## 6.1	Introduction

In the case of device management using external management technologies such as OMA DM, LWM2M or BBF TR069. All management is done through IN-CSE, since only the IN-CSE has the capability to talk to the Management Server. Therefore, in this case, all <node> resource that represents the managed entity is hosted under the <CSEBase> of IN-CSE. The manged entity may be IN, MN, ASN, ADN or NoDN. Then the <mgmtObj> that is used for management is hosted as the child resource of <node> resource. The attribute objectIDs and objectPaths of the <mgmtObj> are set in this case to map to the external management objects.

## 6.2	Use case

An application want to retrieve the current  avaiable memory of the device. In this case, the specialization of <mgmtObj> memory is used Annex D.4 of [2]. In the memory specialization, memAvailable is the attribute that contains the required information. The application can get to know the available memory by retrieving the resource.

Figure: 6.2-1: Use case for management

## 6.3	Architecture

Figure: 6.3-1: Architecture for management using external technology

In the case of management using external management technology, all management related resources are hosted on the IN-CSE. IN-CSE interacts with Management Server through ms interface and triggers the Management Server to send management commands to Managed Entity through the mc interface. mc and ms interface is defined by external management technology or implementation specific which is out of scope of oneM2M.

The Management Server may be deployed together with the IN-CSE, in this case, the IN-CSE directly sends out management commands through mc interface to the Managed Entity. The Management Server may also be deployed separately from the IN-CSE, in this case, the IN-CSE need to send commands to Management Server to trigger the Management Server to send out management commands to the Managed Entity. ms interface may be implementation specific.

## 6.4	Procedures

Figure: 6.4-1: Procedures for management to ADN

001: AE retrieves [memory] resource specialization from IN-CSE over mca interface.

002: On receiving the request, the IN-CSE sends management command to managed entity using external management technology implementation.

003: On the managed entity, the driver aquires the memory information.

004: The managed entity responds with aquired memory information over the mc interface.

005: The IN-CSE updates the [memory] resource and respond the RETRIEVE request with the representation of [memory] resource.

## 6.5	Implementation

In the implementation, the document is using LWM2M as the external management technology. Resource ID and/or entity ID that are defined in Section 5.5.1 is also applicable to current section.

In addition, host name of the managed entity is named as "adn.managed.entity.com", the memory resource name is "memory002", the memory resource ID is "m463245245afg", and the parent resource ID of the memory resource is  "n993051028asd". The request URL for the managed entity is assumed as "coap://adn.managed.entity.com/adn001/memory".

| Step | Message Example |
| --- | --- |
| 001 | HTTP Request GET /~/CSE0034234/server/memory002 HTTP/1.1 Host : in.management.server.com X-M2M-RI : 3454 X-M2M-Origin: C324352841DAS Accept : application/json |
| 002 | CoAP Request Method : 0.01 (GET) Uri-Host : adn.managed.entity.com Uri-Path : adn001 Uri-Path : memory oneM2M-FR : C324352841DAS oneM2M-RQI: 4553 Payload : empty |
| 004 | CoAP Response X-M2M-RSC : 2.05 (OK) oneM2M-RQI : 4553 Content-Format: 50 (application/json) Payload : {memory_object_serialized_in_JSON} |
| 005-2 | HTTP Response X-M2M-RI : 3454 X-M2M-RSC : 2000 { "m2m:mgo" : { "ri":"m463245245afg", "pi":"n993051028asd", "ct":"20161129T121550", "et":"20181231T235959", "lt":"20161130T152341", "ty":13, "rn":"memory002", "mgd":1003, "mma":800, "mmt":1024 } } |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Change to a random string would make more sense