| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#30 |
| Source:* | Bob Flynn, Convida , Flynn.Bob@convidawireless.com Keebum Kim, TTA, Keebum.kim@tta.or.kr |
| Date:* | 2017-07-07 |
| Reason for Change/s:* | To provide TPs for ACP requirements |
| CR against: Release* | 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

R01 includes additional mappings and uses DISCOVERY

R02 includes changes from 0185R01 rewording the initial conditions of tests that are included in this contribution.

R03 rename CSE/DIS/RET/xxx back to CSE/DIS/xxx

| CE/SEC/00001/00001 | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] | REQ-0001-09025 REQ-0001-09026 REQ-0001-09030 REQ-0001-09031 REQ-0001-09032 REQ-0001-09033 | TP/oneM2M/CSE/DMR/CRE/BV/001_06 TP/oneM2M/CSE/DMR/CRE/BV/001_07 |
| --- | --- | --- | --- |

The last column can be used to update the requirements tracking spreadsheet.

| TS-0001_ACP_002 | REQ-0001-09023 | 9.6.2 | TP/oneM2M/CSE/SEC/ACP/CRE/003 TP/oneM2M/CSE/SEC/ACP/CRE/004 |
| --- | --- | --- | --- |
| TS-0001_ACP_013 | REQ-0001-09024 | 9.6.2.1-1 | TP/oneM2M/CSE/SEC/ACP/003 |
| TS-0001_ACP_014 | REQ-0001-09025 | 9.6.2.1-1 | TP/oneM2M/CSE/SEC/ACP/001 – error if ACOR does not have originator. ALL OTHER TESTS if ACOR does have originator. |
| TS-0001_ACP_015 | REQ-0001-09026 | 9.6.2.1-1 | TP/oneM2M/CSE/SEC/ACP/004 |
| TS-0001_ACP_016 | REQ-0001-09027 | 9.6.2.2-1 | TP/oneM2M/CSE/SEC/ACP/005 TP/oneM2M/CSE/SEC/ACP/006 |
| TS-0001_ACP_017 | REQ-0001-09028 | 9.6.2.2-1 | TP/oneM2M/CSE/SEC/ACP/007 TP/oneM2M/CSE/SEC/ACP/008 |
| TS-0001_ACP_018 | REQ-0001-09029 | 9.6.2.2-1 | TP/oneM2M/CSE/SEC/ACP/009 TP/oneM2M/CSE/SEC/ACP/010 |
| TS-0001_ACP_019 | REQ-0001-09030 | 9.6.2.3-1 | TP/oneM2M/CSE/SEC/ACP/004_RET TP/oneM2M/CSE/SEC/ACP/001_RET |
| TS-0001_ACP_020 | REQ-0001-09031 | 9.6.2.3-1 | TP/oneM2M/CSE/SEC/ACP/004_CRE TP/oneM2M/CSE/SEC/ACP/001_CRE |
| TS-0001_ACP_021 | REQ-0001-09032 | 9.6.2.3-1 | TP/oneM2M/CSE/SEC/ACP/004_UPD TP/oneM2M/CSE/SEC/ACP/001_UPD |
| TS-0001_ACP_022 | REQ-0001-09033 | 9.6.2.3-1 | TP/oneM2M/CSE/SEC/ACP/004_DEL TP/oneM2M/CSE/SEC/ACP/001_DEL |
| TS-0001_ACP_023 | REQ-0001-09034 | 9.6.2.3-1 | TP/oneM2M/CSE/DIS/RET/001 ADDED A TEST TO RETURN EMPTY SET WHEN MATCHED RESOURCES DO NOT GRANT DISCOVER PERMISSION TP/oneM2M/CSE/DIS/RET/008 |
| TS-0001_ACP_024 | REQ-0001-09035 | 9.6.2.3-1 | TP/oneM2M/CSE/SUB/NTF/001 – no permission TP/oneM2M/CSE/SUB/NTF/002 |
| TS-0001_ACP_025 | REQ-0001-09036 | 9.6.2-1 | TP/oneM2M/CSE/DMR/CRE/001_SUB/ACP |
| TS-0001_ACP_026 | REQ-0001-09037 | 9.6.2-2 | TP/oneM2M/CSE/SEC/ACP/CRE/001 |
| TS-0001_ACP_027 | REQ-0001-09038 | 9.6.2-2 | TP/oneM2M/CSE/SEC/ACP/CRE/002 |
| TS-0001_ACP_028 | REQ-0001-09039 | 9.6.2-1 |  |
| TS-0001_ACP_010 | REQ-0001-10123 | 10.2.21.1 | TP/oneM2M/CSE/DMR/CRE/001_ACP/CB TP/oneM2M/CSE/DMR/CRE/001_ACP/AE TP/oneM2M/CSE/DMR/CRE/015_ET/ACP TP/oneM2M/CSE/DMR/CRE/003_ACP TP/oneM2M/CSE/DMR/CRE/002_ACP TP/oneM2M/CSE/SEC/ACP/CRE/001 |
| TS-0001_ACP_011 | REQ-0001-10124 | 10.2.21.2 | TP/oneM2M/CSE/DMR/RET/013_ACP TP/oneM2M/CSE/DMR/RET/001_ACP |
| TS-0001_ACP_012 | REQ-0001-10125 | 10.2.21.4 | TP/oneM2M/CSE/DMR/DEL/001_ACP TP/oneM2M/CSE/DMR/DEL/004_ACP |
| TS-0001_ACP_029 | REQ-0001-10126 | 10.2.21.3 | TP/oneM2M/CSE/DMR/UPD/014_ET/ACP TP/oneM2M/CSE/DMR/UPD/014_PV/ACP TP/oneM2M/CSE/DMR/UPD/014_PVS/ACP TP/oneM2M/CSE/DMR/UPD/018_ET/ACP TP/oneM2M/CSE/DMR/UPD/018_PV/ACP TP/oneM2M/CSE/DMR/UPD/018_PVS/ACP TP/oneM2M/CSE/SEC/ACP/UPD/001 |

- Change old req id’s to new requirement ids.

- Identify TP’s for this list.

- Change intitial conditions in several test to specify DISCOVER permission instead of RETRIEVE permission.

- Added new test purpose to cover when resources that match the filter criteria do not include DISCOVER permission.

### -----------------------Start of change 0.1-------------------------------------------

### Resource Type accessControlPolicy

#### 9.6.2.0	Introduction

The Access Control Policies (ACPs) shall be used by the CSE to control access to the resources as specified in the present document and in oneM2M TS-0003 [3].

The ACP is designed to fit different access control models such as access control lists, role or attribute based access control.

The <accessControlPolicy> resource is comprised privileges and selfPrivileges attributes which represent a set of access control rules defining which entities (defined as accessControlOriginators) have the privilege to perform certain operations (defined as accessContolOperations) within specified contexts (defined as accessControlContexts) and are used by the CSEs in making Access Decision to specific resources.

In a privilege, each access control rule defines which AE/CSE is allowed for which operation. So for sets of access control rules an operation is permitted if it is permitted by one or more access control rules in the set.

For a resource that is not of <accessControlPolicy> resource type, the common attribute accessControlPolicyIDs for such resources (defined in table 9.6.1.3.2-1) contains a list of identifiers which link that resource to <accessControlPolicy> resources. The CSE Access Decision for such a resource shall follow the evaluation of the set of access control rules expressed by the privileges attributes defined in the <accessControlPolicy> resources.

The selfPrivileges attribute shall represent the set of access control rules for the <accessControlPolicy> resource itself.

The CSE Access Decision for <accessControlPolicy> resource shall follow the evaluation of the set of access control rules expressed by the selfPrivileges attributes defined in the <accessControlPolicy> resource itself.

Figure 9.6.2-1: Structure of <accessControlPolicy> resource

The <accessControlPolicy> resource shall contain the child resource specified in table 9.6.2-1.

Table 9.6.2-1: Child resources of <accessControlPolicy> resource

| Child Resources of <accessControlPolicy> | Child Resource Type | Multiplicity | Description | <accessControlPolicyAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |

The <accessControlPolicy> resource shall contain the attributes specified in table 9.6.2-2.

Table 9.6.2-2: Attributes of <accessControlPolicy> resource

| Attributes of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| labels | 0..1(L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| privileges | 1 | RW | A set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| selfPrivileges | 1 | RW | A set of access control rules that apply to the <accessControlPolicy> resource itself and accessControlPolicyIDs attribute of any other resource which is linked to this <accessControlPolicy> resource. | MA |

The set of access control rules represented in privileges and selfPrivileges attributes are comprised of 3-tuples (accessControlOriginators, accessControlContexts, accessControlOperations) with parameters shown in table 9.6.2-3 which are further described in the following clauses.

If privileges attribute contains no 3-tuples then this represent an empty set of the access control rules.

The selPrivileges attribute shall contain at least one 3-tuples.

The CSE access granting mechanism shall follow the procedure described in oneM2M TS-0003 [3] in clause 7.1 (Access Control Mechanism).

Table 9.6.2-3: Parameters in access-control-rule-tuples

| Name | Description |
| --- | --- |
| accessControlOriginators | See clause 9.6.2.1 |
| accessControlContexts | See clause 9.6.2.2 |
| accessControlOperations | See clause 9.6.2.3 |

#### 9.6.2.1	accessControlOriginators

The accessControlOriginators is a mandatory parameter in an access-control-rule-tuple. It represents the set of Originators that shall be allowed to use this access control rule. The set of Originators is described as a list of parameters, where the types of the parameter can vary within the list. Table 9.6.2.1-1 describes the supported types of parameters in accessControlOriginators. The following Originator privilege types shall be considered for access control policy check by the CSE.

Table 9.6.2.1-1: Types of Parameters in accessControlOriginators

| Name | Description |
| --- | --- |
| domain | A SP domain or SP sub-domain |
| originatorID | CSE-ID or AE-ID which represent an Originator identity |
| all | Any Originators are allowed to access the resource within the accessControlOriginators constraints |

#### 9.6.2.2	accessControlContexts

The accessControlContexts is an optional parameter in an access-control-rule-tuple that contains a list, where each element of the list, when present, represents a context that is permitted to use this access control rule. Each request context is described by a set of parameters, where the types of the parameters can vary within the set. Table 9.6.2.2-1 describes the supported types of parameters in accessControlContexts.

The following Originator accessControlContexts shall be considered for access control policy check by the CSE.

Table 9.6.2.2-1: Types of Parameters in accessControlContexts

| Name | Description |
| --- | --- |
| accessControlTimeWindow | Represents a time window constraint which is compared against the time that the request is received at the Hosting CSE. |
| accessControlLocationRegion | Represents a location region constraint which is compared against the location of the Originator of the request. |
| accessControlIpIPAddress | Represents an IP address constraint or IP address block constraint which is compared against the IP address of the Originator of the request. |

#### 9.6.2.3	accessControlOperations

The accessControlOperations is a mandatory parameter in an access-control-rule-tuple that represents the set of operations that are authorized using this access control rule. Table 9.6.2.3-1 describes the supported set of operations that are authorized by accessControlOperations.

The following accessControlOperations shall be considered for access control policy check by the CSE.

Table 9.6.2.3-1: Types of parameters in accessControlOperations

| Name | Description |
| --- | --- |
| RETRIEVE | Privilege to retrieve the content of an addressed resource |
| CREATE | Privilege to create a child resource |
| UPDATE | Privilege to update the content of an addressed resource |
| DELETE | Privilege to delete an addressed resource |
| DISCOVER | Privilege to discover the resource |
| NOTIFY | Privilege to receive a notification |

### -----------------------End of change 0.1-------------------------------------------

### -----------------------Start of change 0.2-------------------------------------------

### 10.2.21	<accessControlPolicy> Resource Procedures

#### 10.2.21.1	Create <accessControlPolicy>

This procedure shall be used to create an <accessControlPolicy> resource.

Table 10.2.21.1-1: <accessControlPolicy> CREATE

| <accessControlPolicy> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | Same as clause 10.1.1. |
| Pre-Processing at Originator | Same as clause 10.1.1. |
| Processing at Receiver | Same as clause 10.1.1. However the action (1) in step 002 shall be omitted. |
| Information in Response message | Same as clause 10.1.1. |
| Post-Processing at Originator | Same as clause 10.1.1. |
| Exceptions | Same as clause 10.1.1 |

#### 10.2.21.2	Retrieve <accessControlPolicy>

This procedure shall be used to retrieve attributes and child resource information of the <accessControlPolicy> resource.

Table 10.2.21.2-1: <accessControlPolicy> RETRIEVE

| <accessControlPolicy> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | Same as clause 10.1.2. |
| Pre-Processing at Originator | Same as clause 10.1.2. |
| Processing at Receiver | Addition to clause 10.1.2: The Receiver shall check access control rules defined in selfPrivileges of the <accessControlPolicy> resource>. |
| Information in Response message | Same as clause 10.1.2. |
| Post-Processing at Originator | Same as clause 10.1.2. |
| Exceptions | Addition to clause 10.1.2. |

#### 10.2.21.3	Update <accessControlPolicy>

This procedure shall be used to update attributes information of the <accessControlPolicy> resource.

Table 10.2.21.3-1: <accessControlPolicy> UPDATE

| <accessControlPolicy> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | Same as clause 10.1.3. |
| Pre-Processing at Originator | Same as clause 10.1.3. |
| Processing at Receiver | Addition to clause 10.1.3: The Receiver shall check access control rules defined in selfPrivileges of the <accessControlPolicy> resource. |
| Information in Response message | Same as clause 10.1.3. |
| Post-Processing at Originator | Same as clause 10.1.3. |
| Exceptions | Addition to clause 10.1.3. |

#### 10.2.21.4	Delete <accessControlPolicy>

This procedure shall be used to delete the <accessControlPolicy> resource.

Table 10.2.21.3-1: <accessControlPolicy> DELETE

| <accessControlPolicy> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | Same as clause 10.1.4. |
| Pre-Processing at Originator | Same as clause 10.1.4. |
| Processing at Receiver | Addition to clause 10.1.4: The Receiver shall check access control rules defined in selfPrivileges of the <accessControlPolicy> resource. |
| Information in Response message | Same as clause 10.1.4. |
| Post-Processing at Originator | Same as clause 10.1.4. |
| Exceptions | Addition to clause 10.1.4. |

### -----------------------End of change 0.2-------------------------------------------

### -----------------------Start of change 1-------------------------------------------

##### CE/DIS/00001/00001

Support the Discovery request with filterUsage equals to “Discovery”

###### RETRIEVE OPERATION

TP/oneM2M/CSE/DIS/ 001

| TP Id | TP/oneM2M/CSE/DIS/ 001 |
| --- | --- |
| Test objective | Check that the IUT returns successfully a list all discovered resource addresses |
| Reference | TS-0001 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 1 (Discovery Criteria) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing URIList representation } | IUT ( AE |

TP/oneM2M/CSE/DIS/ 003

| TP Id | TP/oneM2M/CSE/DIS/ 003 |
| --- | --- |
| Test objective | Check that the IUT returns the empty address list when no result matching with filter criteria is discovered |
| Reference | TS-0001 8.1.3 & 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform RETRIEVE operation and FILTER_CRITERIA_CONDITIONS not being applicable to the IUT } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing filterUsage set to 1 (Discovery Criteria) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and no Content } | IUT ( AE |

TP/oneM2M/CSE/DIS004

| TP Id | TP/oneM2M/CSE/DIS /004 |
| --- | --- |
| Test objective | Check that the IUT returns successfully a list of discovered resource addresses with Non-hierarchical addressing form when the Discovery Result Type is provided in the request |
| Reference | TS-0001 8.1.3 & 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Discovery Result Type set to 2 (unstructured) and Filter Criteria containing filterUsage set to 1 (Discovery Criteria) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing URIList representation containing unstructured addresses of discovered resources } | IUT ( AE |

TP/oneM2M/CSE/DIS/ 006

| TP Id | TP/oneM2M/CSE/DIS/ 006 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE sends requests to discover the resource TARGET_RESOURCE_ADDRESS which does not exist in the Hosting CSE |
| Reference | TS-0001 10.2.6.2, TS-0004 7.3.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having not yet created a containe resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 1 (Discovery Criteria) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

TP/oneM2M/CSE/DIS/ 007

| TP Id | TP/oneM2M/CSE/DIS/ 007 |
| --- | --- |
| Test objective | Check that the IUT responds the originator with an error when the originator sends a request including an invalid format of filter criteria to discover the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0001 10.2.6, TS-0004 7.3.3.6 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the originator AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS not being valid format } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4102 (CONTENTS_UNACCEPTABLE) } | IUT ( AE |

TP/oneM2M/CSE/DIS/008

| TP Id | TP/oneM2M/CSE/DIS/008 |
| --- | --- |
| Test objective | Check that the IUT returns the empty address list when resources match the filter criteria but they do not include DISCOVERY permission. |
| Reference | TS-0001 9.6.2.3 & 10.2.6 & TS-0004 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS not allowing the AE to perform DISCOVERY operation and FILTER_CRITERIA_CONDITIONS being applicable to the IUT } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing filterUsage set to 1 (Discovery Criteria) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and no Content } | IUT ( AE |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### Security(SEC)

##### CE/SEC/00001/00001

Support <accessControlPolicy> resource with attributes multiplicity equals 1[1]

###### CREATE OPERATION

TP/oneM2M/CSE/DMR/CRE/001_ACP/CB

TP/oneM2M/CSE/DMR/CRE/001_ACP/AE

TP/oneM2M/CSE/DMR/CRE/015_ET/ACP

TP/oneM2M/CSE/DMR/CRE/003_ACP

TP/oneM2M/CSE/DMR/CRE/002_ACP

TP/oneM2M/CSE/SEC/ACP/CRE/001

| TP Id | TP/oneM2M/CSE/SEC/ACP/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a accessControlPolicy resource with privileges attribute having multiple access control rules |
| Reference | TS-0001 9.6.2-2 & TS-0001 10.2.21 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content containing accessControlPolicy resource containing privileges attribute containing accessControlRule attribute containing ACCESS_CONTROL_RULE_1 and ACCESS_CONTROL_RULE_2 } | IUT ( AE |
|  | then { the IUT creates the accessControlPolicy resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/SEC/ACP/CRE/002

| TP Id | TP/oneM2M/CSE/SEC/ACP/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a accessControlPolicy resource with selfPrivileges attribute having multiple access control rules |
| Reference | TS-0001 9.6.2-2 & TS-0001 10.2.21 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content containing accessControlPolicy resource containing selfPrivileges attribute containing accessControlRule attribute containing ACCESS_CONTROL_RULE_1 and ACCESS_CONTROL_RULE_2 } | IUT ( AE |
|  | then { the IUT creates the accessControlPolicy resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/SEC/ACP/CRE/003

| TP Id | TP/oneM2M/CSE/SEC/ACP/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a accessControlPolicy resource with privileges attribute having empty rules |
| Reference | TS-0001 9.6.2 & TS-0001 10.2.21 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content containing accessControlPolicy resource containing privileges attribute set to empty list } | IUT ( AE |
|  | then { the IUT creates the accessControlPolicy resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/SEC/ACP/CRE/004

| TP Id | TP/oneM2M/CSE/SEC/ACP/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the creation of a accessControlPolicy resource with selfPrivileges attribute having empty rules |
| Reference | TS-0001 9.6.2 & TS-0001 10.2.21 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content containing accessControlPolicy resource containing selfPrivileges attribute set to empty list } | IUT ( AE |
|  | then { the IUT does not create the accessControlPolicy resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

### -----------------------End of change 2---------------------------------------------

# Comments

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-09036

REQ-0001-09039

REQ-0001-09037

REQ-0001-09038

REQ-0001-09023

TS-0001_ACP_003  ??????????

REQ-0001-09024

REQ-0001-09025

REQ-0001-09026

REQ-0001-09027

REQ-0001-09028

REQ-0001-09029

REQ-0001-09030

REQ-0001-09031

REQ-0001-09032

REQ-0001-09033

REQ-0001-09034

REQ-0001-09035

REQ-0001-10123

REQ-0001-10124

REQ-0001-10126

REQ-0001-10125

?? not specified in TS-0004.