| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#30 |
| Source:* | Bob Flynn, Convida , Flynn.Bob@convidawireless.com |
| Date:* | 2017-07-07 |
| Reason for Change/s:* | To provide TPs for AE requirements |
| CR against: Release* | 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

R01 – change req ids in section 10.

| TS-0001_AE_006 | REQ-0001-09091 | Allow subscription child resource under AE | TP/oneM2M/CSE/DMR/CRE/001_SUB/AE |
| --- | --- | --- | --- |
| TS-0001_AE_007 | REQ-0001-09092 | Allow container child resource under AE | TP/oneM2M/CSE/DMR/CRE/001_CNT/AE |
| TS-0001_AE_008 | REQ-0001-09093 | Allow a group child resource under AE | TP/oneM2M/CSE/DMR/CRE/001_GRP/AE |
| TS-0001_AE_009 | REQ-0001-09094 | Allow a ACP child resource under AE | TP/oneM2M/CSE/DMR/CRE/001_ACP/AE |
| TS-0001_AE_010 | REQ-0001-09095 | Allow a pch child resource under AE | TP/oneM2M/CSE/DMR/CRE/001_PCH/AE |
| TS-0001_AE_011 | REQ-0001-09096 | Allow a subscription under AEannc | TP/oneM2M/CSE/DMR/CRE/001_SUB/AEA |
| TS-0001_AE_012 | REQ-0001-09097 | Allow a container under AEannc | TP/oneM2M/CSE/DMR/CRE/001_CNT/AEA |
| TS-0001_AE_013 | REQ-0001-09098 | Allow a containerAnnc under AEannc | TP/oneM2M/CSE/DMR/CRE/0XX_CNTA/AEA |
| TS-0001_AE_014 | REQ-0001-09099 | Allow a group under AEannc | TP/oneM2M/CSE/DMR/CRE/001_GRP/AEA |
| TS-0001_AE_015 | REQ-0001-09100 | Allow a groupAnnc under AEannc | TP/oneM2M/CSE/DMR/CRE/0XX_GRPA/AEA |
| TS-0001_AE_016 | REQ-0001-09101 | Allow a ACP under AEannc | TP/oneM2M/CSE/DMR/CRE/001_ACP/AEA |
| TS-0001_AE_017 | REQ-0001-09102 | Allow a ACPAnnc un AEannc | TP/oneM2M/CSE/DMR/CRE/0XX_ACPA/AEA |
| TS-0001_AE_018 | REQ-0001-09103 | Require specification of requestReachability. | TP/oneM2M/CSE/REG/CRE/020_RR |
| TS-0001_AE_019 | REQ-0001-09104 | Allow specification of optional appName | TP/oneM2M/CSE/REG/CRE/011_APN/AE |
| TS-0001_AE_020 | REQ-0001-09105 | Require specification of App-id | TP/oneM2M/CSE/REG/CRE/020_API |
| TS-0001_AE_021 | REQ-0001-09106 | Do not allow specification of AE-ID. | NO EXAMPLES OF REJECTING RO/NP on CREATE requests |
| TS-0001_AE_022 | REQ-0001-09107 | Alllow specification of POA (list) | TP/oneM2M/CSE/REG/CRE/012_POA/AE |
| TS-0001_AE_023 | REQ-0001-09108 | Allow specification of ontologyRef | TP/oneM2M/CSE/REG/CRE/012_ONT/AE |
| TS-0001_AE_024 | REQ-0001-09109 | Allow specification of a nodelink | TP/oneM2M/CSE/REG/CRE/012_NODLNK/AE |
| TS-0001_AE_025 | REQ-0001-10008 | Create | Already mapped |
| TS-0001_AE_026 | REQ-0001-10009 | retrieve | Already mapped |
| TS-0001_AE_028 | REQ-0001-10011 | delete | Already mapped |
| TS-0001_AE_030 | REQ-0001-10010 | update | Already mapped |

- Change old req id’s to new requirement ids.

- Identify TP’s for this list. There is a lot of overlap with existing tests, so I cross reference them to existing testcases. This can be entered in the tracking spreadsheet.

- Created new TPs shown in table above with the change marks.

### -----------------------Start of change 0.1-------------------------------------------

### 9.6.5	Resource Type AE

An <AE> resource shall represent information about an Application Entity registered to a CSE.

Figure 9.6.5-1: Structure of <AE> resource

The <AE> resource shall contain the child resources specified in table 9.6.5-1.

Table 9.6.5-1: Child resources of <AE> resource

| Child Resources of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <schedule> | 0..1 | See clause 9.6.9 | <scheduleAnnc> |
| [variable] | <pollingChannel> | 0..1 | See clause 9.6.21. When the AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. The <pollingChannel> shall be utilized by the parent resource. | None |

The <AE> resource shall contain the attributes specified in table 9.6.5-2.

Table 9.6.5-2: Attributes of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. Contains the AE-ID-Stem of the AE (see clause 7.2 on identifier formats and clause 10.1.1.2.2 for AE registration procedure). | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| appName | 0..1 | RW | The name of the application, as declared by the application developer(e.g. "HeatingMonitoring"). Several sibling resources may share the appName. | OA |
| App-ID | 1 | WO | The identifier of the Application (see clause 7.1.32). | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..1 (L) | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g. IP address, FQDN, URI). This attribute shall be accessible only by the AE and the Hosting CSE. If this information is not provided, the AE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the AE without using the PoA. | OA |
| ontologyRef | 0..1 | RW | A URI of the ontology used to represent the information that is managed and understood by the AE. | OA |
| requestReachability | 1 | RW | If the AE that created this <AE> resource can receive a request, this attribute is set to "TRUE" otherwise "FALSE" | OA |
| nodeLink | 0..1 | RW | The resource identifier of a <node> resource that stores the node specific information of the node on which the AE represented by this <AE> resource resides. | OA |
| contentSerialization | 0..1 (L) | RW | The list of supported serializations of the Content primitive parameter for receiving a request from its registrar CSE (e.g. XML, JSON). The list shall be ordered so that the most preferred format comes first. | OA |

### -----------------------End of change 0.1-------------------------------------------

### -----------------------Start of change 0.2-------------------------------------------

#### 10.2.1.1	Create <AE>

This procedure shall be used for creating an <AE> resource. This operation is part of the registration procedure for AEs on the Registrar CSE (which is also the Hosting CSE), as described in clause 10.1.1.2.2.

Table 10.2.1.1-1: <AE> CREATE

| <AE> CREATE |
| --- |
| Associated Reference Point | Mca |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: From: Registree AE only Content: The resource content shall provide the information as defined in clause 9.6.5 |
| Processing at Originator before sending Request | According to clause 10.1.1.2.2 |
| Processing at Receiver | According to clause 10.1.1.2.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.2.2 |
| Exceptions | According to clause 10.1.1.2.2 |

#### 10.2.1.2	Retrieve <AE>

This procedure shall be used for retrieving the representation of the <AE> resource.

Table 10.2.1.2-1: <AE> RETRIEVE

| <AE> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <AE> resource as defined in clause 9.6.5 |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.1.3	Update <AE>

This procedure shall be used for updating the attributes and the actual data of an <AE> resource.

Table 10.2.1.3-1: <AE> UPDATE

| <AE> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: attributes of the <AE> resource as defined in clause 9.6.5 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.1.4	Delete <AE>

This procedure shall be used for deleting the <AE> resource with all related information.

Table 10.2.1.4-1: <AE> DELETE

| <AE> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.4 |
| Processing at Receiver | According to clause 10.1.4 |
| Information in Response message | According to clause 10.1.4 |
| Processing at Originator after receiving Response | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 |

### -----------------------End of change 0.2-------------------------------------------

### -----------------------Start of change 1-------------------------------------------

TP/oneM2M/CSE/DMR/CRE/0XX

| TP Id | TP/oneM2M/CSE/DMR/CRE/0XX |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource on the TARGET_RESOURCE_ADDRESS of type announced PARENT_RESOURCE_TYPE |
| Reference | TS-0001 9.6.5, |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the CSE and the Originator having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE containing Resource Type set to RESOURCE_TYPE and To set to TARGET_RESOURCE_ADDRESS and From set to CSE-ID and Content containing RESOURCE_TYPE resource containing no resourceName attribute } | IUT ( CSE |
|  | then { the IUT creates the RESOURCE_TYPE resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing RESOURCE_TYPE resource containing Valid resourceName attribute } | IUT ( CSE |

| TP Id | Reference | RESOURCE_TYPE | PARENT_RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/0XX_CNTA/AEA | 9.6.5-1 | (containerAnnc) | (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/0XX_GRPA/AEA | 9.6.5-1 | (groupAnnc) | (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/0XX_ACPA/AEA | 9.6.5-1 | (accessControlPolicyAnnc) | (AEannc) |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

TP/oneM2M/CSE/DMR/CRE/001

| TP Id | TP/oneM2M/CSE/DMR/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a RESOURCE_TYPE resource on the TARGET_RESOURCE_ADDRESS of type PARENT_RESOURCE_TYPE with resource name not provided |
| Reference | TS-0001 10.1.1.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the Originator having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to RESOURCE_TYPE and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing RESOURCE_TYPE resource containing no resourceName attribute } | IUT ( AE |
|  | then { the IUT creates the RESOURCE_TYPE resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing RESOURCE_TYPE resource containing Valid resourceName attribute } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | PARENT_RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/CB | TS-0001 10.2.4.1 | 3 (container) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/AE | TS-0001 10.2.4.1 | 3 (container) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/CNT | TS-0001 10.2.4.1 | 3 (container) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/001_GRP/CB | TS-0001 10.2.7.2 | 9 (group) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_GRP/AE | TS-0001 10.2.7.2 | 9 (group) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_ACP/CB | TS-0001 10.2.21.1 | 1 (accessControlPolicy) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_ACP/AE | TS-0001 10.2.21.1 | 1 (accessControlPolicy) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SCH/CB |  | 18 (schedule) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_SCH/AE |  | 18 (schedule) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SCH/SUB |  | 18 (schedule) | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/001_PCH/AE | TS-0001 10.2.13.2 | 15 (pollingChannel) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/CB | TS-0001 10.2.11.2 | 23 (subscription) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/AE | TS-0001 10.2.11.2 | 23 (subscription) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/CNT | TS-0001 10.2.11.2 | 23 (subscription) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/ACP | TS-0001 10.2.11.2 | 23 (subscription) | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/SCH | TS-0001 10.2.11.2 | 23 (subscription) | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/GRP | TS-0001 10.2.11.2 | 23 (subscription) | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/001_NOD/CB | TS-0001 9.6.3-1 | 14 (node) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_MGC/CB | TS-0001 9.6.3-1 | 12 (mgmtCmd) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_LCP/CB | TS-0001 9.6.3-1 | 10 (locationPolicy) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_STCG/CB | TS-0001 9.6.3-1 | 22 (statsConfig) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_STCL/CB | TS-0001 9.6.3-1 | 21 (statsCollect) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_MSSP/CB | TS-0001 9.6.3-1 | 11(m2mServiceSubscriptionProfile) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_ASAR/CB | TS-0001 9.6.3-1 | 19(serviceSubscribedAppRule) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/CSR | TS-0001 9.6.4-1 | 23 (subscription) | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/001_SCH/CSR | TS-0001 9.6.4-1 | 18 (schedule) | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/AEA | TS-0001 9.6.5-1 | 23 (Subscription) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/AEA | TS-0001 9.6.5-1 | 3 (Container) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_GRP/AEA | TS-0001 9.6.5-1 | 9 (Group) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_ACP/AEA | TS-0001 9.6.5-1 | 1 (accessControlPolicy) | 10002 (AEannc) |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

TP/oneM2M/CSE/DMR/UPD/018

| TP Id | TP/oneM2M/CSE/DMR/UPD/018 |
| --- | --- |
| Test objective | Check that the IUT updates successfully the value of the attribute MANDATORY_ATTRIBUTE of the RESOURCE_TYPE resource under CSEBase |
| Reference | TS-0001 10.1.3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_IN_PROFILE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the CSEBase resource and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing RESOURCE_TYPE resource containing MANDATORY_ATTRIBUTE attribute set to VALUE } | IUT ( AE |
|  | then { the IUT updates the RESOURCE_TYPE resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing RESOURCE_TYPE resource containing MANDATORY_ATTRIBUTE attribute set to VALUE } | IUT ( AE |

| TP Id | Reference | MANDATORY_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/018_ET/CSR | TS-0001 9.6.4-2 | expirationTime | remoteCSE |
| TP/oneM2M/CSE/DMR/UPD/018_RR/CSR | TS-0001 9.6.4-2 | requestReachability | remoteCSE |
| TP/oneM2M/CSE/DMR/UPD/018_ET/NOD | TS-0001 9.6.18-2 | expirationTime | node |
| TP/oneM2M/CSE/DMR/UPD/018_NI/NOD | TS-0001 9.6.18-2 | nodeID | node |
| TP/oneM2M/CSE/DMR/UPD/018_ET/AE | TS-0001 9.6.5-2 | expirationTime | AE |
| TP/oneM2M/CSE/DMR/UPD/018_RR/AE | TS-0001 9.6.5-2 | requestReachability | AE |
| TP/oneM2M/CSE/DMR/UPD/018_ET/CNT | TS-0001 9.6.6-2 | expirationTime | container |
| TP/oneM2M/CSE/DMR/UPD/018_ET/ACP | TS-0001 9.6.2-2 | expirationTime | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/018_PV/ACP | TS-0001 9.6.2-2 | privileges | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/018_PVS/ACP | TS-0001 9.6.2-2 | selfPrivileges | accessControlPolicy |
| TP/oneM2M/CSE/DMR/UPD/018_ET/SUB | TS-0001 9.6.8-2 | expirationTime | subscription |
| TP/oneM2M/CSE/DMR/UPD/018_NU/SUB | TS-0001 9.6.8-2 | notificationURI | subscription |
| TP/oneM2M/CSE/DMR/UPD/018_NCT/SUB | TS-0001 9.6.8-2 | notificationContentType | subscription |
| TP/oneM2M/CSE/DMR/UPD/018_ET/GRP | TS-0001 9.6.13-2 | expirationTime | group |
| TP/oneM2M/CSE/DMR/UPD/018_MNM/GRP | TS-0001 9.6.13-2 | maxNrOfMembers | group |
| TP/oneM2M/CSE/DMR/UPD/018_MID/GRP | TS-0001 9.6.13-2 | memberIDs | group |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

TP/oneM2M/CSE/REG/CRE/012

| TP Id | TP/oneM2M/CSE/REG/CRE/012 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration with the optional attribute OPTIONAL_ATTRIBUTE provided |
| Reference | TS-0001 10.1.1.2.2, 9.6.5-2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_IN_PROFILE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a CSEBase resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) and From set to AE_ID and Content containing AE resource containing OPTIONAL_ATTRIBUTE attribute } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing AE resource containing OPTIONAL_ATTRIBUTE attribute } | IUT ( AE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/REG/CRE/012_LBL/AE | TS-0001 9.6.5-2 | labels | AE |
| TP/oneM2M/CSE/REG/CRE/012_APN/AE | TS-0001 9.6.5-2 | AppName | AE |
| TP/oneM2M/CSE/REG/CRE/012_POA/AE | TS-0001 9.6.5-2 | pointOfAccess | AE |
| TP/oneM2M/CSE/REG/CRE/012_ONT/AE | TS-0001 9.6.5-2 | OntologyRef | AE |
| TP/oneM2M/CSE/REG/CRE/012_NODLNK/AE | TS-0001 9.6.5-2 | Nodelink | AE |

### -----------------------End of change 4---------------------------------------------

# Comments

Do not allow pch under other resource types (only AE and remoteCSE)

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-09091

REQ-0001-09096

REQ-0001-09092

REQ-0001-09097

REQ-0001-09098

REQ-0001-09093

REQ-0001-09099

REQ-0001-090100

REQ-0001-09094

REQ-0001-09101

REQ-0001-09102

REQ-0001-09095

REQ-0001-09104

REQ-0001-09105

REQ-0001-09106

REQ-0001-09107

REQ-0001-09108

REQ-0001-09103

REQ-0001-09109

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-10008

TS-0001_AE_026

REQ-0001-10010

REQ-0001-10011