| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#30 |
| Source:* | Heejin Joung, heejin,joung.84@tta.or.kr Keebum Kim, keebum.kim@tta.or.kr |
| Date:* | 2017-07-11 |
| Reason for Change/s:* | To provide TPs for SUB requirements |
| CR against: Release* | 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

With respect to subscription resource,

- Change old req id’s to new requirement ids.

- Identify TP’s for this list.

- Add Missing TPs.

The last column can be used to update the requirements tracking spreadsheet.

| REQ ID | New REQ ID | Reference | Description | Related TPs and Comments |
| --- | --- | --- | --- | --- |
| TS-0001_SN_007 | REQ-0001-09135 | 9.6.8-1 | <notificationSchedule> | TP/oneM2M/CSE/DMR/CRE/001_SCH/SUB No TP for when try to create <schedule> with its resource name other than ‘notificationSchedule’ No TP for notification scheduling |
| TS-0001_SN_010 | REQ-0001-09138 | 9.6.8-2 | notificationURI | TP/oneM2M/CSE/DMR/CRE/001_SUB/XX TP/oneM2M/CSE/DMR/CRE/003_SUB TP/oneM2M/CSE/DMR/RET/001_SUB TP/oneM2M/CSE/DMR/RET/013_SUB TP/oneM2M/CSE/DMR/UPD/018_NU/SUB No TP for checking attribute content type No TP for creating SUB under FanOutPoint and checking notificationURI-related processure |
| TS-0001_SN_011 | REQ-0001-09139 | 9.6.8-2 | groupID | TP/oneM2M/CSE/DMR/CRE/015_GPI/SUB TP/oneM2M/CSE/DMR/UPD/014_GPI/SUB TP/oneM2M/CSE/DMR/UPD/017_GPI/SUB No TP for checking groupID as a filter criteria |
| TS-0001_SN_013 | REQ-0001-09141 | 9.6.8-2 | batchNotify | TP/oneM2M/CSE/DMR/CRE/015_BN/SUB TP/oneM2M/CSE/DMR/UPD/014_BN/SUB TP/oneM2M/CSE/DMR/UPD/017_BN/SUB TP/oneM2M/CSE/SUB/UPD/018 TP/oneM2M/CSE/SUB/UPD/020 TP/oneM2M/CSE/SUB/NTF/003 TP/oneM2M/CSE/SUB/NTF/004 |
| TS-0001_SN_014 | REQ-0001-09142 | 9.6.8-2 | rateLimit | TP/oneM2M/CSE/DMR/CRE/015_RL/SUB TP/oneM2M/CSE/DMR/UPD/014_RL/SUB TP/oneM2M/CSE/DMR/UPD/017_RL/SUB No TP for checking rateLimit-related operations |
| TS-0001_SN_015 | REQ-0001-09143 | 9.6.8-2 | preSubscriptionNotify | TP/oneM2M/CSE/DMR/CRE/015_PSN/SUB No TP for testing invalid behavior that it tries to update preSubscriptionNotify No TP for checking preSubscriptionNotif-related operations |
| TS-0001_SN_016 | REQ-0001-09144 | 9.6.8-2 | pendingNotification | TP/oneM2M/CSE/DMR/CRE/015_PN/SUB TP/oneM2M/CSE/DMR/UPD/014_PN/SUB TP/oneM2M/CSE/DMR/UPD/017_PN/SUB (duplicated) No TP for checking pendingNotification -related operations |
| TS-0001_SN_017 | REQ-0001-09145 | 9.6.8-2 | notificationStoragePriority | TP/oneM2M/CSE/DMR/CRE/015_NSP/SUB TP/oneM2M/CSE/DMR/UPD/014_NSP/SUB TP/oneM2M/CSE/DMR/UPD/017_NSP/SUB No TP for checking notificationStoragePriority-related operations |
| TS-0001_SN_018 | REQ-0001-09146 | 9.6.8-2 | latestNotify | TP/oneM2M/CSE/DMR/CRE/015_LN/SUB TP/oneM2M/CSE/DMR/UPD/014_LN/SUB TP/oneM2M/CSE/DMR/UPD/017_LN/SUB TP/oneM2M/CSE/SUB/UPD/020 TP/oneM2M/CSE/SUB/NTF/004 |
| TS-0001_SN_021 | REQ-0001-09149 | 9.6.8-2 | creator | TP/oneM2M/CSE/DMR/CRE/015_CR/SUB TP/oneM2M/CSE/SUB/CRE/010 No TP for testing invalid behavior that it tries to update creator No TP for checking creator-related operation that CSE notifies both NU and CR |
| TS-0001_SN_023 | REQ-0001-09151 | 9.6.8-3 | createdBefore(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_CRB/ENC |
| TS-0001_SN_024 | REQ-0001-09152 | 9.6.8-3 | createdAfter(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_CRA/ENC |
| TS-0001_SN_025 | REQ-0001-09153 | 9.6.8-3 | modifiedSince(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_MS/ENC |
| TS-0001_SN_026 | REQ-0001-09154 | 9.6.8-3 | unmodifiedSince(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_US/ENC |
| TS-0001_SN_027 | REQ-0001-09155 | 9.6.8-3 | stateTagSmaller(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_STS/ENC |
| TS-0001_SN_028 | REQ-0001-09156 | 9.6.8-3 | stateTagBigger(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_STB/ENC |
| TS-0001_SN_029 | REQ-0001-09157 | 9.6.8-3 | expireBefore(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_EXB/ENC |
| TS-0001_SN_030 | REQ-0001-09158 | 9.6.8-3 | expireAfter(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_EXA/ENC |
| TS-0001_SN_031 | REQ-0001-09159 | 9.6.8-3 | sizeAbove(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_SZA/ENC |
| TS-0001_SN_032 | REQ-0001-09160 | 9.6.8-3 | eventType(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_ET/ENC |
| TS-0001_SN_034 | REQ-0001-09161 | 9.6.8-3 | operationMonitor(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_OM/ENC |
| TS-0001_SN_035 | REQ-0001-09162 | 9.6.8-3 | attribute(Tag) | No TP Change 1 proposes TP/oneM2M/CSE/SUB/CRE/XXX_ATR/ENC |
| TS-0001_SN_041 | REQ-0001-09163 | 9.6.8 | <subscription> Deleted when its subscribed-to resource is deleted. | TP/oneM2M/CSE/SUB/DEL/001 (trivial?) |
| TS-0001_SN_042 | REQ-0001-09164 | 9.6.8 | <subscription> Can create when it has RETRIEVE privilege to the subscribed-to resource | TP/oneM2M/CSE/SUB/CRE/007 TP/oneM2M/CSE/SUB/CRE/010 |
| TS-0001_SN_045 | REQ-0001-10064 | 10.2.11.2-1 | Check if the subscribed-to resource, addressed in the To parameter in the Request, is a subscribable resource | TP/oneM2M/CSE/SUB/CRE/001 TP/oneM2M/CSE/DMR/CRE/001_SUB/CB TP/oneM2M/CSE/DMR/CRE/001_SUB/AE TP/oneM2M/CSE/DMR/CRE/001_SUB/CNT TP/oneM2M/CSE/DMR/CRE/001_SUB/ACP TP/oneM2M/CSE/DMR/CRE/001_SUB/SCH TP/oneM2M/CSE/DMR/CRE/001_SUB/GRP |
| TS-0001_SN_046 | REQ-0001-10065 | 10.2.11.2-1 | If a notificationURI is not the Originator, the Hosting CSE may send a Notify request to the notificationURI to verify this <subscription> creation request | TP/oneM2M/CSE/SUB/CRE/003 TP/oneM2M/CSE/SUB/NTF/001 TP/oneM2M/CSE/SUB/NTF/002 |
| TS-0001_SN_051 | REQ-0001-09166 | 9.6.8-2 | pendingNotification When this attribute is set to " sendLatest ", only the last notification shall be sent and it shall have the Event Category set to "latest". If this attribute is not present, the Hosting CSE sends no missed notifications. | No TP Change 2 proposes TP/oneM2M/CSE/SUB/NTF/XXX_SL/PN and TP/oneM2M/CSE/SUB/NTF/XXX_SA/PN |

### -----------------------Start of change 0.1-------------------------------------------

### 9.6.8	Resource Type subscription

The <subscription> resource contains subscription information for its subscribed-to resource.

The <subscription> resource shall be represented as child resource of the subscribed-to resource. For example, <container> resource has <subscription> resource as a child resource (see clause 9.6.6). A <subscription> resource shall be deleted when the parent subscribed-to resource is deleted.

The <subscription> resource shall represent a subscription to a subscribed-to resource. An Originator shall be able to create a resource of <subscription> resource type when the Originator has RETRIEVE privilege to the subscribe-to resource. The Originator which creates a <subscription> resource becomes the resource subscriber.

Each <subscription> may include notification policies that specify which, when, and how notifications are sent. These notification policies may work in conjunction with CMDH policies.

When a <subscription> resource is deleted, a Notify request shall be sent to the subscriberURI if it is provided by the Originator.

Figure 9.6.8-1: Structure of <subscription> resource

The <subscription> resource shall contain the child resources specified in table 9.6.8-1.

Table 9.6.8-1: Child resources of <subscription> resource

| Child Resources of <subscription> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| notificationSchedule | <schedule> | 0..1 | In the context of the <subscription> resource, the notificationSchedule specifies when notifications may be sent by the Hosting CSE to the notificationURI(s). See clause 9.6.9. |

The <subscription> resource shall contain the attributes specified in table 9.6.8-2.

Table 9.6.8-2: Attributes of <subscription> resource

| Attributes of <subscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. |
| resourceID | 1 | RO | See clause 9.6.1.3. |
| resourceName | 1 | WO | See clause 9.6.1.3. |
| parentID | 1 | RO | See clause 9.6.1.3. |
| expirationTime | 1 | RW | See clause 9.6.1.3. |
| creationTime | 1 | RO | See clause 9.6.1.3. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. If no accessControlPolicyIDs value is configured, the accesControlPolicyIDs of the parent resource shall be applied for privilege checking. |
| eventNotificationCriteria | 0..1 | RW | This attribute (notification policy) indicates the event criteria for which a notification is to be generated. |
| expirationCounter | 0..1 | RW | This attribute (notification policy) indicates that the subscriber wants to set the life of this subscription to a limit of a maximum number of notifications. When the number of notifications sent reaches the count of this counter, the <subscription> resource shall be deleted, regardless of any other policy. |
| notificationURI | 1 (L) | RW | This attribute shall be configured as a list consisting of one or more targets that the Hosting CSE shall send notifications to. A target shall be formatted as a oneM2M compliant Resource-ID as defined in clause 7.2 or as an identifier compliant with a oneM2M supported protocol binding (e.g. http, coap, mqtt). If a target is formatted as a oneM2M compliant Resource-ID, then the target shall be formatted as a structured or unstructured CSE-Relative-Resource-ID, SP-Relative-Resource-ID, and/or Absolute-Resource-ID. A Hosting CSE shall use this information to determine proper pointOfAccess, requestReqchability and/or pollingChannel information needed to send a notification to the target. The following is an example. /CSE0001/AE0001 For a target that is formatted as an identifier compliant with a oneM2M supported protocol binding, the details of this format are defined by the respective oneM2M protocol specification. The following is an example of an HTTP URI compliant with oneM2M HTTP protocol binding. https://172.25.30.25:7000/notification/handler For a subscription to a <fanOutPoint> Resource, if subscription resource in request contains a notificationForwardingURI, then the group hosting CSE shall configure the notificationURI of the fanout subscription request with a Resource-ID specified by the group Hosting CSE. |
| groupID | 0..1 | RW | The ID of a <group> resource in case the subscription is made through a group. This attribute may be used in the Filter Criteria to discover all subscription resources created via a <fanOutPoint> resource to a specific groupID. |
| notificationForwardingURI | 0..1 | RW | The attribute is a forwarding attribute that shall be present only for group related subscriptions. It represents the resource subscriber notification target. It shall be used by group Hosting CSE for forwarding aggregated notifications. See clauses 10.2.7.11 and 10.2.7.12. This attribute shall be configured with target of the subscriber. The target is used by the Group Hosting CSE to determine where to send aggregated notifications. A target shall be formatted as a oneM2M compliant Resource-ID as defined in clause 7.2 or as an identifier compliant with one of the oneM2M supported protocol bindings (the detailed format of which are defined by each respective oneM2M protocol binding specification). |
| batchNotify | 0..1 | RW | This attribute (notification policy) indicates that the subscription originator wants to receive batches of notifications rather than receiving them one at a time. This attribute includes : the number of notifications to be batched for delivery and the duration. When only the number is specified by the subscription originator, the Hosting CSE shall set the default duration given by M2M Service Provider. If batchNotify is used simultaneously with latestNotify, only the latest notification shall be sent and have the Event Category set to "latest". |
| rateLimit | 0..1 | RW | This attribute (notification policy) indicates that the subscriber wants to limit the rate at which it receives notifications. This attribute expresses the subscriber's notification policy and includes two values: a maximum number of events that may be sent within some duration, and the rateLimit window duration. When the number of generated notifications within the rateLimit window duration exceeds the maximum number, notification events are temporarily stored, until the end of the window duration, when the sending of notification events restarts in the next window duration. The sending of notification events continues as long as the maximum number of notification events is not exceeded during the window duration. The rateLimit policy may be used simultaneously with other notification policies. |
| preSubscriptionNotify | 0..1 | WO | This attribute (notification policy) indicates that the subscriber wants to be sent notifications for events that were generated prior to the creation of this subscription. This attribute has a value of the number of prior notification events requested. If up-to-date caching of retained events is supported on the Hosting CSE and contains the subscribed events then prior notification events will be sent up to the number requested. The preSubscriptionNotify policy may be used simultaneously with any other notification policy. |
| pendingNotification | 0..1 | RW | This attribute (notification policy), if set, indicates how missed notifications due to a period of no connectivity are handled(according to the reachability and notification schedules). The possible values for pendingNotification are: "sendLatest" "sendAllPending" This policy depends upon caching of retained notifications on the hosted CSE. When this attribute is set to " sendLatest ", only the last notification shall be sent and it shall have the Event Category set to "latest". If this attribute is not present, the Hosting CSE sends no missed notifications. This policy applies to all notifications regardless of the selected delivery policy (batchNotify, latestNotify, etc.) Note that unreachability due to reasons other than scheduling is not covered by this policy. |
| notificationStoragePriority | 0..1 | RW | Indicates that the subscriber wants to set a priority for this subscription relative to other subscriptions belonging to this same subscriber. This attribute sets a number within the priority range. When storage of notifications exceeds the allocated size, this policy is used as an input with the storage congestion policy (notificationCongestionPolicy) specified in clause 9.6.3 to determine which stored and generated notifications to drop and which ones to retain. |
| latestNotify | 0..1 | RW | This attribute (notification policy) indicates if the subscriber wants only the latest notification. If multiple notifications of this subscription are buffered, and if the value of this attribute is set to true, then only the last notification shall be sent and it shall have the Event Category value set to "latest". |
| notificationContentType | 1 | RW | Indicates a notification content type that shall be contained in notifications. The allowed values are: "modified attributes" "all attributes" "ID" of the resource indicated in the eventType condition If it is not given by the Originator at the creation procedure, default is "all attributes". |
| notificationEventCat | 0..1 | RW | This attribute (notification policy) indicates the subscriber's requested Event Category to be used for notification messages generated by this subscription. |
| creator | 0..1 | WO | AE-ID or CSE-ID which created the <subscription> resource. |
| subscriberURI | 0..1 | WO | This attribute shall be configured with the target of the subscriber. The target is used by the Hosting CSE to determine where to send a notification when the subscription is deleted. A target shall be formatted as a oneM2M compliant Resource-ID as defined in clause 7.2 or as an identifier compliant with one of the oneM2M supported protocol bindings (the detailed format of which are defined by each respective oneM2M protocol binding specification). |

Table 9.6.8-3 describes the eventNotificationCriteria conditions.

Table 9.6.8-3: eventNotificationCriteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| stateTagSmaller | 0..1 | The stateTag attribute of the resource is smaller than the specified value. |
| stateTagBigger | 0..1 | The stateTag attribute of the resource is bigger than the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| sizeAbove | 0..1 | The contentSize attribute of the <contentInstance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <contentInstance> resource is smaller than the specified value. |
| eventType | 0..n | The type of event. Possible event type values are: Update to attributes of the subscribed-to resource Deletion of the subscribed-to resource , Creation of a direct child of the subscribed-to resource , Deletion of a direct child of the subscribed-to resource The other conditions in eventNotificationCriteria conditions apply to the selected eventType. For example, if eventType is "Creation of a direct child of the subscribed-to resource" then other eventNotificationCriteria conditions is applied to the direct child resources of the subscribed-to resource. If this condition is not specified, the default value is "Update to attributes of the subscribed-to resource" |
| operationMonitor | 0..n | The operations accessing the subscribed-to resource matches with the specified value. It allows monitoring which operation is attempted to the subscribed-to resource regardless of whether the operation is performed. This feature is useful when to find malicious AEs. Possible string arguments are: create, retrieve, update, delete. |
| attribute | 0..n | A list of attribute names of a subscribed-to-resource. This list is only applicable when eventType has a value of “Update to attributes of the subscribed-to resource”. If this list is present, then it is used to specify a subset of a subscribed-to-resource’s attributes for which updates shall result in a notification. If ANY attribute specified on this list is updated, then a notification shall be generated. If an attribute that is not specified in this list is updated, then a notification shall not be generated. If this list is not presented, then the default attribute list is the full set of a subscribed-to-resource’s attributes. If ANY attribute of a subscribed-to-resouce is updated, then a notification shall be generated. |

### -----------------------End of change 0.1-------------------------------------------

### -----------------------Start of change 0.2-------------------------------------------

#### 10.2.11.2	Create <subscription>

This procedure shall be used to request the creation of a new <subscription> resource to be notified for the modifications of a subscribed-to resource. The generic create procedure is described in clause 10.1.1.1.

Table 10.2.11.2-1: <subscription> CREATE

| <subscription> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.8 |
| Processing at Originator before sending Request | According to clause 10.1.1.1 with the following additions: The Request shall address a subscribable resource The Request shall include notificationURI(s) If the request includes notificationURI(s) which is not the Originator, the Originator should send the request as non-blocking request (see clauses 8.2.2 and 9.6.12) |
| Processing at Receiver | According to clause 10.1.1.1 with the following Which is also the Hosting CSE shall validate the followings: Check if the subscribed-to resource, addressed in the To parameter in the Request, is a subscribable resource Check if the Originator has privileges for retrieving the subscribed-to resource If a notificationURI is not the Originator, the Hosting CSE may send a Notify request to the notificationURI to verify this <subscription> creation request. If the Hosting CSE initiates the verification, it shall check if the verification result in the Notify response is successful or not. If any notificationURI contained in a list fails verification then the <subscription> create process fails If any of the checks above fails, the Hosting CSE shall send an unsuccessful response to the Originator with corresponding error information. Otherwise, the Hosting CSE shall create the <subscription> resource and send a successful response to the Originator |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: address of the created <subscription> resource, according to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

### -----------------------End of change 0.2-------------------------------------------

### -----------------------Start of change 1-------------------------------------------

##### CE/SUB/00002/00010

Support the eventNotificationCriteria attribute of <subscription> resource

###### CREATE OPERATION

TP/oneM2M/CSE/DMR/CRE/015_ENC/SUB

TP/oneM2M/CSE/SUB/CRE/007

| TP Id | TP/oneM2M/CSE/SUB/CRE/007 |
| --- | --- |
| Test objective | Check that the IUT sends a Notify request to the subscriber resource when notifiationEventType attribute is set to "Create_of_Direct_Child_Resource" and an create operation has been performed on the subscribed-to resource |
| Reference | TS-0001 9.6.8-3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered the AE2 and the AE1 having created a <subscribed-to type> resource containing subscription child resource containing notificationURI attribute set to AE2_RESOURCE_ADDRESS and eventNotificationCriteria attribute containing notificationEventType set to 3 (Create_of_Direct_Child_Resource) and the AE1 having privileges to perform RETRIEVE operation on the subscribed-to resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE1 containing To set to SUBSCRIBED_TO_RESOURCE_ADDRESS and From set to AE1_RESOURCE_ADDRESS and Content containing CHILD_RESOURCE_TYPE resource containing resourceName attribute set to NAME } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and the IUT sends a NOTIFY Request contaning Content containing Notification message containing notificationEvent attribute containing representation attribute containing CHILD_RESOURCE_TYPE resource containing All attributes } | IUT  AE1 IUT  AE2 |

TP/oneM2M/CSE/SUB/CRE/008

| TP Id | TP/oneM2M/CSE/DMR/CRE/008 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a subscription resource with the eventNotificationCriteria attribute which includes a CONDITION_TAG condition provided |
| Reference | TS-0001 9.6.8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the Originator having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing supscription resource containing eventNotificationCriteria attribute containing CONDITION_TAG condition set to VALUE } | IUT ( AE |
|  | then { the IUT creates the subscription resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

| TP Id | Reference | CONDITION_TAG |
| --- | --- | --- |
| TP/oneM2M/CSE/SUB/CRE/008_CRB | TS-0001 9.6.8 | createdBefore |
| TP/oneM2M/CSE/SUB/CRE/008_CRA | TS-0001 9.6.8 | createdAfter |
| TP/oneM2M/CSE/SUB/CRE/008_MS | TS-0001 9.6.8 | modifiedSince |
| TP/oneM2M/CSE/SUB/CRE/008_US | TS-0001 9.6.8 | unmodifiedSince |
| TP/oneM2M/CSE/SUB/CRE/008_STS | TS-0001 9.6.8 | stateTagSmaller |
| TP/oneM2M/CSE/SUB/CRE/008_STB | TS-0001 9.6.8 | stateTagBigger |
| TP/oneM2M/CSE/SUB/CRE/008_EXB | TS-0001 9.6.8 | expireBefore |
| TP/oneM2M/CSE/SUB/CRE/008_EXA | TS-0001 9.6.8 | expireAfter |
| TP/oneM2M/CSE/SUB/CRE/008_SZA | TS-0001 9.6.8 | sizeAbove |
| TP/oneM2M/CSE/SUB/CRE/008_SZB | TS-0001 9.6.8 | sizeBelow |
| TP/oneM2M/CSE/SUB/CRE/008_ET | TS-0001 9.6.8 | eventType |
| TP/oneM2M/CSE/SUB/CRE/008_OM | TS-0001 9.6.8 | operationMonitor |
| TP/oneM2M/CSE/SUB/CRE/008_ATR | TS-0001 9.6.8 | attribute |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### CE/SUB/00002/00005

Support the pendingNotification attribute of <subscription> resource

###### CREATE OPERATION

TP/oneM2M/CSE/DMR/CRE/015_PN/SUB

###### UPDATE OPERATION

TP/oneM2M/CSE/DMR/UPD/014_PN/SUB

TP/oneM2M/CSE/DMR/UPD/017_PN/SUB

###### NOTIFY OPERATION

TP/oneM2M/CSE/SUB/NTF/005

| TP Id | TP/oneM2M/CSE/SUB/NTF/005 |
| --- | --- |
| Test objective | Check that the IUT sends the latest cached notification after IUT escapes from connectionless state |
| Reference | TS-0001 9.6.8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered the AE2 and the AE1 having created a <subscribed-to type> resource containing subscription child resource containing notificationURI attribute set to AE2_RESOURCE_ADDRESS and pendingNotification attribute set to 1 (sendLatest) and the AE2 having privileges to perform RETRIEVE operation on the subscribed-to resource and the IUT having frequently received from AE1 a valid UPDATE Requests to subscribed-to resource and the IUT being in the “connectionless state” } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT escapes from the “connectionless state” } | NA |
|  | then { The IUT sends a valid NOTIFY Request contaning Content containing the latest notification message } | IUT  AE2 |

TP/oneM2M/CSE/SUB/NTF/006

| TP Id | TP/oneM2M/CSE/SUB/NTF/006 |
| --- | --- |
| Test objective | Check that the IUT sends the aggregated notification of cached notification messages after IUT escapes from connectionless state |
| Reference | TS-0001 9.6.8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered the AE2 and the AE1 having created a <subscribed-to type> resource containing subscription child resource containing notificationURI attribute set to AE2_RESOURCE_ADDRESS and pendingNotification attribute set to 2 (sendAllPending) and the AE2 having privileges to perform RETRIEVE operation on the subscribed-to resource and the IUT having frequently received from AE1 a valid UPDATE Requests to subscribed-to resource and the IUT being in the “connectionless state” } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT escapes from the “connectionless state” } | NA |
|  | then { The IUT sends a valid NOTIFY Request contaning Content containing the aggregated notification message } | IUT  AE2 |

### -----------------------End of change 2---------------------------------------------

# Comments

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-09163

REQ-0001-09164

REQ-0001-09135

REQ-0001-09138

REQ-0001-09139

REQ-0001-09141

REQ-0001-09142

REQ-0001-09143

REQ-0001-09144

REQ-0001-09166

REQ-0001-09145

REQ-0001-09146

REQ-0001-09149

REQ-0001-09151

REQ-0001-09152

REQ-0001-09153

REQ-0001-09154

REQ-0001-09155

REQ-0001-09156

REQ-0001-09157

REQ-0001-09158

REQ-0001-09159

REQ-0001-09160

REQ-0001-09161

REQ-0001-09162

TS-0001_SN_002

REQ-0001-10064

REQ-0001-10065