| Work Item |
| --- |
| Work Item Title:* | Conformance Test Release 2 |
| Document Number* | WI-00XX |
| Supporting Members or Partner type 2* | Huawei Technologies Co., Ltd., KETI, TTA, Convida Wireless, Sensinov |
| Date:* | 2017-07-10 |
| Abstract:* | The WI defines conformance test that applies to oneM2M Release 2. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

1	Title (Acronym)

Conformance Test Release 2

2	Justification

The present Work Item proposes to update the series of Conformance testing specifications TS-0017 (PICS), TS-0018 (TSS and TP) and TS-0019 (ATS & PIXIT) to match the requirements of the Release 2 versions of TS-0001 and TS-0004.

It is also intended to add new Tests in order to address the new resources, features and fucntions specified in the Release 2.

3	Intended Output

| Tick all the appropriate cases |  |
| --- | --- |
|  | Change request(s) to existing Technical Specification(s) |
|  | Change request(s) to existing Technical Reports(s) |
| √ | New Normative Technical Specifications(s) |
|  | New Permanent Technical Reports(s) |
|  | New Temporary Technical Reports(s) |

- Impact

###### Impact on other Technical Specifications and Technical Reports

TS-0017, TS-0018 and TS-0019 for Release 1 (WI-0032 : conformance test)

###### Impact on other oneM2M Work Items

None expected

5	Scope

The scope of the WI includes identification of the functions and features needed to be tested:

TS-0017 – Implementation Conformance Statements

-	Check list for the ICS.

TS-0018 – Test Suite Structure and Test Purposes

-	Organize the functions and features need to be tested into test suites.

-	Specify test purposes and test descriptions for conformance test.

-	Define test cases.

TS-0019 – Abstract Test Suite and Implementation eXtra Information for Test

-	Definition of the Abstract Protocol Tester (APT)

-	Definition of TTCN-3 test architecture

-	Development of TTCN-3 test suite, e.g. naming conventions, code documentation, test case structure.

-	IXIT proforma.

6	Schedule and impacted specifications

Provide the schedule of tasks to be performed;

| New Specifications (if any) |
| --- |
| Document Type | Document Number* | Title | Schedule (TP No.) | Lead WG | Impacted WGs | Comments |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |  |
| TS | 0017 | Implementation Conformance Statements | TP31 | TP35 | TP36 | TP40 | WG6 | None | Rapporteur: KETI & Laurent Velez |
| TS | 0018 | Test Suite Structure and Test Purposes | TP31 | TP35 | TP36 | TP40 | WG6 | None | Rapporteur: KETI & Laurent Velez |
| TS | 0019 | Abstract Test Suite and Implementation eXtra Information for Test | TP31 | TP35 | TP36 | TP40 | WG6 | None | Rapporteur: Miguel Angel Reina Ortega |

7	Work Item Rapporteur(s)

Miguel Angel Reina Ortega (ETSI)

8	History

| Document history |
| --- |
| V0.0.1 | 10 July 2017 | Initial draft for WI complied to oneM2M Release 2 |

-------------------------------