| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#31 |
| Source:* | Maciej Goluch, ORANGE, maciej.goluch@orange.com, Paweł Strzemecki |
| Date:* | 2017-09-13 |
| Reason for Change/s:* | Add new content and make corrections |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0054> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0039 ‘Developer guide: Interworking Proxy using SDT’ |
| Clauses * | 5.1, 8.3, 9.3, 9.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This document brings a legal note regarding Philips Hue API in 5.1 section and call flows for subscription mechanism in 8.3.3.5 section. It also corrects short names for resources (which shall be specific for SDT representations) in each HTTP request. It also brings a description of verification request in 9.4.3.5 and some corrections in 8.3 section.

### -----------------------Start of change 1 ------------------------------------------

## 5.1	Abstraction description via the bulbs example

This guide is based on the following use case: an application on Gateway, Cloud/Server, or Smartphone want to monitor and control bulbs. Due to the abstraction layer provided by oneM2M, the monitoring and controlling processes  can be performed independently from underlying connectivity technologies. This tutorial is based on the example of Philips Hue bulbs (these bulbs require dedicated bridge for connection with Gateway). Figure 5.1-1 presents the general architecture of the use case.

NOTE: The terms of use of Philips Hue API are available at https://developers.meethue.com/documentation/terms-use.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### 8.2.2 SDT Device resource tree creation in MN-CSE

The procedure to create resource tree for particular SDT Device (deviceLight in this use case) is as follows:

- Device adapter (IPE-AE) sends a CREATE request to gateway (MN-CSE) to create <flexContainer> for SDT Device.

- Gateway (MN-CSE) responds with URI of the new <flexContainer> for SDT Device.

- Device adapter (IPE-AE) sends a CREATE reqest to gateway (MN-CSE) to create a <flexContainer> for a single Module with associated customAttributes (DataPoints). Please note that there is sent one such request per each Module.

- Gateway (MN-CSE) responds with URI for created Module.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

### 8.3.2 Discovery Requests

The procedure to discover SDT Device is as follows:

- Utility application (ADN-AE-1) sends a RETRIEVE request to server (IN-CSE) including filter criteria conditions, especially it could be a containerDefinition attribute 
(e.g. org.onem2m.home.devices.deviceLight)

- Server (IN-CSE) responds with list of URIs of the discovered resources, if any (especially URI for deviceLight which represents a bulb).

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

### 8.3.3.2		DataPoint value retrieving

Retrieving value of a DataPoint is possible only through retrieving all DataPoints which belong to particular ModuleClass.The procedure to get values of all DataPoints  which belong to particular ModuleClass is as follows:

- Utility application (ADN-AE-1) sends a RETRIEVE request to server (IN-CSE) with information which ModuleClass's DataPoints should be retrieved.

- Server (IN-CSE) responds with current values of all DataPoints   which belong to the ModuleClass that was requested.

Figure 8.3.3.2-1: DataPoint retrievement

### 8.3.3.3		DataPoint value changing

The procedure to change DataPoint value is as follows:

- Utility application (ADN-AE-1) sends an UPDATE request to server (IN-CSE) with <flexContainer> which contains the new value of the DataPoint. . There is also a possibility to change more than one DataPoint of particular ModuleClass in a single request (in this case the <flexContainer> contains new values of all needed DataPoints.

- Server (IN-CSE) responds with status of DataPoint’s UPDATE operation

Figure 8.3.3.3-1: Change value of a DataPoint

### 8.3.3.4		Action triggering

The procedure to trigger an Action with no arugments is as follows:

- Utility application (ADN-AE-1) sends an UPDATE request to server (IN-CSE) with empty <flexContainer>.

- Server (IN-CSE) responds with status of UPDATE operation

Figure 8.3.3.4-1: Action triggering procedure

### 8.3.3.5		Subscription mechanism

Following diagrams show four parts of subscription mechanism: subscription creation, listener's status verification, notification message triggered by DataPoint value change and subsription deletion.

The procedure of creating a <subscription> resource is as follows:

- Utility application (ADN-AE-1) sends a CREATE request to server (IN-CSE).

- Server (IN-CSE) responds with all parameters of  created <subscription> resource.

Figure 8.3.3.5-1: Subscription creation procedure

There's a mechanism that allows Server to check listener's availability. The procedure of listener's (ADN-AE-1) status verification is as follows:

- Server (IN-CSE) sends verification request to listener (ADN-AE-1).

- Listener (ADN-AE-1) responds with HTTP 200 OK status.

Figure 8.3.3.5-2: Listener's status verification procedure

A change of DataPoint’s value triggers a notification message with new DataPoint value that is sent to listener. The procedure of notification mechanism is as follows:

- DataPoint value change occurs.

- Server (IN-CSE) sends to utility application (ADN-AE-1) notification with new DataPoint value.

- Utility application (ADN-AE-1)  sends confirmation of receiving the notification.

Figure 8.3.3.5-3: Notification mechanism procedure

The procedure of deletion of a <subsription> resource is as follows:

- Utility application (ADN-AE-1) sends a DELETE request to server (IN-CSE).

- Server (IN-CSE) responds with deletion confirmation.

Figure 8.3.3.5-4: Deletion of <subscription> resource procedure

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5---------------------------------------------

### 9.3.2 SDT Device resource tree creation in MN-CSE (Resources registration)

This clause describes creation of device resource tree which consists of Device, ModuleClasses and Actions. Firstly, a Device resource is created. Device is mapped to flexContainer resource, so a flexContainer resource is created.

The following request creates flexContainer resource for deviceLight. In response, there is a Content-Location header which indicates the new Device address to be used later in ModuleClass creation.

POST /~/mn-cse/ae-CAE340304178 HTTP/1.1
Host: mncse.provider.com:8080
X-M2M-Origin: Soriginator

Content-Type: application/xml;ty=28

X-M2M-RI: home_gateway-12

<?xml version="1.0" encoding="UTF-8"?>

<hd:devLt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="deviceLight">

<cnd>org.onem2m.home.device.deviceLight</cnd>

</hd:devLt>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: home_gateway-12

Content-Location: /mn-cse/DL3404345178

Flex Container creation procedure is comprehensively described in 10.2.4.16 TS-0001.

To create ModuleClass on Device, the creation request is sent to Device address taken from Device creation request response. In SDT,  ModuleClasses are mapped to flexContainer and DataPoints are mapped to customAttribute. To create binarySwitch ModuleClass, the following request is sent

POST /~/mn-cse/DL3404345178 HTTP/1.1
Host: mncse.provider.com:8080

X-M2M-Origin: Soriginator

Content-Type: application/xml;ty=28

X-M2M-RI: home_gateway-43

<?xml version="1.0" encoding="UTF-8"?>

<hd:binSh xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="binarySwitch">

<cnd>org.onem2m.home.moduleclass.binaryswitch</cnd>

<powSe type="xs:boolean">false</powSe>

</hd:binSh>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: home_gateway-43

Content-Location: _/mn-cse/MC43546456

In response there's Content-Location header which indicates created ModuleClass address which is used later to create Toggle Action and to modificate state of particular DataPoint.

In SDT, Actions are also mapped to FlexContainer. To add new Action to ModuleClass, the following request is sent to the ModuleClass address.

POST /~/mn-cse/MC43546456 HTTP/1.1
Host: mncse.provider.com:8080

X-M2M-Origin: Soriginator

Content-Type: application/xml;ty=28

X-M2M-RI: home_gateway-44

<?xml version="1.0" encoding="UTF-8"?>

<hd:toggle xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="toggle">

<cnd>org.onem2m.home.moduleclass.binaryswitch.toggle</cnd>

</hd:toggle>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: home_gateway-44

Content-Location: /mn-cse/AC-54783722

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6---------------------------------------------

### 9.4.3.2	DataPoint value retrieving

To monitor powerState, a RETRIEVE request to binarySwitch resource (/mn-cse/MC43546456)is sent as following. In response there is xml payload which contains whole binarySwitch representation.

Remark: Retrieving value of a DataPoint is possible only through retrieving all DataPoints which belong to particular ModuleClass. The set of all ModuleClass's DataPoints is sent in response.

GET /~/mn-cse/MC43546456?rcn=1 HTTP/1.1
Host: incse.provider.com:8080
X-M2M-Origin: Soriginator

Content-Type: application/xml

X-M2M-RI: server-12346

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: server-12346

<?xml version="1.0" encoding="UTF-8"?>

<hd:binSh xmlns:m2m="http://www.onem2m.org/xml/protocols">

<powSe type="xs:boolean">true</powSe>

</hd:binSh>

### 9.4.3.3	DataPoint value changing

To change powerState value,  a request to binarySwitch resource  (/mn-cse/MC43546456)is sent with xml (or json) representation of new powerState value. PUT request is used because whole resource is updated.

Following requests changes powerState DataPoint to 'true'.

PUT /~/mn-cse/MC43546456 HTTP/1.1
Host: incse.provider.com:8080
X-M2M-Origin: Soriginator

Content-Type: application/xml

X-M2M-RI: server-12346

<?xml version="1.0" encoding="UTF-8"?>

<hd:binSh xmlns:m2m="http://www.onem2m.org/xml/protocols" >

<powSe type="xs:boolean">true</powSe>

</hd:binSh>

HTTP Response:

204 Updated

X-M2M-RSC: 2004

X-M2M-RI: server-12346

### 9.4.3.4	Action trigerring

To trigger Toggle action,  a null content parameter is sent to toggle resource address. (see TS-0023,  6.2.4 Clause, Rule 3-4).

Following request sends null content and triggers Toggle action.

PUT /~/mn-cse/AC-54783722 HTTP/1.1
Host: incse.provider.com:8080
X-M2M-Origin: Soriginator

Content-Type: application/xml

X-M2M-RI: server-12346

<?xml version="1.0" encoding="UTF-8"?>

<hd:toggle xmlns:m2m="http://www.onem2m.org/xml/protocols" >

</hd:toggle>

HTTP Response:

204 Updated

X-M2M-RSC: 2004

X-M2M-RI: server-12346

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7---------------------------------------------

### 9.4.3.5	Subscription mechanism

Following request creates subscription on binarySwitch resource (mn-cse/MC43546456) which allows to send notifications after its state change. There are two mandatory parameters.

NotificationURI parameter is represented by <nu> xml tag and indicates the address of the device which is supposed to be notificated about ouccured changes. In our case smartphone IP address is used.

Remark: In our use case smartphone IP address is used as a receiver of notifications but in other usage there can be used notification server with static IP address assigned. In such use case this server would be responsible to send notification directly on smartphone address.

NotificationContentType is represented by <nct> xml tag and indicates the type of notification. Its value is one of the following:

- 1: all atributes

- 2: modified attributes,

- 3: resourceID

In our example <nct> is set to 2.

In response there is a whole set of subscription resource parameters.

POST /~/mn-cse/MC43546456 HTTP/1.1
Host: incse.provider.com:8080
X-M2M-Origin: Soriginator

Content-Type: application/xml

X-M2M-RI: server-12346

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="sub_45346345">

<nu>192.168.10.1</nu>

<nct>2</nct>

</m2m:sub>

HTTP Response

HTTP/1.1 200 OK

X-M2M-RSC: 2000

X-M2M-RI: server-12345<rn>sub_45346345</rn>

<ty>23</ty>

<ri>/~/mn-cse/MC43546456/sub-45346345</ri>

<pi>/~/mn-cse/MC43546456/fcnt-45352623</pi>

<ct>20170802T143815</ct>

<lt>20170802T143815</lt>

<nu>192.168.10.1</nu>

<nct>2</nct>

After subscription creation, server starts to send verification requests to listener periodically. Verification request has <vrq> attribute set to true. Listener answers with HTTP 200 status to confirm that it is still available. Verification request and listener's response is as follows:

POST 192.168.10.1 / HTTP/1.1

Host: 192.168.10.1

X-M2M-Origin: Soriginator

X-M2M-RI: notif-12345

Content-Type: application/vnd.onem2m-ntfy+xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sgn xmlns:m2m="http://www.onem2m.org/xml/protocols">

<vrq>true</vrq>

<sud>false</sud>

</m2m:sgn>

HTTP Response

HTTP/1.1 200 OK

X-M2M-RSC: 2000

X-M2M-RI: notif-12345

Here is the example of notification which is supposed to be sent after powerState value change. Notification is sent to address which was set in subsription creation request and contains representation of changed DataPoints of binarySwitch resource.

POST 192.168.10.1 / HTTP/1.1

Host: 192.168.10.1

X-M2M-Origin: Soriginator

X-M2M-RI: notif-12345

Content-Type: application/vnd.onem2m-ntfy+xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sgn xmlns:m2m="http://www.onem2m.org/xml/protocols">

<nev>

<rep>

<powSe type="xs:boolean">true</powSe>

</rep>

<rss>1</rss>

</nev>

<sur> mn-cse/MC43546456/sub-45346345</sur>

</m2m:sgn>

HTTP Response

HTTP/1.1 200 OK

X-M2M-RSC: 2000

X-M2M-RI: notif-12345

Following request deletes subscription on binarySwitch.

DELETE /~/mn-cse/MC43546456/sub-45346345 HTTP/1.1

Host: incse.provider.com:8080
X-M2M-Origin: Soriginator

Accept: application/xml

HTTP Response

HTTP/1.1 204 No Content

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8---------------------------------------------

### -----------------------End of change 8---------------------------------------------