| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS #40 |
| Source:* | Bei Xu, Huawei Technologies Co.,Ltd., echo.xubei@huawei.com Dale Seed, Convida Wireless, Dale.Seed@InterDigital.com |
| Date:* | 2019-05-17 |
| Reason for Change/s:* | The CR is to add new feature of 3GPP QoS interworking. |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 |
| Clauses * | 8.X |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TR-0024 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The this solution can support the two deployments as below:

- zero hop bewteen the IN-CSE and ASN/MN-CSE

- one hops between the ASN/MN-CSE and the ASN/MN-CSE

The other deployments are FFS.

When creating QoS, the creator focus on the QoS between the Originator and the targeted node for the specified resource type. This solution supports the E2E QoS creation, but only supports the QoS flow between IN-CSE and ADN-AE or ASN/MN-CSE which is 3GPP UE.

QoS Requirements in TS-0002:

| OSR-038 | The oneM2M System shall support the inclusion of M2M Application's QoS preference in service requests to Underlying Networks. | Not implemented |
| --- | --- | --- |
| OSR-039 | The oneM2M System shall be able to authorize service requests with QoS preference at service level, but shall pass M2M Application's QoS preference in service requests to Underlying Network for authorization and granting or negotiation of the service QoS requests. | Not implemented |
| OSR-042 | The oneM2M System shall be able to support different QoS-levels specifying parameters, such as guaranteed bitrate, delay, delay variation, loss ratio and error rate, etc. | Not implemented |

R01:

Delete the service flow in this contribution.

R03:

Update the solution according to the discussion by email.

R04:

Update the resourceIDList to optional.

### -----------------------Start of change 1-------------------------------------------

## 8.x	Setting up an AS session with required QoS procedure

### 8.x.4 oneM2M solution

#### 8.x.4.1	Resource Structure

##### 8.x.4.1.1 Resource Type e2eQosSession

The <e2eQosSession> resource defines end-to-end (E2E) QoS session requirements for the exchange of oneM2M request and response primitives between oneM2M entities. This resource consists of a set of QoS parameters and an applicable set of oneM2M entities that exchange oneM2M requests and responses with one another and function as the session endpoints.  A Hosting CSE uses the information configured within this resource to configure and manage E2E QoS between these session endpoints.  For example, the Hosting CSE can manage the establishment and tear-down of QoS session(s) in underlying network(s) that interconnect oneM2M entities with one another,  A Hosting CSE can also use this information to manage the scheduling and store-and-forwarding of requests and responses that it performs at the oneM2M service layer. When establishing a QoS session in an underlying network, a Hosting CSE can configure the QoS parameters based on the requirements defined by the <e2eQosSession> resource.  For cases where the oneM2M entities are separated by multiple hops, each hop may require the establishment and configuration of a separate underlying network QoS session.   For this case, a Hosting CSE can coordinate with its registrar and registree CSEs to assist it with the configuration of a QoS session in each respective underlying network involved in a multi-hop E2E QoS session such that the E2E QoS requirements defined within the <e2eQosSession> can be satisfied across the multiple hops.

Note – This current solution supports the 0-hop scenario and the 1-hop scenario involving a <e2eQosSession> Hosting CSE that is the registrar CSE of the session endpoints. The details for how an E2E QoS session is supported for multiple hop scenarios is for FFS.

The following are some examples of E2E oneM2M communication flows that an <e2eQosSession> resource Hosting CSE can manage using this QoS information.

Example #1

A first oneM2M entity that is a session endpoint sends a request to the <e2eQosSession> resource Hosting CSE and the To parameter targets a remote oneM2M entity that is also a session endpoint of the same QoS session.  The <e2eQosSession> resource Hosting CSE can establish an individual underlying network QoS session between itself and each of the session endpoints such that each underlying network QoS session meets the QoS requirements defined in the <e2eQosSession> resource.  In doing so, the E2E exchange of oneM2M request and response primitives between the session endpoint entities meets the E2E QoS requirements defined in the <e2eQosSession> resource.

Example #2

A first oneM2M entity that is a session endpoint is a subscriber to a <flexContainer> resource that is hosted by the <e2eQosSession> resource Hosting CSE.  A second oneM2M entity, that is also a session endpoint of the same QoS session, sends a request to update the <flexContainer> resource.  The update results in a notification being sent to the first oneM2M entity.  The <e2eQosSession> resource Hosting CSE can establish an individual underlying network QoS session between itself and each of the session endpoints such that each underlying network QoS sessions meets the QoS requirements defined in the <e2eQosSession> resource.  In doing so, the E2E exchange involving the second oneM2M entity sending the <flexContainer> update request and the resulting notification request that is sent to the first oneM2M entity meets the E2E QoS requirements defined in the <e2eQosSession> resource.

The <e2eQosSession> resource contains the child resources specified in table 8.x.4.1.1-1.

Table 8.x.4.1.1-1: Child resources of <e2eQosSession> resource

| Child Resources of <e2eQosSession> | Child Resource Type | Multiplicity | Description | <e2eQosSession> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8. | <subscription> |

The <e2eQosSession> resource contains the attributes specified in table 8.x.4.1.1-2.

Table 8.x.4.1.1-2: Attributes of <e2eQosSession> resource

| Attributes of <e2eQosSession> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 |
| resourceID | 1 | RO | See clause 9.6.1.3 |
| resourceName | 1 | WO | See clause 9.6.1.3 |
| parentID | 1 | RO | See clause 9.6.1.3 |
| creationTime | 1 | RO | See clause 9.6.1.3 |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 |
| expirationTime | 1 | RW | See clause 9.6.1.3 |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3. |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 |
| sessionEndpoints | 1 | WO | Indicates the oneM2M endpoints within one oneM2M E2E QoS session. The end points include AE-IDs or CSE-IDs. If an AE-ID is used and the AE is not a Registree of the <e2eQosSession> Hosting CSE, then the AE-ID will be formatted as a SP-Relative-AE-ID or Absolute-AE-ID to allow the <e2eQosSession> Hosting CSE to extract the CSE-ID of the CSE that hosts the destination endpoint <AE> resource. |
| e2eQosRequirements | 1(L) | RW | Defines the E2E QoS requirements expressed as a list of tuples. Each tuple in the list defines a single QoS session requirement applicable to the bi-directional exchange of oneM2M requests and responses between all the endpoints. Each tuple in the list contains the set of elements as defined below in table 8.x.4.1.1-3. |
| e2eQosPolicies | 0..1(L) | RW | Defines E2E session QoS policies expressed as a list of tuples. Each tuple in the list defines a single policy that the <e2eQosSession> Hosting CSE uses to manage the session. Each tuple in the list contains the set of elements as defined below in table 8.x.4.1.1-4. |

Table 8.x.4.1.1-3: Elements of an e2eQosRequirements tuple

| Name | Mandatory/Optional | Description |
| --- | --- | --- |
| qosLevel | M | Defines the required QoS level for this session. Expressed as a range from 0 (lowest) to 100 (highest). How a <e2eQosSession> Hosting CSE uses this parameter to manage the QoS of a session is implementation dependent (e.g. a Hosting CSE may map this value to an underlying network operator’s session QoS parameter values). |
| resourceIDList | O | Defines the resource identifier list between the endpoints which the QoS requirement applies to. If a Resource-ID is used and the resource is not hosted by the <e2eQosSession> Hosting CSE, then it will be formatted as a SP-Relative-Resource-ID or Absolute-Resource-ID to allow the <e2eQosSession> Hosting CSE to extract the CSE-ID of the CSE that hosts the destination endpoint resource. The use of a Resource-ID enables a destination E2E QoS session endpoint to be defined at the granularity of an individual targeted resource. |
| sessionSchedule | O | Defines the time periods for when bi-directional exchange of oneM2M requests and responses between the session endpoints at the specified qosLevel is required to be enabled. If this parameter is not specified, then the scheduling of the oneM2M requests and responses between the session endpoints will be managed at the discretion of the <e2eQosSession> Hosting CSE based on the specified qosLevel. The schedule is composed of seven fields consisting of second, minute, hour, day of month, month, day of week and year. |
| numOfRequests | O | Defines the minimum number of requests required to be transferred at the specified qosLevel via the bi-directional exchange of oneM2M requests and responses between the session endpoints. If this parameter is not specified, then the number of requests and responses allowed between the session endpoints will be managed at the discretion of the <e2eQosSession> Hosting CSE based on the specified qosLevel. |
| numOfBytes | O | Defines the minimum number of bytes required to be transferred at the specified qosLevel via the bi-directional exchange of oneM2M requests and responses between the session endpoints. If this parameter is not specified, then the number of bytes allowed to be transferred between the session endpoints will be managed at the discretion of the <e2eQosSession> Hosting CSE based on the specified qosLevel. |

Table 8.x.4.1.1-4: Elements of an e2eQosPolicy tuple

| Name | Mandatory/Optional | Description |
| --- | --- | --- |
| status | M | When the e2eQosStatus attribute of the <e2eQosSession> resource transitions to the value specified in this element, the <e2eQosSession> Hosting CSE performs the action specified in the action element. The following are the allowed status values: FAILED DISABLED USAGE_EXHAUSTED |
| action | M | Defines a session related action that is performed by the <e2eQosSession> Hosting CSE when the value of an e2eQosStatus attribute of the <e2eQosSession> resource transitions to the value specified by the status element. The following are the allowed action values: RE-ENABLE: The <e2eQosSession> Hosting CSE will attempt to re-enable the E2E QoS session in a manner that is consistent with the e2eQosRequirements. DISABLE: The <e2eQosSession> Hosting CSE will disable the E2E QoS session (if already not disabled). DELETE: The Hosting CSE will delete the E2E QoS session |

##### 8.x.4.1.2 Resource Type CSEBase

Table 8.x.4.1.2-1 Child resources of <CSEBase> resource

| Child Resources of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <e2eQosSession> | 0..1 | See clause 9.6.aa |

##### 8.x.4.1.3 Resource Type remoteCSE

Table 8.x.4.1.3-1: Child resources of <remoteCSE> resource

| Child Resources of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <e2eQosSession> | 0..1 | See clause 8.x.4.1.1 | < e2eQosSession Annc> |

##### 8.x.4.1.4 Resource Type AE

Table 8.x.4.1.4-1: Child resources of <AE> resource

| Child Resources of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <e2eQosSession> | 0..1 | See clause 8.x.4.1.1 | < e2eQosSession Annc> |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?