| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS#40 |
| Source:* | SeungMyeong JEONG, KETI, sm.jeong@keti.re.kr |
| Date:* | 2019-05-13 |
| Reason for Change/s:* | Clean-up on semantic representation types |
| CR against: Release* | 3 |
| CR against: WI* | Active MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0034 v3.0.1 |
| Clauses * | 6.1 <semanticDescriptor> Operations 6.8 <ontology> Operations |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | n/a |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As follow-up actions to the agreed contributions below,

- SDS-2018-0001R04-TS-0004_R3_CR_-_allowed_semantic_representation_types

- SDS-2018-0002R04-TS-0004_R2_CR_-_allowed_semantic_representation_types

there has been the action item assigned:

| Number | Action |
| --- | --- |
| A-SDS-39-03 | Follow up action related to SDS-2018-0001 and allowed semantic descriptor representation types, SeungMyeong will add text to TS-0001 and/or TS-0004 regarding unsupported parameter and attribute settings. |

In Rel-3/4 TS-0001 does not specify the semantic resources CRUD procedures but the TS-0034 does. Therefore this CR proposes changes on the missing resource specific procedures.

### ********** Start of change 1 **********

### ********** End of change 1 **********

## <semanticDescriptor> Operations

### Introduction

The <semanticDescriptor> resource is used to store a semantic description pertaining to a resource and potentially sub-resources. Such a description may be provided according to ontologies. The semantic information is used by the semantic functionalities of the oneM2M system and is also available to applications or CSEs. For resource type description see [1] clause 9.6.30.

### Create <semanticDescriptor>

This procedure shall be used for creating a <semanticDescriptor > resource.

Table 6.1.2-1: <semanticDescriptor> CREATE

| <semanticDescriptor> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in oneM2M TS-0001 [1] table 8.1.2-2 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.30 in oneM2M TS-0001 [1] |
| Processing at Originator before sending Request | According to clause 10.1.2 in oneM2M TS-0001 [1] |
| Processing at Receiver | The Hosting CSE shall follow the basic procedure according to clause 10.1.2 of [1], with the following specific details: shall check that the descriptor attribute conforms to the syntax as defined in the descriptorRepresentation attribute shall trigger the semantic validation process as specified in clause 7.10 if the validationEnable attribute of the <semanticDescriptor> resource is set to true, and shall set the semanticValidated attribute of <semanticDescriptor> resource according to the validation result. |
| Information in Response message | According to clause 10.1.2 in oneM2M TS-0001 [1] |
| Processing at Originator after receiving Response | According to clause 10.1.2 in oneM2M TS-0001 [1] |
| Exceptions | According to clause 10.1.2 in oneM2M TS-0001 [1] |

### Retrieve <semanticDescriptor>

This procedure shall be used for retrieving the attributes of a <semanticDescriptor> resource.

Table 6.1.3-1: <semanticDescriptor> RETRIEVE

| <semanticDescriptor > RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in oneM2M TS-0001 [1] table 8.1.2-2. |
| Processing at Originator before sending Request | According to clause 10.1.3. in oneM2M TS-0001 [1] |
| Processing at Receiver | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Information in Response message | All parameters defined in oneM2M TS-0001 [1] table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.3 in oneM2M TS-0001 [1]. |

### Update <semanticDescriptor>

This procedure shall be used for updating attributes of a <semanticDescriptor > resource.

Table 6.1.4-1: <semanticDescriptor> UPDATE

| <semanticDescriptor> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in oneM2M TS-0001 [1] table 8.1.2-2 apply with the specific details for: the Content request parameter which may contain the new descriptor information in one of the following ways: 1) full representation of the descriptor attribute; or 2) partial representation of the descriptor attribute as described in SPARQL statements [2] in the semanticOpExec attribute. |
| Processing at Originator before sending Request | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Processing at Receiver | The hosting CSE shall follow the basic procedure according to clause 10.1.4 in oneM2M TS-0001 [1], with the following specific details: check if both semanticOpExec attribute and ontologyContent attribute exist in the the Content request parameter, if so, return an error code; shall update the descriptor attribute according to the execution result of the SPARQL statements [2] in the semanticOpExec attribute, if it presents in the Content request parameter; shall check that the descriptor attribute conforms to the syntax as defined in the descriptorRepresentation attribute, if it presents in the Content request parameter shall trigger the semantic validation process as specified in clause 7.10 if the validationEnable attribute of the <semanticDescriptor> resource is set to true, and shall update the semanticValidated attribute of <semanticDescriptor> resource according to the validation result. |
| Information in Response message | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Processing at Originator after receiving Response | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.4 in oneM2M TS-0001 [1]. |

### ********** Start of change 2 **********

## <ontology> Operations

### Introduction

Each <ontology> resource represents an ontology under management in the oneM2M system. It may contain the full representation or the IRI reference of the managed ontology. It is managed by simple CRUD operations as ordinary resource or by more advanced SPARQL operations (contained in the payload of the Update and Retrieve) at the granularity of RDF-triple level.

### Create <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 6.8.2-1: <ontology> CREATE

| <ontology> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1] apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.51 in oneM2M TS-0001 [1]. |
| Processing at Originator before sending Request | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.2 in oneM2M TS-0001 [1] with the specific details as follows: The Hosting CSE shall check that the ontologyContent attribute conforms to the syntax as defined in the ontologyFormat attribute. |
| Information in Response message | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Processing at Originator after receiving Response | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.2 in oneM2M TS-0001 [1]. |

### Retrieve <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 6.8.3-1: <<ontology> RETRIEVE

| <ontology> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1]. |
| Processing at Originator before sending Request | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Information in Response message | All parameters defined in table 8.1.3-1 in oneM2M TS-0001 [1] apply. |
| Processing at Originator after receiving Response | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.3 in oneM2M TS-0001 [1]. |

### Update <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 6.8.4-1: <ontology> UPDATE

| <ontology> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1] shall apply with the specific details for the Content request parameter which may contain the new ontology information in one of the following ways: the full representation of the new ontology triples in the ontologyContent attribute; or the new IRI of the ontology in the ontologyContent attribute; or the partial representation of the new ontology as described in SPARQL statements [2] in the semanticOpExec attribute in the case that the ontologyFormat is not 'IRI'. |
| Processing at Originator before sending Request | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.4 in oneM2M TS-0001 [1] with the specific details as follows: Check if both semanticOpExec attribute and ontologyContent attribute exist in the the Content request parameter, if so, return an error code. In the case that the Content request parameter contains partial representation of the new ontology as described in SPARQL statements [2] in the semanticOpExec attribute, and the ontologyFormat is not set to 'IRI', the Hosting CSE shall update the ontologyContent attribute according to the execution result of the SPARQL statements [2]. In the case that the Content request parameter contains the ontologyContent attribute, the Hosting CSE shall check that the ontologyContent attribute conforms to the syntax as defined in the ontologyFormat attribute. |
| Information in Response message | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Processing at Originator after receiving Response | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.4 in oneM2M TS-0001 [1]. |

### ********** End of change 2 **********

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?