| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS#41 |
| Source:* | Kenichi Yamamoto, KDDI, kc-yamamoto@kddi.com |
| Date:* | 2019-06-28 |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 3GPP Interworking V4.1.0 |
| Clauses * | 8.3, 7.14 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add the error handling of MonitoringEvent API to clause 8.3 of TS-0026 (release 4) in order to address following Editor’s Note in clause 7.14.3.2.

Editor’s Note: 3GPP is currently revisiting the decision of whether to use a 400 Bad Request or a 500 Internal Server Error for the case where the SCEF doesn’t support the event requested by the SCS(IN-CSE). Based on their final decision, oneM2M may need to update the above text accordingly.

If a SCEF does not support a monitoring type requested by the SCS(IN-CSE), the SCEF will reject the request by sending a "500 Internal Server Error" HTTP error response with the application error "EVENT_UNSUPPORTED". The error procedure was added in 3GPP TS29.122 f40 published on June 2019 as follow (highlighted with yellow):

### 4.4.2	Monitoring Procedures (TS29.122)

#### 4.4.2.2	Monitoring Events Configuration

##### 4.4.2.2.1	General

In order to subscribe a new monitoring event configuration, the SCS/AS shall send an HTTP POST message to the SCEF to the resource "Monitoring Event Subscriptions". The body of the HTTP POST message shall include:

-	SCS/AS Identifier;

-	Monitoring Type;

-	Notification Destination Address; and

-	one of External Identifier or MSISDN or External Group Identifier, the External Identifier or MSISDN indicates the subscription for an individual UE and the External Group Identifier indicates a group of UEs.

-	In addition, the HTTP POST request may include:

-	Maximum Number of Reports;

-	Monitoring Duration indicated by the property "monitorExpireTime";

-	Group Reporting Guard Time.

If the Subscription_modification feature is supported, the SCS/AS may send an HTTP PUT message, in order to update an existing monitoring event subscription, the SCS/AS may send an HTTP PUT message to the resource "Individual Monitoring Event Subscription" replacing all properties in the existing configuration.

For one-time monitoring request, the SCS/AS shall include the Maximum Number of Reports with the value be set to 1, and shall not include the Monitoring Duration in the HTTP request message sent to the SCEF.

Upon receipt of the HTTP POST or PUT request message, if the SCS/AS is authorized to perform the request, the SCEF shall check whether the parameters (e.g. Maximum Number of Reports, Monitoring Duration, Maximum Latency, Maximum Response Time, Suggested number of downlink packets) in the HTTP request body are within the range defined by operator policies, if one or more of these parameters are not within the range, the SCEF shall:

-	either reject the request message by sending an HTTP response to the SCS/AS with a status code set to 403 Forbidden and may indicate the "PARAMETER_OUT_OF_RANGE" error in the "cause" attribute of the "ProblemDetails" structure and indicate which parameters are out of the range in the "invalidParams" attribute of the "ProblemDetails" structure; or

-	modify the parameters which are not within the range by selecting different values which are in the range.

For individual UE configuration request, the SCEF shall also check whether the Idle Status Indication is included for UE reachability event, if the Idle Status Indication is received in the request but not supported by the network, the SCEF may reject the request message by sending an HTTP response to the SCS/AS with a status code set to 403 Forbidden, and may indicate the "IDLE_STATUS_UNSUPPORTED" error in the "cause" attribute of the "ProblemDetails" structure.

If the SCEF receives an HTTP POST request to create a subscription resource for a monitoring event, but without an indication of the support for the feature corresponding to the monitoring event, the SCEF shall reject the request by sending a "400 Bad Request" HTTP error response with the application error "EVENT_FEATURE_MISMATCH".

If the SCEF receives an HTTP POST request to create a subscription resource for a monitoring event that it does not support, the SCEF shall reject the request by sending a "500 Internal Server Error" HTTP error response with the application error "EVENT_UNSUPPORTED".

After validation, the SCEF shall store the parameters and

-	may assign an SCEF Reference ID related to the created monitoring event subscription resource; and based on operator policies, shall

-	map the accuracy into permissible granularity for location reporting event;

-	map the location area into a list of cells, eNodeB(s) and/or RAI(s)/TAI(s) and derive the corresponding MME(s)/SGSN(s), for number of UEs present in a geographic area event.

In order to delete a previous active configured monitoring event subscription at the SCEF, the SCS/AS shall send an HTTP DELETE message to the SCEF to the resource "Individual Monitoring Event Subscription" which is received in the response to the request that has created the monitoring events subscription resource. The SCEF shall detemine the SCEF Reference ID related to the active monitoring subscription resource.

## 5.3	MonitoringEvent API(TS29.122)

###### 5.3.3.2.3.4	POST

The POST method creates a new subscription resource to monitor an event for a given SCS/AS. The SCS/AS shall initiate the HTTP POST request message and the SCEF shall respond to the message. The SCEF shall construct the URI of the created resource.

This method shall support the URI query parameters, request and response data structures, and response codes, as specified in the table 5.3.3.2.3.4-1 and table 5.3.3.2.3.4-2.

Table 5.3.3.2.3.4-1: URI query parameters supported by the POST method on this resource

| Name | Data type | Cardinality | Remarks |
| --- | --- | --- | --- |
| none specified |  |  |  |

Table 5.3.3.2.3.4-2: Data structures supported by the POST request/response by the resource

| Request body | Data type | Cardinality | Remarks |
| --- | --- | --- | --- |
|  | MonitoringEventSubscription | 1 | Parameters to register a subscription to notifications about monitoring event with the SCEF. |
| Response body | Data type | Cardinality | Response codes | Remarks |
|  | MonitoringEventSubscription | 1 | 201 Created | The subscription resource was created successfully. The URI of the created resource shall be returned in the "Location" HTTP header. |
|  | MonitoringEventReport | 1 | 200 OK | The operation is successful, and corresponding monitoring event report is included. This is only applicable for the one-time monitoring request if report is available in the response. |
|  | ProblemDetails | 1 | 400 Bad Request | The subscription resource is not allowed to be created since the supported feature corresponding to the monitoring event is not supported by the client. (NOTE 4) |
|  | ProblemDetails | 1 | 403 Forbidden | The subscription resource is not allowed to be created since one or more of the received parameters are out of the range defined by operator policies. (NOTE 2) |
|  | ProblemDetails | 1 | 403 Forbidden | The subscription resource is not allowed to be created since the Idle Status Indication is received in the request but not supported by the network. (NOTE 3) |
|  | ProblemDetails | 1 | 500 Internal Server Error | The subscription resource is not allowed to be created since the event is not supported by the server. (NOTE 5) |
| NOTE 1: The mandatory HTTP error status codes for the POST method listed in table 5.2.6-1 also apply. NOTE 2: The "cause" attribute within the "ProblemDetails" data structure may be set to "PARAMETER_OUT_OF_RANGE" as defined in subclause 5.3.5.3. In such case, the "invalidParams" attribute may be included within the "ProblemDetails" data structure to indicate which parameters are out of range. NOTE 3: The "cause" attribute within the "ProblemDetails" data structure may be set to "IDLE_STATUS_UNSUPPORTED" as defined in subclause 5.3.5.3. NOTE 4: The "cause" attribute within the "ProblemDetails" data structure may be set to "EVENT_FEATURE_MISMATCH" as defined in subclause 5.3.5.3. NOTE 5: The "cause" attribute within the "ProblemDetails" data structure may be set to "EVENT_UNSUPPORTED" as defined in subclause 5.3.5.3. |

#### 5.3.5.3	Application Errors

The application errors defined for MonitoringEvent API are listed in table 5.3.5.3-1. The SCEF shall include in the HTTP status code a “ProblemDetails” data structure with the “cause” attribute indicating the application error as listed in table 5.3.5.3-1.

Table 5.3.5.3-1: Application errors

| Application Error | HTTP status code | Description |
| --- | --- | --- |
| PARAMETER_OUT_OF_RANGE | 403 Forbidden | Indicates that the resource is not allowed to be created since one or more of the received parameter are out of range defined by operator policies. |
| IDLE_STATUS_UNSUPPORTED | 403 Forbidden | Indicates that the resource is not allowed to be created since the Idle Status Indication is received in the request but not supported by the network. |
| OPERATION_PROHIBITED | 403 Forbidden | Indicates the HTTP method is not supported. |
| EVENT_FEATURE_MISMATCH | 400 Bad Request | Indicates the resource creation is not allowed since the supported feature corresponding to the monitoring event is not supported by the client. |
| EVENT_UNSUPPORTED | 500 Internal Server Error | Indicates the required monitoring event is not supported by the server. |

The CR also proposes to delete following Editor’s Note in clause 7.14. Because adding Number of UEs in an area of Monitoring Event API to TS-0026 was agreed at SDS40.

Editor’s Note: The procedures for Number of UEs in an area of Monitoring Event API are currently FFS.

### -----------------------Start of change 1-------------------------------------------

## 8.3		Error Handling

An IN-CSE that interworks to a 3GPP SCEF via the T8 reference point shall support handling the following types of error conditions:

        - Unavailable SCEF – If the IN-CSE sends a request to the SCEF, but the SCEF does not respond back, the IN-CSE shall be robust to this scenario.  At a minimum, the IN-CSE shall support timing out the request.  The IN-CSE may support retrying requests but these details are out of scope of the present document.

        - Errors returned by the SCEF to the IN-CSE within T8 responses -  Table 8.3-1 provides a list of the supported T8 error response codes defined by 3GPP 29.122 [4].  40x response codes indicate a problem due to malformed requests from the IN-CSE that need to be addressed.   50x response codes typically indicate a problem with the SCEF that needs to be addressed.

Table 8.3-1: T8 Error response codes

| Response Codes | Remarks |
| --- | --- |
| 400 Bad Request | Incorrect parameters were passed in the request issued by the IN-CSE. |
| 401 Unauthorized | The IN-CSE is not authorized to issue request to SCEF. |
| 403 Forbidden | This represents the case when the SCEF is able to understand the request but unable to fulfil the request due to errors (e.g. the requested parameters are out of range). More information may be provided in the “detail” attribute and/or the “invalidParams” attribute of the “ProblemDetails” structure. |
| 404 Not Found | The resource URI was incorrect, for instance because of a wrong “scsAsId” field. More information may be provided in the “detail” attribute of the “ProblemDetails” structure. |
| 409 Conflict | The operation is not allowed given the current status of the resource. This response shall be used when the creation of a resource with an “scsAsId” is requested and a resource with the same such identifiers already exists and has not been deleted; or the change cannot be made due to conflict with current state of the resource. More information may be provided in the “detail” attribute of the “ProblemDetails” structure. |
| 412 Precondition Failed | Can be used according to IETF RFC 7232 [18]. Also used for the supported feature mechanism as described in subclause 5.2.7. More information may be provided in the “detail” attribute of the “ProblemDetails” structure. |
| 500 Internal Server Error | The server encountered an unexpected condition that prevented it from fulfilling the request. More information may be provided in the “detail” attribute of the “ProblemDetails” structure. |
| 503 Service Unavailable | The server is unable to handle the request. More information may be provided in the “detail” attribute of the “ProblemDetails” structure. |

NOTE: Depending on the specific procedure, the IN-CSE performs different error handling actions.  These procedure specific error-handling actions are defined in the respective sub-clauses of this specification.

### 8.3.1		Error handling for Monitoring events

If a SCEF receives a Monitoring event request to create a subscription resource for a monitoring event that it does not support, the SCEF will reject the request by sending a "500 Internal Server Error" HTTP error response with the application error "EVENT_UNSUPPORTED".

Figure 8.3.1-1 shows an example of the error handling procedure for the case where the SCEF doesn’t support the event requested by the SCS (IN-CSE). The SCEF supports the monitoring type of UE Reachability and does not support the monitoring type of Location Reporting. If an IN-CSE sends a Monitoring Event Subscription Request with the monitoring type of Location Reporting, the SCEF will reject the request by sending the above error response with the application error.

If the IN-CSE receives the error response from the SCEF, the IN-CSE may obtain the location information of an ASN/MN-CSE or ADN-AE by using Device-based method or Sharing-based method configured with locationSource attributes of <locationPolicy> resource based on the IN-CSE local policy.

Figure 8.3.1-1: Error handling procedures for Location Reporting of Monitoring events

Figure 8.3.1-2 shows another example of the error handling procedure. The SCEF supports the monitoring type of UE Reachability and does not support the monitoring type of UE Loss of Connectivity. If an IN-CSE sends a Monitoring Event Subscription Request with the monitoring type of UE Loss of Connectivity, the SCEF will reject the request by sending the above error response with the application error.

If the IN-CSE receives the error response from the SCEF, the IN-CSE may retry the request with the monitoring type of UE Reachability for managing unreachable devices, based on the IN-CSE local policy.

Figure 8.3.1-2: Error handling procedures for UE Loss of Connectivity of Monitoring events

### -----------------------End of Change 2 ---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 7.14	Supported features

### 7.14.1	General Concepts

The supported features are negotiated separately for each API. For each of the APIs, the applicable list of features is contained in the related API definition defined in 3GPP TS29.122 [4]. The procedure to negotiate applicable features is defined in 3GPP TS29.500 [i.5]. Each resource for a SCEF API will contain a "supportedFeatures" attribute of the SupportedFeatures data type defined in 3GPP TS 29.571 [i.6] containing a bitmask to indicate supported features. The features and their positions in that bitmask are defined separately for each API.

The SCEF/3GPP Network Entities will determine the supported features for the corresponding resource by comparing the supported features indicated by an IN-CSE with the supported features the SCEF/3GPP Network Entities support. The SCEF will include the "supportedFeatures" attribute indicating those features in the representation of the resource it returns to the IN-CSE in the response confirming the creation of the resource.

### 7.14.2	Normal Procedures

This clause introduces normal procedures for a supportedFeatures. If a SCEF receives a Monitoring Event Subscription Request for a Monitoring Event with the corresponding supportedFeatures, the SCEF sends an HTTP POST response to the IN-CSE with a "201 CREATED" status code as described in 3GPP TS29.122 [4].

Figure 7.14.2.-1 shows an example of the normal procedure for a supportedFeatures. A SCEF supports Location Reporting of Monitoring Event API. If an IN-CSE sends a Monitoring Event Subscription Request (monitoringType attribute is set to LOCATION_REPORTING), the supportedFeatures needs to be set to the value of Location_Notifications and the SCEF will response the request by sending the above status code.

If the IN-CSE receives the Monitoring Event Subscription Response, the IN-CSE will identify it as a successful response and continue the procedure for the Monitoring Event.

Figure 7.14.2.-1: Normal procedures for a supportedFeatures

### 7.14.3		Error handling

If a SCEF receives a request from an IN-CSE, but without an indication of the support for the feature, the SCEF will ignore the feature or reject the request by sending an error response. The response from the SCEF is different depending on the type of supportedFeatures. The following clauses introduce error handling procedures according to the type of supportedFeatures.

#### 7.14.3.1	Error handling for optional features

This clause introduces error handling procedure for an optional supportedFeatures. If a SCEF receives a request from an IN-CSE, and does not support an optional supportedFeatures, the SCEF will ignore the value of the supportedFeatures.

Figure 7.14.3.1-1 shows an example of the error handling procedures for an optional supportedFeatures. A SCEF supports the Number of UEs in an area of Monitoring Event API and the 4G requirement, and does not support the 5G requirement. If an IN-CSE sends a Monitoring Event Subscription Request (monitoringType is set to NUMBER_OF_UES_IN_AN_AREA, supportedFeatures is set to values of Number_of_UEs_in_an_area_notification  and Number_of_UEs_in_an_area_notification_5G), the SCEF will ignore the value of Number_of_UEs_in_an_area_notification_5G, and sends a Monitoring Event Subscription Response with a response code of 201 CREATED.

If the IN-CSE receives the Monitoring Event Subscription Response, the IN-CSE may identify it as a successful response and continue the procedure for 4G UEs.

Figure 7.14.3.1-1: Error handling procedures for an optional supportedFeatures

#### 7.14.3.2	Error handling for mandatory features

This clause introduces error handling procedures for a mandatory supportedFeatures. If a SCEF receives a Monitoring Event Subscription Request for a Monitoring Event, but without an indication of the support for the feature corresponding to the Monitoring Event, the SCEF will reject the request by sending a "400 Bad Request" HTTP error response with the application error "EVENT_FEATURE_MISMATCH" as described in 3GPP TS29.122 [4].

Figure 7.14.3.2-1 shows an example of the error handling procedure for a mandatory supportedFeatures. A SCEF supports Location Reporting of Monitoring Event API. If an IN-CSE sends a Monitoring Event Subscription Request (monitoringType is set to LOCATION_REPORTING, supportedFeature is set to a value of Roaming Status Notification) , the SCEF will reject the request by sending the above error response with the application error. Because the feature corresponding to the event type of Monitoring Event needs to be set to the value of Location Notifications.

If the IN-CSE receives the error response from the SCEF, the IN-CSE may retry the request with the value of Location _Notifications.

Figure 7.14.3.2-1: Error handling procedures for a mandatory supportedFeatures

### -----------------------End of Change 2 ---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?