| CHANGE REQUEST |
| --- |
| Meeting ID:* | TP 42 |
| Source:* | Preeti Rani(preetir@cdot.in), Poornima Shandilya (poornima@cdot.in), Anupama Chopra (anupama@cdot.in) |
| Date:* | 2019-09-26 |
| Reason for Change/s:* | See Introduction |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0022 v2_4_0 |
| Clauses * | 7.1.4, 7.1.7, 7.1.8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

It is proposed to change the create/update optionality of the attributes of below mentioned resources to maintain consistency.

### 7.1.4	Resource [authenticationProfile]

The [authenticationProfile] specialization of the <mgmtObj> is used to convey the configuration information regarding establishing mutually-authenticated secure communications. The security principal using this configuration information can be a CSE or AE or the Managed ADN/ASN/MN acting as security principal on behalf of AEs on the Node.

An [authenticationProfile] instance identifies a security framework, TLS cipher suites, and credentials to be used. The applicable security framework is identified by the SUID attribute. The interpretation of SUID is specified in Table 7.1.4-3.

NOTE 1:	The present document does not support using [authenticationProfile] for identifying ESData credentials.

The [authenticationProfile] resource does not include any credentials, but either identifies credentials which are stored locally on the Managed Entity or identifies an M2M Authentication Function (MAF) which is to be used to facilitate establishing symmetric keys. The intended security principal on the Managed Entity is the security principal which can use either all the credentials identified by the [authenticationProfile] resource, or (in the case that a MAF is identified) all of the credentials required for mutual authentication with the MAF.

NOTE 2:	The other security principal can be any of the following: CSE; AE; a Node terminating the security protocol on behalf of AE on Node; and an M2M Authentication Function (MAF).

Figure 7.1.4-1: Structure of [authenticationProfile]

The [authenticationProfile] resource shall contain the child resource specified in table 7.1.4-1.

Table 7.1.4-1: Child resources of [authenticationProfile] resource

| Child Resources of [authenticationProfile] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of oneM2M TS-0001 [2] |

The [authenticationProfile] resource shall contain the attributes specified in table 7.1.4-2.

Table 7.1.4-2: Attributes of [authenticationProfile] resource

| Attributes of [authenticationProfile] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| labels | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| mgmtDefinition | 1 | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. This attribute shall have the fixed value 1022 ("authenticationProfile"). |
| objectIDs | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| objectPaths | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| description | 0..1 | RW | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| SUID | 1 | WO | Describes how the authentication profile is to be used. Further details about interpretation of each SUID are specified in Table 7.1.4-3 of the present document. |
| TLSCiphersuites | 0..1(L) | RW | If the security framework identified by SUID uses TLS, then this attributes provides a list of allowed TLS cipher suites. |
| symmKeyID | 0..1 | WO | Present when a symmetric key is to be used for mutual authentication. Identifier for a symmetric key already stored locally on the Managed Entity, or to be provisioned to the Managed Entity |
| symmKeyValue | 0..1 | WO | Optionally present when a symmetric key is to be used for mutual authentication. Contains the value of the symmetric key to be used for mutual authentication. |
| MAFKeyRegLabels | 0..1(L) | WO | Optionally present when a MAF is to be used to facilitate establishing a symmetric key for mutual authentication. Provides the content of the labels parameter in the MAF Key Registration request; see Table 8.8.2.7-1, oneM2M TS-0003 [3]. |
| MAFKeyRegDuration | 0..1 | WO | Present when a MAF is to be used to facilitate establishing one or more symmetric keys for mutual authentication. Provides the maximum duration for which an established symmetric key may be used. |
| mycertFingerprint | 0..1 | WO | Present when certificate-based authentication is to be used. Provides a hash value for identifying the certificate to be used by the intended security principal on the Managed Entity to authenticate itself to other security principals. |
| rawPubKeyID | 0..1 | WO | Present when certificate-based authentication is to be used and the other security principal will authenticate itself with a Raw Public Key Certificate. |
| mgmtLink | 0..1(L) | RW | Present when MAF is to be used to facilitate establishing one or more symmetric keys for mutual authentication or certificate-based authentication is to be used. In the former case, the list contains one reference to a [MAFClientRegCfg] resource. In the latter case, the list contains one or more references pointing to [trustAnchorCred] resources. |

### 7.1.7	Resource [MAFClientRegCfg]

This <mgmtObj> specialization is used to convey instructions regarding the MAF Client Registration procedure (clause 8.8.2.3 of oneM2M TS-0003 [3]).

Figure 7.1.7-1: Structure of [MAFClientRegCfg] resource

The [MAFClientRegCfg] resource shall contain the child resource specified in table 7.1.7-1.

Table 7.1.7-1: Child resources of [MAFClientRegCfg] resource

| Child Resources of [authenticationProfile] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of oneM2M TS-0001 [2] |

The [MAFClientRegCfg] resource shall contain the attributes specified in table 7.1.7-2.

Table 7.1.7-2: Attributes of [MAFClientRegCfg] resource

| Attributes of [authenticationProfile] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| labels | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| mgmtDefinition | 1 | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. This attribute shall have the fixed value 1025 ("MAFClientRegCfg"). |
| objectIDs | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| objectPaths | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| description | 0..1 | RW | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| fqdn | 1 | WO | See clause 8.8.3.2 of oneM2M TS-0003 [3] |
| adminFQDN | 1 | WO | See clause 8.8.3.2 of oneM2M TS-0003 [3] |
| httpPort | 0..1 | WO | See clause 8.8.3.2 of oneM2M TS-0003 [3] |
| coapPort | 0..1 | WO | See clause 8.8.3.2 of oneM2M TS-0003 [3] |
| websocketPort | 0..1 | WO | See clause 8.8.3.2 of oneM2M TS-0003 [3] |
| mgmtLink | 1 | RW | A link to a [authenticationProfile] resource containing the parameters for the MAF Client to establish mutually-authenticated secure communications with the MAF. |

The MAF Client shall perform the MAF Client Registration Procedure specified in clause 8.8.2.3 of oneM2M TS-0003 [3], using the linked authentication profile for mutual authentication of the MAF Client and MAF.

The MOs configured to the Managed Entity via [MAFClientRegCfg] resources are expected to be protected by a secure environment on the Managed Entity, in order to preserve integrity of the attributes. Optimal protection is provided when the integrity protection of the management protocol message is verified in the secure environment.

### 7.1.8	Resource [MEFClientRegCfg]

This <mgmtObj> specialization is used to convey instructions regarding the MEF Client Registration procedure (clause 8.3.5.2.3 of oneM2M TS-0003 [3]).

Figure 7.1.8-1: Structure of [MEFClientRegCfg] resource

The [MEFClientRegCfg] resource shall contain the child resource specified in table 7.1.8-1.

Table 7.1.8-1: Child resources of [MEFClientRegCfg] resource

| Child Resources of [authenticationProfile] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of oneM2M TS-0001 [2] |

The [MEFClientRegCfg] resource shall contain the attributes specified in table 7.1.8-2.

Table 7.1.8-2: Attributes of [MEFClientRegCfg] resource

| Attributes of [authenticationProfile] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| labels | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| mgmtDefinition | 1 | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. This attribute shall have the fixed value 1026 ("MEFClientRegCfg"). |
| objectIDs | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| objectPaths | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| description | 0..1 | RW | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| fqdn | 1 | WO | See clause 8.3.7 of oneM2M TS-0003 [3] |
| adminFQDN | 1 | WO | See clause 8.3.7 of oneM2M TS-0003 [3] |
| httpPort | 0..1 | WO | See clause 8.3.7 of oneM2M TS-0003 [3] |
| coapPort | 0..1 | WO | See clause 8.3.7 of oneM2M TS-0003 [3] |
| websocketPort | 0..1 | WO | See clause 8.3.7 of oneM2M TS-0003 [3] |
| mgmtLink | 1 | RW | A link to a [authenticationProfile] resource containing the parameters for the MEF Client to establish mutually-authenticated secure communications with the MEF. |

The MEF Client shall perform the MEF Client Registration Procedure specified in clause 8.8.2.3 of oneM2M TS-0003 [3], using the linked authentication profile for mutual authentication of the MEF Client and MEF.

The MOs configured to the Managed Entity via [MEFClientRegCfg] resources are expected to be protected by a secure environment on the Managed Entity, in order to preserve integrity of the attributes. Optimal protection is provided when the integrity protection of the management protocol message is verified in the secure environment.

### -----------------------Start of change 1-------------------------------------------

### 7.2.4	Resource [authenticationProfile]

#### 7.2.4.1	Introduction

Table 7.2.4.1-1: Data Type Definition of [authenticationProfile]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| authenticationProfile | DCFG-authenticationProfile-v2_3_0.xsd |  |

Table 7.2.4.1-2: Resource specific attributes of [authenticationProfile]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. | "authenticationProfile" |
| objectID | O | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |
| objectPaths | O | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |
| description | O | O | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |
| SUID | M | NP | m2m:suid | Allowed values are listed in table 7.1.4-3. |
| TLSCiphersuites | O | O | dcfg:listOfTLSCiphersuite |  |
| symmKeyID | O | NP | sec:credentialID |  |
| symmKeyValue | O | NP | xs:hexBinary | The minimum key length is 256 bits. |
| MAFKeyRegLabels | O | NP | m2m:labels |  |
| MAFKeyRegDuration | O | NP | xs:duration |  |
| mycertFingerprint | O | NP | dcfg:niURI or dcfg:nihURI |  |
| rawPubKeyID | O | NP | dcfg:niURI or dcfg:nihURI |  |
| mgmtLink | O | O | See clause 7.4.15 of oneM2M TS-0004 [4]. |  |

Table 7.2.4.1-3: Child resources of [authenticationProfile] resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.4.8 of oneM2M TS-0004 [4] |

#### 7.2.4.2		Resource specific procedure on CRUD operations

When management is performed using technology specific protocols, the procedures defined in clause 7.4.15.2 of oneM2M TS-0004 [4], '<mgmtObj> specific procedures' shall be used. There is no change from the generic procedures in clause 7.2.2 of oneM2M TS-0004 [4] for operations on this resource. oneM2M TS-0005 [5] and oneM2M TS-0006 [6] provide the mapping of these resources into the technology specific protocol data model.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 7.2.7	Resource [MAFClientRegCfg]

#### 7.2.7.1	Introduction

Table 7.2.7.1-1: Data Type Definition of [MAFClientRegCfg]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| MAFClientRegCfg | DCFG-MAFClientRegCfg-v2_3_0.xsd |  |

Table 7.2.7.1-2: Resource specific attributes of [MAFClientRegCfg]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. | "MAFClientRegCfg" |
| fqdn | M | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| adminFQDN | M | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| httpPort | O | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] | At least one of these attributes shall be present |
| coapPort | O | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| websocketPort | O | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| mgmtLink | M | O | m2m:mgmtLinkRef | 1 link to a [authenticationProfile] resources instance |
| NOTE: For further details of these attributes, see clauses 8.8.3.2 and 12.4.2 of oneM2M TS-0003 [3]. |

Table 7.2.7.1-3: Child resources of [MAFClientRegCfg] resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.4.8 of oneM2M TS-0004 [4] |

#### 7.2.7.2	Resource specific procedure on CRUD operations

When management is performed using technology specific protocols, the procedures defined in clause 7.4.15.2 of oneM2M TS-0004 [4], '<mgmtObj> specific procedures' shall be used. There is no change from the generic procedures in clause 7.2.2 of oneM2M TS-0004 [4] for operations on this resource. oneM2M TS-0005 [5] and oneM2M TS-0006 [6] provide the mapping of these resources into the technology specific protocol data model.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 7.2.8	Resource [MEFClientRegCfg]

#### 7.2.8.1	Introduction

Table 7.2.8.1-1: Data Type Definition of [MEFClientRegCfg]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| MEFClientRegCfg | DCFG-MEFClientRegCfg-v2_3_0.xsd |  |

Table 7.2.8.1-2: Resource specific attributes of [MEFClientRegCfg]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause 7.4.15 of oneM2M TS-0004 [4]. | "MEFClientRegCfg" |
| fqdn | M | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| adminFQDN | M | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| httpPort | O | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] | At least one of these attributes shall be present |
| coapPort | O | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| websocketPort | O | NP | See table 12.4.2-1 of oneM2M TS-0003 [3] |  |
| mgmtLink | M | O | m2m:mgmtLinkRef | 1 link to a [authenticationProfile] resources instance |
| NOTE: For further details of these attributes, see clauses 8.3.7.2 and 12.4.2 of oneM2M TS-0003 [3]. |

Table 7.2.8.1-3: Child resources of [MEFClientRegCfg] resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.4.8 of oneM2M TS-0004 [4] |

#### 7.2.8.2	Resource specific procedure on CRUD operations

When management is performed using technology specific protocols, the procedures defined in clause 7.4.15.2 of oneM2M TS-0004 [4], '<mgmtObj> specific procedures' shall be used. There is no change from the generic procedures in clause 7.2.2 of oneM2M TS-0004 [4] for operations on this resource. oneM2M TS-0005 [5] and oneM2M TS-0006 [6] provide the mapping of these resources into the technology specific protocol data model.

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?