| oneM2M Technical Specification |
| --- |
| Document Number | TS-0006-Management_Enablement_(BBF)-V0_1_0 |
| Document Name: | Management Enablement (BBF) |
| Date: | 2014-03-12 |
| Abstract: | Specifies the usage of the BBF TR-069 protocol and the corresponding message flows including normal cases as well as error cases to fulfil the oneM2M management requirements. Protocol mapping between the oneM2M service layer and BBF TR-069 protocol. The Mca reference point, ms interface and la interface are possibly involved in this protocol mapping. Mapping between the oneM2M management related resources and the TR-069 protocol RPCs and TR-181i2 data model. Specification of new TR-181 data model elements to fulfil oneM2M specific management requirements that cannot be currently translated. |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© 2014, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols, abbreviations and acronyms	4

3.1	Definitions	4

3.2	Symbols	4

3.3	Abbreviations	5

3.4	Acronyms	5

4	Conventions	5

5	Mapping of basic data types	5

6	Mapping of identifiers	5

6.2	Identifier of an object instance	6

7	Mapping of resources	6

7.1	General mapping assumptions	6

7.2	Resource deviceInfo	6

7.3	Resource memory	6

7.4	Resource battery	7

7.5	Resource areaNwkInfo	7

7.6	Resource areaNwkDeviceInfo	7

7.7	Resource eventLog	8

7.8	Resource deviceCapability	9

7.9	Resource firmware	9

7.10	Resource software	10

7.11	Resource reboot	11

8	Mapping of procedures for management	11

8.2 Fault Code Mapping	11

8.2.1 CPE Generated Fault Codes	11

9	Server Interactions	13

9.1	Communication Session Establishment	14

9.1.1	IN-CSE to ACS Communication Session Establishment	14

9.1.2	ACS to IN-CSE Communication Session Establishment	14

9.2.3	ACS and IN-CSE Communication Session Requirements	14

9.2	Processing of Requests and Responses	14

9.2.1	Request and Notification Formatting	14

9.2.2	ACS Request Processing Requirements	14

9.2.3	ACS Notification Processing Requirements	15

9.3	Discovery and Synchronization of Resources	15

9.4	Access Management	15

9.4.1	Access Management Requirements	15

10	New Management Technology Specific Resources	15

Proforma copyright release text block	16

Annexes	16

Annex <y>: Bibliography	17

History	17

# 1	Scope

The present document describes the protocol mappings between the management Resources for oneM2M and the BBF TR-181i2 Data Model [6].

# 2	References

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: “oneM2M Functional Architecture”.

[2]	oneM2M TS-0004: “oneM2M Protocol Specification”.

[3]	oneM2M TR-0004: “Definitions and Acronyms”.

Editors Note: naming of TR-0004 to the new TS name.

[4]	BBF: “TR-069 CPE WAN Management Protocol” Issue: 1 Amendment 5, November 2013.

[5]	BBF: “TR-106 Data Model Template for TR-069-Enabled Devices”, Issue 1, Amendment 7,
September 2013.

[6]	BBF: “TR-181 Device Data Model for TR-069, Issue 2 Amendment 7”, November 2013.

[7]	BBF: “TR-131 ACS Northbound Interface Requirements, Issue:1”, November 2009.

[8]	IETF/RFC 3986: “Uniform Resource Identifier (URI): Generic Syntax”.

[9]	POSIX.1-2008: “The Open Group Technical Standard Base Specifications”, Issue 7.

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions, symbols, abbreviations and acronyms

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR-0004 [3] apply.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

CPE	Customer Premise Equipment

OUI	Organizationally Unique Identifier

PC	Product Class

RPC	Remote Procedure Call

SN	Serial Number

## 3.4	Acronyms

For the purposes of the present document, the acroynms given in TR-0004 [3] apply.

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Mapping of basic data types

TR-106 [5] specifies the object structure supported by TR-069 enabled devcices. It specifies the structural requirements for the data hierarchy. This includes the mapping attribute data types to TR-181 [6] parameters which follows the conventions of section 3 of TR-106 [5] and data types described in Table 4 of TR-106 [5].

Specifically the following conventions will be used when mapping data types:

- String: Maps directly to the “string” data type

- Long: Maps directly to the “long” data type

- UnsignedLong: Maps directly to the “unsignedLong” data type

- UnsignedInt: Maps directly to the “unsignedInt” data type

- Lists of Strings: When a data structure is represented by comma separated list of type "string", any whitespace or comma characters  contained in an item of such a list MUST be escaped using percent as defined in Section 3.2.3 of TR-106 [5].

# 6	Mapping of identifiers

Editors Note: The device identifier would need to be aligned with decisions on the Node.

The TR-069 [4] specification defines three (3) types of devices, known as CPEs, that are capable of being managed from the perspective of the TR-069 agent:

CPE that hosts the TR-069 agent: Section A.3.3.1 Inform of TR-069 [4] defines the required fields for a CPE to be identified. These fields include the OUI and Serial Number of the CPE assigned by the CPE manufacturer. Optionally the manufacturer may assign a Product Class to the CPE. The format of the identifier is as follows: OUI-[PC-]SN.

Virtual Device: This type of device is addressed as a CPE. The Virtual Device has its own OUI-[PC-]SN.

Embedded Device: This type of device is addressed as one or more objects within the data model of the CPE that hosts the TR-069 agent.

The objectPath attribute of the <mgmtObj> resource contains the CPE identifier that hosts the TR-069 agent in the form OUI-[PC-]-SN. The Product Class (PC) is an optional field. All elements of the CPE identifier is assigned by the manufacturer of the CPE.

## 6.2	Identifier of an object instance

The TR-069 [4] permits objects to have multiple instances. Each object instance is contained within the objectPath attribute of the <mgmtObj> resource.

# 7	Mapping of resources

This clause contains all information on how to map subtypes of the <mgmtObj> resource to their equivalent managed object and parameters as defined in the TR-181 [6] data model or the Remote Procedure Call (RPC) in TR-069 [4].

Editors Note: Resource attributes need to be rechecked to ensure all attribles of the mgmtObj resources are in the mapping tables (e.g., DeviceInfo:deviceId).

## 7.1	General mapping assumptions

TR-069 [4] specifies a protocol for communication between a CPE (Customer Premises Equipment) and an ACS (Auto-Configuration Server).  Any TR-069 enabled device has to follow the data model as described in the TR-106 [5] and TR-181 [6] as well as RPCs described in TR-069 [4].

## 7.2	Resource deviceInfo

The Resource deviceInfo is a read-only Resource that maps directly to the Device.DeviceInfo object of TR-181 [6].

The information is retrieved using the GetParameterValues RPC of TR-069 [4].

| Attribute Name of deviceInfo | TR-181 Parameter |
| --- | --- |
| deviceLabel | Device.DeviceInfo.Description |
| manufacturer | Device.DeviceInfo.Manufacturer |
| model | Device.DeviceInfo.ModelNumber |
| deviceType | Device.DeviceInfo.ProductClass |
| fwVersion | Device.DeviceInfo.SoftwareVersion if the device supports only 1 software version. If the device support multiple software versions this would map to Device.DeviceInfo.AdditionalSoftwareVersion |
| swVersion | Device.DeviceInfo.SoftwareVersion |
| hwVersion | Device.DeviceInfo.HardwareVersion |

## 7.3	Resource memory

The Resource memory is a read-only Resource that maps directly to the Device.DeviceInfo.MemoryStatus object of TR-181 [6].

The information is retrieved using the GetParameterValues RPC of TR-069 [4].

Attempts to modify the attributes of the memory Resource causes an error code “operation unsupported” to be returned.

Editors Note: Need to define an Error code for: “operation unsupported”

| Attribute Name of memory | TR-181 Parameter |
| --- | --- |
| memAvailable | Device.DeviceInfo.MemoryStatus.Free |
| memTotal | Device.DeviceInfo.MemoryStatus.Total |

## 7.4	Resource battery

The Resource memory is a read-only Resource that maps directly to an instance of Device.DeviceInfo.X_oneM2M_BatteryStatus.{i} object.

The information is retrieved using the GetParameterValues RPC of TR-069 [4].

| Attribute Name of battery | TR-181 Parameter |
| --- | --- |
| batteryLevel | Device.DeviceInfo.X_oneM2M_BatteryStatus.batteryLevel |
| batteryStatus | Device.DeviceInfo.X_oneM2M_BatteryStatus.batteryStatus |

## 7.5	Resource areaNwkInfo

The Resource areaNwkInfo is a multi-instance Resource where each instance of the Resource maps directly to an instance of Device.X_oneM2M_AreaNetwork.{i} object.

As the areaNwkInfo Resource is a multi-instance Resource, the AreaNetwork object is an multi-object instance that can be created and deleted.

| Attribute Name of areaNwkInfo | X_oneM2M Parameter |
| --- | --- |
| areaNwkType | Device.X_oneM2M_AreaNetwork.{i}.Type |
| listOfDevices | Device.X_oneM2M_AreaNetwork.{i}.ListOfDevices |

## 7.6	Resource areaNwkDeviceInfo

The Resource areaNwkDeviceInfo is a multi-instance Resource where each instance of the Resource maps directly to an instance of Device.X_oneM2M_AreaNetworkDevice.{i} object.

As the areaNwkDeviceInfo Resource is a multi-instance Resource, the AreaNetworkDevice object is an multi-object instance that can be created and deleted.

Instances of the areaNwkDeviceInfo Resource is referenced in the listOfDevices attribute of the associated AreaNwkInfo Resource.

| Attribute Name of areaNwkDeviceInfo | X_oneM2M Parameter |
| --- | --- |
| devId | Device.X_oneM2M_AreaNetworkDevice.{i}.DeviceId |
| devType | Device.X_oneM2M_AreaNetworkDevice.{i}.DeviceType |
| areaNwkId | Reference to Device.X_oneM2M_AreaNetworkDevice.{i}.AreaNetwork.{i} |
| sleepInterval | Device.X_oneM2M_AreaNetworkDevice.{i}.SleepInterval |
| sleepDuration | Device.X_oneM2M_AreaNetworkDevice.{i}.SleepDuration |
| status | Device.X_oneM2M_AreaNetworkDevice.{i}.Status |
| listOfNeighbors | Device.X_oneM2M_AreaNetworkDevice.{i}.ListOfNeighbors |

## 7.7	Resource eventLog

Editors Note: Need to determine if this the ETSI Performance Log (self test diagnostics or the System log).

The Resource eventLog is a multi-instance Resource where each instance of the Resource maps directly to an instance of Device.DeviceInfo.VendorLogFile.{i} object.

While the eventLog Resource is a multi-instance Resource, the VendorLogFile is a read-only object where only the device is able to create and delete instances of the VendorLogFile.

The contents of a VendorLogFile instance is retrieved using the Upload RPC of TR-069 [4].

The VendorLogFile.Name parameter does not support the capability to set the name. Attempts to modify the TypeId attribute of the eventLog Resource causes an error code “operation unsupported” to be returned.

The VendorLogFile object instance does not support action capabilities to start or stop the log. The VendorLogFile instance always returns a value of “Started” as an ActionStatus and when read the logStart is always returns “True” while the logStop Attribute always returns a value of “False”. An error code “unsupported value” will be returned for an attempt to set the values of logStart and logStop attributes to any value other than was is returned.

Editors Note: Need to flesh out the error code mappings once the TS-0004 Error codes are defined.

| Attribute Name of eventLog | TR-181 Parameter |
| --- | --- |
| logTypeId | Device.DeviceInfo.VendorLogFile.{i}.Name |
| logData | Upload RPC using the Device.DeviceInfo.VendorLogFile.{i} as the FileType. |
| logActionStatus | Always returns the value of “True”. |
| logStart | Always returns the value of “True”. |
| logStop | Always returns the value of “False”. |

RPC Upload Argument

URL: URL of the Server that M2M Node uses to uplod the event log in order to retrieve the contents of the eventLog.

FileType: “4 Vendor Log File <i>”

Username: Username credential of the Server that the M2M Node uses to upload the event log.

Password: Password credential of the Server that the M2M Node uses to upload the event log.

CommandKey: Automatically set by the M2M node in order to correlate the TransferComplete response.

DelaySeconds: 0 (immediate)

## 7.8	Resource deviceCapability

Editors Note: Need to flesh out the mapping once the list of device capabilities are defined in TS-0001 and TS-0004.

| Attribute Name of capabilityInstance | X_oneM2M Parameter |
| --- | --- |
| capabilityName |  |
| attached |  |
| capabilityActionStatus |  |
| enable |  |
| disable |  |

## 7.9	Resource firmware

The firmware Resource represents a firmware instance and  is not considered a TR-069 managed entity within the device until the the firmware Resource’s update attribute has been written a value of “True”. When this occurs, the TR-069 Download RPC is invoked.

Note: In many instances, the server from which the firmware is downloaded requires authentication in the form of Username and Password credentials. The M2M Node that executes firmware download shall maintain the a mapping of the username and password of the download server needed to download the firmware outside the lifecycle of the specific firmware

| Attribute Name of firmware | RPC Download Arguments |
| --- | --- |
| URL | URL |
| update | When set to the value of “True” executes the Download operations with a FileType “1 Firmware Upgrade Image” is performed. |
|  | Username: Received from the M2M node for the download server where the update is set to “True”. |
|  | Password: Received from the M2M node for the download server where the update is set to “True”. |
|  | CommandKey: Automatically set by the M2M node where the update is set to “True” in order to correlate the TransferComplete response. |
|  | FileSize: 0 (not used) |
|  | TargetFileName: <empty> (not used) |
|  | DelaySeconds: 0 (immediate) |
|  | SuccessURL: <empty> (not used) |
|  | FailureURL: <empty> (not used) |

## 7.10	Resource software

The Resource software is a multi-instance Resource where each instance of the Resource maps directly to an instance of Device.SoftwareModules.DeploymentUnit.{i} object for the deployment aspects (install, remove) of the software Resource.  The install operation of software Resource is performed using the ChangeDUState RPC.

Once a software Resource has been deployed, the Resource maps to the associated Device.SoftwareModules.ExecutionUnit.{i} objects in order to activate and deactivate the associated execution unit.

The software Resource version and name are retrieved using the GetParameterValues RPC of TR-069 [4].

The activate and deactive operations of the software Resource is performed by manipulating the Device.SoftwareModules.ExecutionUnit.{i}.RequestedState parameter using the SetParameterValues RPC.

Editors Note: Missing Remove action for the deployment unit.

| Attribute Name of software | Description |
| --- | --- |
| version | Device.SoftwareModules.DeploymentUnit.{i.Version |
| name | Device.SoftwareModules.DeploymentUnit.{i}.Name |
| URL | Device.SoftwareModules.DeploymentUnit.{i}.URL |
| install | Use the ChangeDUState:InstallOpStruct |
| installStatus | Status is defined as 0% if the install operation has not been initiated or has failed. If the install operation has completed successfully, the value of 100% is used in indicate a successful completion of the installation. |
| activate | The action that activates software previously installed. |
| deactivate | The action that deactivates software. |
| activeStatus | Status is defined as 0% if the last operation has not been has failed or a new operation has been initiaited. If the current operation has completed successfully, the value of 100% is used in indicate a successful completion of the operation. |

RPC ChangeDUState:InstallOpStruct Argument

URL: URL of the Server that M2M Node uses to download the DU.

Username: Username credential of Server that the M2M Node uses to download the DU – Supplied by the M2M Node.

Password: Password credential of Server that the M2M Node uses to download the DU – Supplied by the M2M Node.

UUID: <empty> not used

ExecurtionEnvRef: <empty> not used

## 7.11	Resource reboot

The Resource reboot maps to either the Reboot RPC or FactoryReset RPC of TR-069 [4]

| Attribute Name of reboot | Description |
| --- | --- |
| reboot | Executes the Reboot RPC |
| factoryReset | FactoryReset RPC |

RPC Reboot Arguments

CommandKey: Automatically set by the M2M node where the reboot is set to “True” in order to correlate the “M-Reboot” Event from the next Inform.

# 8	Mapping of procedures for management

Editor’s Note: The section specifies the mapping between oneM2M operation (i.e, Create, Retrieve, Update and Delete) and BBF TR-069 RPCs. The mapping includes the handling of normal cases and error cases.

The object instances are created using the AddObject RPC of TR-069 [4].

The object instances are deleted using the DeleteObject RPC of TR-069 [4].

The attribute values are retrieved using the GetParameterValues RPC of TR-069 [4].

The attribute values are modified using the SetParameterValues RPC of TR-069 [4].

The notifications on attributes are set using the SetParameterAttributes RPC of TR-069 [4].

The notifications on attributes are modified using the SetParameterAttributes RPC of TR-069 [4].

eventLog Resource data attributes are read using the Upload RPC of TR-069 [4].

firmware Resources are dowloaded using the the Download RPC of TR-069 [4].

software Resources are installed using the ChangeDUState RPC of TR-069 [4].

reboot Resources are executed using the Reboot or FactoryReset RPCs of TR-069 [4].

Editors Note: Need to flesh out the procedures for each of the above uses of RPCs.

## 8.2 Fault Code Mapping

TR-069 [4] defines a set of fault codes that are to be mapped into oneM2M Service Layer fault codes.

Editors Note: Need to flesh out the error code mappings once the TS-0004 Error codes are defined.

### 8.2.1 CPE Generated Fault Codes

| Fault code | Description | Type |
| --- | --- | --- |
| 9000 | Method not supported | Server |
| 9001 | Request denied (no reason specified) | Server |
| 9002 | Internal error | Server |
| 9003 | Invalid arguments | Client |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) | Server |
| 9005 | Invalid Parameter name (associated with Set/GetParameterValues, GetParameterNames, Set/GetParameterAttributes, AddObject, and DeleteObject) | Client |
| 9006 | Invalid Parameter type (associated with SetParameterValues) | Client |
| 9007 | Invalid Parameter value (associated with SetParameterValues) | Client |
| 9008 | Attempt to set a non-writable Parameter (associated with SetParameterValues) | Client |
| 9009 | Notification request rejected (associated with SetParameterAttributes method). | Server |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). | Server |
| 9011 | Upload failure (associated with Upload, TransferComplete or AutonomousTransferComplete methods). | Server |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). | Server |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). | Server |
| 9014 | File transfer failure: unable to join multicast group (associated with Download, TransferComplete or AutonomousTransferComplete methods). | Server |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). | Server |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). | Server |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). | Server |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). | Server |
| 9019 | File transfer failure: file authentication failure (associated with Download, TransferComplete or AutonomousTransferComplete methods). | Server |
| 9020 | File transfer failure: unable to complete download within specified time windows (associated with TransferComplete method). | Client |
| 9021 | Cancelation of file transfer not permitted in current transfer state (associated with CancelTransfer method). | Client |
| 9022 | Invalid UUID Format (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) | Server |
| 9023 | Unknown Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) | Server |
| 9024 | Disabled Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) | Server |
| 9025 | Deployment Unit to Execution Environment Mismatch (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) | Server |
| 9026 | Duplicate Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) | Server |
| 9027 | System Resources Exceeded (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) | Server |
| 9028 | Unknown Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update and Uninstall) | Server |
| 9029 | Invalid Deployment Unit State (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update and Uninstall) | Server |
| 9030 | Invalid Deployment Unit Update – Downgrade not permitted (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) | Server |
| 9031 | Invalid Deployment Unit Update – Version not specified (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) | Server |
| 9032 | Invalid Deployment Unit Update – Version already exists (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) | Server |
| 9800 – 9899 | Vendor defined fault codes | - |

# 9	Server Interactions

This clause specifies how the IN-CSE interacts with an ACS in order to manage the Resources described in this specification. The IN-CSE interaction with an ACS includes:

Establishment of the communication session between the IN-CSE and ACS

Processing of requests and notifications between the IN-CSE and the ACS

Discovery

Note: The Broadband Forum has not defined a protocol specification for the Northbound Interface of an ACS. As such, this document only describes the expectations of this interface in the form of requirements on the ACS.

## 9.1	Communication Session Establishment

## 9.1.1	IN-CSE to ACS Communication Session Establishment

When the IN-CSE detects that it has to delegate an interaction with the a device resource to an ACS, the IN-CSE establishes a communication session with the ACS. The establishment of a communication session between the IN-CSE and ACS  provides security dimensions for Access control, Authentication, Non-repudiation, Data confidentiality, Communication security, Data integrity and Privacy adhering to the following TR-131 [7] Architectural requirement A7.

The IN-CSE may establish multiple sessions with a ACS based on the security model utilized between the IN-CSE and the ACS.

## 9.1.2	ACS to IN-CSE Communication Session Establishment

When the ACS detects a change to resources it manages that the IN-CSE has expressed interest, the ACS  requests the IN-CSE to establish a session if a session doesn’t exist for the resource being managed. The establishment of a communication session between the IN-CSE and ACS  provides security dimensions for Access control, Authentication, Non-repudiation, Data confidentiality, Communication security, Data integrity and Privacy adhering to the following TR-131 [7] Architectural requirement A7.

The ACS may establish multiple sessions with a IN-CSE based on the security model utilized between the IN-CSE and the ACS.

While a session between the ACS and IN-CSE is not established, the AS retains any notifications or changes in the resources based on a Event retention policy (i.e., time, number of events).

When a ACS to IN-CSE interaction is required and a session does not exist, the ACS requests to initiate a session based on a Session Initiation Policy (i.e., Periodic contact establishment (schedule), upon event detection with timeframe window).

### 9.2.3	ACS and IN-CSE Communication Session Requirements

When establishing a session from the ACS to the IN-CSE:

If a session doesn’t exist between the IN-CSE and ACS, the ACS shall retain any notifications or changes in the resources based on a Event retention policy (i.e., time, number of events).

When an ACS to IN-CSE interaction is required and a session does not exist, the ACS shall be capable to initiate a session based on a Session Initiation Policy (i.e., Periodic contact establishment (schedule), upon event detection with timeframe window)

## 9.2	Processing of Requests and Responses

### 9.2.1	Request and Notification Formatting

Requests and Notifications mechanisms between the IN-CSE and the DM Server format the XML schema of the CPE methods defined in TR-069 [4] as an ACS would format the CPE methods that it would pass to the CPE. The IN-CSE would then also process the CPE methods as defined in TR-069 [4]. Likewise the ACS would send notifications in the format of the XML schema of the CPE for sending events using the Inform RPC.

### 9.2.2	ACS Request Processing Requirements

When receiving requests from the IN-CSE the ACS  shall be capable of defining mechanisms to support triggering of immediate operations to device. If the device is not available the ACS MUST return an appropriate error code.

The ACS shall provide capability for the IN-CSE to indicate request policies to include: Retry policy, Request Time out.

### 9.2.3	ACS Notification Processing Requirements

When sending notifications to the IN-CSE:

The ACS shall be capable of providing a mechanism for the IN-CSE  to subscribe to events.

The ACS shall be capable of providing a list of events for which the IN-CSE can subscribe.

The ACS shall be capable of providing a mechanism for the IN-CSE to unsubscribe from events.

The ACS shall be capable of providing an event delivery mechanism.

The ACS shall be capable of providing the capability for the IN-CSE to request event filters including: Event Code; Specific parameters changing value; Device; Any combination of the previous criteria.

The IN-CSE shall be capable of subscribing to be notified of changes to resources it manages.

The ACS  shall be capable of notifying the IN-CSE of changes to resources to which the client has subscribed.

## 9.3	Discovery and Synchronization of Resources

For devices under management, the IN-CSE  may discover resources of interest (metadata and values) within a device using the ACS.

For resources of interest, the IN-CSE may also express an interest to be notified of a resource if a resource is changed (added, deleted, updated).

The IN-CSE shall be capable to discover and subscribe to changes of resources in order to synchronize the IN-CSE with resources of interest of the ACS.

## 9.4	Access Management

Once a request has performed an Access Decision by the IN-CSE to allow the request, the IN-CSE must select the appropriate ACS along with elements the ACS would need to implement access management within the ACS. These would include the Identity of the subject (oneM2M Originator) of the request which is needed in scenarios where the original issuer of the request is needed to be known – this could be done by correlating principals (e.g., Roles, Accounts) used by the IN-CSE and ACS.

## 9.4.1	Access Management Requirements

The ACS shall be capable of providing a mechanism for the IN-CSE to discover the Access Management elements used to authorize and authenticate access to resources controlled by the ACS.

The IN-CSE shall be capable of correlating Access Management elements provided by the ACS to Access Management elements used by the IN-CSE.

The IN-CSE shall be capable of providing secured storage of Access Management elements within the IN-CSE.

# 10	New Management Technology Specific Resources

TR-181 [6] provides a list of management objects that have been standardized by the Broadband Forum and where possible, clause 7 provides a mapping of the Resources to standardized management objects. This clause provides the oneM2M vendor specific extensions to the TR-181 [6] data model as specified in the oneM2M_TR-181.xml.

Editors Note: Need to develop the oneM2M_TR-181.xml once the TS-0004 attributes are defined.

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (Informative/Normative):Remove Informative or Normative as appropriatTitle of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 18 Feb 2014 | Initial Skeleton |
| V.0.1.0 | 12 Mar 2014 | Incorporate the following contributions: MAS-2014-0336R01-TS-0006_Updates |