| oneM2M Technical Specification |
| --- |
| Document Number | 0.3.2 |
| Document Name: | HTTP Protocol Binding Technical Specification |
| Date: | 2014-June-18 |
| Abstract: | HTTP Protocol binding TS |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© 2013, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols, abbreviations and acronyms	4

3.1	Definitions	4

3.2	Symbols	5

3.3	Abbreviations & Acronyms	5

4	Conventions	5

5	Overview	5

5.1	Actors	6

5.2	Basic Flow (Blocking Request)	6

5.3	Basic Flow (Non-Blocking Request)	7

5.4	Notification using WebSocket	8

5.5	Authentication on HTTP Request Message	9

5.6	Overview of HTTP binding	9

6	High Level Mapping	10

6.1	HTTP Method Mapping	10

6.2	Status Code Mapping	10

8	Security Consideration	11

Proforma copyright release text block	11

Annexes	11

Annex <y>: Bibliography	12

History	12

# 1	Scope

The specification will cover the protocol specific part of communication protocol used by oneM2M compliant systems as ‘RESTful HTTP binding’.

The scope of this Work Item includes (not limited to as shown below):

-	Binding oneM2M Protocol primitive types to HTTP method

-	Binding oneM2M response codes (successful/unsuccessful) to HTTP resopnse codes

-	Binding oneM2M RESTful resources to HTTP resources

This specification is depending on Core API protocol specification (TS-0008) for data types.

EXAMPLE:	The present document provides the necessary adaptions to the endorsed document.

The Scope shall not contain requirements.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

[1]	 RFC2617: “HTTP Authentication: Basic and Digest Access Authentication”, IETF, June 1999

[2]	RFC6750: “The OAuth 2.0 Authorization Framework: Bearer Token Usage”, IETF, October 2012.

[3]	RFC6455:“The WebSocket Protocol”, IETF, December 2011.

[4]	IETF RFC2616 Hypertext Transfer Protocol - HTTP/1.1

[5]	oneM2M TS-0001: Architecture TS

[6]	oneM2M TS-0004: Core Protocol TS

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions, symbols, abbreviations and acronyms

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

If a definition is taken from an external source, use the format below where [N] identifies the external document which must be listed in Section 2 References.

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations & Acronyms

For the purposes of the present document, the following abbreviations and acronyms apply:

HTTP		Hyper Text Transfer Protocol

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Overview

This clause describes fundamental procedures which are required to a CSE, when it processes requests for performing CRUD+N operations against the resource[5], using HTTP-REST binding.The CSE implements the mechanism to accept Notification messages on behalf of the AE. This mechanism is enabled with AE Registration(clause 10.2.1.1 in [5]) at the begging of the system use.

The Registrar CSE also works to guard of the oneM2M system against unauthorized access from AEs, such as DoS attacks. The CSE will heck the identity of an AE, and should allow the request to operate upon only from successfully registered AE.

The issued request on HTTP-REST binding should be processed in one of two ways. There is Blocking Request and Non-Blocking Request(clause 8.2 in [5]). The Hosting CSEshould return a final result for Blocking Request as an HTTP responses, and it should not return a final result for Non-Blocking Request. In case of Non-blocking Request , the Hosting CSE should return a response only if the request is accepted (e.g. 202 Accepted status) or not, then Originator should fetch the final result of the request when the request were completed.

## 5.1	Basic Flow (Blocking Request)

The basic communication flow for ‘Blocking Request’ case between HTTP Client and HTTP Server,  is shown below.

Figure 5.1-1 Basic Flow (Blocking Request)

In ‘Blocking Request’ case, the HTTP Client will receive final result(s) of request(s) from HTTP Server.
The Basic Flow is performed by following steps:

- [Step 1] The HTTP Client connects to the targeted HTTP Server.

- [Step 2] The TLS session between HTTP Client and HTTP Server is optionally established.
Note: Applying TLS on HTTP transport is strongly recommended.

- [Step 3] The HTTP Client issues a HTTP request to targeted HTTP Server.

- [Step 4] The HTTP Client should wait for a response from HTTP Server.

- [Step 5] The HTTP Client may issue further HTTP Requests one by one, if those Requests is targeted on same HTTP Server.

- [Step 6] The HTTP Client should wait for HTTP Server’s response until all issued requests are processed.

- [Step 7] When HTTP Client receives all responses for issued request, HTTP Client can disconnect the connection to the HTTP Server.

## 5.2	Basic Flow (Non-Blocking Request)

The basic communication flow for ‘Non-Blocking Request’ case between HTTP Client and HTTP Server, is shown below.

Figure 5.2-1 Basic Flow (Non-Blocking Request)

For ‘Non-Blocking Request’ case, the HTTP Client will not receive final result(s) of request(s) from HTTP Server. Instead, if the request was determined as acceptable, the status  code ‘202 Accepted’  will be returned.

The Basic Flow is performed by following steps:

- [Step 1] The HTTP Client connects to the targeted HTTP Server.

- [Step 2] The TLS session between HTTP Client and HTTP Server is optionally established.
Note: Applying TLS on HTTP transport is strongly recommended.

- [Step 3] The HTTP Client issues a HTTP request to targeted HTTP Server.

- [Step 4] The HTTP Client should wait for a response (‘202 Accepted’) from HTTP Server.

- [Step 5] The HTTP Client may issue further HTTP Requests one by one, if those Requests is targeted on same HTTP Server.

- [Step 6] The HTTP Client should wait for HTTP Server’s response to confirm acceptance of non-blocking request(s).

- [Step 7] When HTTP Client receives all responses for issued request, HTTP Client can disconnect the connection to the HTTP Server.

Note that the HTTP Client does not need to specify the request to be processed as non-blocking manner. When the Server determined the result of request cannot be return in short time period, the Server may returns ‘202 Accepted’ to let Client know the final response has to be retrieved by separate request. The HTTP Client may request the operation as ‘non-blocking request’ explicitly, but the HTTP Server may reject the request to avoid abuse of ‘non-blocking request’.

When the request was accepted by HTTP Server with ‘202 Accepted’ status code. The HTTP Client can get final result of non-blocking request(s) by ‘Non-Blocking Result Retrieval’.

Figure 5.2-2 Basic Flow (Non-Blocking Result Retrieval)

The current status, or final result of ‘accepted non-blocking Request’ is performed by following steps:

- [Step 1] The HTTP Client connects to the targeted HTTP Server.

- [Step 2] The TLS session between HTTP Client and HTTP Server is optionally established.
Note: Non-expired TLS session may be reused.

- [Step 3] The HTTP Client issues a HTTP request to targeted HTTP Server.

- [Step 4] The HTTP Client should wait for a response (i.e. current status of request) from HTTP Server.

- [Step 5] The HTTP Client may issue further HTTP Request to retrieve final result of non-blocking request from the HTTP Server.

- [Step 6] The HTTP Client should wait for HTTP Server’s response to receive final result data for non-blocking request. 
Note: If the Request was still on processing, ‘503 Service Unavailable’ should be returned.

- [Step 7] When HTTP Client receives all responses for issued request, HTTP Client can disconnect the connection to the HTTP Server. [Step 7]

## 5.3	Notification using WebSocket

WebSocket as described in RFC6455 can be used for transporting notifications to an AE/CSE. This can be useful when  AE/CSE sent  a notification which is not server-capable or cannot be reachable for delivery of unsolicited requests ..

The entity which is not server-capable (Receiver of notification message) shall provide reachability information for implementing retargeting mechanism as detailed in the Architecture TS.

Any CSE may provide the optional feature called ‘Notification using WebSocket  described in this sub-clause. When the Notification using Web Scoket is provided, the AE will receive information to configure their own PoA.

An AE may establish a WebSocket a connection to notification hosting CSE, when AE needs to receive a notification message from the CSE.

When the new notification message has arrived, the notification event message will be sent to the AE as the data frame of WebSocket.

Editor’s Note: definition and data format of ‘notification event message’ is FFS.

Editor:s Note: Applicability of this solution to be considered in later in stage 3.

## 5.4	Authentication on HTTP Request Message

When sending the credential to be checked by Registrar CSE, “Proxy-Authorization” header should be used as specified in HTTP/1.1 (see RFC2617).

When sending the credential to be checked by Hosting CSE, ‘Authorization’ header should be used as specified in HTTP/1.1.

When the credential to be checked by Hosting CSE was the access_token which is compatible with OAuth 2.0 framework, the authentication schema ‘Bearer’ shall be used as specified in RFC6750.

## 5.5	Overview of HTTP binding

### 5.5.1	HTTP Version

HTTP 1.1 shall be supported by the present document.

### 5.5.2	HTTP REST Resource

### 5.5.2.1	Resource Representation

### 5.5.3	Caching

### 5.5.4	Header Fields

Editor’s Note: Some HTTP header fields are to be added, sub-clauses below are provisional.

### 5.5.4.1	Accept

### 5.5.4.1	Content-Encoding

### 5.5.4.2	Content-Location

### 5.5.5	Request URI

### 5.5.6	Request Parameters

# 6	High Level Mapping

## 6.1	HTTP Method Mapping of Request Operations

The oneM2M operations shall be mapped as follows.

Table 6.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT |
| Delete | DELETE |
| Notify | TBD |

Editor’s Note: Method mapping for Notify operation is FFS.

## 6.2	Status Code Mapping

### 6.2.1	Successful Status Codes

Table 6.2.1-1: Successful Status Code Mapping

| oneM2M Status Codes | HTTP Status Codes |
| --- | --- |
| STATUS_OK | 200 |
| STATUS_CREATED | 201 |
| STATUS_ACCEPTED | 202 |
| STATUS_DELETED | TBD |
| STATUS_CHANGED | 204 |
| STATUS_CONTENT | 205 |

Editor’s Note: contents in the table is FFS.

### 6.2.2	Un-successful Status Codes

Table 6.2.2-1: Un-successful Status Code Mapping

| oneM2M Status Codes | HTTP Status Codes |
| --- | --- |
| STATUS_BAD_REQUEST | 400 |
| STATUS_UNAUTHORIZED | 401 |
| STATUS_FORBIDDEN | 403 |
| STATUS_NOT_FOUND | 404 |
| STATUS_METHOD_NOT_ALLOWED | 405 |
| STATUS_NOT_ACCEPTABLE | 406 |
| STATUS_REQUEST_TIMEOUT | 408 |
| STATUS_REQUEST_ENTITY_TOO_LARGE | 413 |
| STATUS_UNSUPPORTED_MEDIA_TYPE | 415 |
| STATUS_INTERNAL_SERVER_ERROR | 500 |
| STATUS_NOT_IMPLEMENTED | 501 |

Editor’s Note: contents in the table is FFS.

- Editor’s Note: the set of status codes will be considered to add/delete on Core Protocol TS.

- Editor’s: futher detailed to be described in this protocol binding TS as FFS.

## Common Operation Mapping

### Compose Request Primitive (Originator AE/CSE)

The originator AE or CSE, shall compose a Request message for HTTP-REST protocol mapping.

#### Setting Standard Headers and Parameters

The Originator shall compose Request message as specified in HTTP/1.1(RFC2616)[(ref-RFC2616)] unless further requirements in use of oneM2M compliant M2M System described below.

##### Request-URI

The Request-URI parameter shall be set with the equivalent of the address for to parameter.

##### From

The From parameter shall be set with the Originator’s either AE-ID or CSE-ID which is applicable.

The Host parameter shall be set with the hostname or IP address with port number to communicate with the next-hop CSE.

##### Query String

The use of query string is described in clause (TBD).

Editor’s Note: Actual use of query string is FFS

##### Media Type

The Media Type shall be set with ‘application/onem2m-resource+xml’ or ‘application/onem2m-resource+json’ when oneM2M Resource Type is transferred.

#### Setting Private Extended Headers and Parameters

Editor’s Note: This clause shall be added if needed.

#### Setting Resource Content

Editor’s Note: detailed specification is FFS.

### Send a Request to the Receiver CSE (Originator AE/CSE)

The originator AE or CSE, shall send a composed Request message for HTTP-REST protocol mapping following section 6 of HTTP/1.1(see details in section 6 ‘Connections’ of RFC2616[(ref-rfc2616)]) .

# 8	Security Consideration

<Text>

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (Informative/Normative):Remove Informative or Normative as appropriatTitle of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| v.0.1.0 | 2014-Jan-10 | Initial version of the TS |
| v.0.1.1 | 2014-Mar-04 | The first baseline TS with table of contents agreed with: 1. PRO-2014-0107R01-HTTP Binding TS TOC |
| v.0.2.0 | 2014-Apr-22 | Includes an agreed contribution at PRO#9.3 meeting: 1. PRO-2014-0125R01-HTTP_Basic_Flows Includes agreed contributions at PRO#10 F2F meeting: 1. PRO-2014-0131R03-HTTP-REST Overview 2. PRO-2014-0147-HTTP_binding_TS_clause2_clause3 3. PRO-2014-0148R01-HTTP_binding_TS_clause5 4. PRO-2014-0149R02-HTTP_binding_TS_clause6_clause7 5. PRO-2014-0159R03-HTTP Authentication 6. PRO-2014-0160R03-WebSocket based Notification Includes Rapporteur’s input: 1. Re-numbering clause numbers, figure numbers in clause 5 and a table number in clause 6.1 |
| v0.3.2 | 2014-Jun-18 | Includes agreed contribution at PRO#10.6 and PRO#10.7 meetings: 1. PRO-2014-0201R02-CRUD_mapping_on_HTTP 2. PRO-2014-0207-more_mapping_of_HTTP_status_codes Includes agreed contributions at PRO#11 meeting: 1. PRO-2014-0226R01-Send_Request_in_HTTP 2. PRO-2014-0240-TS-0009 cleanup |