| oneM2M Technical Specification |
| --- |
| Document Number | oneM2M- TS-0023-V3.7.3 |
| Document Name: | Home Appliances Information Model and Mapping |
| Date: | 2019-04-18 |
| Abstract: | This technical specification includes oneM2M defined information model for home appliances and the mapping with other information models from external organization. |
| Template Version: January 2017 (Do not modify) |

The present document is provided for future development work within oneM2M only. The Partners accept no liability for any use of this specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2019, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright extends to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

Contents

1	Scope	8

2	References	8

2.1	Normative references	8

2.2	Informative references	9

3	Definition of terms and abbreviations	9

3.1	Terms	9

3.2	Abbreviations	10

4	Conventions	11

5	Home Appliance Information Model	11

5.1	Introduction	11

5.2	Design Principle of the Home Appliance Information Model	11

5.2.1	Basic design principle of information modelling	11

5.2.2	Description rules for Module Classes and Device models	12

5.3	ModuleClasses	13

5.3.1	3Dprinter	13

5.3.2	acousticSensor	14

5.3.3	airConJobMode	14

5.3.4	airFlow	15

5.3.5	airPurifierJobMode	15

5.3.6	airQualitySensor	15

5.3.7	alarmSpeaker	16

5.3.8	audioVolume	16

5.3.9	autoDocumentFeeder	17

5.3.10	battery	17

5.3.11	binaryObject	17

5.3.12	binarySwitch	18

5.3.13	bioElectricalImpedanceAnalysis	18

5.3.14	bodyCompositionAnalyser	18

5.3.15	boiler	19

5.3.16	brewing	19

5.3.17	brightness	19

5.3.18	clock	20

5.3.19	clothesDryerJobMode	20

5.3.20	clothesWasherJobMode	20

5.3.21	clothesWasherDryerJobMode	20

5.3.22	clothesWasherJobModeOption	21

5.3.23	colour	21

5.3.24	colourSaturation	21

5.3.25	cookerHoodJobMode	22

5.3.26	credentials	22

5.3.27	dehumidifierJobMode	22

5.3.28	dishWasherJobMode	23

5.3.29	doorStatus	23

5.3.30	electricVehicleConnector	23

5.3.31	energyConsumption	23

5.3.32	energyGeneration	24

5.3.33	faultDetection	24

5.3.34	filterInfo	25

5.3.35	foaming	25

5.3.36	geoLocation	25

5.3.37	glucometer	26

5.3.38	grinder	27

5.3.39	heatingZone	27

5.3.40	height	27

5.3.41	hotWaterSupply	27

5.3.42	impactSensor	27

5.3.43	keepWarm	28

5.3.44	keypad	28

5.3.45	liquidLevel	28

5.3.46	liquidRemaining	29

5.3.47	lock	29

5.3.48	mediaSelect	29

5.3.49	motionSensor	29

5.3.50	numberValue	30

5.3.51	openLevel	30

5.3.52	operationMode	31

5.3.53	overcurrentSensor	31

5.3.54	oximeter	31

5.3.55	ozoneMeter	32

5.3.56	phoneCall	32

5.3.57	playerControl	33

5.3.58	powerSave	33

5.3.59	printQueue	33

5.3.60	pulsemeter	33

5.3.61	pushButton	34

5.3.62	recorder	34

5.3.63	refrigeration	34

5.3.64	relativeHumidity	34

5.3.65	remoteControlEnable	35

5.3.66	robotCleanerJobMode	35

5.3.67	runState	35

5.3.68	securityMode	36

5.3.69	sessionDescription	36

5.3.70	signalStrength	36

5.3.71	smokeSensor	36

5.3.72	sphygmomanometer	37

5.3.73	spinLevel	37

5.3.74	steamClosetJobMode	37

5.3.75	televisionChannel	38

5.3.76	temperature	38

5.3.77	temperatureAlarm	38

5.3.78	textMessage	39

5.3.79	timer	39

5.3.80	turbo	40

5.3.81	uvSensor	40

5.3.82	waterFlow	41

5.3.83	waterSensor	41

5.3.84	weight	41

5.4	SubDevice models	41

5.4.1	subDeviceCuff	41

5.4.2	subDevicePowerOutlet	42

5.5	Device models	42

5.5.1	device3DPrinter	42

5.5.2	deviceAirConditioner	42

5.5.3	deviceAirPurifier	43

5.5.4	deviceAirQualityMonitor	43

5.5.5	deviceAudioReceiver	44

5.5.6	deviceBloodPressureMonitor	44

5.5.7	deviceCamera	44

5.5.8	deviceClothesDryer	44

5.5.9	deviceClothesWasher	45

5.5.10	deviceClothesWasherDryer	45

5.5.11	deviceCoffeeMachine	45

5.5.12	deviceCookerHood	46

5.5.13	deviceCooktop	46

5.5.14	deviceDehumidifier	46

5.5.15	deviceDishWasher	47

5.5.16	deviceDoor	47

5.5.17	deviceDoorLock	47

5.5.18	deviceElectricVehicleCharger	47

5.5.19	deviceFan	47

5.5.20	deviceFoodProbe	48

5.5.21	deviceFreezer	48

5.5.22	deviceGlucosemeter	48

5.5.23	deviceHeartRateMonitor	48

5.5.24	deviceHomeCCTV	48

5.5.25	deviceHumidifier	49

5.5.26	deviceKettle	49

5.5.27	deviceLight	49

5.5.28	deviceMicrogeneration	49

5.5.29	deviceMultiFunctionPrinter	50

5.5.30	deviceOutdoorLamp	50

5.5.31	deviceOven	50

5.5.32	devicePrinter	50

5.5.33	devicePulseOximeter	51

5.5.34	deviceRefrigerator	51

5.5.35	deviceRobotCleaner	51

5.5.36	deviceScanner	52

5.5.37	deviceSecurityPanel	52

5.5.38	deviceSetTopBox	52

5.5.39	deviceSmartElectricMeter	52

5.5.40	deviceSmartPlug	53

5.5.41	deviceSteamCloset	53

5.5.42	deviceStorageBattery	53

5.5.43	deviceSwitch	53

5.5.44	deviceTelevision	54

5.5.45	deviceThermometer	54

5.5.46	deviceThermostat	54

5.5.47	deviceWaterHeater	54

5.5.48	deviceWaterValve	54

5.5.49	deviceWeightScaleAndBodyCompositionAnalyser	55

5.5.50	deviceWindowShade	55

5.6	Enumeration type definitions	55

5.6.1	hd:enum3DprinterTechnology	55

5.6.2	hd:enumAdfState	55

5.6.3	hd:enumAirConJobMode	56

5.6.4	hd:enumAirPurifierJobMode	56

5.6.5	hd:enumAlertColourCode	56

5.6.6	hd:enumCallState	57

5.6.7	hd:enumClothesDryerJobMode	57

5.6.8	hd:enumClothesWasherDryerJobMode	57

5.6.9	hd:enumClothesWasherJobMode	58

5.6.10	hd:enumCookerHoodJobMode	58

5.6.11	hd:enumDehumidifierJobMode	58

5.6.12	hd:enumDishWasherJobMode	58

5.6.13	hd:enumDoorState	59

5.6.14	hd:enumFoamStrength	59

5.6.15	hd:enumGeneralLevel	59

5.6.16	hd:enumGeneralSpeed	59

5.6.17	hd:enumGeneralTemperature	60

5.6.18	hd:enumGrainsLevel	60

5.6.19	hd:enumGrindCoarseness	60

5.6.20	hd:enumHorizontalDirection	60

5.6.21	hd:enumJobStates	61

5.6.22	hd:enumLiquidLevel	61

5.6.23	hd:enumMachineState	61

5.6.24	hd:enumOzoneStatus	62

5.6.25	hd:enumPlayerMode	62

5.6.26	hd:enumRobotCleanerJobMode	62

5.6.27	hd:enumSecurityMode	62

5.6.28	hd:enumSpinLevelStrength	63

5.6.29	hd:enumSteamClosetJobMode	63

5.6.30	hd:enumSupportedMediaSources	63

5.6.31	hd:enumTasteStrength	64

5.6.32	hd:enumTone	64

5.6.33	hd:enumUvStatus	64

5.6.34	hd:enumVerticalDirection	65

5.6.35	hd:enumWaterFlowStrength	65

5.7	Universal and Common Properties for Device models	65

6	The Principle of Resource Mapping for Home Appliance Information Model	65

6.1	Introduction	65

6.2	The Resource Mapping Rules	66

6.2.1	Introduction	66

6.2.2	Resource mapping for Device model	66

6.2.3	Resource mapping for ModuleClass	66

6.2.4	Resource mapping for Action	67

6.2.5	Resource mapping for Property	67

6.2.6	Resource mapping for DataPoint	67

6.2.7	Resource mapping for SubDevice model	67

6.3	Short names	68

6.3.1	Introduction	68

6.3.2	Resource types	68

6.3.3	Resource attributes for properties and data points	72

6.4	containerDefinition values	77

6.4.1	Introduction	77

6.4.2	Device models	77

6.4.3	ModuleClasses	77

6.4.4	Actions	77

6.5	XSD definitions	77

6.5.1	Introduction	77

6.5.2	XSD definitions for Device models	77

6.5.3	XSD definitions for ModuleClass	78

6.5.4	XSD definitions for Action	78

6.5.5	XSD definitions for SubDevices	78

7	Mapping with Other Information Models from External Organizations	78

7.1	Introduction	78

7.2	OMA GotAPI(DWAPI)	78

7.2.1	Introduction	78

7.2.2	Device Models	79

7.2.2.1	device3Dprinter	79

7.2.2.2	deviceBloodPressureMonitor	80

7.2.2.3	deviceGlucosemeter	80

7.2.2.4	devicePulseOximeter	81

7.2.2.5	deviceThermometer	81

7.2.2.6	deviceWeightScaleAndBodyCompositionAnalyser	82

7.2.2.7	deviceHeartRateMonitor	82

7.2.3	Data Types	83

8	Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology	83

Annex A (informative):  Resource Mapping Examples	85

A.1	Introduction	85

A.2	Example for Device model 'deviceAirConditioner'	85

A.3	Example of ModuleClass 'binarySwitch'	88

A.4	Example of Action 'toggle'	89

Annex B (informative):  Introduction of External Organizations' Data Models	91

B.1	OMA Got API(DWAPI-PCH)	91

B.2	OCF	91

B.2.1	Introduction	91

B.2.2	Device Type Mapping	91

History	93

# Scope

The present document describes the oneM2M defined information model for home appliances, including the description of how it is mapped with other information models from external organizations. It also explains the ontology for the home domain information model.

# References

## Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	Home Gateway Initiative Smart Device Template.

NOTE:	Available at https://git.onem2m.org/MAS/SDT/tree/master.

[2]	"Java code conventions".

NOTE:	Available at https://www.oracle.com/technetwork/java/codeconventions-150003.pdf.

[3]	oneM2M TS-0001: "Functional Architecture".

[4]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[5]	ISO 80000-1: "Quantities and units -- Part 1: General".

[6]	Open Mobile AllianceTM OMA-ERELD-DWAPI-V1_0-20160419-C: "Enabler Release Definition for DWAPI 1.0".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-ERELD-DWAPI_V1_0-20160419-C.pdf.

[7]	Open Mobile AllianceTM OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C: "Blood Pressure Monitor APIs".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C.pdf.

[8]	Open Mobile AllianceTM OMA-TS-Glucometer_APIs-V1_0-20160419-C: "Glucometer APIs".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Glucometer_APIs-V1_0-20160419-C.pdf.

[9]	Open Mobile AllianceTM OMA-TS-Heart-Rate-Monitor-APIs-V1-0-20160419-C: "Heart Rate Monitor APIs".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C.pdf.

[10]	Open Mobile AllianceTM OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C: "Pulse Oximeter APIs".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C.pdf.

[11]	Open Mobile AllianceTM OMA-TS-Thermometer_APIs-V1_0-20160419-C: "Thermometer APIs".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Thermometer_APIs-V1_0-20160419-C.pdf.

[12]	Open Mobile AllianceTM OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C: "Weight Scale / Body Composition Analyzer APIs".

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C.pdf.

[13]	W3C Recommendation: "XML Schema Part 2: Datatypes", 28 October 2004

NOTE:	Available at https://www.w3.org/TR/xmlschema-2/.

[14]	NIST standard FIPS PUB 180-4: "Secure Hash Standard (SHS)".

NOTE:	Available at https://csrc.nist.gov/publications/detail/fips/180/4/final.

[15]	IETF RFC 4566: "SDP: Session Description Protocol".

[16]	IANA: "Time Zone Database".

NOTE:	Available at https://www.iana.org/time-zones.

[17]	Open Mobile AllianceTM OMA-ER-GotAPI-V1_1-20151215-C: "Generic Open Terminal API Framework (GotAPI)".

## Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf.

[i.2]	oneM2M TR-0017: "Home Domain Abstract Information Model".

[i.3]	Void.

[i.4]	IEEE 802.15.4: "IEEE Standard for Local and metropolitan area networks--Part 15.4: Low-Rate Wireless Personal Area Networks (LR-WPANs)".

[i.5]	oneM2M TS-0012: "Base Ontology".

[i.6]	https://en.wikipedia.org/w/index.php?title=Multiple_inheritance&oldid=864942988.

[i.7]	Void.[i.8]	Open Connectivity: "OCF Device Specification" V1.3.0.

NOTE:	Available at https://openconnectivity.org/specs/OCF_Device_Specification_v1.3.0.pdf.

# Definition of terms and abbreviations

## Terms

For the purposes of the present document, the following terms apply:

Device Class ID: URN to identify the Device model definition

ModuleClass ID: URN to identify the ModuleClass model definition

## Abbreviations

For the purposes of the present document, the following abbreviations apply:

A	Ampere (unit of measure)

ACO	Auto Change Over

ADF	Auto Document Feeder

AE	Application Entity

AI	Artificial Intelligence

API	Application Programing Interface

BIA	Bio-Electrical Impedance Analysis

BMI	Body Mass Index

C	Celsius (unit of measure)

CCTV	Closed-Circuit Television

CH2O	Formaldehyde (chemical formula)

cm	Centimeter (unit of measure)

CO	Carbon Monoxide (chemical formula)

CO2	Carbon Dioxide (chemical formula)

CRUD		Create, Retrieve, Update, Delete

CSE	Common Services Entity

dl		Decilitre (unit of measure)

DLP	Digital Light Processing

DWAPI	Device Web Application Programming Interface

DWAPI-3DP	Device Web Application Programming Interface for 3D Printer

DWAPI-PCH	Device Web Application Programming Interface for Personal Connected Healthcare

DVI		Digital Video Interactive

FDM	Fused Deposition Modelling

FFF	Fused Filament Fabrication

GotAPI	Generic open terminal Application Programming Interface

GSM	Global System for Mobile Communications

HAIM	Home Appliances Information Model and Mapping

HDMI	High-Definition Multimedia Interface

HEMS	Home Energy Management System

HGI	Home Gateway Initiative

Hz	Hertz (unit of measure)

ID	Identifier

IEEE	Institute of Electrical and Electronics Engineers

IETF	Internet Engineering Task Force

IPE	Interworking Proxy Entity

JSON	JavaScript Object Notation

Kg 	Kilogram (unit of measure)

Kcal	Kilocalorie (unit of measure)

KWh	Kilowatt Hour (unit of measure)

LOM	Laminated Object Manufacturing

mAh	Milliampere Hour (unit of measure)

MFP	Multi Function Printer

mg	Milligrams (unit of measure)

mmHg	Millimetre of Mercury (unit of measure)

OAuth	Open Authentication

OCF	Open Connectivity Foundation

OMA	Open Mobile Alliance

PBP	Powder Bed & inkjet head 3D Printing

PBX	Private Branch Exchange

PPM	Parts Per Million

RGB	Red, Green, Blue

RO	Read Only

RR	Respiratory Rate

RW	Read Write

SCART	Syndicat des Constructeurs d'Appareils Radiorécepteurs et Téléviseurs

SDP	Session Description Protocol

SDT	Smart Device Template

SHA		Secure Hash Algorithm

SI	Système International d'unités (International System of Units)

SLA	Stereolithography Apparatus

SLS	Selective Laser Sintering

SOS	Save our Souls (distress signal)

SPO2	Oxygen Saturation

SVIDEO	Separate video

TV	TeleVision

TZ	Time Zone

URI	Uniform Resource Identifier

URL	Uniform Resource Locator

UV	Ultraviolet

VOC	Volatile Organic Compounds

V	Volt (unit of measure)

W	Watt (unit of measure)

Wh	Watt Hour (unit of measure)

WAN	Wide Area Network

WO	Write Only

XML	Extensible Markup Language

XSD	XML Schema Definition

# Conventions

The key words "Shall", "Shall not", "May", "Need not", "Should", "Should not" in the present document are to be interpreted as described in the oneM2M Drafting Rules [i.1].

# Home Appliance Information Model

## Introduction

The present document intends to provide the unified means in the oneM2M system by defining a home appliance information model for the home domain devices such as TV, refrigerator, air conditioner, clothes washer, oven, and robot cleaner. For the reasons of interworking with external technologies and efficiency, the principle of the home appliance information model is designed based on HGI SDT 3.0 [1].

The principle of defining the home appliance information model is introduced in clause 5.2. ModuleClasses which oneM2M systems support are explained in clause 5.3. In the subsequent clause 5.5, Device models are defined.

## Design Principle of the Home Appliance Information Model

### Basic design principle of information modelling

The design principle of the oneM2M abstract information model of home appliance, is to use SDT 3.0 as introduced in oneM2M TR-0017 [i.2]. Note that those terms starting with a capital letter in this clause are SDT terms and are explained in [1].

Domain is a unique name which acts like a namespace (e.g. "org.oneM2M.home.modules"). It is set by the organization creating the SDT, allowing reference to a package of definitions for the contained ModuleClasses and Device models.

ModuleClasses specifies a single service (e.g. audioVolume, powerOn/Off) with one or more Actions, Properties, DataPoints and Events. Each service which is described as a ModuleClass can be re-used in many Devices.

Device model is a physical, addressable, identifiable appliance, sensor and actuator with one or more Modules, Properties and SubDevices.

SubDevice is a device which may be embedded in a Device and/or is addressed via another Device.

Module is an instantiation of a ModuleClass for a specific Device or SubDevice.

Figure 5.2.1-1 depicts the basic structure of SDT 3.0.

Specifications of new Device models and ModuleClasses are encouraged to re-use the definitions specified in the present document as much as possible. If re-use is not possible and new Device and/or ModuleClasses definitions are necessary, it is strongly advised to closely follow the guidelines and definition style from the present document.

Figure 5.2.1-1: Design Structure of the Home Appliance Information Model using SDT 3.0

### Description rules for Module Classes and Device models

When the Home Appliances Information Model is described based on SDT, the following rules shall be applied:

Rule 1: CamelCase rule:

When naming each element, lowerCamelCase shall be used as the Java coding rules [2].

Rule 2: Rule for description of Action, DataPoint:

DataPoint shall be used to represent stateless operations. (e.g. powerState of binarySwitch for on/off operations).

Action shall be used when describing stateful condition, handling unknown internal state conditions (e.g. upVolume/downVolume by increasing/decreasing the audioVolume in steps, handling transactional procedures, or checking integrity using username plus password at the same time).

Rule 3: Rule for description of DataPoint and Property:

Non-functional information shall be described as a Property. Functional information shall be described as a DataPoint. (E.g. non-functional information: version, id; functional information: targetTemperature, targetVolume).

Rule 4: Definition of the Domain:

The Domain, in the case of the Home Appliance Information Model, is specified as "org.onem2m.home".

The sub-domain for Device and ModuleClass shall be specified as "org.onem2m.home.devices" and "org.onem2m.home.moduleclasses" respectively.

Rule 5: Naming rule for the element:

The name of each element should be concise and avoid repeating its parent element name; but

It may include the name of its parent element for readability. (e.g., lightDimmerUp, lightDimmerDown under lightDimmer).

Rule 6: Criteria for marking elements as optional or mandatory:

An element shall only be defined as mandatory if it is foreseen to be universally mandatory to all implementing technologies.

Rule 7: Enumeration type:

When describing the meaning of values for enumeration type elements, they may be described in another clause.

The enumeration types for Home Appliance Information Model are based on <xs:integer>, and the numeric values are interpreted as specified in clause 5.6.

The name of an enumeration type shall start with the prefix "enum". This prefix shall not be used with non-enumeration type names.

Rule 8: Rule for unit in documentation:

SI (International Systems of Units in [z]) measurement (e.g. meter, kilogram, second.) should be considered as first candidate.

Otherwise, it may be kept consistency with implementing technologies such as other SDO's specification.

NOTE:	Popular unit in particular industrial domain should be considered (e.g. cm for human height, calories for energy consumption in healthcare domain).

Rule 9: Rule for type:

Measured and/or calculated values should be represented in float (without taking care of resolution of values).

Rule 10: Inheritance of ModuleClasses:

A ModuleClass may inherit from another existing ModuleClass in order to provide additional functionalities based on the existing ModuleClass. However, inheritance from multiple ModuleClasses is not allowed (due to the "diamond problem" [i.6]).

Inheritance of ModuleClass shall only be used in the case that extending an existing ModuleClass is not appropriate, i.e. the functionality to be added is irrelevant to the original design purpose of the existing ModuleClass (e.g. adding a 'time' DataPoint to a 'binarySwitch' ModuleClass).

Rule 11: When to differentiate between current and target Data Points in ModuleClasses:

Device operations, which are executed when setting data points to specific values, may take some time to reach the desired result. For example, setting a new temperature to a heater does not immediately change the room temperature, but it may take some time for the heater to increase the temperature. Therefore, it is sometimes necessary to distinguish between current and target data points.

A ModuleClass shall provide an additional "target" data point when the "current" data point:

is writable; and

the functionality that is mapped to the data point is an operation, not a configuration function; and

the operation may take some time to start and/or to complete, or reach the desired result.

When a ModuleClass provides current and target data points then the name for the current data point shall have the prefix "current", and the name for the target data point shall have the prefix "target". Both data points shall have the same suffix, for example "currentTemperature" and "targetTemperature".

## ModuleClasses

### 3Dprinter

This ModuleClass provides capabilities for a 3D printer.

Table 5.3.1-1: Actions of 3Dprinter

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | start3Dprint | none | true | Start 3D printing. |
| none | stop3Dprint | none | true | Stop 3D printing. |

Table 5.3.1-2: DataPoints of 3Dprinter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| printType | hd:enum3DprinterTechnology | true | false | false | The type of printing technology (see clause 5.6.1). |
| printSizeX | xs:float | true | false | false | This data point represents the maximum size of a printing object in the direction of X-axis. The unit of measure is "mm". (1/10cm). |
| printSizeY | xs:float | true | false | false | This data point represents the maximum size of printing object in the direction of Y-axis. The unit of measure is "mm". (1/10cm). |
| printSizeZ | xs:float | true | false | false | This data point represents the maximum size of printing object in the direction of Z-axis. The unit of measure is "mm". (1/10cm). |
| network | xs:boolean | true | false | false | This value indicates the Wide Area Network (WAN) connectivity of the 3D printer, such as Internet or GSM. "False" indicates that the printer does not have network connectivity to a WAN. "True" indicates that the printer has WAN network connectivity. |
| memorySize | xs:float | true | false | false | This value represents the total memory size of the printer. The unit of measure is MB (Mega Bytes). |

### acousticSensor

This ModuleClass provides capabilities for an acoustic sensor.

Table 5.3.2-1: DataPoints of acousticSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| loudness | xs:float | true | false | false | The unit of measure of the loudness is "dB2". |
| acousticStatus | xs:integer | true | false | true | The acousticStatus is expressed in percent, whereas a value of 0 means "no sound" and a value of 100 means "most noisy". |

### airConJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of an air conditioner.

Table 5.3.3-1: DataPoints of airConJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:enumAirConJobMode | true | true | false | Currently active job mode (see clause 5.6.3). |
| currentJobModeName | xs:string | true | false | true | Name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:enumAirConJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.3). |

### airFlow

This ModuleClass provides capabilities for controlling the air flow of a device.

Table 5.3.4-1: DataPoints of airFlow ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| speed | xs:integer | true | true | false | The current speed level in the range of the [minSpeed, maxSpeed] data points. |
| minSpeed | xs:integer | true | false | true | The minimum value for the speed level. If not present, the default is 0. |
| maxSpeed | xs:integer | true | false | true | The maximum value for the speed level. If not present, the default is 100. |
| verticalDirection | hd:enumVerticalDirection | true | true | true | The vertical direction of the air flow (see clause 5.6.34). |
| supportedVerticalDirection | List of hd:enumVerticalDirection | true | false | true | List of supported vertical directions. |
| horizontalDirection | hd:enumHorizontalDirection | true | true | true | The horizontal direction of the air flow (see clause 5.6.20). |
| supportedHorizontalDirection | List of hd:enumHorizontalDirection | true | false | true | List of supported horizontal directions. |
| automode | xs:Boolean | true | true | true | Status of the automode feature. "True" indicates that the speed is set by the device, "False" indicates that the device is not controlling the speed. |

### airPurifierJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of an airPurifier.

Table 5.3.5-1: DataPoints of airPurifierJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:enumAirPurifierJobMode | true | true | false | Currently active job mode (see clause 5.6.4). |
| currentJobModeName | xs:string | true | false | true | Name of the current job mode as astring. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:enumAirPurifierJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.4). |

### airQualitySensor

This ModuleClass provides capabilities for a monitoring sensor that measures the air quality.

Table 5.3.6-1: DataPoints of airQualitySense ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| sensorPM1 | xs:integer | true | false | true | The concentration of particle matter under 1 ㎛. The minimum value is 0, and the maximum value is 1 000. |
| sensorPM2 | xs:integer | true | false | true | The concentration of particle matter under 2,5 ㎛. The minimum value is 0, and the maximum value is 1 000. |
| sensorPM10 | xs:integer | true | false | true | The concentration of particle matter under 10 ㎛. The minimum value is 0, and the maximum value is 1 000. |
| sensorOdor | xs:integer | true | false | true | The concentration of odor that reflects air pollution. The minimum value is 0, and the maximum value is 1 000. |
| sensorHumidity | xs:integer | true | false | true | The measured humidity. The minimum value is 0, and the maximum value is 100. |
| monitoringEnabled | xs:boolean | true | true | true | The current status of monitoring. "True" indicates enabled, and "False" indicates not enabled. |
| co2 | xs:integer | true | false | true | This value indicates the CO2 level in ppm (parts per million). |
| co | xs:integer | true | false | true | This value indicates the CO level in ppm. |
| ch2o | xs:integer | true | false | true | This value indicates the CH2O level in ppm. |
| voc | xs:integer | true | false | true | This value indicates the VOC (Volatile Organic Compounds) value in ppm. |

### alarmSpeaker

This ModuleClass provides the capabilites to initiate and monitor an alarm.

Table 5.3.7-1: DataPoints of alarmSpeaker ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| tone | hd:enumTone | true | true | true | Representing the tones of the alarm (see clause 5.6.32). |
| light | hd:enumAlertColourCode | true | true | true | Representing the lighting mode of the alarm (see clause 5.6.5). |
| alarmStatus | xs:boolean | true | true | false | "True" indicates the alarm start while "False" indicates the alarm stop. |

### audioVolume

This ModuleClass provides capabilities to control and monitor volume.

Table 5.3.8-1: Actions of audioVolume

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | upVolume | none | true | Increase the volume by the amount of the stepValue up to the maxValue. |
| none | downVolume | none | true | Decrease the volume by the amount of the stepValue down to 0. |

Table 5.3.8-2: DataPoints of audioVolume

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| volumePercentage | xs:integer | true | true | false | The rounded percentage of the current volume in the range of [0, maxValue]. 0 percentage shall mean no sound produced. |
| stepValue | xs:integer | true | false | true | Step value used by the "UpVolume" and "DownVolume" actions. |
| maxValue | xs:integer | true | false | true | Maximum value allowed for Volume. maxValue is 100 by default if "maxValue" is not provided. |
| muteEnabled | xs:boolean | true | true | false | The current status of the mute enablement. "True" indicates enabled (that is, no sound), and "False" indicates not enabled (that is, sound is played). |

### autoDocumentFeeder

This ModuleClasses provides capabilities to monitor the state of autoDocumentFeeder (ADF). ADF is a feature which takes several pages and feeds the paper one page at a time into a scanner or printer, allowing the user to scan, print or fax, multiple-page documents without having to manually replace each page.

Table 5.3.9-1: DataPoints of autoDocumentFeeder ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentAdfState | hd:enumAdfState | true | false | false | Current state of the ADF. |
| adfStates | list of hd:enumAdfState | true | false | false | List of possible ADF states that are supported by the device (see clause 5.6.2). |

### battery

This ModuleClass provides capabilities to indicate the detection of low battery and gives an alarm if the triggering criterion is met. The level data point in the ModuleClass represents the current battery charge level.

Table 5.3.10-1: DataPoints of battery ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| level | xs:integer | true | false | false | The rounded percentage of the current charging level of a battery in the range of [0, 100]. 0 percentage shall mean that no charge remains. |
| capacity | xs:integer | true | false | true | The total capacity of battery in mAh. |
| charging | xs:boolean | true | false | true | The status of charging. "True" indicates enabled, and "False" indicates not enabled. |
| discharging | xs:boolean | true | false | true | The status of discharging. "True" indicates charging, and "False" indicates not charging. |
| lowBattery | xs:boolean | true | false | true | To indicate that the battery is on a low charge level. |
| batteryThreshold | xs:integer | true | true | true | When a battery's "level" is less than "batteryThreshold" then "lowBattery" is set to "True". This datapoint can be used to raise an alarm, depending on the implementation. |
| electricEnergy | xs:integer | true | false | true | Rated electric energy. The unit of measure is ampere (A). |
| voltage | xs:integer | true | false | true | Rated voltage. The unit of measure is volts (V). |
| material | xs:string | true | false | true | The material of the cell (for example lithium ion, nickel and lead. |

### binaryObject

This ModuleClass describes the handling of a binary object (blob).

Table 5.3.11-1: DataPoints of binaryObject ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| object | xs:string | true | true | false | This data point contains the base64 encoded binary object. |
| objectType | xs:string | true | true | false | This data point contains the type and subtype of the binary object as a MIME type. |
| size | xs:integer | true | true | true | The size of the decoded binary object. |
| hash | xs:string | true | true | true | The hash code of the blob. If present, it is used to check the decoded content of the "object" data point for integrity. The algorithm used for generating the hash value is SHA-2 [14]. The data point contains the hash as a hex encoded value. |

### binarySwitch

This ModuleClass provides capabilities to control and monitor the state of power.

Table 5.3.12-1: Actions of binarySwitch ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | toggle | none | true | Toggle the switch. |

Table 5.3.12-2: DataPoints of binarySwitch ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| powerState | xs:boolean | true | true | false | The current status of the binarySwitch. "True" indicates turned-on, and "False" indicates turned-off. |

### bioElectricalImpedanceAnalysis

This ModuleClass provides the analysis of human body tissue based on impedance measurement.

Table 5.3.13-1: DataPoints of bioElectricalImpedanceAnalysis ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| water | xs:float | true | false | false | The water content measurement from the BIA. The unit of measure is percentage. |
| fat | xs:float | true | false | false | The fat content measurement from the BIA. The unit of measure is percentage. |
| muscle | xs:float | true | false | false | The muscle content measurement from the BIA. The unit of measure is percentage. |
| bone | xs:float | true | false | false | The bone content measurement from the BIA. The unit of measure is percentage. |
| visceraFat | xs:float | true | false | false | The viscera fat content measurement from the BIA. The unit of measure is percentage. |
| kcal | xs:float | true | false | false | The kcal (kilocalories) measurement from the BIA. |
| resistance | xs:float | true | false | false | The resistance of human body. The unit of measure is ohm. |

### bodyCompositionAnalyser

This ModuleClass provides the capability to report the measurement of body composition analyser characteristics.

Table 5.3.14-1: DataPoints of body composition analyser ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| bodyLength | xs:float | true | false | true | The measurement of body length by Weight scale and Body composition analyser. The unit of measure is centimetre(cm). |
| Bmi | xs:float | true | false | true | The measurement of Body Mass Index (BMI) by a weight scale and a body composition analyser. The unit of measure is kg/m2. |
| fatFreeMass | xs:float | true | false | true | The measurement of fat free mass by a weight scale and a body composition analyser. The unit of measure is kilogram (kg). |
| softLeanMass | xs:float | true | false | true | The measurement of soft lean mass by a weight scale and a body composition analyser. The unit of measure is kilogram (kg). |
| muscleMass | xs:float | true | false | true | The measurement of muscle mass by a weight scale and a body composition analyser. The unit of measure is kilogram (kg). |
| basalMetabolism | xs:float | true | false | true | The measurement of basal metabolism by a weight scale and a body composition analyser. The unit of measure is kilocalorie (kcal). |
| impedance | xs:float | true | false | true | The measurement of impedance by a weight scale and a body composition analyser. The unit of measure is ohm. |

### boiler

This ModuleClass provides capabilities to control the status of the boiling functionality for water heaters.

Table 5.3.15-1: DataPoints of boiler ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| status | xs:boolean | true | true | false | The status of boiling. "True" indicates boiling, "False" indicates not boiling. |

### brewing

This ModuleClass provides capabilities to control and monitor a brewing process. It is intended to be part of devices that prepare hot drinks such as a coffee or a tea.

Table 5.3.16-1: DataPoints of brewing ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| cupsNumber | xs:integer | true | true | false | The current number of the cups requested to brew. |
| strength | hd:enumTasteStrength | true | true | true | The current strength of the drink taste (see clause 5.6.31). A higher value indicates a stronger taste. |

### brightness

This ModuleClass provides capabilities to control and monitor the brightness of a light for example from a lamp. Brightness is scaled as a percentage. A lamp or a monitor can be adjusted to a level of light between very dim (0 % is the minimum brightness) and very bright (100 % is the maximum brightness).

Table 5.3.17-1: DataPoints of brightness ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| brightness | xs:integer | true | true | false | The status of brightness level in percentage. |

### clock

This ModuleClass provides capabilities to control and monitor time and date information.

Table 5.3.18-1: DataPoints of clock ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentTime | xs:time | true | true | false | Information of the current time |
| currentDate | xs:date | true | true | false | Information of the current date |
| currentTimeZone | xs:string | true | true | true | Name of current time zone according to the IANA Timezone data format (TZ) [16], for example, "America/New York" |

### clothesDryerJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a clothes dryer.

Table 5.3.19-1: DataPoints of clothesDryerJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:enumClothesDryerJobMode | true | true | false | Currently active job mode (see clause 5.6.7). |
| currentJobModeName | xs:string | true | false | true | The name of current job mode as a string. This can be used when "currentJobMode" is vendor-specific. |
| jobModes | list of hd:enumClothesDryerJobMode | true | false | false | List of possible job states the device supports. |

### clothesWasherJobMode

This ModuleClasses provides capabilities to control and monitor the job mode of a washer.

Table 5.3.20-1: DataPoints of clothesWasherJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: enumClothesWasherJobMode | true | true | false | Currently active job mode (see clause 5.6.8). |
| currentJobModeName | xs:string | true | true | true | The name of the current job mode as a string. This can be used when the currentJobMode is vendor-specific. |
| jobModes | list of hd:enumClothesWasherJobMode | true | false | false | List of possible job states that the device supports (see clause 5.6.8). |

### clothesWasherDryerJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of clothesWasherDryer.

Table 5.3.21-1: DataPoints of clothesWasherDryerJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: enumClothesWasherDryerJobMode | true | true | false | Currently active job (see clause 5.6.8). |
| currentJobModeName | xs:string | true | true | true | The name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:enumClothesWasherDryerJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.8). |

### clothesWasherJobModeOption

This ModuleClasses provides capabilities to control and monitor the washing job mode options of a washer.

Table 5.3.22-1: DataPoints of clothesWasherJobModeOption ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| washTemp | hd:enumGeneralTemperature | true | true | true | This data point represents the water temperature level (see clause 5.6.17). |
| soilLevel | hd:enumGeneralLevel | true | true | true | This data point represents the washing level (see clause 5.6.15). |
| spinSpeed | hd:enumGeneralSpeed | true | true | true | This data point represents the spin-dry speed level (see clause 5.6.16). |
| preWash | xs:boolean | true | true | true | This data point indicates pre-wash. "True" indicates enabled, "False" indicates disabled. |
| speedWash | xs:boolean | true | true | true | This data point indicates speed wash. "True" indicates enabled, "False" indicates disabled. |
| steamTreat | xs:boolean | true | true | true | This data point indicates steam treat. "True" indicates enabled, "False" indicates disabled. |
| coldWash | xs:boolean | true | true | true | This data point indicates cold wash. "True" indicates enabled, "False" indicates disabled. |
| extraRinse | xs:boolean | true | true | true | This data point indicates extra rinse. "True" indicates enabled, "False" indicates disabled. |

### colour

This ModuleClass provides the capabilities to set the value of the Red, Green, and Blue colour channels for a colour device.

Table 5.3.23-1: DataPoints of colour ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| red | xs:integer | true | true | false | The value of the Red colour channel of RGB. The range is [0,255]. |
| green | xs:integer | true | true | false | The value of the Green colour channel of RGB. The range is [0,255]. |
| blue | xs:integer | true | true | false | The value of the Blue colour channel of RGB. The range is [0,255]. |

### colourSaturation

This ModuleClass provides capabilities to control and monitor a colour saturation value.

Table 5.3.24-1: DataPoints of colourSaturation ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| colourSaturation | xs:integer | true | true | false | The status of colour saturation level. "colourSaturation" has a range of [0,100]. A "colourSaturation" value of 0 means that a device displays or produces black and white images. A "colourSaturation" value of 50 means that a device displays or produces normal colour images. A "colourSaturation" value of 100 means that a device displays or produces very colourful images. |

### cookerHoodJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a cookerHood.

Table 5.3.25-1: DataPoints of cookerHoodJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: enumCookerHoodJobMode | true | true | false | The currently active job mode. |
| currentJobModeName | xs:string | true | false | true | The name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd: enumCookerHoodJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.10). |

### credentials

This ModuleClass provides the capability to manage user credentials which allows a user to authenticate on an appliance or a server that is associated with the appliance. The authentication depends on a user login and password, or on a token. An example appliance which may include this ModuleClass is a camera.

Table 5.3.26-1: DataPoints of credentials ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| loginName | xs:string | false | true | true | The user's login name. |
| password | xs:string | false | true | true | The user's password. |
| token | xs:string | false | true | true | An authentication token, for example an OAuth token. |

### dehumidifierJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a dehumidifier device.

Table 5.3.27-1: DataPoints of dehumidifierJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:enumDehumidifierJobMode | true | true | false | The currently active job mode (see clause 5.6.11). |
| currentJobModeName | xs:string | true | false | true | The name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:enumDehumidifierJobMode | true | false | false | List of possible job states the device supports. |

### dishWasherJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a dishWasher.

Table 5.3.28-1: DataPoints: DataPoints of dishWasherJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: enumDishWasherJobMode | true | true | false | The currently active job mode. |
| currentJobModeName | xs:string | true | false | true | The name of the current job mode as a string. This can be used when the currentJobMode is vendor-specific. |
| jobModes | list of hd: enumDishWasherJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.12) |

### doorStatus

This ModuleClass provides the status of a door. It is intended to be part of a device such as a refrigerator and an oven that might have multiple doors.

Table 5.3.29-1: DataPoints of doorStatus ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| doorState | hd:enumDoorState | true | false | false | Current state of the door (see clause 5.6.13). |
| openDuration | m2m:timestamp | true | false | true | The time duration the door has been open. |
| openAlarm | xs:boolean | true | true | true | The state of the door open alarm. "True" indicates that the open alarm is active. "False" indicates that the open alarm is not active. |

### electricVehicleConnector

This ModuleClass provides information about charging/discharging devices for electric vehicles.

Table 5.3.30-1: DataPoints of electricVehicleConnector ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| Status | xs:boolean | true | false | false | The status of connection. "True" means connected, "False" means not connected. |
| chargingCapacity | xs:integer | true | false | true | Rated charging capacity. The unit of measure is ampere hours. |
| dischargingCapacity | xs:integer | true | false | true | Rated discharging capacity. The unit of measure is ampere hours. |

### energyConsumption

This ModuleClass describes the measured energy consumed by the device since power up. One particular use case for the energyConsumption ModuleClass is a smart meter.

Table 5.3.31-1: DataPoints of energyConsumption ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| power | xs:float | true | false | false | The power of the device. The unit of measure is Watt (W). |
| absoluteEnergyConsumption | xs:float | true | false | true | The absolute energy consumption, reflecting the real measurement of accumulative energy. The unit of measure is Watt-hour (Wh). |
| roundingEnergyConsumption | xs: integer | true | false | true | This energy consumption data is calculated by multiplying significantDigits with multiplyingFactors, and rounding down the result. |
| significantDigits | xs:integer | true | false | true | The number of effective digits for data. |
| multiplyingFactors | xs:float | true | false | true | The unit for data multiplying factors, for example 1 kWh, 0,1 kWh, 0,01 kWh, etc. |
| voltage | xs:float | true | false | true | The voltage of the device. The unit of measure is volts (V). |
| current | xs:float | true | false | true | The current of the device. The unit of measure is ampere (A). |
| frequency | xs:float | true | false | true | The frequency of the device. The unit of measure is hertz (Hz). |
| measuringScope | xs:string | true | true | true | The measuring scope of the meter, for example the whole house, a room, or a device. |

### energyGeneration

This ModuleClass provides information about generation data on electric generator devices such as a photo voltaic power system, fuel cells, or microgeneration.

Table 5.3.32-1: DataPoints of energyGenerationModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| powerGenerationData | xs:float | true | false | true | Amount of instantaneous generation data. The unit of measure is Watt (W). |
| roundingEnergyGeneration | xs:integer | true | false | true | This energy consumption data is calculated by multiplying significantDigits with multiplyingFactors, and rounding down the result. |
| significantDigits | xs:integer | true | false | true | The number of effective digits for data. |
| multiplyingFactors | xs:floatr | true | false | true | The unit for data multiplying factors, for example 1 kWh, 0,1 kWh, 0,01 kWh, etc. |
| generationSource | xs:string | true | true | false | The type of generating source. |

### faultDetection

This ModuleClass provides information about whether a fault has occurred in a device.

Table 5.3.33-1: DataPoints of faultDetection ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| status | xs:boolean | true | false | false | The status of fault detection. |
| code | xs:integer | true | false | true | The numeric representation of the fault. |
| description | xs:string | true | false | true | The message representation of the fault. |

### filterInfo

This ModuleClass is for monitoring filter information of a device.

Table 5.3.34-1: DataPoints of filterInfo ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| usedTime | xs:integer | true | false | false | The cumulative used time in seconds of a filter. |
| needsReplacement | xs:boolean | true | false | true | This value indicates that the filter needs to be replaced. |
| filterLifetime | xs:integer | true | false | true | Percentage life time remaining for the water filter. |

### foaming

This ModuleClass provides capabilities to control and monitor desired parameters of foam e.g. for foaming milk. It is initially intended to be part of a device that prepare drinks with milk (for example a coffee machine or hot chocolate machine).

Table 5.3.35-1: DataPoints of foaming ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| foamingStrength | hd:enumFoamStrength | true | true | false | The current strength of foamed milk. A higher value indicates more foamed milk (see clause 5.6.14) |

### geoLocation

This ModuleClass provides the capability to get or set geo-location information.

Table 5.3.36-1: DataPoints of geoLocation ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| latitude | xs:float | true | true | false | The current latitude part of a geo-location. The unit of measures is degrees. |
| longitude | xs:float | true | true | false | The current longitude part of a geo-location. The unit of measures is degrees. |
| altitude | xs:float | true | true | true | The optional current altitude part of a geo-location. The unit of measures is meters. |
| heading | xs:float | true | true | true | The azimuth of a device measured in degrees to true north. North is 0,0°, east is 90,0°, south is 180,0°, west is 270,0°. A negative value indicates an unknown heading. |
| horizontalAccuracy | xs:float | true | false | true | The optional current horizontal accuracy of the geo-location. The unit of measures is meters and describes a radius around the latitude/longitude coordinate. |
| verticalAccuracy | xs:float | true | false | true | The optional current vertical accuracy of the altitude. The unit of measures is meters. |
| headingAccuracy | xs:float | true | false | true | The optional current maximum deviation between the heading and the true geomagnetic heading. The unit of measures is degrees. |
| targetLatitude | xs:float | true | true | true | The optional target latitude part of a geo-location. This can be used to move a device to a new location. The unit of measures is degrees. |
| targetLongitude | xs:float | true | true | true | The optional target longitude part of a geo-location. This can be used to move a device to a new location. The unit of measures is degrees. |
| targetAltitude | xs:float | true | true | true | The optional target altitude part of a geo-location. This can be used to move a device to a new altitude. The unit of measures is meters. |

### glucometer

This ModuleClass provides the capability to report the measurement of glucose characteristics.

Table 5.3.37-1: DataPoints of glucometer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| concentration | xs:float | true | false | false | The measurement of concentration by Glucometer. The unit of measure is mg/dl. |
| hba1c | xs:float | true | false | true | The measurement of HbA1c by Glucometer. The unit of measure is percentage. |
| contextExercise | xs:float | true | false | true | The measurement of context exercise by Glucometer. The unit of measure is percentage. |
| contextMedication | xs:float | true | false | true | The measurement of context medication by Glucometer. The unit of measure is mg/dl. |
| contextCarbohydratesAmount | xs:float | true | false | true | The measurement of context carbohydrates by Glucometer. The unit of measure is gram (g). |
| contextCarbohydratesSource | xs:string | true | false | true | The timing of meals (for example "breakfast carbohydrates"). |
| contextMeal | xs:string | true | false | true | The style of meals (for example "casual"). |
| contextLocation | xs:string | true | false | true | The body location where the Glucometer is worn (for example "finger"). |
| contextTester | xs:string | true | false | true | The test style (for example "self"). |
| contextHealth | xs:string | true | false | true | The severity of symptoms (for example "minor"). |

### grinder

This ModuleClass is for controlling a grinder, for example in a coffee machine.

Table 5.3.38-1: DataPoints of grinder ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| useGrinder | xs:boolean | true | true | false | The current status of the grinder enablement. "True" indicates enabled, and "False" indicates disabled. |
| coarseness | hd:enumGrindCoarseness | true | true | true | The wished coarseness of the solid supplies after grinding, for example for coffee beans (see clause 5.6.19). |
| grainsRemaining | hd:enumGrainsLevel | true | false | true | The level of remaining grains in a machine having a grinder, for example for remaining coffee beans in the coffee machine grinder (see clause 5.6.18). |

### heatingZone

This ModuleClass provides the capabilities to monitor the status of the heating zone, for example for a cooktop.

Table 5.3.39-1: DataPoints of heatingZone ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| heatingLevel | xs:integer | true | false | false | The current heating level of the zone. The value range is from 0 (indicating that the zone is not heating) up to the maxHeatingLevel. |
| maxHeatingLevel | xs:integer | true | false | false | The maximum value allowed for the heating level of the zone. |

### height

This ModuleClass provides the capability to report the measurement of height.

Table 5.3.40-1: DataPoints of height ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| height | xs:float | true | false | false | The height measurement. The unit of measure is centimetre (cm). |

### hotWaterSupply

This ModuleClass provides information about the status of supplying hot water into tanks or bath tubs.

Table 5.3.41-1: DataPoints of hotWaterSupply ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| bath | xs:boolean | true | true | true | The status of whether a bath tub is filled. |

### impactSensor

This ModuleClass describes the capabilities on an impact sensor. The impact is a high force or shock over a short time period and the impactSensor detects this.

Table 5.3.42-1: DataPoints of impactSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| impactStatus | xs:boolean | true | false | false | The "impactStatus" indicates as follows: "True" means that a physical impact is detected, "False" means indicates a normal status (no impact detected). |
| impactLevel | xs:float | true | false | true | The "impactLevel" provides the level of impact. The unit of measure is "g" (G-force). |
| impactDirectionHorizontal | xs:float | true | false | true | The "impactDirection" indicates the horizontal direction where the impact comes from. The value is 0° to 360°. 0 is the front of the sensor and with clockwise increment. |
| impactDirectionVertical | xs:float | true | false | true | The "impactDirection" indicates the vertical direction where the impact comes from. The value is 0° to 360°. 0 is the front of the sensor and with upward increment. |

### keepWarm

This module allows to control the 'keep warm' feature in devices like coffee machines, kettles, etc. It allows to keep water warm for a desired time. This ModuleClass inherits from binarySwitch (see clause 5.3.12) to store setting for the 'keep warm' feature. If the "powerState" data point in a keepWarmSwitch is "True" then the 'keep warm' function will be performed just after boiling (or heating) process is finished (otherwise this function will not be applied).

Table 5.3.43-1: DataPoints of keepWarm ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| time | xs:integer | true | true | true | The desired duration of 'keep water warm' function. It indicates how long water shall be kept warm, for example after the boiling in a kettle. The value indicates a time expressed in minutes. |

### keypad

This ModuleClass provides the capability to perform a user defined service through the key-in number. For example, a user can define key 1 as "perform a takeout from a restaurant with combo meal 1". The IoT service provider or user can define the services.

Table 5.3.44-1: DataPoints of keypad ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| keyNumber | xs:integer | true | false | false | The number of the pressed key. |

### liquidLevel

This ModuleClass provides the desired level of water (or other liquid) for an appliance, for example the desired level of milk for a cup of coffee from a coffee machine.

Table 5.3.45-1: DataPoints of liquidLevel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| liquidLevel | hd:enumLiquidLevel | true | true | false | The desired level of water or other liquid, for example the desired level of milk in a cup of coffee (see clause 5.6.22). |

### liquidRemaining

This ModuleClass provides the status of water level (or other liquid) for an appliance, for example the level of remaining milk in a coffee machine.

Table 5.3.46-1: DataPoints of liquidRemaining ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| liquidRemaining | hd:enumLiquidLevel | true | false | false | The remaining level of water or other liquid in an appliance (see clause 5.6.22). |

### lock

This ModuleClass provides the function to lock and unlock an object.

Table 5.3.47-1: DataPoints of lock ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| lock | xs:boolean | true | true | false | "True" indicates the object is locked, while "False" indicates the object is not locked. |

### mediaSelect

This ModuleClass provides capabilities to control and monitor media input and output of device such as TV or SetTopBox.

Table 5.3.48-1: DataPoints of mediaSelect ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| mediaID | xs:integer | true | true | false | The numeric index of the activated media in the supported media sources list "supportedMediaSources". |
| supportedMediaSources | list of hd:enumSupportedMediaSource | true | false | false | List of supported input or output media for the given device (see clause 5.6.30). |
| mediaName | xs:string | true | false | true | Specifies a pre-defined media input or output. |
| status | xs:boolean | true | false | true | Specifies whether the specific media instance is selected ("True") or not ("False"). |
| mediaType | hd:enumSupportedMediaSource | true | false | false | Specifies the type of the media (see clause 5.6.30). |

### motionSensor

This ModuleClass provides the capabilities to indicate the occurrence of motion and raising of an alarm if the triggering criterion is met.

Table 5.3.49-1: DataPoints of motionSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | true | false | false | The detection of the motion occurrence. |
| silentTime | xs:integer | true | true | true | The time that a motionSensor restrains from sending an alarm in case continuous motions are detected after one alarm is produced. This data point can be used to avoid repeated alarm reports. The unit of measure is seconds. |
| sensitivity | xs:integer | true | true | true | The level of the detection accuracy of the motion sensor. This data point can be used to control the number of the report. |

### numberValue

This ModuleClass provides the capabilities to represent a number. It also has capabilities for controlled increment and decrement a counter. It can be used to present a number-related functionality in a technology where there is only a weak semantic specification of that functionality.

Table 5.3.50-1: Actions of numberValue ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | decrementNumberValue | none | true | Decrement the "numberValue" by the value of "step", down to the value of "minimum". |
| none | incrementNumberValue | none | true | Increment the "numberValue" by the value of "stepValue", up to the value of "maxValue". |
| none | resetNumberValue | none | true | Reset the "numberValue" to its "defaultValue". |

Table 5.3.50-2: DataPoints of numberValue ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| numberValue | xs:float | true | true | false | The actual value of the number. |
| minValue | xs:float | true | true | true | The optional minimum value of the number. The default is the system-specific minimum value for a float value. |
| maxValue | xs:float | true | true | true | The optional maximum value of the number. The default is the system-specific maximum value for a float value. |
| defaultValue | xs:float | true | true | true | The optional default value for the number. The default is 0,0. |
| step | xs:float | true | true | true | The optional step size for controlled increment and decrement. The default is 1,0, even when this data point is not implemented. |

### openLevel

This ModuleClass provides the capabilities to control and monitor the open status of an entity, for example a curtain.

Table 5.3.51-1: Actions of openLevel ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | open | None | true | Increase the open level by the amount of the "stepValue" up to the "maxLevel". |
| none | close | None | true | Decrease the open level by the amount of the "stepValue" down to the "minLevel". |

Table 5.3.51-2: DataPoints of openLevel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| openLevel | xs:integer | true | true | false | The rounded percentage of the current open level of entity in the range of [0, 100]. 0 percentage shall mean the entity is closed. |
| stepValue | xs:integer | true | true | true | The step value used by the "open" and "close" actions. |
| minLevel | xs:integer | true | true | true | The minimum value allowed for the "openLevel" status. The default value is 0, which means fully closed. |
| maxLevel | xs:integer | true | true | true | The maximum value allowed for the "openLevel" status. The default value is 100, which means fully opened. |

### operationMode

This ModuleClasses provides capabilities to control or monitor the operation mode of appliances.

Table 5.3.52-1: DataPoints of operationMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| startPause | xs:boolean | true | true | false | A value of "True" triggers or starts an operation, and "False" pauses the operation. |

### overcurrentSensor

This ModuleClass provides capabilities for an over-current sensor.

Table 5.3.53-1: DataPoints of overcurrentSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| overcurrentStatus | xs:boolean | true | false | false | The overcurrentStatus indicates as follows: "True" indicates that an over-current is detected, and "False" indicates a normal status, this means that an over-current is not detected. |
| detectedTime | m2m:timestamp | true | false | true | The time when the over-current was detected. |
| duration | xs:float | true | false | true | The duration of the detected over-current. The unit of measure is "ms". |

### oximeter

This ModuleClass provides the capability to report the measurement of blood oxygen characteristics.

Table 5.3.54-1: DataPoints of oximeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| oxygenSaturation | xs:integer | true | false | false | The measurement of oxygensaturation by Oximeter. The unit of measure is in percentage. |

### ozoneMeter

This ModuleClass provides capabilities for an ozone meter. The "ozoneValue…" attributes are optional, but one of them SHALL be provided.

Table 5.3.55-1: DataPoints of ozoneMeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| ozoneValuePPM | xs:float | true | false | true | The unit of measure of ozone measurement is "ppm". |
| ozoneValueMG | xs:float | true | false | true | The unit of measure of ozone measurement is "mg/m3". |
| ozoneStatus | hd:enumOzoneStatus | true | false | true | The ozoneStatus indicates the level of ozone status. (See clause 5.6.24). |
| maxValue | xs:float | true | false | true | The mazimum value shows the measurement range of the ozone meter (for example maxValue = 5 means the range is 0 to 5 ppm). This attribute is only used that the ozoneMeter provides "ppm" value. |

### phoneCall

This ModuleClass provides the capability get or set the caller and recipient IDs as well as to initiate and terminate a call.

Table 5.3.56-1: Actions of phoneCall ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | call | none | true | Initiate an outgoing call. |
| none | answer | none | true | Answer (pickup) an incoming call. |
| none | hangup | none | true | Hangup an established call. |

Table 5.3.56-2: DataPoints of phoneCall ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| callerID | xs:string | true | true | false | This data point represents the initiating caller identiﬁcation of a call. In case of an outgoing call this would be the local line ID. This data point is optional. When it is empty for an incoming call, then the caller ID is unknown. When it is empty for an outgoing call, then it is expected that it is set by the PBX or the operator. The format of caller ID is not speciﬁed here. |
| recipientID | xs:string | true | true | false | This data point represents the receiving caller identiﬁcation of a call. In case of an incoming call this would be the local line ID and optionally extension. The format of caller ID is not speciﬁed here. |
| callState | hd:enumCallState | true | false | true | This data point represents the current state of an associated phone device regarding calls. |

### playerControl

This ModuleClass provides capabilities to control and monitor the operational modes of a media player functionality.

Table 5.3.57-1: Actions of playerControl ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | nextTrack | none | true | Go forward to a next chapter, section or similar marker in the media. |
| none | previousTrack | none | true | Go back to a previous chapter, section or similar marker in the media. |

Table 5.3.57-2: DataPoints of playerControl ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentPlayerMode | hd:enumPlayerMode | true | true | false | The current mode of the player. |
| currentPlayerModeName | xs:string | true | false | true | Name of current player mode in string. This can be used when "currentPlayerMode" is vendor-specific. |
| supportedPlayerModes | list of hd:enumPlayerMode | true | false | false | List of supported modes for a player. |
| speedFactor | xs:float | true | true | true | The optional factor of speeding up or slowing down playback, rewind or fast forward. |

### powerSave

This ModuleClass provides capabilities to enable the power saving mode of a device and monitor the current status.

Table 5.3.58-1: DataPoints of powerSave ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| powerSaveEnabled | xs:boolean | true | true | false | The current status of the power saving mode. "True" indicates enabled, and "False" indicates not enabled. |

### printQueue

This ModuleClass provides the capabilities for monitoring printing list information.

Table 5.3.59-1: DataPoints of printQueue ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| uri | list of xs:uri | true | false | false | The URI of the printing file. The URI could be "file://www.example.com/file.extension". |
| printingState | list of hd:enumJobState | true | false | false | The printingState is indicating the status of the printing file. |

### pulsemeter

This ModuleClass provides the capability to report the measurement of pulse characteristics.

Table 5.3.60-1: DataPoints of pulsemeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| pulseRate | xs:float | true | false | false | The measurement of pulserate by pulsemeter. The unit of measure is in beats per minute. |
| rr | xs:float | true | false | true | The measurement of RR interval by pulsemeter. The unit of measure is millisecond (ms). |
| energy | xs:float | true | false | true | The measurement of energy by pulsemeter. The unit of measure is kilocalorie per hour. |
| modality | xs:string | true | false | true | The modality of a particular SpO2 measurement. |

### pushButton

This ModuleClass provides the capability to indicate the operation of a push button style switch. A typical application can be an SOS button.

Table 5.3.61-1: DataPoints of pushButton ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| pushed | xs:boolean | true | false | false | This data point indicates the press of the button. |

### recorder

This ModuleClass provides the capability to record video/audio for a defined duration.

Table 5.3.62-1: DataPoints of recorder ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| duration | xs:integer | true | true | false | The duration for video/audio recording. Set to trigger the recorder. The unit of measure is seconds. |

### refrigeration

This ModuleClass provides capabilities for a refrigeration function.

Table 5.3.63-1: DataPoints of refrigeration ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| rapidFreeze | xs:boolean | true | True | true | Controls the rapid freeze capability. "True" indicates active, "False" indicates inactive. |
| rapidCool | xs:boolean | true | True | true | Controls the rapid cool capability. "True" indicates active, "False" indicates inactive. |
| defrost | xs:boolean | true | True | true | Controls the defrost cycle. "True" indicates active, "False" indicates inactive. |

### relativeHumidity

This ModuleClass provides the capability for a device to report the humidity based on a specified rule that is vendor dependent.

Table 5.3.64-1: DataPoints of relativeHumidity ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| relativeHumidity | xs:float | true | false | false | The measurement of the relative humidity value; the unit of measure is percentage. |
| desiredHumidity | xs:float | true | true | true | Desired value for humidity. This data point indicates the desired humidity. |

### remoteControlEnable

This ModuleClasses provides capabilities to monitor the remote controllability of the appliance.

Table 5.3.65-1: DataPoints of remoteControlEnable ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| remoteControlEnabled | xs:boolean | true | false | false | This data point enables or disables remote controllability and is set by a user locally. "True" indicates enabled remote access, and "False" indicates disabled remote access. |

### robotCleanerJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a robotCleaner.

Table 5.3.66-1: DataPoints of robotCleanerJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:enumRobotCleanerJobMode | true | true | false | Currently active job mode (see clause 5.6.26). |
| currentJobModeName | xs:string | true | false | true | Name of current job mode as a string. This can be used when "currentJobMode" is vendor-specific. |
| jobModes | list of hd:enumRobotCleanerJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.26). |

### runState

This ModuleClasses provides capabilities to control and the monitor machine state of appliances.

Table 5.3.67-1: DataPoints of runState ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentMachineState | hd:enumMachineState | true | true | false | The currently active machine state (see clause 5.6.23). |
| machineStates | list of hd:enumMachineState | true | false | false | A list of possible machine states the device supports (see clause 5.6.23). |
| currentJobState | hd:enumJobState | true | false | true | The currently active job state at the level of some transaction being executed by the device (see clause 5.6.21). |
| jobStates | list of hd:enumJobState | true | false | true | The list of possible job states that the device supports (see clause 5.6.21). |
| progressPercentage | xs:float | true | false | true | The indication of current job progress in percentage. |

### securityMode

This ModuleClasses provides capabilities to control and monitor a security mode.

Table 5.3.68-1: DataPoints of securityMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentSecurityMode | hd:enumSecurityMode | true | true | false | Current security mode (see clause 5.6.27). |
| securityModes | list of hd:enumSecurityMode | true | false | false | List of possible security modes the device supports (see clause 5.6.27). |

### sessionDescription

This ModuleClass provides the capabilities for a sessionDescription containing a URL at which the specified media can be accessed and the definition of media using SDP.

Table 5.3.69-1: DataPoints of mediaType ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| url | xs:uri | true | false | true | A URL at which the specified media can be accessed. |
| sdp | xs:string | true | false | true | Media description using SDP. One or more comma separated multiple SDP lines (SDP media or attribute line) can be included using SDP description syntax as defined in the SDP specification in IETF RFC 4566 [15]. |

### signalStrength

This ModuleClass provides the capability to monitor the strength of the signal.

Table 5.3.70-1: DataPoints of signalStrength ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| lqi | xs:integer | true | false | false | The current value of link quality indicator, which reflects the scaling of rssi by dividing the received signal strength over reference signal strength. The common unit for lqi is percentage [0, 100]. For the detailed definition, please see IEEE 802.15.4 [i.4], clause 6.7.8. |
| rssi | xs:float | true | false | true | The current value of received signal strength indicator, which reflects the raw signal level. |

### smokeSensor

This ModuleClass provides the capabilities to indicate the detection of smoke and raising an alarm if the triggering criterion is met.

Table 5.3.71-1: DataPoints of smokeSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | true | false | false | The alarm is indicated as follows: "True" indicates that smoke has been detected, "False" indicates a normal status, that means that smoke is not detected. |
| detectedTime | m2m:timestamp | true | true | true | The date and time the smoke is detected. |
| smokeThreshold | xs:integer | true | true | true | The Threshold to trigger the alarm. The unit of measure is ppm. |
| currentValue | xs:integer | true | false | true | The current data value of the smoke sensor. |

### sphygmomanometer

This ModuleClass provides the capability to report the measurement of blood pressure characteristics.

Table 5.3.72-1: DataPoints of sphygmomanometer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| diastolicPressure | xs:float | true | false | false | The measurement of diastolic pressure by sphygmomanometer. The unit of measure is millimetre of mercury (mmHg). |
| systolicPressure | xs:float | true | false | false | The measurement of systolic pressure by sphygmomanometer. The unit of measure is millimetre of mercury (mmHg). |
| meanPressure | xs:float | true | false | false | The measurement of mean arterial pressure by sphygmomanometer. The unit of measure is millimetre of mercury (mmHg). |

### spinLevel

This ModuleClass provides capabilities to control and monitor the level of spin. It is intended to be part of devices which use spinning function such as a washing machine and a dryer.

Table 5.3.73-1: DataPoints of spinLevel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| spinLevelStrength | hd:enumSpinLevelStrength | true | true | false | The value of spin-dry level (see clause 5.6.28). A higher value indicates a higher spin level. |

### steamClosetJobMode

This ModuleClass provides capabilities to control and monitor the job modes of steamCloset.

Table 5.3.74-1: DataPoints of steamClosetJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:enumSteamClosetJobMode | true | true | false | Currently active job mode (see clause 5.6.29). |
| currentJobModeName | xs:string | true | false | true | Name of current job mode as a string. This can be used when "currentJobMode" is vendor-specific. |
| jobModes | list of hd:enumSteamClosetJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.29). |

### televisionChannel

This ModuleClass provides capabilities to set and get channels of a device that has a channel list.

Table 5.3.75-1: Actions of televisionChannel ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | upChannel | None | true | Change the current channel to the next channel in the stored list of available channels. If the current channel is the last one in the list, the new set channel may be the first one in the list. |
| none | downChannel | None | true | Change the current channel to the previous channel in the stored list of available channels. If the current channel is the first one in the list, the new set channel may be the last one in the list. |

Table 5.3.75-2: DataPoints of televisionChannel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| channelNumber | xs:integer | true | true | false | Current channel number. |
| availableChannels | list of xs:integer | true | false | true | The list of available channel numbers which may be built by automatic scan and/or manual selection. |
| previousChannel | xs:integer | true | false | true | The channel number which was selected previously. |
| channelName | xs:string | true | false | true | Current human-friendly channel name in string, for example 'CNN'. |

### temperature

This ModuleClass provides capabilities to represent the current temperature and target temperature of devices such as an air conditioner, refrigerator, oven, etc.

Table 5.3.76-1: DataPoints of temperature ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentTemperature | xs:float | true | false | false | The current temperature. |
| targetTemperature | xs:float | true | true | true | The desired temperature to reach. |
| unit | xs:string | true | false | true | The unit of measure for the temperature values. The default is Celsius (C). |
| minValue | xs:float | true | false | true | Minimum value of "targetTemperature". |
| maxValue | xs:float | true | false | true | Maximum value of "targetTemperature". |
| stepValue | xs:float | true | false | true | Step value allowed for "targetTemperature". |

### temperatureAlarm

This ModuleClass provides the capabilities to indicate the detection of abnormal temperatures and raises an alarm if the triggering criterion is met.

Table 5.3.77-1: DataPoints of temperatureAlarm ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | true | false | false | This data point indicates the status of detection of an abnormal temperature. "True" indicates an abnormal temperature, "False" indicates a normal temperature. |
| temperature | xs:float | true | false | true | To report the value of the temperature. The unit of measure is Celsius (C). |
| temperatureThreshold | xs:integer | true | true | true | The threshold to trigger the alarm. |

### textMessage

This ModuleClass provides capabilities to set and get a text message.

Table 5.3.78-1: Actions of textMessage ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | resetTextMessage | none | true | Reset the receiver of the message to the "defaultValue". |

Table 5.3.78-2: DataPoints of textMessage ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| textMessage | xs:string | true | true | false | The current message value. |
| supportedMessageValues | list of xs:string | true | false | true | List of supported values for the message. Each of the values in this list shall be URL-encoded. An encoded value shall not contain white spaces. |
| minLength | xs:integer | true | false | true | The optional minimum length in characters of the message. The default is 0. |
| maxLength | xs:integer | true | false | true | The optional maximum length in characters of the message. The default is unlimited. |
| messageEncoding | xs:string | true | false | true | The optional expected method for character encoding of the message. The default is "UTF-8". |
| defaultValue | xs:string | true | true | true | The optional default value for "textMessage". The default is an empty string. |

### timer

This ModuleClass provides capabilities to monitor and control the times when the appliance executes its operations, that means when it starts, when it ends, etc.

Table 5.3.79-1: Actions of timer ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | activateClockTimer | None | true | Activate current clock timer. |
| none | deactivateClockTimer | None | true | Deactivate current clock timer. |

Table 5.3.79-2: DataPoints of timer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| referenceTimer | xs:integer | true | false | true | A timer (for example. a time-based value, App Defined Epoch, Progressive) expressed in seconds. The value indicates a time counter to be used as reference for the other time-based data points of this ModuleClass. Usually it is the time since the last event of power-on of the producer (or more in detail the time since the boot of its connectivity node). |
| targetTimeToStart | xs:integer | true | true | true | A time span (for example a time-based value, App Defined Epoch, Fixed) expressed in seconds. The value indicates the time when the appliance is expected to start its operation, starting counting from the last "referenceTimer". |
| targetTimeToStop | xs:integer | true | true | true | A time span (for example a time-based value, App Defined Epoch, Fixed) expressed in seconds. The value indicates the time when the appliance is expected to stop its operation, starting counting from the last "referenceTimer". |
| estimatedTimeToEnd | xs:integer | true | false | true | A timer (for example a time-based value, App Defined Epoch, Progressive) expressed in seconds. The value indicates the time to the end of an appliance's operations. It is calculated at runtime by the device itself during the execution of its operation. |
| runningTime | xs:integer | true | false | true | A timer (for example a time-based value, App Defined Epoch, Progressive) expressed in seconds. It indicates the time of the current operation. Usually its value is increasing one value per second. It starts counting from 0 when the operation starts and stops counting when the operation ends. |
| targetDuration | xs:integer | true | false | true | A time span (for a time-based value, App Defined Epoch, Fixed) expressed in seconds. The value indicates a time that represents the target duration of the operation as per user selection. |
| absoluteStartTime | m2m:timestamp | true | true | true | An absolute time to specify the start time. |
| absoluteStopTime | m2m:timestamp | true | true | true | An absolute time to specify the stop time. |

### turbo

This ModuleClass provides capabilities to enable turbo mode and monitor the current status of the turbo function. It is intended to be part of devices which use turbo function such as an air conditioner, a washing machine, etc.

Table 5.3.80-1: DataPoints of turbo ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| turboEnabled | xs:boolean | true | true | false | The current status of the turbo mode. "True" indicates enabled, and "False" indicates not enabled. |

### uvSensor

This ModuleClass describes the capabilities of an ultraviolet sensor.

Table 5.3.81-1: DataPoints of uvSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| uvValue | xs:float | true | false | false | The unit of measure of the UV intensity of radiation is "mW/cm2". |
| uvStatus | hd:enumUvStatus | true | false | true | The "uvStatus" indicates the level of the UV radiation status (see clause 5.6.33). |

### waterFlow

This ModuleClass provides capabilities for controlling the water strength of a device.

Table 5.3.82-1: DataPoints of waterFlow ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| waterLevelStrength | hd:enumWaterFlowStrength | true | true | false | The desired level of water flow (see clause 5.6.35). A higher value indicates higher water flow. |

### waterSensor

This ModuleClass provides the capabilities to indicate whether or not water has been sensed, and raising an alarm if the triggering criterion is met.

Table 5.3.83-1: DataPoints of waterSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | True | false | false | The detection of water. The alarm is indicated as follows: "True" indicates that water has been detected, "False" indicates a normal status, that means that water is not detected. |

### weight

This ModuleClass provides the capability to report the measurement of weight.

Table 5.3.84-1: DataPoints of weight ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| weight | xs:float | true | false | false | The weight measurement. The common unit is kilogram (kg). |

## SubDevice models

### subDeviceCuff

A cuff is a subDevice that expresses the attachment device for measuring blood pressure.

Table 5.4.1-1: Modules of subDeviceCuff model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| sphygmomanometer | sphygmomanometer | false | See clause 5.3.72. |
| pulsemeter | pulsemeter | false | See clause 5.3.60. |

### subDevicePowerOutlet

A powerOutlet is a subDevice that specifies the attachment device for deviceSmartPlug.

Table 5.4.2-1: Modules of subDevicePowerOutlet model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| energyConsumption | energyConsumption | true | See clause 5.3.31. |
| overcurrentSensor | overcurrentSensor | true | See clause 5.3.53. |
| dimmingLevel | numberValue | true | See clause 5.3.50. This provides the capability to change the energy. |

## Device models

### device3DPrinter

A 3D printer is a smart home appliance to provide 3D printing capabilities.

Table 5.5.1-1: Modules of device3DPrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| 3Dprinter | 3Dprinter | false | See clause 5.3.1. |
| runState | runState | false | See clause 5.3.67. |
| temperature | temperature | false | See clause 5.3.76. This value of "currentTemperature" in this module instance represents the temperature of the nozzle. This value SHALL be a float number in a range from 0,0 to 1 000,0. |
| printQueue | printQueue | false | See clause 5.3.59. |

### deviceAirConditioner

An air conditioner is a home appliance used to alter the properties of air (primarily temperature and humidity) to more comfortable conditions. This air conditioner information model provides capabilities to control and monitor air conditioner specific functions and resources.

Table 5.5.2-1: Modules of deviceAirConditioner Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| airConJobMode | airConJobMode | true | See clause 5.3.1. |
| airConOperationMode | operationMode | true | See clause 5.3.52. This module instance is used to trigger an airCon operation that is pre-set in "airConJobMode". If this data point is not present, then the air conditioner's job mode can be triggered by setting the "airConJobMode". |
| airCleanOperationMode | operationMode | true | See clause 5.3.52. This module instance is used to trigger airClean operation. |
| temperature | temperature | true | See clause 5.3.76. |
| timer | timer | true | See clause 5.3.79. |
| sleepTimer | timer | true | See clause 5.3.79. The sleep function, which is vendor-specific algorithm (for example increasing the temperature by one degree for every 30 minutes), is triggered instantly when "targetDuration" is set, and it indicates the time to the end of appliance operation. It is set at runtime by a user application. |
| turbo | turbo | true | See clause 5.3.80. |
| airFlow | airFlow | true | See clause 5.3.4. |
| powerSave | powerSave | true | See clause 5.3.58. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| filterInfo | filterInfo | true | See clause 5.3.34. |

### deviceAirPurifier

An airPurifier is a home appliance is used to prevent dust and other particles from air by filtering, washing or electrostatic precipitation. This airPurifier information model provides capabilities to control and monitor airPurifier specific functions and resources.

Table 5.5.3-1: Modules of deviceAirPurifier Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| airPurifierJobMode | airPurifierJobMode | true | See clause 5.3.5. |
| airPurifierOperationMode | operationMode | true | See clause 5.3.52. This module instance is used to trigger the airPurifier operation. |
| timer | timer | true | See clause 5.3.79. |
| powerSave | powerSave | true | See clause 5.3.58. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| filterInfo | filterInfo | true | See clause 5.3.34. |

### deviceAirQualityMonitor

An air quality monitor is a home appliance for monitoring the air quality. This airQualityMonitor information model provides capabilities to monitor the airQualityMonitor functions and resources.

Table 5.5.4-1: Modules of deviceAirQualityMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| airQualitySensor | airQualitySensor | false | See clause 5.3.6. |

### deviceAudioReceiver

An audio receiver is a device that receives audio signals from a number of sources, processing them to drive speakers.

Table 5.5.5-1: Modules of deviceAudioReceiver model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| audioVolume | audioVolume | false | See clause 5.3.8. |
| mediaInput | mediaSelect | true | See clause 5.3.48. |
| mediaOutput | mediaSelect | true | See clause 5.3.48. |

### deviceBloodPressureMonitor

A blood pressure monitor is a device that can be used to monitor the blood pressure and is composed of one or more cuffs and a main monitor machine.

Table 5.5.6-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| battery | battery | false | See clause 5.3.10 |
| binarySwitch | binarySwitch | true | See clause 5.3.12 |

Table 5.5.6-2: Subdevice of deviceBloodPressureMonitor Device model

| Subdevice Instance Name | Subdevice Name | Optional | Description |
| --- | --- | --- | --- |
| cuff0 | subDeviceCuff | false | See clause 5.4.1 |
| cuff1 | subDeviceCuff | true | See clause 5.4.1 |
| cuff2 | subDeviceCuff | true | See clause 5.4.1 |
| cuff3 | subDeviceCuff | true | See clause 5.4.1 |
| cuff4 | subDeviceCuff | true | See clause 5.4.1 |
| cuff5 | subDeviceCuff | true | See clause 5.4.1 |

### deviceCamera

A camera is an optical instrument for recording or capturing images, which may be stored locally or transmitted to another location.

Table 5.5.7-1: Modules of deviceCamera Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| sessionDescription | sessionDescription | false | See clause 5.3.69. |
| playerControl | playerControl | true | See clause 5.3.57. |
| motionSensor | motionSensor | true | See clause 5.3.49. |

### deviceClothesDryer

A clothes dryer is a home appliance for drying clothes. This clothesDryer information model provides capabilities to control and monitor clothes dryer specific functions and resources.

Table 5.5.8-1: Modules of deviceClothesDryer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| clothesDryerJobMode | clothesDryerJobMode | true | See clause 5.3.19. |
| clothesDryerOperationMode | operationMode | true | See clause 5.3.52. This module instance is used to trigger the clothesDryer operation. |

### deviceClothesWasher

A clothes washer is a home appliance that is used to wash laundry, such as clothing and sheets. This information model provides capabilities to interact with specific functions and resources of clothes washers.

Table 5.5.9-1: Modules of deviceClothesWasher Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| clothesWasherOperationMode | operationMode | true | See clause 5.3.52. |
| runState | runState | false | See clause 5.3.67. |
| clothesWasherJobMode | clothesWasherJobMode | false | See clause 5.3.20. |
| clothesWasherJobModeOption | clothesWasherJobModeOption | true | See clause 5.3.22. |
| remoteControlEnable | remoteControlEnable | true | See clause 5.3.65. |
| timer | timer | true | See clause 5.3.79. |

### deviceClothesWasherDryer

A clothes washer dryer is a home appliance that is a combination of cloth washer and cloth dryer in a single cabinet. This information model provides capabilities to interact with specific functions and resources of clothes washers and dryers.

Table 5.5.10-1: Modules of deviceClothesWasherDryer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| clothesWasherDryerOperationMode | operationMode | true | See clause 5.3.52. |
| runState | runState | false | See clause 5.3.67. |
| clothesWasherDryerJobMode | clothesWasherDryerJobMode | false | See clause 5.3.21. |
| clothesWasherJobModeOption | clothesWasherJobModeOption | true | See clause 5.3.22. |
| remoteControlEnable | remoteControlEnable | true | See clause 5.3.65. |
| timer | timer | true | See clause 5.3.79. |

### deviceCoffeeMachine

A coffee machine is a device that is used to brew a coffee, may add foamed milk, and may include some variants, for example a grinder.

Table 5.5.11-1: Modules of deviceCoffeeMachine Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| runState | runState | true | See clause 5.3.67. |
| clock | clock | true | See clause 5.3.18. |
| brewing | brewing | false | See clause 5.3.16. |
| waterStatus | liquidRemaining | true | See clause 5.3.46. |
| milkStatus | liquidRemaining | true | See clause 5.3.46. |
| grinder | grinder | true | See clause 5.3.38. |
| milkFoaming | foaming | true | See clause 5.3.35. |
| milkQuantity | liquidLevel | true | See clause 5.3.45. |
| brewingSwitch | binarySwitch | false | See clause 5.3.12. |
| keepWarm | keepWarm | true | See clause 5.3.43. |

### deviceCookerHood

A cooker hood is a device containing a mechanical fan that hangs above the stove or cooktop in the kitchen.

Table 5.5.12-1: Modules of deviceCookerHood model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| airFlow | airFlow | true | See clause 5.3.4. |
| cookerHoodJobMode | cookerHoodJobMode | true | See clause 5.3.25. |

### deviceCooktop

A cooktop is a device that is a kitchen appliance designed for the purpose of cooking food.

Table 5.5.13-1: Modules of deviceCooktop model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| heatingZone0 | heatingZone | false | See clause 5.3.39. |
| heatingZone1 | heatingZone | true | See clause 5.3.39. |
| heatingZone2 | heatingZone | true | See clause 5.3.39. |
| heatingZone3 | heatingZone | true | See clause 5.3.39. |
| heatingZone4 | heatingZone | true | See clause 5.3.39. |
| heatingZone5 | heatingZone | true | See clause 5.3.39. |

### deviceDehumidifier

A dehumidifier is a device that is used to monitor or control the state of a dehumidifying appliance.

Table 5.5.14-1: Modules of deviceDehumidifier Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| relativeHumidity | relativeHumidity | true | See clause 5.3.64. |
| runState | runState | true | See clause 5.3.67. |
| dehumidifierJobMode | dehumidifierJobMode | true | See clause 5.3.27. |
| dehumidifierOperationMode | operationMode | true | See clause 5.3.52. This module instance is used to trigger dehumidifier operation. |
| Timer | timer | true | See clause 5.3.79. |
| powerSave | powerSave | true | See clause 5.3.58. |

### deviceDishWasher

A dish washer is a home appliance used to wash dishes. This information model provides capabilities to interact with specific functions and resources of a dish washer.

Table 5.5.15-1: Modules of deviceDishWasher Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| dishWasherJobMode | dishWasherJobMode | true | See clause 5.3.28. |

### deviceDoor

A deviceDoor is a device that is used to open and close a door.

Table 5.5.16-1: Modules of deviceDoor model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | true | See clause 5.3.51. |
| doorlock | lock | true | See clause 5.3.47. |
| doorStatus | doorStatus | true | See clause 5.3.28. |

### deviceDoorLock

A door lock is a device that can be used to lock, for example, a door.

Table 5.5.17-1: Modules of deviceDoorLock Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| doorLock | lock | false | See clause 5.3.47. |
| doorStatus | doorStatus | true | See clause 5.3.28. |
| battery | battery | true | See clause 5.3.10. |

### deviceElectricVehicleCharger

An electric vehicle charger is a device that is used for charging or discharging electric vehicles.

Table 5.5.18-1: Modules of deviceElectricVehicleCharger Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | false | See clause 5.3.33. |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | false | See clause 5.3.67. |
| battery | battery | false | See clause 5.3.10. |
| electricVehicleConnector | electricVehicleConnector | false | See clause 5.3.30. |

### deviceFan

A fan is a device that is used to monitor or control the state of a fanning device.

Table 5.5.19-1: Modules of deviceFan model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |

### deviceFoodProbe

A food probe is a device that is used to measure the internal temperature of food.

Table 5.5.20-1: Modules of deviceFoodProbe model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| temperature | temperature | false | See clause 5.3.76. |

### deviceFreezer

A freezer is a large container like a fridge in which the temperature is kept below freezing point, so that food can be stored inside of it for long periods. This freezer information model provides capabilities to monitor freezer specific functions and resources.

Table 5.5.21-1: Modules of deviceFreezer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| temperature | temperature | false | See clause 5.3.76. |

### deviceGlucosemeter

A glucometer is a device that can be used to monitor the blood glucose level.

Table 5.5.22-1: Modules of deviceGlucoseMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| glucometer | glucometer | false | See clause 5.3.37. |
| battery | battery | false | See clause 5.3.10. |

### deviceHeartRateMonitor

A heart rate monitor is a device that can be used to monitor the heart rate.

Table 5.5.23-1: Modules of deviceHeartRateMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | false | See clause 5.3.60. |
| battery | battery | false | See clause 5.3.10. |

### deviceHomeCCTV

A home CCTV is a smart home appliance to provide monitoring capabilities when people stay away from their home or a room, or to monitor the environmental status of their home or room.

Table 5.5.24-1: Modules of deviceHomeCCTV Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| sessionDescription | sessionDescription | false | See clause 5.3.69. |
| playerControl | playerControl | true | See clause 5.3.57. |
| runState | runState | true | See clause 5.3.67. |
| motionSensor | motionSensor | true | See clause 5.3.49. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| ozoneMeter | ozoneMeter | true | See clause 5.3.55. |
| smokeSensor | smokeSensor | true | See clause 5.3.71. |
| acousticSensor | acousticSensor | true | See clause 5.3.1. |
| impactSensor | impactSensor | true | See clause 5.3.42. |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| alarmSpeaker | alarmSpeaker | true | See clause 5.3.7. |

### deviceHumidifier

A humidifier is a device that is used to monitor or control the state of a humidifying appliance.

Table 5.5.25-1: Modules of Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |

### deviceKettle

Kettle is a device used to boil water. It may set a desired temperature for water and may keep water warm for a desired time.

Table 5.5.26-1: Modules of deviceKettle Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| runState | runState | true | See clause 5.3.67. |
| waterStatus | liquidRemaining | true | See clause 5.3.46. |
| boilingSwitch | binarySwitch | false | See clause 5.3.12. |
| temperature | temperature | true | See clause 5.3.76. |
| keepWarm | keepWarm | true | See clause 5.3.43. |

### deviceLight

A light is a device that is used to control the state of an illumination appliance.

Table 5.5.27-1: Modules of deviceLight Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| colour | colour | true | See clause 5.3.23. |
| colourSaturation | colourSaturation | true | See clause 5.3.24. |
| brightness | brightness | true | See clause 5.3.17. |

### deviceMicrogeneration

A microgeneration is a Home Energy Management System (HEMS) device that is used to generate energy. Examples of microgeneration devices are photovoltaics device or fuel cells.

Table 5.5.28-1: Modules of deviceMicrogeneration Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| energyGeneration | energyGeneration | false | See clause 5.3.32. |

### deviceMultiFunctionPrinter

A Multi Function Printer (MFP) is an office machine which incorporates the functionality of multiple devices in one, so as to have a smaller footprint in home or office. A typical MFP may act as a combination of printer, scanner and more. This MFP information model provides capabilities to control and monitor MFP specific functions and resources.

Table 5.5.29-1: Modules of deviceMultiFunctionPrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| printerRunState | runState | false | See clause 5.3.67. |
| scannerRunState | runState | true | See clause 5.3.67. |
| autoDocumentFeeder | autoDocumentFeeder | true | See clause 5.3.9. |
| printQueue | printQueue | true | See clause 5.3.59. |

### deviceOutdoorLamp

An outdoor lamp is a smart home appliance to provide lights and information for outside of home with smart sensing capabilities such as ultraviolet sensing.

Table 5.5.30-1: Modules of deviceOutdoorLamp Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| brightness | brightness | true | See clause 5.3.17. |
| motionSensor | motionSensor | true | See clause 5.3.49. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| uvSensor | uvSensor | true | See clause 5.3.81. |
| timer | timer | true | See clause 5.3.79. The timer is used to set duration of giving lights from the moment of triggering by the "brightness" module or "motionSensor" module. |
| faultDetection | faultDetection | true | See clause 5.3.33. |

### deviceOven

An oven is a home appliance used to roast and heat food in a complete stove. This information model is applicable to different types of ovens: gas ovens, electrical ovens, steam ovens, microwave ovens, etc. This information model provides capabilities to interact with specific functions and resources of ovens.

Table 5.5.31-1: Modules of deviceOven Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. Depending on the manufacturer policies or regulations, the binary switch might only be used to turn the device off. |
| runState | runState | true | See clause 5.3.67. |
| timer | timer | true | See clause 5.3.79. |
| temperature | temperature | false | See clause 5.3.76. |

### devicePrinter

A printer is a device that is used to monitor or control the state of a printing appliance.

Table 5.5.32-1: Modules of devicePrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| printQueue | printQueue | true | See clause 5.3.59. |

### devicePulseOximeter

A pulseoximeter is a device that can be used to monitor the blood characteristics.

Table 5.5.33-1: Modules of devicePulseOxiMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | true | See clause 5.3.60. When the "oximeter" module does not exist, then the "pulsemeter" module is mandatory. |
| oximeter | oximeter | true | See clause 5.3.54. When the "pulsemeter" module does not exist, then the "oximeter" module is mandatory. |
| battery | battery | false | See clause 5.3.10. |

### deviceRefrigerator

A refrigerator is a home appliance used to store food at temperatures which are a few degrees above the freezing point of water. This information model provides capabilities to interact with specific functions and resource of refrigerators.

Table 5.5.34-1: Modules of deviceRefrigerator Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| powerSave | powerSave | true | See clause 5.3.58. |
| doorStatus | doorStatus | true | See clause 5.3.28. |
| frozenTemperature | temperature | true | See clause 5.3.76. |
| fridgeTemperature | temperature | false | See clause 5.3.76. |
| customTemperature | temperature | true | See clause 5.3.76. This module can be configured to fridge temperature or frozen temperature based on its usage by manufacturer. |
| refrigeration | refrigeration | true | See clause 5.3.63. |
| controlPanelLock | lock | true | See clause 5.3.47. |
| waterFilterInfo | filterInfo | true | See clause 5.3.34. |

### deviceRobotCleaner

A robot cleaner is an autonomous robotic vacuum cleaner that has intelligent programming and a limited vacuum cleaning system. This robot cleaner information model provides capabilities to control and monitor robot cleaner specific functions and resources.

Table 5.5.35-1: Modules of deviceRobotCleaner Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| robotCleanerJobMode | robotCleanerJobMode | false | See clause 5.3.66. |
| robotCleanerOperationMode | operationMode | true | See clause 5.3.52. |
| battery | battery | true | See clause 5.3.10. |
| timer | timer | true | See clause 5.3.79. |

### deviceScanner

A scanner is a device that optically scans images, printed text, handwriting or an object, and converts it to a digital image.

Table 5.5.36-1: Modules of deviceScanner model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | false | See clause 5.3.67. |
| autoDocumentFeeder | autoDocumentFeeder | true | See clause 5.3.9. |

### deviceSecurityPanel

A security panel is a device that can change the security mode of, for example, an alarm system.

Table 5.5.37-1: Modules of deviceSecurityPanel model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| securityMode | securityMode | false | See clause 5.3.68. |

### deviceSetTopBox

A set top box is a device that in general contains a TV tuner input and displays output to a TV.

Table 5.5.38-1: Modules of deviceSetTopBox model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| audioVolume | audioVolume | true | See clause 5.3.8. |
| Channel | televisionChannel | true | See clause 5.3.75. |
| mediaInput | mediaSelect | true | See clause 5.3.48. |
| mediaOutput | mediaSelect | true | See clause 5.3.48. |

### deviceSmartElectricMeter

A smart electric meter is a metering device that is used to measure consumption data for electricity.

Table 5.5.39-1: Modules of deviceSmartElectricMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| clock | clock | true | See clause 5.3.18. |
| energyConsumption | energyConsumption | false | See clause 5.3.31. |
| energyGeneration | energyGeneration | true | See clause 5.3.32. |

### deviceSmartPlug

A smart plug is a device that can turn on and off a connected appliance.

Table 5.5.40-1: Modules of deviceSmartPlug model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| remoteControlEnable | remoteControlEnable | true | See clause 5.3.65. |

Table 5.5.40-2: Subdevice of deviceSmartPlug Device model

| Subdevice Instance Name | Subdevice Name | Optional | Description |
| --- | --- | --- | --- |
| powerOutlet0 | subDevicePowerOutlet | false | See clause 5.4.2. |
| powerOutlet1 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet2 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet3 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet4 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet5 | subDevicePowerOutlet | true | See clause 5.4.2. |

### deviceSteamCloset

A deviceSteamCloset is a home appliance that de-wrinkles, sanitizes and dries to clean fabrics similar to a dry cleaner. This information model provides capabilities to interact with specific functions and resources of the steam closet.

Table 5.5.41-1: Modules of deviceSteamCloset Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| steamClosetJobMode | steamClosetJobMode | false | See clause 5.3.74. |
| steamClosetOperationMode | operationMode | true | See clause 5.3.52. |

### deviceStorageBattery

A storage battery is a Home Energy Management System HEMS device that is used to provide the home with electrical energy.

Table 5.5.42-1: Modules of deviceStorageBattery Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| battery | battery | false | See clause 5.3.10. |

### deviceSwitch

A switch is a device that is used to control and monitor the state of power.

Table 5.5.43-1: Modules of deviceSwitch Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |

### deviceTelevision

A television (TV) is a home appliance used to show audio and visual content such as broadcasting programs and network streaming. This TV information model provides capabilities to control and monitor TV specific resources.

Table 5.5.44-1: Modules of deviceTelevision Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| audioVolume | audioVolume | true | See clause 5.3.8. |
| televisionChannel | televisionChannel | true | See clause 5.3.75. |
| playerControl | playerControl | true | See clause 5.3.57. |
| mediaInput | mediaSelect | true | See clause 5.3.48. |
| mediaOutput | mediaSelect | true | See clause 5.3.48. |

### deviceThermometer

A thermometer is a device that can be used to check, for example, the body or other temperatures.

Table 5.5.45-1: Modules of deviceThermoMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| temperature | temperature | false | See clause 5.3.76. |
| battery | battery | false | See clause 5.3.10. |

### deviceThermostat

A thermostat is used to control the ambient temperature of rooms within, for example, a house. This information model provides capabilities to interact with specific functions of thermostats.

Table 5.5.46-1: Modules of deviceThermostat Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| runState | runState | true | See clause 5.3.67. The possible values of the "supportedModes" datapoint for the thermostat device are included in clause 5.6.21. |
| timer | timer | true | See clause 5.3.79. |
| temperature | temperature | false | See clause 5.3.76. |

### deviceWaterHeater

A water heater is a device that is used to provide hot water through home facilities.

Table 5.5.47-1: Modules of deviceWaterHeater Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.33. |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.67. |
| clock | clock | true | See clause 5.3.18. |
| boiler | boiler | true | See clause 5.3.15. |
| hotWaterSupply | hotWaterSupply | true | See clause 5.3.41. |

### deviceWaterValve

A water valve is a device that is used to turn the water supply ON or OFF remotely.

Table 5.5.48-1: Modules of waterValve model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | false | See clause 5.3.51. |

### deviceWeightScaleAndBodyCompositionAnalyser

A weight scale and body composition analyser is a device that can be used to monitor the weight and body composition.

Table 5.5.49-1: Modules of deviceWeightScaleAndBodyCompositionAnalyser Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| weight | weight | false | See clause 5.3.84. |
| bodyCompositionAnalyser | bodyCompositionAnalyser | false | See clause 5.3.14. |
| bioElectricalImpedanceAnalysis | bioElectricalImpedanceAnalysis | false | See clause 5.3.13. |
| battery | battery | false | See clause 5.3.10. |

### deviceWindowShade

The window shade is an appliance that provides the ability to cover windows. This device type includes but not limited to roller shades, drapes, and tilt-only blinds.

Table 5.5.50-1: Modules of deviceWindowShade Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | false | See clause 5.3.51. |
| battery | battery | true | See clause 5.3.10. |

## Enumeration type definitions

### hd:enum3DprinterTechnology

Used for the "printType" data point of the "3Dprinter" ModuleClass.

Table 5.6.1-1: Interpretation of hd:enum3DprinterTechnology

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Fused Filament Fabrication | FFF |
| 2 | Fused Deposition Modelling | FDM |
| 3 | Digital Light Processing | DLP |
| 4 | Powder Bed & inkjet head 3D Printing | PBP |
| 5 | Photopolymer Jetting Technology | PolyJet |
| 6 | Laminated Object Manufacturing | LOM |
| 7 | Stereolithography Apparatus | SLA |
| 8 | Selective Laser Sintering | SLS |
| NOTE: See clause 5.3.1 "3Dprinter". |

### hd:enumAdfState

Used for the "currentAdfState" and "adfStates" data points of the "autoDocumentFeeder" ModuleClass.

Table 5.6.2-1: Interpretation of hd:enumAdfState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | processing |  |
| 2 | empty |  |
| 3 | jam |  |
| 4 | loaded |  |
| 5 | mispick | The product did not pick up the paper in the document feeder. |
| 6 | hatchOpen | The product hatch is open. |
| 7 | duplexPageTooShort |  |
| 8 | duplexPageTooLong |  |
| 9 | multipickDetected |  |
| 10 | inputTrayFailed |  |
| 11 | inputTrayOverloaded |  |
| NOTE: See clause 5.3.9 "autoDocumentFeeder". Negative values are reserved for vendor specific modes. |

### hd:enumAirConJobMode

Used for the "currentJobMode" and "jobModes" data point of the "airConJobMode" ModuleClass.

Table 5.6.3-1: Interpretation of hd:enumAirConJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | cool | This value is for deviceAirConditioner and indicates cool mode. |
| 2 | airDry | This value is for deviceAirConditioner and indicates air dry mode. |
| 3 | fan | This value is for deviceAirConditioner and indicates fan mode. |
| 4 | AI | This value is for deviceAirConditioner and indicates artificial intelligence mode. |
| 5 | heat | This value is for deviceAirConditioner and indicates heat mode. |
| 6 | airClean | This value is for deviceAirConditioner and indicates air clean mode. |
| 7 | ACO | This value is for deviceAirConditioner and indicates Auto Change Over mode. |
| 8 | aroma | This value is for deviceAirConditioner and indicates aroma mode. |
| NOTE: See clause 5.3.3 "airConJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumAirPurifierJobMode

Used for the "currentJobMode" and "jobModes" data points of the "airPurifierJobMode" ModuleClass.

Table 5.6.4-1: Interpretation of hd:enumAirPurifierJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normalClean | This indicates the normal mode that operates the basic function. |
| 2 | sleep | This indicates the sleep mode that turns the operating function off at the time set by a timer. |
| 3 | silent | This indicates the silent mode that generates low noise. |
| 4 | wet | This indicates the wet mode that passes the air that's already filtered through water filter once again to provide the humidification effect. |
| 5 | circulate | This indicates the circulate mode that circulates the purified air by rotating the fan on top of the air purifier. |
| 6 | dual | This indicates the dual mode that operates both the upper and lower parts of the air purifier. |
| 7 | auto | This indicates the auto mode that first measures the pollution level (e.g. good, normal, bad, very bad) and then, triggers appropriate modes based on the measured level. In case of bad and very bad condition, the rotating fan on the upper side starts its operation. |
| NOTE: See clause 5.3.5 "airPurifierJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumAlertColourCode

Used for the "light" data point of the "alarmSpeaker" ModuleClass.

Table 5.6.5-1: Interpretation of hd:enumAlertColourCode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | red | This colour indicates the alarm status. |
| 2 | green | This colour indicates the alarm has been cleared. |
| NOTE: See clause 5.3.7 "alarmSpeaker". |

### hd:enumCallState

Used for the "callState" data point in the "phoneCall" ModuleClass.

Table 5.6.6-1: Interpretation of hd:enumCallState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | hangup |  |
| 2 | calling |  |
| 3 | ringing |  |
| 4 | busy |  |
| 5 | answered |  |
| 6 | noline |  |
| NOTE: See clause 5.3.56 "phoneCall". |

### hd:enumClothesDryerJobMode

Used for the "currentJobMode" and "jobModes" data points of the "clothesDryerJobMode" ModuleClass.

Table 5.6.7-1: Interpretation of hd:enumClothesDryerJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal | Normal cycle. |
| 2 | quickDry | About half the length of a normal cycle, this setting uses high heat to dry a few items. |
| 3 | permanentPress | Slow drying with low heat helps wrinkle-free garments live up to their name and keeps the hard creases out of things that can be ironed. |
| 4 | heavyDuty | Tumbling for an extended period with high heat for sturdy items (towels, sweats, jeans). |
| 5 | delicates | A short, low-heat cycle for delicates and other items such as spandex workout gear, which loses its stretch when too much heat is used. |
| 6 | airDry | A cool-air setting for items that cannot take any heat, such as plastic tablecloths and rubber-backed rugs. |
| 7 | extendedTumble | Periodically tumbles clothes without heats for a preset amount of time after they are dry to prevent wrinkles. |
| NOTE: See clause 5.3.19 "clothesDryerJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumClothesWasherDryerJobMode

Used for "currentJobModes" and "jobModes" data points of "clothesWasherDryerJobMode" ModuleClass. Manufacturers can define their own courses by setting this value to negative values.

Table 5.6.8-1: Interpretation of hd:enumClothesWasherJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal |  |
| 2 | quick |  |
| 3 | auto |  |
| 4 | delicates |  |
| 5 | heavy duty |  |
| NOTE: See clause 5.3.21 "clothesWasherDryerJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumClothesWasherJobMode

Used for the "currentJobModes" and "jobModes " data points of the "clothesWasherJobMode" ModuleClass. Washing options such as water temperature and spin speed are decided to pre-set values upon selected washing course. Manufacturers can define their own courses by setting this value to negative values.

Table 5.6.9-1: Interpretation of hd:enumClothesWasherJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal |  |
| 2 | smallLoad |  |
| 3 | delicate |  |
| 4 | comforter |  |
| 5 | expressWash |  |
| 6 | cleanWash |  |
| 7 | kidsWear |  |
| 8 | workoutWears |  |
| NOTE: See clause 5.3.20 "clothesWashingJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumCookerHoodJobMode

Used for the "currentJobMode" and "jobModes" DataPoints of the "cookerHoodJobMode" ModuleClass.

Table 5.6.10-1: Interpretation of hd:enumCookerHoodJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Always-on | This value indicates the always-on mode which keeps running the fan for ventilation. |
| 2 | Intensive | This value indicates the intensive mode used when a large volume of cooking fume is being produced. |
| 3 | Sensor | This value indicates the sensor mode which changes fan speed depend on the volume and heat of cooking fume. |
| NOTE: See clause 5.3.25 "cookerHoodJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumDehumidifierJobMode

Used for "currentJobMode" and "jobModes" data points of the "dehumidifierJobMode" ModuleClass.

Table 5.6.11-1: Interpretation of hd:enumDehumidifierJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | smart | This value indicates the smart mode that first gets the target humidity level from user input, next detects the current relative humidity, then automatically change the dehumidity level to keep the target humidity level. |
| 2 | fast | This value indicates the fast mode that speeds the operating level up to quickly dehumidify when the humidity level is so high. It is a kind of turbo mode. |
| 3 | silent | This value indicates the silent mode that can be used when a user sleeps. It reduces the noise. |
| 4 | focus | This value indicates the focus mode that dehumidifies focusing on a particular part. |
| 5 | clothes | This value indicates the clothes mode that dehumidifies adjusting the wind direction vertically. It is normally used to dehumidify clothes. |
| NOTE: See clause 5.3.27 "dehumidifierJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumDishWasherJobMode

Used for the "currentJobMode" and "jobModes" DataPoints of the "dishWasherJobMode" ModuleClass.

Table 5.6.12-1: Interpretation of hd:enumDishWasherJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Normal wash |  |
| 2 | Intensive wash |  |
| 3 | Quick wash |  |
| 4 | Sensor wash |  |
| 5 | Eco wash |  |
| 6 | Quiet wash |  |
| 7 | Maintenance wash |  |
| NOTE: See clause 5.3.28 "dishWasherJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumDoorState

Used for the "doorState" DataPoint of "doorStatus" ModuleClass.

Table 5.6.13-1: Interpretation of hd:enumDoorState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | closed | This indicates that door is closed. |
| 2 | open | This indicates that the door is open. |
| 3 | opening | This indicates that the door is opening. |
| 4 | closing | This indicates that the door is closing. |
| 5 | stopped | This indicates that the door is in stationary state. |
| NOTE: See clause 5.3.29 "doorStatus". |

### hd:enumFoamStrength

Used for data points indicating the strength of a foam, for example, foaming milk from a coffee machine.

Table 5.6.14-1: Interpretation of hd:enumFoamStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | low |  |
| 3 | medium |  |
| 4 | high |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.35 "foaming". |

### hd:enumGeneralLevel

Used for the "soilLevel" data point of the "clothesWasherJobModeOption " ModuleClass.

Table 5.6.15-1: Interpretation of hd:enumGeneralLevel

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | light |  |
| 2 | normal |  |
| 3 | heavy |  |
| NOTE: See clause 5.3.20 "clothesWasherJobModeOption. |

### hd:enumGeneralSpeed

Used for the "spinSpeed" data point of the "clothesWasherJobModeOption" ModuleClass.

Table 5.6.16-1: Interpretation of hd:enumGeneralSpeed

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | low |  |
| 2 | medium |  |
| 3 | high |  |
| 4 | extraHigh |  |
| NOTE: See clause 5.3.22 "clothesWasherJobModeOption". |

### hd:enumGeneralTemperature

Used for the "washTemp" data point of the "clothesWasherJobModeOption" ModuleClass.

Table 5.6.17-1: Interpretation of hd:enumGeneralTemperature

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | cold | The actual temperature is defined by the manufacturer. |
| 2 | warm |  |
| 3 | hot |  |
| NOTE: See clause 5.3.22 "clothesWasherJobModeOption". |

### hd:enumGrainsLevel

Used for the "grainsRemaining" data point of the "grinder" ModuleClass. This type specifies a level for supplies that have a grain-aspect, for example the level of remaining coffee beans in the grinder part of a coffee machine, or the desired level of coffee beans in this machine.

Table 5.6.18-1: Interpretation of hd:enumGrainsLevel

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | low |  |
| 3 | medium |  |
| 4 | high |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.38 "grinder". |

### hd:enumGrindCoarseness

Used for the coarseness data points of the "grinder" ModuleClass. This type specifies the level of coarseness of a solid after grinding, for example grinded coffee beans.

Table 5.6.19-1: Interpretation of hd:enumGrindCoarseness

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | ultrafine |  |
| 2 | fine |  |
| 3 | medium |  |
| 4 | coarse |  |
| 5 | coarsest |  |
| NOTE: See clause 5.3.38 "grinder". |

### hd:enumHorizontalDirection

Used for the "horizontalDirection" and "supportedHorizontalDirection" of the "airflow" ModuleClass, indicating horizontal directions.

Table 5.6.20-1: Interpretation of hd:enumHorizontalDirection

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | auto |  |
| 2 | center |  |
| 3 | left |  |
| 4 | right |  |
| NOTE: See clause 5.3.4 "airFlow". |

### hd:enumJobStates

Used for the "currentJobState" and "jobStates" data points of the "runState" ModuleClass.

Table 5.6.21-1: Interpretation of hd:enumJobState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | aborted |  |
| 2 | cancelled |  |
| 3 | completed |  |
| 4 | paused |  |
| 5 | pending |  |
| 6 | processing |  |
| NOTE: See clause 5.3.67 "runstate". |

### hd:enumLiquidLevel

Used for the "liquidLevel" and "liquidRemaining" data points in the respective "liquidLevel" and "liquidRemaining" ModuleClasses.

Table 5.6.22-1: Interpretation of hd:LiquidLevel

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | low |  |
| 3 | medium |  |
| 4 | high |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.45 "liquidLevel" and clause 5.3.46 "liquidRemaining". |

### hd:enumMachineState

Used for the "currentMachineState" and "machineStates" data points of the "runState" ModuleClass.

Table 5.6.23-1: Interpretation of hd:enumMachineState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | idle | Machine is ready to operate |
| 2 | preActive | Machine is operating its pre-functions (ex. pre-heat) |
| 3 | active | Machine is operating its functions |
| 4 | reserved | Reservation is made by user |
| 5 | stopped | Operation is stopped/aborted by some other reasons |
| 6 | error | Error has occurred |
| 7 | diagnostic | Machine reports diagnostic information to the server |
| 8 | test | Particular functions run for test |
| 9 | maintenance | Machine is needed to maintain |
| 10 | clear | The result is not removed yet |
| 11 | charging | Machine is being charged |
| NOTE: See clause 5.3.67 "runState". |

### hd:enumOzoneStatus

Used for the "ozoneStatus" property of the "ozoneMeter" ModuleClass.

Table 5.6.24-1: Interpretation of hd:enumOzoneStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Good | For example, 0 to 0,030 ppm. |
| 2 | Normal | For example, 0,031 to 0,090 ppm. |
| 3 | Bad | For example, 0,091 to 0,150 ppm. |
| 4 | Very bad | For example, 0,151 ppm or above. |
| NOTE: See clause 5.3.55 "ozoneMeter". |

### hd:enumPlayerMode

Used for the "currentMode" and "supportedModes" data points in the "playerControl" ModuleClass.

Table 5.6.25-1: Interpretation of hd:enumPlayerMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | stop |  |
| 2 | play |  |
| 3 | pause |  |
| 4 | resume |  |
| 5 | record |  |
| 6 | rewind |  |
| 7 | fast-rewind |  |
| 8 | forward |  |
| 9 | fast-forward |  |
| 10 | searchPrevious |  |
| 11 | searchNext |  |
| NOTE: See clause 5.3.57 "playerControl". |

### hd:enumRobotCleanerJobMode

Used for the "currentJobMode" and "jobModes" data points of the "robotCleanerJobMode" ModuleClass.

Table 5.6.26-1: Interpretation of hd:enumRobotCleanerJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zigzag | The machine moves forward by going at an angle first to one side then to the other |
| 2 | sectorBase | The machine first cleans a specific sector (for example, 1 x 1 m), then moves to another sector |
| 3 | spot | The machine cleans a targeted area of about specific spot |
| NOTE: See clause 5.3.66 "robotCleanerJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumSecurityMode

Used for the "currentSecurityMode" and "securityModes" data points of the "securityMode" ModuleClass.

Table 5.6.27-1: Interpretation of hd:enumSecurityMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | active | Unit is active |
| 2 | armedAway | Unit is armed for away |
| 3 | armedInstant | Unit is armed instantly |
| 4 | armedMaximum | Unit is armed at maximum level |
| 5 | armedNightStay | Unit is armed in night stay |
| 6 | armedStay | Unit is armed in stay mode |
| NOTE: See clause 5.3.68 "securityMode". |

### hd:enumSpinLevelStrength

Used for the "spinLevelStrength" data points of the "spinLevel" ModuleClass, indicating the strength of a spinLevel.

Table 5.6.28-1: Interpretation of hd:enumSpinLevelStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | sensitive |  |
| 3 | weak |  |
| 4 | medium |  |
| 5 | strong |  |
| 6 | maximum |  |
| NOTE: See clause 5.3.73 "spinLevel". |

### hd:enumSteamClosetJobMode

Used for "currentJobMode" and "jobModes" data points of the "steamClosetJobMode" ModuleClass.

Table 5.6.29-1: Interpretation of hd:enumSteamClosetJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | reduceOdor | Using pure water, the machine helps to remove the smells on clothes. |
| 2 | steamWrinkle | The machine steams away wrinkles and also creates pant creases, as well as keep them crisp. |
| 3 | helpClean | Using pure water without chemical additives, the machine sanitizes fabrics and items that are difficult to wash. |
| 4 | gentleDry | The machine dries fragile garments without worrying about shrinkage or damage. |
| NOTE: See clause 5.3.74 "steamClosetJobMode". Negative values are reserved for vendor specific modes. |

### hd:enumSupportedMediaSources

Used for the "supportedMediaSources" data point of the "mediaSelect" ModuleClass.

Table 5.6.30-1: Interpretation of hd:enumSupportedMediaSources

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | tuner |  |
| 2 | component |  |
| 3 | composite |  |
| 4 | svideo |  |
| 5 | rgb |  |
| 6 | dvi |  |
| 7 | hdmi |  |
| 8 | displayPort |  |
| 9 | scart |  |
| 10 | externalStorage |  |
| 11 | network |  |
| NOTE: See clause 5.3.48 "mediaSelect". Negative values are reserved for vender specific sources. |

### hd:enumTasteStrength

Used for the "strength" data point of the "brewing" ModuleClass, indicating strength of a drink taste, for example coffee strength.

Table 5.6.31-1: Interpretation of hd:enumTasteStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | sensitive |  |
| 3 | medium |  |
| 4 | strong |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.16 "brewing". |

### hd:enumTone

Used for the "tone" data point of the "alarmSpeaker" ModuleClass.

Table 5.6.32-1: Interpretation of hd:enumTone

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | fire |  |
| 2 | theft |  |
| 3 | emergency |  |
| 4 | doorbell |  |
| 5 | deviceFail |  |
| NOTE: See clause 5.3.7 "alarmSpeaker". |

### hd:enumUvStatus

Used for the "uvStatus" data point of the "uvSensor" ModuleClass.

Table 5.6.33-1: Interpretation of hd:enumUvStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Good |  |
| 2 | Normal |  |
| 3 | Bad |  |
| 4 | Very Bad |  |
| 5 | Danger |  |
| NOTE: See clause 5.3.81 "uvSensor". |

### hd:enumVerticalDirection

Used for the "verticalDirection" and "supportedVerticalDirection" data points of the "airFlow" ModuleClass, indicating vertical direction.

Table 5.6.34-1: Interpretation of hd:enumVerticalDirection

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | auto |  |
| 2 | center |  |
| 3 | up |  |
| 4 | down |  |
| NOTE: See clause 5.3.4 "airFlow". |

### hd:enumWaterFlowStrength

Used for the "waterLevelStrength" data point of the "waterFlow" ModuleClass, indicating the strength of a waterflow.

Table 5.6.35-1: Interpretation of hd:enumWaterFlowStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | sensitive |  |
| 3 | weak |  |
| 4 | medium |  |
| 5 | strong |  |
| 6 | maximum |  |
| NOTE: See clause 5.3.82 "waterFlow". |

## Universal and Common Properties for Device models

Universal and common properties are defined as the specialized [objectAttibute]s of the [deviceInfo] resource in clause D.8 of TS-0001 [3]. Some properties are mandatory for all device models and called "Univeral Properties", since they are universally seen in typical device types and carry necessary information to identify each device instance. Others are optional for all device models and called "Common Properties", since they are commonly used in many device types but not always. The multiplicity of properties shall follow the definition in Table 8-2 in TS-0001 [3].

Universal and common properties are applicable to all device models. They are not repeated in the property table of each device model in clause 5.5, where only device specific properties shall be specified.

NOTE:	The instantiated values of the universal properties might be empty in case of exceptional scenarios, e.g. interworking with non-oneM2M device models.

# The Principle of Resource Mapping for Home Appliance Information Model

## Introduction

Home appliance information models which are defined in clause 5 need to be represented as resources in the oneM2M system. This clause defines the principle of resource mapping based on <flexContainer>. The individual information mapping is provided in annexes A and B.

## The Resource Mapping Rules

### Introduction

The present clause specifies the rule to map the "Home Appliance Information Model" in clause 5, to oneM2M resources.

### Resource mapping for Device model

When the AE exposes a controlling interface for a home domain device which is specified as an information model in clause 5.5, a specialization of the <flexContainer> resource shall be created as the mapping of the model following conversion rules:

Rule 1-1: Each Device model defined in clause 5.5 shall be mapped to a specialization of <flexContainer> resource with associated 'DeviceClass ID' (e.g. "org.onem2m.home.device.tv") on containerDefinition attributes.

Rule 1-2: Each entry of 'Module' table shall be mapped to child resource(s) which is mapped as a specialized <flexContainer> following the rule in clause 6.2.3 'Resource mapping for ModuleClass'.

Rule 1-3: Each 'Property' of a Device model shall be mapped to a specialized [objectAttribute] of a [deviceInfo] resource that is defined in clause D.8 of TS-0001 [3]. The specialized <flexContainer> resource of the Device model shall contain the nodeLink attribute. As defined in TS-0001 [3] and in TS-0004 [4] nodeLink is an optional attribute common to all <flexContainer> specializations. The nodelink attribute of a <flexContainer> specialization which represents a Device model links to a <node> resource that is hosted on the same hosting CSE as the <flexContainer>. That <node> resource shall contain as child-resource the [deviceInfo] resource of the Device model instance. The <node> resource contains all the management information as specialized <mgmtObj> resources (e.g. [firmware]) about the Device model instance for different management purposes.

Rule 1-4: XSD file for each Device model shall be named according to the following naming convention:
'HD-<name of Device model>-v<version of TS>.xsd'
For example, XSD file for 'deviceAirConditioner' as defined in TS-0023v3.7.0 is named as 'HD-deviceAirConditioner-v3_7_0.xsd'.

### Resource mapping for ModuleClass

The ModuleClass models (in clause 5.3) shall be mapped to the specializations of <flexContainer> resource. The following rules shall be applied.

When the Device model in clause 5.5 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with a ModuleClass in the model, a <flexContainer> resource which is mapped from ModuleClass definitions shall be created as a child resource:

Rule 2-1: The ModuleClass ID shall be specified on the containerDefinition attribute (e.g. "org.onem2m.home.moduleclass. audiovolume").

Rule 2-2: Each entry of 'Action', 'Property', and 'DataPoint' in ModuleClass definitions shall be mapped following the resource mapping rules for them.

Rule 2-3: XSD file for each ModuleClass shall be named following naming convention:
'HD-mod-<name of ModuleClass>-v<version of TS>.xsd'
For example, the XSD file for 'binarySwitch' is named as 'HD-mod-binarySwitch-v1_0_0.xsd. The Device model which refer any ModuleClass shall include the XSD of the ModuleClasses.

### Resource mapping for Action

When the Device model in clause 5.5 or the ModuleClass model in clause 5.3 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with the Action in the model, a <flexContainer> resource which is mapped from the Action definition shall be created as a child resource:

Rule 3-1: The Action ID shall be specified on the containerDefinition attribute (e.g. "org.onem2m.home.moduleclass.audiovolume.upvolume").

Rule 3-2: When the Action supports any 'Arguments' or 'Return Type', they are mapped to [customizedAttribute] with its variable names.

Rule 3-3: XSD file for each Action shall be named following naming convention:
'HD-act-<name of Action>-v<version of TS>.xsd'. 
For example, XSD file for 'toggle' is named as 'HD-act-toggle-v1_0_0.xsd'. The device or ModuleClass which refers any Action shall include the XSD of the Action.

Rule 3-4: When the Action does not support any 'Argument' or 'Return Type', the Action shall be triggered by updating with null Content parameter.

### Resource mapping for Property

When the Device model (in clause 5.5) or the ModuleClass model (in clause 5.3) is mapped to the <flexContainer> resource, and if the device supports a Property, the following rules shall be applied:

Rule 4-1: Each entry of 'Property' table in ModuleClass model, shall be mapped to the [customAttribute] of <flexContainer> resource which is mapped from associated ModuleClass model, with its Property name with prefix 'prop'.

Rule 4-2: Each 'Property' of a Device model is mapped to a specialized [objectAttribute] of a [deviceInfo] resource following Rule 1-3.

### Resource mapping for DataPoint

When the ModuleClass model (in clause 5.3) is mapped to the <flexContainer> resource, and if the ModuleClass supports a DataPoint, the following rules shall be applied:

Rule 5-1: Each entry of DataPoint table in ModuleClass model, shall be mapped to [customAttribute] of <flexContainer> resource which is mapped from associated ModuleClass model, with its DataPoint name.

### Resource mapping for SubDevice model

When the AE exposes a controlling interface for a home domain sub-device which is specified as an information model in clause 5.4, a specialization of the <flexContainer> resource shall be created as the mapping of the model following conversion rules:

- When the SubDevice model in clause 5.4 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with a SubDevice in the model, a <flexContainer> resource which is mapped from SubDevices definitions shall be created as a child resource.

- Rule 7-1: Follow rules 1-1, 1-2, and 1-3 of clause 6.2.2 "Resource mapping for Device model".

- Rule 7-2: The XSD file for each SubDevice model shall be named following naming convention:

'HD-<name of SubDevice model>-v<version of TS>.xsd'

For example, the XSD file for 'subDeviceCuff is named as 'HD-subDeviceCuff-v1_0_0.xsd'.

- Rule 7-3: If there is more than one SubDevice with the same name, then the SubDevices are numbered by appending an incrementing integer, starting with 0. Example:

'HD-subDeviceCuff0-v1_0_0.xsd','HD-subDeviceCuff1-v1_0_0.xsd', 'HD-subDeviceCuff3-v1_0_0.xsd'.

## Short names

### Introduction

XML and JSON representations require the explicit encoding of the names of resource attributes, (in the case of XML) and resource types. Whenever a protocol binding transfers such a name over a oneM2M reference point, it shall use a shortened form of that name. Short names enable payload reduction on involved telecommunication interfaces.

The mapping between the full names and their shortened form is given in the clauses that follow.

### Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3DPrinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |

In protocol bindings resource type names for SubDevice model shall be translated into short names of Table 6.3.2-2.

Table 6.3.2-2: Specialization type short names (SubDevice models)

| Resource Type Name | Short Name |
| --- | --- |
| cuff0 | cuff0 |
| cuff1 | cuff1 |
| cuff2 | cuff2 |
| cuff3 | cuff3 |
| cuff4 | cuff4 |
| cuff5 | cuff5 |
| powerOutlet0 | powO0 |
| powerOutlet1 | powO1 |
| powerOutlet2 | powO2 |
| powerOutlet3 | powO3 |
| powerOutlet4 | powO4 |
| powerOutlet5 | powO5 |
| subDeviceCuff | suDCf |
| subDevicePowerOutlet | sDPOt |

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-3.

Table 6.3.2-3: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| 3DPrinter | thDPr |
| acousticSensor | acoSr |
| airCleanOperationMode | aCOM0 |
| airConJobMode | aCJMe |
| airConOperationMode | aCOMe |
| airFlow | airFw |
| airPurifierJobMode | aPJMe |
| airPurifierOperationMode | aPOMe |
| airQualitySensor | aiQSr |
| alarmSpeaker | alaSr |
| audioVolume | audVe |
| autoDocumentFeeder | auDFr |
| battery | bat |
| binaryObject | binOt |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| bodyCompositionAnalyser | boCAr |
| boiler | boilr |
| boilingSwitch | boiSh |
| brewing | brewg |
| brewingSwitch | breSh |
| brightness | brigs |
| channel | chanl |
| clock | clock |
| clothesDryerJobMode | cDJMe |
| clothesDryerOperationMode | cDOMe |
| clothesWasherDryerJobMode | cWDJM |
| clothesWasherDryerOperationMode | cWDOM |
| clothesWasherJobMode | cWJMe |
| clothesWasherJobModeOption | cWJMO |
| clothesWasherOperationMode | cWOMe |
| colour | color |
| colourSaturation | colSn |
| controlPanelLock | coPLk |
| cookerHoodJobMode | cHJMe |
| credentials | creds |
| customTemperature | cusTe |
| dehumidifierJobMode | deJMe |
| dehumidifierOperationMode | deOMe |
| dishWasherJobMode | dWJMe |
| doorLock | dooLk |
| doorlock | doork |
| doorStatus | dooSs |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| filterInfo | filIo |
| foaming | foamg |
| fridgeTemperature | friTe |
| frozenTemperature | froTe |
| geoLocation | geoLn |
| glucometer | glucr |
| grinder | grinr |
| heatingZone | heaZe |
| heatingZone0 | heaZ0 |
| heatingZone1 | heaZ1 |
| heatingZone2 | heaZ2 |
| heatingZone3 | heaZ3 |
| heatingZone4 | heaZ4 |
| heatingZone5 | heaZ5 |
| height | heigt |
| hotWaterSupply | hoWSy |
| impactSensor | impSr |
| keepWarm | keeWm |
| keypad | keypd |
| liquidLevel | liqLl |
| liquidRemaining | liqRg |
| lock | lock |
| mediaInput | medIt |
| mediaOutput | medOt |
| mediaSelect | medSt |
| milkFoaming | milFg |
| milkQuantity | milQy |
| milkStatus | milSs |
| motionSensor | motSr |
| numberValue | numVe |
| openLevel | opeLl |
| operationMode | opeMe |
| overcurrentSensor | oveSr |
| oximeter | oximr |
| ozoneMeter | ozoMr |
| phoneCall | phoCl |
| playerControl | plaCl |
| powerSave | powS0 |
| printerRunState | prRSe |
| printQueue | priQe |
| pulsemeter | pulsr |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| remoteControlEnable | reCEe |
| robotCleanerJobMode | rCJMe |
| robotCleanerOperationMode | rCOMe |
| runState | runSe |
| scannerRunState | scRSe |
| securityMode | secMe |
| sessionDescription | sesDn |
| signalStrength | sigSh |
| sleepTimer | sleTr |
| smokeSensor | smoSr |
| sphygmomanometer | sphyr |
| spinLevel | spiLl |
| steamClosetJobMode | sCJMe |
| steamClosetOperationMode | sCOMe |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage | texMe |
| timer | timer |
| turbo | turbo |
| uvSensor | uveSr |
| waterFilterInfo | waFIo |
| waterFlow | watFw |
| waterSensor | watSr |
| waterStatus | watSs |
| weight | weigt |

In protocol bindings resource type names for actions shall be translated into short names of Table 6.3.2-4.

Table 6.3.2-4: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| activateClockTimer | acCTr |
| answer | answr |
| call | call |
| close | close |
| deactivateClockTimer | deCTr |
| decrementNumberValue | deNVe |
| downChannel | dowCl |
| downVolume | dowVe |
| hangup | hangp |
| incrementNumberValue | inNVe |
| nextTrack | nexTk |
| open | open |
| previousTrack | preTk |
| resetNumberValue | reNVe |
| resetTextMessage | reTMe |
| start3Dprint | staDt |
| stop3Dprint | stoDt |
| toggle | togge |
| upChannel | uphCl |
| upVolume | upoVe |

### Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |

In protocol bindings resource attributes names for data points of module classes shall be translated into short names of Table 6.3.3-2.

Table 6.3.3-2: Resource attribute short names (ModuleClass data points)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| acousticStatus | acousticSensor | acoSs |
| adfStates | autoDocumentFeeder | adfSs |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| altitude | geoLocation | altie |
| automode | airFlow | autoe |
| availableChannels | televisionChannel | avaCs |
| basalMetabolism | bodyCompositionAnalyser | basMm |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bmi | bodyCompositionAnalyser | bmi |
| bodyLength | bodyCompositionAnalyser | bodLh |
| bone | bioElectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| callerID | phoneCall | calID |
| callState | phoneCall | calSe |
| capacity | battery | capay |
| ch2o | airQualitySensor | ch2o |
| channelId | televisionChannel | chaId |
| channelName | televisionChannel | chaNe |
| charging | battery | charg |
| chargingCapacity | electricVehicleConnector | chaCy |
| co | airQualitySensor | co |
| co2 | airQualitySensor | co2 |
| coarseness | grinder | coars |
| code | faultDetection, filterInfo | code |
| coldWash | clothesWasherJobModeOption | colWh |
| colourSaturation | colourSaturation | colSn |
| concentration | glucometer | concn |
| contextCarbohydratesAmount | glucometer | coCAt |
| contextCarbohydratesSource | glucometer | coCSe |
| contextExercise | glucometer | conEe |
| contextHealth | glucometer | conHh |
| contextLocation | glucometer | conLn |
| contextMeal | glucometer | conMl |
| contextMedication | glucometer | conMn |
| contextTester | glucometer | conTr |
| cupsNumber | brewing | cupNr |
| current | energyConsumption | currt |
| currentAdfState | autoDocumentFeeder | cuASe |
| currentDate | clock | curDe |
| currentJobMode | airConJobMode, airPurifierJobMode, clothesDryerJobMode, clothesWasherDryerJobMode, clothesWasherJobMode, cookerHoodJobMode, dehumidifierJobMode, dishWasherJobMode, robotCleanerJobMode, steamClosetJobMode | cuJMe |
| currentJobModeName | airConJobMode, airPurifierJobMode, clothesDryerJobMode, clothesWasherDryerJobMode, clothesWasherJobMode, cookerHoodJobMode, dehumidifierJobMode, dishWasherJobMode, robotCleanerJobMode, steamClosetJobMode | cJMNe |
| currentJobState | runState | cuJSe |
| currentMachineState | runState | cuMSe |
| currentPlayerMode | playerControl | cuPMe |
| currentPlayerModeName | playerControl | cPMNe |
| currentSecurityMode | securityMode | cuSMe |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| currentTimeZone | clock | cuTZe |
| currentValue | smokeSensor | crv |
| defaultValue | numberValue, textMessage | defVe |
| defrost | refrigeration | defrt |
| description | faultDetection | dc |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | overcurrentSensor, smokeSensor | detTe |
| diastolicPressure | sphygmomanometer | diaPe |
| discharging | battery | discg |
| dischargingCapacity | electricVehicleConnector | disCy |
| doorState | doorStatus | dooSe |
| duration | overcurrentSensor, recorder | dur |
| electricEnergy | battery | eleEy |
| energy | pulsemeter | enery |
| estimatedTimeToEnd | timer | eTTEd |
| extraRinse | clothesWasherJobModeOption | extRe |
| fat | bioElectricalImpedanceAnalysis | fat |
| fatFreeMass | bodyCompositionAnalyser | faFMs |
| filterLifetime | filterInfo | filLe |
| foamingStrength | foaming | foaSh |
| frequency | energyConsumption | freqy |
| generationSource | energyGeneration | genSe |
| grainsRemaining | grinder | graRg |
| green | colour | green |
| hash | binaryObject | hash |
| hba1c | glucometer | hba1c |
| heading | geoLocation | headg |
| headingAccuracy | geoLocation | heaAy |
| heatingLevel | heatingZone | heaLl |
| height | height | heigt |
| horizontalAccuracy | geoLocation | horAy |
| horizontalDirection | airFlow | horDn |
| impactDirectionHorizontal | impactSensor | imDHl |
| impactDirectionVertical | impactSensor | imDVl |
| impactLevel | impactSensor | impLl |
| impactStatus | impactSensor | impSs |
| impedance | bodyCompositionAnalyser | impee |
| jobModes | airConJobMode, airPurifierJobMode, clothesWasherDryerJobMode, clothesWasherJobMode, cookerHoodJobMode, dehumidifierJobMode, dishWasherJobMode, robotCleanerJobMode steamClosetJobMode | jobMs |
| jobStates | runState | jobSs |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keyNumber | keypad | keyNr |
| latitude | geoLocation | latie |
| level | battery | lvl |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining | liqRg |
| lock | lock | lock |
| loginName | credentials | logNe |
| longitude | geoLocation | longe |
| loudness | acousticSensor | louds |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| machineStates | runState | macSs |
| material | battery | matel |
| maxHeatingLevel | heatingZone | maHLl |
| maxLength | textMessage | maxLh |
| maxLevel | openLevel | maxLl |
| maxSpeed | airFlow | maxSd |
| maxValue | audioVolume, numberValue, ozoneMeter, temperature | maxVe |
| meanPressure | sphygmomanometer | meaPe |
| measuringScope | energyConsumption | meaSe |
| mediaID | mediaSelect | medID |
| mediaName | mediaSelect | medNe |
| mediaType | mediaSelect | medTe |
| memorySize | 3DPrinter | memSe |
| messageEncoding | textMessage | mesEg |
| minLength | textMessage | minLh |
| minLevel | openLevel | minLl |
| minSpeed | airFlow | minSd |
| minValue | numberValue, temperature | minVe |
| modality | pulsemeter | moday |
| monitoringEnabled | airQualitySensor | monEd |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muscleMass | bodyCompositionAnalyser | musMs |
| muteEnabled | audioVolume | mutEd |
| network | 3DPrinter | netwk |
| numberValue | numberValue | numVe |
| object | binaryObject | objet |
| objectType | binaryObject | objTe |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| openLevel | openLevel | opeLl |
| overcurrentStatus | overcurrentSensor | oveSs |
| oxygenSaturation | oximeter | oxySn |
| ozoneStatus | ozoneMeter | ozoSs |
| ozoneValueMG | ozoneMeter | ozVMG |
| ozoneValuePPM | ozoneMeter | oVPPM |
| password | credentials | pwd |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| preWash | clothesWasherJobModeOption | preWh |
| printingState | printQueue | priSe |
| printSizeX | 3DPrinter | priSX |
| printSizeY | 3DPrinter | priSY |
| printSizeZ | 3DPrinter | priSZ |
| printType | 3DPrinter | priTe |
| progressPercentage | runState | proPe |
| pulseRate | pulsemeter | pulRe |
| pushed | pushButton | pushd |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall | recID |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| remoteControlEnabled | remoteControlEnable | reCEd |
| resistance | bioElectricalImpedanceAnalysis | resie |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rr | pulsemeter | r0 |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sdp | sessionDescription | sdp |
| securityModes | securityMode | secMs |
| sensitivity | motionSensor | sensy |
| sensorHumidity | airQualitySensor | senHy |
| sensorOdor | airQualitySensor | senOr |
| sensorPM1 | airQualitySensor | sePM1 |
| sensorPM10 | airQualitySensor | sePM0 |
| sensorPM2 | airQualitySensor | sePM2 |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject | size |
| smokeThreshold | smokeSensor | smoTd |
| softLeanMass | bodyCompositionAnalyser | soLMs |
| soilLevel | clothesWasherJobModeOption | soiLl |
| speed | airFlow | speed |
| speedFactor | playerControl | speFr |
| speedWash | clothesWasherJobModeOption | speWh |
| spinLevelStrength | spinLevel | spLSh |
| spinSpeed | clothesWasherJobModeOption | spiSd |
| startPause | operationMode | staPe |
| status | boiler, electricVehicleConnector, faultDetection, filterInf, mediaSelect | sus |
| steamTreat | clothesWasherJobModeOption | steTt |
| step | numberValue | step |
| stepValue | audioVolume, openLevel, temperature | steVe |
| strength | brewing | streh |
| supportedHorizontalDirection | airFlow | suHDn |
| supportedMediaSources | mediaSelect | suMSs |
| supportedMessageValues | textMessage | suMVs |
| supportedPlayerModes | playerControl | suPMs |
| supportedVerticalDirection | airFlow | suVDn |
| systolicPressure | sphygmomanometer | sysPe |
| targetAltitude | geoLocation | tarAe |
| targetDuration | timer | tarDn |
| targetLatitude | geoLocation | tarLe |
| targetLongitude | geoLocation | tarL0 |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshold | temperatureAlarm | temTd |
| textMessage | textMessage | texMe |
| time | keepWarm | time |
| token | credentials | tk |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| uri | printQueue | ur0 |
| url | sessionDescription | ur1 |
| useGrinder | grinder | useGr |
| uvStatus | uvSensor | uvtSs |
| uvValue | uvSensor | uvaVe |
| verticalAccuracy | geoLocation | verAy |
| verticalDirection | airFlow | verDn |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voc | airQualitySensor | voc |
| voltage | battery | volte |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| washTemp | clothesWasherJobModeOption | wasTp |
| water | bioElectricalImpedanceAnalysis | water |
| waterFlowStrength | waterFlow | waFSh |
| weight | weight | weigt |

## containerDefinition values

### Introduction

Each specialization has a containerDefinition attribute which can be used as a unique identifier and contains the information of the resource. In this clause, the detailed values of containerDefinition attributes in every specialization for the home appliance information models are given.

### Device models

The containerDefinition attribute of specializations for device models shall have the values that comply with the following rule.

Rule: "org.onem2m.home.device.[device name]"

For example, the containerDefinition attribute of specialization for deviceAirConditioner shall be "org.onem2m.home.device.deviceAirConditioner".

### ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values that comply with the following rule.

Rule: "org.onem2m.home.moduleclass.[moduleclass name]"

For example, the containerDefinition attribute of specialization for alarmSpeaker shall be "org.onem2m.home.moduleclass.alarmSpeaker".

### Actions

The containerDefinition attribute of specializations for actions shall have the values that comply with the following rule.

Rule: "org.onem2m.home.moduleclass.[name of moduleclass that the action belongs to].[action name]"

For example, the containerDefinition attribute of specialization for activateClockTimer in the timer ModuleClass shall be "org.onem2m.home.moduleclass.timer.activateclocktimer".

## XSD definitions

### Introduction

The present clause specifies how to name the files which define data types in XSD for Device models, ModuleClass, and Actions.

Generation process of XSD file is explained in annex A using some examples.

### XSD definitions for Device models

The XSD definitions for Device models are specified upon the following rule.

Rule: HD-[device name]-v<TS-version>.xsd where the string '<TS-version>' shall be interpreted as the version of the present document

For example, the XSD definition for deviceAirConditioner specified in TS-0023 v3.3.0 shall be "HD-deviceAirConditioner-v3_3_0.xsd".

### XSD definitions for ModuleClass

The XSD definitions for ModuleClass are specified upon the following rule.

Rule: HD-mod-[ModuleClass name]-v<TS-version>.xsd where the string '<TS-version>' shall be interpreted as the version of the present document

For example, the XSD definition for alarmSpeaker specified in TS-0023 v3.3.0shall be "HD-mod-alarmSpeaker-v3_3_0.xsd".

### XSD definitions for Action

The XSD definitions for Actions are specified upon the following rule.

Rule: HD-act-[action name]-v<TS-version>.xsd where the string '<TS-version>' shall be interpreted as the version of the present document

For example, the XSD definition for activateClockTimer specified in TS-0023 v3.3.0 shall be "HD-act- activateClockTimer -v3_3_0.xsd".

### XSD definitions for SubDevices

The XSD definitions for SubDevices are specified upon the following rule.

Rule: HD-[SubDevice name]-v<TS-version>.xsd where the string '<TS-version>' shall be interpreted as the version of the present document

For example, the XSD definition for subDeviceCuff specified in TS-0023 v3.3.0 shall be "HD-subDeviceCuff-v3_3_0.xsd".

# Mapping with Other Information Models from External Organizations

## Introduction

This clause specifies how the Home Appliance Information Model (HAIM) defined in the clause 5 of the present document can be mapped with existing external models from OCF, ECHONET, OMA GotAPI, etc. and introduction of these models is written in annex B. The mapping shall be to enable the interworking between the oneM2M system and external technologies at the information model level. This means a oneM2M native application which understand only oneM2M standardized HAIM shall be able to interact with non-oneM2M home appliances of different technologies in a consistent way without knowing the technology specific details. An IPE shall be responsible for translating the HAIM to/from technology specific information model bidirectionally following the mapping specification in this clause. Using HAIM as a bridge, home appliances and applications of different technologies shall be able to also interact with each other via the oneM2M system (with IPEs).

## OMA GotAPI(DWAPI)

### Introduction

The following clauses are intended to specify the mapping relationship between HAIM and OMA DWAPI with tables.

OMA DWAPI (Device Web Application Programming Interface) [6] is based on OMA GotAPI (Generic Open Terminal Application Programming Interface) [17] and supports Personal Healthcare Devices (DWAPI-PCH) and 3D printer (DWAPI-3DP).

OMA DWAPI has no concept that corresponds to ModuleClass in oneM2M. The mappings of DataPoints to data objects of OMA DWAPI are expressed in following clauses.

### Device Models

#### device3Dprinter

The device3Dprinter of HAIM shall be mapped to 3D printer of OMA DWAPI-3DP on the basis of Table 7.2.2-1.

Table 7.2.2-1: Map of device3Dprinter of oneM2M HAIM to OMA DWAPI-3DP

| ModuleClass | Data Points of oneM2M HAIM | data objects of OMA DWAPI-3DP |  | Description |
| --- | --- | --- | --- | --- |
| binarySwitch | powerState | - |  | See clause 5.3.12. The powerState is not supported in OMA DWAPI-3DP data object. The power state is assumed power-on in OMA DWAPI-3DP. |
| faultDetection | code | operatingStatus |  | See clause 5.3.33. It shall be the integer type at HAIM, but shall be the string type at OMA DWAPI-3DP. See Table 7.2.2-2. |
| 3Dprinter | printType | printType |  | See clause 5.3.1. |
|  | printSizeX | printSizeX |  |  |
|  | printSizeY | printSizeY |  |  |
|  | printSizeZ | printSizeZ |  |  |
|  | network | network |  |  |
|  | memorySize | memorySize |  |  |
| runState | currentMachineState | operatingStatus |  | See clause 5.3.67. This value represents the machineState of the 3D printer itself. This value SHALL be interpreted by using hd:enumMachineState and generated operatingStatus as a string. See Table 7.2.2-2. |
| temperature | currentTemperature | nozzleTemp |  | See clause 5.3.76. This value represents the temperature of the nozzle. This value SHALL be a float number in a range from 0,0 to 1 000,0. The unit is C. |
| printQueue | uri | uri |  | See clause 5.3.59. |
|  | printingState | msg |  | See clause 5.3.59. This value represents the machineState of the queued printing job. This value shall be interpreted by using hd:enumMachineState and generated msg as a string. See the Table 7.2.2-3. |

Table 7.2.2-2: Map of hd:enumMachineState of oneM2M HAIM to operatingStatus of OMA DWAPI-3DP

| Value | Interpretation | operatingStatus of OMA DWAPI-3DP | Note |
| --- | --- | --- | --- |
| 1 | idle | RDY | Ready to use |
| 2 | preActive |  | Not available |
| 3 | active | RUN | Under printing operation |
| 4 | reserved |  | Not available |
| 5 | stopped |  | Not available |
| 6 | error | MAN | Maintenance needed |
| 7 | diagnostic |  | Not available |
| 8 | test |  | Not available |
| 9 | maintenance | MAN | Maintenance needed |
| 10 | clear | CLR | Printing completed but the result is not removed yet |
| 11 | charging |  | Not available |

Table 7.2.2-3: Map of hd:enumJobState of oneM2M HAIM to msg of OMA DWAPI-3DP

| Value | Interpretation | msg of OMA DWAPI-3DP | Note |
| --- | --- | --- | --- |
| 1 | aborted |  | Not available |
| 2 | cancelled |  | Not available |
| 3 | completed | Completed |  |
| 4 | paused | Waiting |  |
| 5 | pending | Waiting |  |
| 6 | processing | Good Start |  |

#### deviceBloodPressureMonitor

DeviceBloodPressureMonitor of HAIM shall be mapped to Blood Pressure Monitor of OMA DWAPI-PCH [7] on the basis of Table 7.2.2-4.

Table 7.2.2-4: Map of deviceBloodPressureMonitor of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | Data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| sphygmomanometer | diastolicPressure | diastolic | See clause 5.3.72. |
|  | systolicPressure | systolic |  |
|  | meanPressure | mean |  |
| pulsemeter | pulseRate | pulse | See clause 5.3.60 |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0,0, 1,0] at OMA DWAPI-PCH. |

#### deviceGlucosemeter

DeviceGlucometer of HAIM shall be mapped to Glucometer of OMA DWAPI-PCH [8] on the basis of Table 7.2.2-5.

Table 7.2.2-5: Map of deviceGlucometer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | Data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| glucometer | concentration | concentration | See clause 5.3.37. |
|  | hba1c | hba1c |  |
|  | contextExercise | contextExercise |  |
|  | contextMedication | contextMedication |  |
|  | contextCarbohydratesAmount | contextCarbohydrates |  |
|  | contextCarbohydratesSource | contextCarbohydrates |  |
|  | contextMeal | contextMeal |  |
|  | contextLocation | contextLocation |  |
|  | contextTester | contextTester |  |
|  | contextHealth | contextHealth |  |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0,0, 1,0] at OMA DWAPI-PCH. |

#### devicePulseOximeter

DevicePulseOximeter of HAIM shall be mapped to Pulse Oximeter of OMA DWAPI-PCH [10] on the basis of Table 7.2.2-6.

Table 7.2.2-6: Map of devicePulseOximeter of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | Data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | modality | spo2, pulse | See clause 5.3.60. When oximeter module does not exist, pulsemeter module is mandatory. |
| oximeter | modality | spo2, pulse | See clause 5.3.54. When pulsemeter module does not exist, oximeter module is mandatory. |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0,0, 1,0] at OMA DWAPI-PCH. |

#### deviceThermometer

DeviceTermometer of HAIM shall be mapped to Thermometer of OMA DWAPI-PCH [11] on the basis of Table 7.2.2-7.

Table 7.2.2-7: Map of deviceThermometer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | Data Points of oneM2M HAIM | Data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| temperature | unit | temperature | See clause 5.3.76. |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0,0, 1,0] at OMA DWAPI-PCH. |

#### deviceWeightScaleAndBodyCompositionAnalyser

DeviceWeightScaleAdBodyCompositionAnalyser of HAIM shall be mapped to Weight Scale Body Composition Analyser of OMA DWAPI-PCH [12] on the basis of Table 7.2.2-8.

Table 7.2.2-8: Map of deviceWeightScaleAdBodyCompositionAnalyser of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | Data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| bodyCompositionAnalyser | bodyLength | bodyLength | See clause 5.3.14. |
|  | Bmi | bmi |  |
|  | fatFreeMass | fatFreeMass |  |
|  | softLeanMass | softLeanMass |  |
|  | muscleMass | muscleMass |  |
|  | basalMetabolism | basalMetabolism |  |
|  | impedance | impedance |  |
| weight | weight | bodyMass | See clause 5.3.84. |
| bioElectricalImpedanceAnalysis | water | bodyWater | See clause 5.3.13. |
|  | fat | bodyFat |  |
|  | muscle | musclePercentage |  |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0,0, 1,0] at OMA DWAPI-PCH. |

#### deviceHeartRateMonitor

DeviceHeartRateMonitor of HAIM shall be mapped to Heart Rate Monitor of OMA DWAPI-PCH [9] on the basis of Table 7.2.2-9.

Table 7.2.2-9: Map of deviceHeartRateMonitor of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | Data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | pulseRate | rate | See clause 5.3.60. |
|  | rr | rr |  |
|  | energy | energy |  |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0,0, 1,0] at OMA DWAPI-PCH. |

### Data Types

Data types of oneM2M HAIM and OMA DWAPI-PCH shall be mapped each other on the basis of Table 7.2.3-1.

Table 7.2.3-1: Map of data types between oneM2M and OMA DWAPI-PCH

| oneM2M data type | Mapping to data type in OMA DWAPI | Description |
| --- | --- | --- |
| xs:integer | int, number, string | Data type for 32-bit signed integer. For indicating 3D printerState, the integer value should be interpreted into string by referring the tables in clause 7.2.2.1. |
| xs:string | string, array | Data type for text. The length limitation should be considered for the mapping. |
| xs:float | float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 [13] as the float primitive type. |
| xs:boolean | boolean | Data type for Boolean. |

# Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology

Table 8-1 shows a mapping of the Home Appliance Information Model to the oneM2M Base Ontology in oneM2M TS-0012 [i.5].

The table only shows mapping of SDT concepts that are used to classify all concepts in the Home Appliance Information Model. Therefore, since any concept in the Home Appliance Information Model can be classified according to a specific SDT concept it also (transitively) maps to the related class of the oneM2M Base Ontology.

Table 8-1: Mapping between SDT concepts in the Home Appliance Information Model 
and the oneM2M Base Ontology

| SDT Concept in the Home Appliance Information Model | Mapping relationship | Class in Base Ontology | Property in Base Ontology | Comment |
| --- | --- | --- | --- | --- |
| SDT: Device | sub-class of | Device |  |  |
| SDT: SubDevice | sub-class of | Device |  | The base ontology allows a Device to consist of (sub-) Devices |
| SDT: Action | sub-class of | Operation |  |  |
| SDT: Args (of an Action) | sub-class of | OperationInput |  |  |
| SDT: ReturnType (of an Action) | sub-class of | OperationOutput |  |  |
| SDT: Event | sub-class of | Operation |  |  |
| SDT: Data (of an Event) | sub-class of | OutputDataPoint |  |  |
| SDT: Module | sub-class of | Service |  | The base ontology allows a Service to have subServices. Each SDT:Module implements one SDT:ModuleClass Therefore SDT:Module can be considered a subclass of SDT:ModuleClass and therefore subclass of oneM2M:Service See note |
| SDT: ModuleClass | sub-class of | Service |  | See note |
| SDT: UnitOfMeasure | sub-class of | MetaData |  |  |
| SDT: DataPoint | sub-class of | InputDataPoint |  | If SDT:DataPoint is writable |
| SDT: DataPoint | sub-class of | OutputDataPoint |  | If SDT:DataPoint is readable |
| SDT: Property (of a Device) | sub-class of | ThingProperty |  |  |
| SDT: Property (of a ModuleClass) | sub-class of | Aspect |  | Aspect (of the Functionality) |
| SDT: SimpleType | sub-property of |  | hasDataType | The base ontology's SimpleTypeVariable class has data properties: hasDataType hasDataRestriction |
| SDT: Constraint | sub-property of |  | hasDataRestriction |  |
| NOTE: In RESTful technologies the Service (i.e. the electronic representation of a Functionality in a network) is implicitly bound to its Functionality by the naming of the used resources (e.g. the Functionality of ModuleClass "AudioVolume" is implemented as a Service through CRUD operations on a [audioVolume] <flexContainer> specialization). |

Annex A (informative): 
Resource Mapping Examples

# Introduction

The AE may construct oneM2M resource tree on hosting CSE as the mapping of associated device, and each XSD definition for the device information models is generated following 'Resource Mapping Rule' in clause 6.2.

The present clause explains how to use the oneM2M resource tree to map Device model for each device (see clause 5.5).

# Example for Device model 'deviceAirConditioner'

The present clause explains the creation process for the device typed 'deviceAirConditioner' (see clause 5.5.1 for device model definition of 'deviceAirConditioner').

Using the definition, 'deviceAirConditioner' model is mapped to [deviceAirConditioner] resource which is a specialization of <flexContainer> resource (See Figure A.2-1).

Figure A.2-1: Structure of [deviceAirConditioner] resource

The AE creates the [deviceAirConditioner] specialization of <flexContainer> resource for the Device model [deviceAirConditioner] resource.

The [deviceAirConditioner] resource contains the child resource specified in Table A.2-1.

Table A.2-1 : Child resources of [deviceAirConditioner] resource

| Child Resources of [deviceAirConditioner] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <flexContainer> as defined in the specialization [binarySwitch] | 0..1 | This resource is used to map 'binarySwitch' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [runState] | 0..1 | This resource is used to map 'runState' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airConJobMode] | 0..1 | This resource is used to map 'airConJobMode' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airConOperationMode] | 0..1 | This resource is used to map 'airConOperationMode' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airCleanOperationMode] | 0..1 | This resource is used to map 'airCleanOperationMode' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [temperature] | 0..1 | This resource is used to map 'temperature' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [timer] | 0..1 | This resource is used to map 'timer' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [sleepTimer] | 0..1 | This resource is used to map 'sleepTimer' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [turbo] | 0..1 | This resource is used to map 'turbo' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airFlow] | 0..1 | This resource is used to map 'airFlow' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [powerSave] | 0..1 | This resource is used to map 'powerSave' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airQualitySensor] | 0..1 | This resource is used to map 'airQualitySensor' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [filterInfo] | 0..1 | This resource is used to map 'filterInfo' ModuleClass defined in clause 5. |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [3]. |

The [deviceAirConditioner] resource contains the attributes specified in Table A.2-2.

Table A.2-2: Attributes of [deviceAirConditioner] resource

| Attributes of [deviceAirConditioner] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| stateTag | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3]. |
| creator | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [3]. |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.device.airconditioner". |
| ontologyRef | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [3]. |
| contentSize | 1 | RO | See clause 9.6.35 in oneM2M TS-0001 [3]. |
| nodeLink | 1 | RO | nodeLink attribute links to a <node> resource that is hosted on the same hosting CSE of the <flexContainer>. See clauses 6.2.2 and 6.2.5 for more details. |

# Example of ModuleClass 'binarySwitch'

The [binarySwitch] resource is used to share information regarding the modelled binary switch module as a ModuleClass. The [binarySwitch] resource is a specialization of the <flexContainer> resource.

Figure A.3-1: Structure of [binarySwitch] resource

The [binarySwitch] resource contains the child resource specified in Table A.3-.

Table A.3-1: Child resources of [binarySwitch] resource

| Child Resources of [binarySwitch] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <flexContainer> as defined in the specialization [toggle] | 0..1 | This resource is used to map 'toggle' Action defined in clause 5.3.12. |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [3]. |

The [binarySwitch] resource contains the attributes specified in Table A.3-2.

Table A.3-2: Attributes of [binarySwitch] resource

| Attributes of [binarySwitch] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| stateTag | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| creator | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [3] |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.moduleclass.binaryswitch" |
| ontologyRef | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [3] |
| contentSize | 1 | RO | See clause 9.6.35 in oneM2M TS-0001 [3] |
| nodeLink | 0..1 | RW | Not applicable to a ModuleClass specialization. This attribute is not present in an instantiation of this resource |
| powerState | 1 | RW | See clause 5.3.12 |

# Example of Action 'toggle'

The [toggle] resource is used to share information regarding the modelled toggle as an Action. The [toggle] resource is a specialization of the <flexContainer> resource.

Figure A.4-1: Structure of [toggle] resource

The [toggle] resource contains the child resource specified in Table A.4-1.

Table A.4-1: Child resources of [toggle] resource

| Child Resources of [toggle] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [3] |

The [toggle] resource contains the attributes specified in Table A.4-2.

Table A.4-2: Attributes of [toggle] resource

| Attributes of [toggle] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| stateTag | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [3] |
| creator | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [3] |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.moduleclass.binaryswitch.toggle" |
| ontologyRef | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [3] |
| contentSize | 1 | RO | See clause 9.6.35 in oneM2M TS-0001 [3] |
| nodeLink | 0..1 | RW | Not applicable to an Action specialization. This attribute is not present in an instantiation of this resource |

Annex B (informative): 
Introduction of External Organizations' Data Models

# OMA Got API(DWAPI-PCH)

OMA GotAPI(OMA Generic Open Terminal API Framework) provides the framework to enable applications and multitype devices through GotAPI Servers and Extension Plug-Ins [5]. When APIs are implemented in Extension Plug-Ins under the GotAPI framework, these APIs are called as OMA Device WebAPIs Enabler. In case of healthcare devices, these APIs are called as OMA DWAPI-PCH(Device WebAPIs for Personal Connected Healthcare).

Healthcare devices can be a one of the smart home devices so OMA DWWAPI-PCH can have relationship with oneM2M SDT [3].

# OCF

## Introduction

OCF specifications provide a common, open connectivity framework for embedded developers that enables a common device discovery and interaction model, common data model and a robust security framework whilst abstracting away the physical connectivity hardware (and related protocols).

OCF Device Specification [i.8]defines list of smart home devices. Each smart home device contains a unique identifier and list of mandatory/optional resources. Each resource definition contains a unique identifier, identification of the default interface and other supported interfaces, list of supported methods, list of allowed actions and list of the mandatory/optional property(-ies) the resource exposes.

This clause specifies the mapping relationship between oneM2M and OCF Devices.

## Device Type Mapping

Table B.2.2-1 captures the equivalency mapping between OCF defined Device Types and oneM2M defined Devices. The minimum module sets for each oneM2M device is provided in the present document. The minimum resource sets for each OCF Device is provided in the OCF Device Specification [i.8].

Table B.2.2-1: OCF to oneM2M Device Type Mapping

| OCF Device Name | OCF Device Type | oneM2M Device |
| --- | --- | --- |
| Active Speaker | oic.d.speaker | N/A |
| Air Conditioner | oic.d.airconditioner | deviceAirConditioner |
| Air Purifier | oic.d.airpurifier | deviceAirPurifier |
| Air Quality Monitor | oic.d.airqualitymonitor | deviceAirQualityMonitor |
| Battery | oic.d.battery | deviceStorageBattery |
| Blind | oic.d.blind | deviceWindowShade |
| Camera | oic.d.camera | deviceCamera |
| Clothes Washer Dryer | oic.d.washerdryer | deviceClothesWasherDryer |
| Coffee Machine | oic.d.coffeemachine | deviceCoffeeMachine |
| Cooker Hood | oic.d.cookerhood | deviceCookerHood |
| Cooktop | oic.d.cooktop | deviceCooktop |
| Dehumidifier | oic.d.dehumidifier | deviceDehumidifier |
| Dishwasher | oic.d.dishwasher | deviceDishWasher |
| Door | oic.d.door | deviceDoor |
| Dryer (Laundry) | oic.d.dryer | deviceClothesDryer |
| Electric Vehicle Charger | oic.d.electricvehiclecharger | deviceElectricVehicleCharger |
| Electric Meter | oic.d.electricmeter | deviceSmartElectricMeter |
| Energy Generator | oic.d.energygenerator | deviceMicrogeneration |
| Fan | oic.d.fan | deviceFan |
| Food Probe | oic.d.foodprobe | deviceFoodProbe |
| Freezer | oic.d.freezer | deviceFreezer |
| Garage Door | oic.d.garagedoor | deviceDoor |
| Generic Sensor | oic.d.sensor | N/A |
| Grinder | oic.d.grinder | N/A |
| Humidifier | oic.d.humidifier | deviceHumidifier |
| Light | oic.d.light | deviceLight |
| Oven | oic.d.oven | deviceOven |
| Printer | oic.d.printer | devicePrinter |
| Printer Multi-Function | oic.d.multifunctionprinter | deviceMultiFunctionPrinter |
| Receiver | oic.d.receiver | deviceAudioReceiver |
| Refrigerator | oic.d.refrigerator | deviceRefrigerator |
| Robot Cleaner | oic.d.robotcleaner | deviceRobotCleaner |
| Scanner | oic.d.scanner | deviceScanner |
| Security Panel | oic.d.securitypanel | deviceSecurityPanel |
| Set Top Box | oic.d.stb | deviceSetTopBox |
| Smart Lock | oic.d.smartlock | deviceDoorLock |
| Smart Plug | oic.d.smartplug | deviceSmartPlug |
| Switch | oic.d.switch | deviceSwitch |
| Television | oic.d.tv | deviceTelevision |
| Thermostat | oic.d.thermostat | deviceThermostat |
| Washer (Laundry) | oic.d.washer | deviceClothesWasher |
| Water Heater | oic.d.waterheater | deviceWaterHeater |
| Water Valve | oic.d.watervalve | deviceWaterValve |
| Window | oic.d.window | N/A |

# History

| Publication history |
| --- |
| V3.7.3 | 2018-08-18 | Release 3 - Publication |

# Comments

In this case we have to use "void" since this reference was already listed in the previous version of TS-0023

Thank you for the clarification

the present document? this version does not exist in WPM.

If you intend to refer to another version of the present document, this reference should be added to clause 2.1. or 2.2.

Answer:

“the present document” but this is an example how to name the xsd. So, that was a (fictionous) version. I hope the changed text and adapted version numbers clarifies this

I have left as it was, since this is an example using the number of the document will be clearer than "the present document". I have done the same in the other clauses containing this kind of example.

Okay, thank you

Question to editHelp: How does one correctly use automatic references in Word so that tables in annexes (with different numbering scheme (A, B, …)) automatically follow this scheme?

In the first part (A.2) you have to use a field "styleref" (like you have correctly done in the rest of the document) with the appropriate heading style (in this case heading 1) add also the code "r". In the second part starting after the dash you have to use a field "seqfig" if you wish to number figures or a "seqtab" if you wish to number tables. add the code "r"+1 to start the numbering afresh. See also clause 6.9.2 of EDRs.

Thank you!