| oneM2M Technical Report |
| --- |
| Document Number | oneM2M-TR-0014-V-0.1.0 |
| Document Name: | oneM2M and AllJoyn Interworking |
| Date: | 05 DEC 2014 |
| Abstract: | This technical report indetifies interworking scenarios and its requirements between oneM2M and AllJoyn systems and analyze possible architectural solutions to address the requirements. |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© 2014, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols, abbreviations  and acronyms	4

3.1	Definitions	4

3.2	Symbols	5

3.3	Abbreviations	5

3.4	Acronyms	5

4	Conventions,	5

5	Technical Comparison of oneM2M and AllJoyn	5

5.1	Introduction to AllJoyn	5

5.1.1	Design Principle	5

5.1.2	System Architecture	6

5.1.2.1	AllJoyn System Overview	6

5.1.2.2	Network Architecture	7

5.1.2.2.1	Standalone AllJoyn Network	7

5.1.2.2.2	Remote Accessible AllJoyn Network	7

5.1.2.3	Device Architecture	8

5.1.2.4	AllJoyn System Protocol Stack	9

5.2	Technical Comparison	9

6	Scenarios for oneM2M and AllJoyn Interworking	9

History	13

# 1	Scope

This technical report describes:

- Technical comparison of oneM2M and AllJoyn Systems

- Identification of interworking scenarios between oneM2M and AllJoyn systems and the resulting new requirements on the oneM2M system

- Identification of architectural solutions to address the new requirements. These solutions will include the following aspects:

  - Functional architecture configurations

  - Resource mapping definitions

  - Procedure descriptions

- Identification of possible impact on existing oneM2M Technical Specifications as well as need for new Technical Specification

- Avoiding any overlaps with existing oneM2M work items.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2] 	AllJoyn System Description version 14.06

[i.3]	ITU-T Y.2060, Overview of the Internet of Things

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

## 3.2	Symbols

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

## 3.3	Abbreviations

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

## 3.4	Acronyms

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

# 4	Conventions,

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Technical Comparison of oneM2M and AllJoyn

## 5.1	Introduction to AllJoyn

This section describes the introduction to AllJoyn system as basic information for comparison of oneM2M and AllJoyn System. For more detail of the AllJoyn system is described in [i.2].

## 5.1.1	Design Principle

The main objectives of the AllJoyn system is to interwork between proximal IoT networks via Internet and to enable devices for the IoT within each proximal network dynamically discover and communicate over direct peer-to-peer(P2P) connection. As can be clearly seen in the figure below, devices within each proximal network can also discovery and communicate with additional cloud-based service to make use of specific functionality (e.g., remote device management).

Figure 5-1	IoT Network (From AllJoyn System Viewpoint)

NOTE: For cases where some of these devices are behind NAT, the can discover each other via some cloud-based discovery services.

## 5.1.2	System Architecture

## 5.1.2.1	AllJoyn System Overview

The AllJoyn software system is a proximity-based, P2P communication platform that can be embedded in heterogeneous distributed systems. Within each proximal network as depicted in the figure 5-2, AllJoyn-enabled devices run one or more AllJoyn applications and form a P2P AllJoyn network and an AllJoyn-enabled application can be a provider (implementing services and advertising) and a consumer (discovering interested services) or both depending on its service model.

Figure 5-2	AllJoyn Proximal Network

In the figure 5-2, the AllJoyn framework establishes an underlying bus architecture for communication among AllJoyn-enabled devices and AllJoyn Applications can advertise, discover and make use of each other’s functionality.  One of key components of the AllJoyn framework is AllJoyn router that provides core functionality of the AllJoyn framework, including P2P advertisement/discovery, connection establishment, broadcast signalling and control/data messages routing.

## 5.1.2.2		Network Architecture

The AllJoyn network can be divided into two different architecture that is dependent upon the network deployment scenarios.

## 5.1.2.2.1	Standalone AllJoyn Network

As described in the figure 1-2, this architecture is simple with two or more AllJoyn-enabled devices coming together to form an AllJoyn Network. The devices can be connected over different access networks such as Wi-Fi.

## 5.1.2.2.2	Remote Accessible AllJoyn Network

This architecture supports remote access to devices within AllJoyn proximal network so the devices are accessible and/or controllable from outside the proximal network. The remote accessibility is achieved by deploying a Gateway node in the network. The Gateway node exposes AllJoyn-enabled application’s functionality and control to cloud-based service via standardized APIs (e.g., REST) so device outside the proximal network can communicate with devices in the proximal network via the Gateway node.

For example, oneM2M IN-CSE can play the role of a cloud-based service node and MN-CSE can be installed in the Gateway node with AllJoyn framework.

Figure 5-3 Remote Accessible AllJoyn Network Architecture

## 5.1.2.3	Device Architecture

As previously stated, the AllJoyn router can be bundled with each of these applications on devices. The app supports application-specific services and one or more AllJoyn service framework. The application connects to the AllJoyn router via the AllJoyn standard core library call.

Figure 5-4 AllJoyn Device Architecture

- AllJoyn Service Framework (Base service)

AllJoyn Service Framework provides some of the basic and core functionalities as enablers for higher layer application services. This service frameworks sit on top of the AllJoyn router and provide APIs to application developer to invoke the functions. This is similar concept of CSE defined by oneM2M.

- Application Layer Service (App-specific service)

Application Layer Service provides services to achieve intended application functionality. This service can make use of the AllJoyn Service Framework. This is similar concept of AE which contains application-specific service logic.

Note that [i.2] defines the other AllJoyn device architectures such as multiple app with bundled AllJoyn router and multiple apps with standalone AllJoyn router.

## 5.1.2.4	AllJoyn System Protocol Stack

Figure 5-5 AllJoyn Protocol Stack

The AllJoyn router support multiple underlying transports for discovery and communication and provides an abstraction layer for each supported transport. Based on the definition of ITU-T Y.2060 IoT Reference Model [i.2], the AllJoyn system components belongs to Service Layer except for the app-specific services.

## 5.2	Technical Comparison

# 6	Scenarios for oneM2M and AllJoyn Interworking

Several scenarios are presented in this section. The oneM2M system may support several of these scenarios simultaneously.

In the following figures, the arrows between the AllJoyn Network or the AllJoyn enabled mobile device and the oneM2M system may use the interfaces which are the conversions of Mca/Mcc, or may be the new defined interfaces up to the solutions.

Figure 6-1 shows the scenario that the AllJoyn network is deployed in the field domain, the AllJoyn network communicates with an oneM2M Infrastructure Domain network. An AllJoyn enabled mobile device accesses the oneM2M Infrastructure Domain network and remotely controls the devices in the AllJoyn network through the oneM2M Infrastructure domain. The vertical line represents the demarcation between the field domain and the infrastructure domain.

Figure 6-1: AllJoyn enabled mobile device controls AllJoyn Network in the field domain 
through oneM2M Infrastructure Domain

In Figure 6-2 the AllJoyn network is also deployed in the field domain, the difference with the above scenario in Figure 6-1 is that An oneM2M enabled mobile device remotely controls the devices in the AllJoyn network through the oneM2M Infrastructure domain. Considering the oneM2M system may support interworking with multiple IOT technologies, i.e. there are many local networks in field domain using different IOT technologies, these local networks all have ability to interworking with an oneM2M platform for remote control. It’s possible to use multiple control applications installed in one mobile device or even multiple mobile devices  each specially for one IOT technology to remotely control the local networks,  but if we can use a generic oneM2M enabled mobile device  to remotely control the devices using different IOT technologies, it will be more efficient.

Figure 6-2: oneM2M enabled mobile device controls AllJoyn Network in the field domain
through oneM2M Infrastructure Domain

Figure 6-3 provides the scenario that two AllJoyn Network in the field domain communicates with each other through oneM2M Infrastructure Domain. One device in an AllJoyn network may need to communicate with a device in another AllJoyn network, but if the two AllJoyn networks are deployed at different location, it is impossible for them to communicate directly. If the two AllJoyn Network are both able to communicate with the oneM2M Infrastructure Domain, it’s possible for them to communicate with each other through the oneM2M Infrastructure Domain.

Figure 6-3: Two AllJoyn Network in the field domain communicates with each other 
through oneM2M Infrastructure Domain

The scenario depicts in Figure 6-4 is similar with Figure 6-3, the difference is one field domain network is AllJoyn network, the other is the oneM2M Field Domain Network, they can communicate with each other through oneM2M Infrastructure Domain.

Figure 6-4: AllJoyn Network in the field domain communicates with oneM2M field domain Network through oneM2M Infrastructure Domain

Figure 6-5 provides the scenario that an AllJoyn Network in the field domain directly communicates with an oneM2M Field Domain Network. The assumption is the two networks are deployed in the same location, thus it’s possible for them to communication with each other locally without going through the oneM2M Infrastructure Domain.

Figure 6-5: AllJoyn Network in the field domain directly communicates with oneM2M field domain Network

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

# History

| Publication history |
| --- |
| V.1.1.1 | <dd Mmm yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 29/10/2014 | Skeleton draft |
| V.0.1.0 | 05/12/2014 | Applied the following CRs: ARC-2014-1630R01-TR-0014_Introduction_to_AllJoyn ARC-2014-1641R02-Scenarios_for_OneM2M_and_AllJoyn_Interworking |