| oneM2M Technical Report |
| --- |
| Document Number | TR-0033-Study_on_Enhanced_Semantic_Enablement-V0_2_0 |
| Document Name: | Study on Enhanced Semantic Enablement |
| Date: | 2016-Dec-31 |
| Abstract: | In this study requirements on enhanced semantic enablement and approaches for addressing these requirements will be developed and discussed. The intention is to achieve agreement between the interested participants on the approaches to be pursued in oneM2M. On this basis normative contributions to Technical Specifications can then be made. |
| Template Version: 08 September 2015 (Dot not modify) |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright and the foregoing restriction extend to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	5

2	References	5

2.1	Normative references	5

2.2	Informative references	5

3	Definitions, symbols and abbreviations	5

3.1	Definitions	5

3.2	Symbols	6

3.3	Abbreviations	6

4	Conventions,	6

5	Requirements	6

5.1	Overview	6

6	Semantic modelling & ontologies	8

6.1	Introduction	8

7	Architecture for semantics	9

7.1	Introduction	9

7.2	Semantic functionality in CSFs	9

7.3	Resources related to semantics	9

7.3.1	Resource <semanticDescriptor>	9

7.3.2	Example showing the uses of the Semantic Descriptor resource	10

7.3.3 	Enhancement of Resource Type <semanticDescriptor>	12

7.3.4	Ontology Repository	14

7.4 	Implementation options	15

7.4.1	Introduction	15

7.4.2	The hierarchically layered architecture	15

7.4.2.1	Data layer as upper layer	15

7.4.2.2	Semantic layer as upper layer	16

7.4.3	The parallel architecture	17

7.5 	Approaches to Access Control	18

7.5.1	Access Control for semantic discovery, based on the ACPs in resource tree and triples in the graph store	18

7.5.1.1	Introduction	18

7.5.1.2	Solution A: Semantic filtering based on graph store	18

7.5.1.3	Solution B: Graph division based semantic filtering	24

7.5.2	Direct access control of semantic graph store	25

7.5.2.1	Introduction	25

7.5.2.2	Access control modelling in semantic graph store	25

7.5.2.3	Examples of SPARQL query procedure	28

7.5.3	Access control using temporary semantic graph stores	30

8	Semantic functionalities	33

8.1	Introduction	33

8.2	Semantic annotations	34

8.2.1	Overview	34

8.2.2	Semantic instance management	34

8.2.2.1	Overview	34

8.2.2.2	Concrete example of managing semantic instance	34

8.2.2.3	Managing semantic instances using SPARQL update operation	34

8.3 	Semantic validation	39

8.3.1	Problem statement	39

8.3.2	Proposed solution	42

8.4	Semantic filtering and discovery	43

8.5	General semantic queries	44

8.5.1	Semantic query vs. semantic resource discovery	44

8.5.2	Introduction to semantic graph scoping (SGS)	45

8.5.3	Solutions to semantic graph scoping	46

8.6	Query scopes	48

8.7	Semantic reasoning	49

8.8	Semantic mash-up	49

8.8.1	Introduction	49

8.8.1.1	Semantic mashup definition	49

8.8.1.2	Semantic mashup example: smart parking application	49

8.8.2	Problem statement	50

8.8.2.1	Entities involved in sematic mashup	50

8.8.2.2	Technical analysis of semantic mashup	50

8.8.3	Semantic Mashup Function (SMF)	51

8.8.3.1	High-level architecture	51

8.8.3.2	High-level operations	53

8.8.3.3	Functional paradigms	55

8.9	Semantics-based data analytics	55

8.10	Ontology management	55

8.11	Semantic Access Control	55

8.11.1	Synchronizing ACP information between the Resource Tree and the Semantic Graph Store.	55

8.11.2	Synchronizing SD-related triples between the Resource Tree and the Semantic Graph Store	60

8.11.2.1	Introduction	60

8.11.2.2	Procedure for Creating ACP-SD binding triples and SD relationship triples in SGS	61

8.11.2.3	Procedure for updating ACP-SD binding triples in SGS	62

8.11.2.4	Procedure for updating SD relationship triples in SGS	64

8.11.2.5	Procedure for deleting SD relationship triples and ACP-SD binding triples in SGS	65

9	Conclusions	66

Proforma copyright release text block	66

Annexes	66

History	67

# 1	Scope

The present document …

EXAMPLE:	The present document provides the necessary adaptions to the endorsed document.

The Scope shall not contain requirements.

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

As a Technical Report (TR) is entirely informative it shall not list normative references.

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

[i.2]	oneM2M TS 0002: "onM2M Requirements".

# 3	Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

If a definition is taken from an external source, use the format below where [N] identifies the external document which must be listed in Section 2 References.

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Abbreviation format

ARIB	Association of Radio Industries and Businesses

ATIS	Alliance for Telecommunications Industry Solutions

CCSA	China Communications Standards Association

ETSI	European Telecommunications Standards Institute

TIA	Telecommunications Industry Association,

TSDSI	Telecommunications Standards Development Society

TTA	Telecommunications Technology Association

TTC	Telecommunication Technology Committee

<ABBREVIATION1>	<Explanation>

<ABBREVIATION2>	<Explanation>

<ABBREVIATION3>	<Explanation>

# 4	Conventions,

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Requirements

## 5.1	Overview

Table 5.1-1 lists the requirements on Abstraction and Semantics. It is based on those identified in oneM2M TS-0002 [i.2]. As the result of the work described in this Technical Report, the original requirements have been refined, new requirements have been added and the overall consistency has been checked. The requirements have been categorized according to different key semantic aspects, i.e. semantics annotation, ontology, semantics query, semantics mashup, data analytics and semantic reasoning.

Table 5.1-1: Requirements on abstraction and semantics

| No. | Category | Requirement |
| --- | --- | --- |
| 1 | Semantics Annotation | The M2M System shall provide capabilities to manage semantic information about the oneM2M resources, e.g. create, retrieve, update, delete, associate/link. |
| 2 | Ontology | The M2M System shall support modelling semantic descriptions of Things (including relationships among them) by using ontologies. |
| 3 | Semantics Annotation | The M2M System shall support a common language for semantic description, e.g. RDF. |
| 4 | Ontology | The M2M System shall support a common modeling language for ontologies (e.g. OWL). |
| 5 | Ontology | The M2M System should be able to provide translation capabilities from different modeling languages for ontologies to the language adopted by oneM2M if the expressiveness of the imported ontology allows. |
| 6 | Semantics Query | The M2M System shall provide capabilities to discover M2M Resources based on semantic descriptions. |
| 7 | Ontology | The M2M System shall provide the capability to retrieve semantic descriptions and ontologies stored outside of the M2M System. |
| 8 | Data Analytics | The M2M System shall be able to support capabilities (e.g. processing function) for performing M2M data analytics based on semantic descriptions from M2M Applications and /or from the M2M System. |
| 9 | Semantics Mashup | The M2M system shall provide the capability to host processing functions for mash-up. |
| 10 | Semantics Mashup | The M2M system shall enable Applications to provide processing functions for mash-up. |
| 11 | Semantics Mashup | The M2M system itself may provide pre-provisioned or dynamically created processing functions for mash-up. |
| 12 | Semantics Mashup | The M2M system shall be able to create and execute mash-ups based on processing functions. |
| 13 | Semantics Mashup | The M2M system shall be able to expose mash-ups as resources e.g. virtual devices. |
| 14 | Semantics Annotation | The M2M System shall support semantic annotation of oneM2M resources for example application related data contained in containers. |
| 15 | Semantics Annotation | The M2M System shall support semantic annotation based on related ontologies. |
| 16 | Ontology | The M2M System shall provide support for linking ontologies defined in the context of the M2M system with ontologies defined outside this context. |
| 17 | Ontology | The M2M System shall be able to support extending ontologies in the M2M system. |
| 18 | Ontology | The M2M System shall be able to use ontologies that contain concepts representing aspects (e.g. a room) that are not represented by resources of the M2M System. |
| 19 | Ontology | The M2M System shall be able to re-use common ontologies (e.g., location, time ontologies, etc.) which are commonly used in M2M Applications. |
| 20 | Ontology | The M2M System shall be able to support simultaneous usage of multiple ontologies for the same M2M resource. |
| 21 | Semantics Reasoning | The M2M system shall be able to update ontologies as a result of the ontology reasoning. |
| 22 | Ontology | The M2M system shall provide the capability for making ontology available in the M2M System, e.g. through announcement. |
| 23 | Ontology | The M2M system shall be able to support mechanisms to import external ontologies into the M2M system. |
| 24 | Ontology | The M2M System shall be able to support update of ontologies. |
| 25 | Semantics Reasoning | The M2M System shall be able to support semantic reasoning e.g. ontology reasoning or semantic rule-based reasoning. |
| 26 | Semantics Reasoning | The M2M System shall be able to support adding and updating semantic information based on semantic reasoning. |
| 27 | Data Analytics | The M2M System shall provide the capability of interpreting and applying service logic (e.g. rules/policies of triggering operations upon other resources or attributes according to the change of the monitored resource) described with semantic annotation and ontology. |
| 28 | Data Analytics | The M2M system shall support a standardized format for the rules/policies used to define service logic. |
| 29 | Ontology | The M2M System shall enable functions for data conversion based on ontologies. |
| 30 | Semantics Annotation | The M2M System shall provide the capability for making semantic descriptions available in the M2M System, e.g. announcement. |
| 31 | Semantics Annotation | The M2M system shall enable applications to retrieve an ontology representation related to semantic information used in the M2M system. |
| 32 | Ontology | The M2M system shall be able to model devices based on ontologies which may be available outside the M2M system (e.g. HGI device template). |
| 33 | Ontology | The M2M System shall support storage, management and discovery of ontologies. |

Figure 5.1-1 shows dependencies and relations between the requirements listed in table 5.5-1. It can be used as a basis for prioritizing the addressing of requirements and to make sure that all preconditions are addressed first.

# Figure 5.1-1: Dependencies and relations between requirements6	Semantic modelling & ontologies

## 6.1	Introduction

<Text>

# 7	Architecture for semantics

## 7.1	Introduction

<Text>

## 7.2	Semantic functionality in CSFs

## 7.3	Resources related to semantics

### 7.3.1	Resource <semanticDescriptor>

The <semanticDescriptor> resource is used to store a semantic description pertaining to a resource and potentially sub-resources. Such a description can be provided according to ontologies. The semantic information is used by the semantic functionalities of the oneM2M system and is also available to applications or CSEs.

Resources of several types (e.g. <AE>, <container>, <contentInstance>) optionally can have one or more semantic descriptor resources. See [i.39] clause 9.6.1.1 for a complete list of resources which may have a <semanticDecriptor> child resource and [i.39] clause 8.5.2.3 for a complete description of this resource.

Figure 7.3.1-1: Structure of <semanticDescriptor> resource

The <semanticDescriptor> resource contains the child resources specified in table 7.3.1-1.

Table 7.3.1-1: Child resources of <semanticDescriptor> resource

| Child Resources of <semanticDescriptor> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See [i.39], clause 9.6.8 where the type of this resource is described. |

The <semanticDescriptor> resource contains the attributes specified in table 7.3.1-2.

Table 7.3.1-2: Attributes of <semanticDescriptor> resource

| Attributes of <semanticDescriptor> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See [i.39], clause 9.6.1.3 |
| resourceID | 1 | RO | See [i.39], clause 9.6.1.3 |
| resourceName | 1 | WO | See [i.39], clause 9.6.1.3. |
| parentID | 1 | RO | See [i.39], clause 9.6.1.3. |
| accessControlPolicyIDs | 0..1 (L) | RW | See [i.39], clause 9.6.1.3 |
| creationTime | 1 | RO | See [i.39], clause 9.6.1.3 |
| expirationTime | 1 | RW | See [i.39], clause 9.6.1.3 |
| lastModifiedTime | 1 | RO | See [i.39], clause 9.6.1.3 |
| labels | 0..1 (L) | RW | See [i.39], clause 9.6.1.3 |
| descriptor | 1 | RW | The semantic description of the resource whose child resource the <semanticDescriptor> resource is. |
| announceTo | 0..1 (L) | RW | See [i.39], clause 9.6.1.3. |
| announcedAttribute | 0..1 (L) | RW | See [i.39], clause 9.6.1.3. |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See [i.39], clause 9.6.1.3. |
| creator | 0..1 | RO | See [i.39], clause 9.6.1.3. |
| descriptorRepresentation | 1 | RW | Indicates the type used for the serialization of the descriptor attribute, e.g. RDF serialized in XML. |
| semanticOpExec | 0..1 | RW | This attribute cannot be retrieved. Contains a SPARQL query request for execution of semantic operations on the descriptor attribute e.g. SPARQL update as described in [3]. |
| descriptor | 1 | RW | Stores a semantic description pertaining to a resource and potentially sub-resources. Such a description shall be according to subject-predicate-object triples as defined in the RDF graph-based data model [4]. The encoding of the RDF triples used in oneM2M is defined in oneM2M TS-0004 [3]. The elements of such triples may be provided according to ontologies. Examples of such descriptors in RDF can be found in [i.28]. |
| ontologyRef | 0..1 | WO | A reference (URI) of the ontology used to represent the information that is stored in the descriptor attribute. If this attribute is not present, the ontologyRef from the parent resource is used if present. |
| relatedSemantics | 0..1(L) | WO | List of URIs for resources containing related semantic information to be used in processing semantic queries. The URI(s) may reference either a <group> resource or other <semanticDescriptor> resources. |

### 7.3.2	Example showing the uses of the Semantic Descriptor resource

This clause gives an example of how semantic annotations based on the Smart Appliance REFerence Ontology (SAREF) can be used to describe an AE representing a smart appliance.

Figure 7.3.2-1: Resource structure of smart washing machine AE

Figure 7.3.2-1 shows the resource structure of an AE representing a smart washing machine.

NOTE:	The assumption here is that the Washing Machine acts as an AE using the Mca interface. Here no distinction is made between the Washing Machine AE and the washing machine as a physical device. This can be done under the given assumption, but could lead to problems in other cases, e.g. if an interworking proxy is involved.

The resource includes an ontologyRef attribute, which contains the URI of the ontology concept of the smart washing machine, e.g. "http://ontology.tno.nl/saref#WashingMachine". The startStopContainer and the stateContainer represent the functional interface aspects of the washing machine, i.e. it can be started and stopped and the current state can be requested.

Table 7.3.2-1 shows the semantic annotation stored in the descriptor attribute of the semanticDescriptor resource. The information provides the link between the operations of the washing machines and the containers of the smart washing machine AE and describes the REST methods that can be executed on the containers. The washing operation can be started by executing a Create request on the startStopContainer whose URI is provided, the same for the state operation, where a Retrieve request on the latest contentInstance of the stateContainer will provide the current state of the washing machine.

Table 7.3.2-1: Semantic resource description of smart washing machine AE based on SAREF

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>LG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#StateService_123"/> </rdf:Description> <rdf:Description rdf:about="http://ontology.tno.nl/saref#WashingService_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingService"/> <msm:hasOperation rdf:resource="http://ontology.tno.nl/saref#WashingOperation_123"/> </rdf:Description> <rdf:Description rdf:about="http://ontology.tno.nl/saref#WashingOperation_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingOperation"/> <hr:hasMethod>Create</hr:hasMethod> <hr:hasURITemplate>/CSE1/WASH_LG_123/startStopContainer </hr:hasURITemplate> <msm:hasInput rdf:resource="http://ontology.tno.nl/saref#Action"/> </rdf:Description> <rdf:Description rdf:about="http://ontology.tno.nl/saref#StateService123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#StateService"/> <msm:hasOperation rdf:resource=”http://ontology.tno.nl/saref#StateOperation123"http://www.tno.com/saref#StateOperation123"/> </rdf:Description> <rdf:Description rdf:about= http://ontology.tno.nl/saref#StateOperation123> <rdf:type rdf:resource="http://ontology.tno.nl/saref#StateOperation"/> <hr:hasMethod>Retrieve</hr:hasMethod> <hr:hasURITemplate>/CSE1/WASH_LG_123/state/stateContainer/latest</hr:hasURITemplate> <msm:hasOutput rdf:resource="http://ontology.tno.nl/saref#State"/> </rdf:Description> </rdf:RDF>

Editor’s note: reference to SAREF has to be added to References.

#### 7.3.3 	Enhancement of Resource Type <semanticDescriptor>

Two additional attributes are introduced in <semanticDescriptor>: semanticValidated and validationEnable to support semantic validation capability as described in clause 8.3. See details in figure 7.3.3-1 and table 7.3.3-1.

Figure 7.3.3-1: Structure of <semanticDescriptor> resource

The <semanticDescriptor> resource shall contain the attributes specified in table 7.3.3-1.

Table 7.3.3-1: Attributes of <semanticDescriptor> resource

| Attributes of <semanticDescriptor> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| resourceID | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| resourceName | 1 | WO | See clause 9.6.1.3 in TS-0001. |
| parentID | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| creationTime | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| expirationTime | 1 | RW | See clause 9.6.1.3 in TS-0001. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in TS-0001. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in TS-0001. |
| creator | 0..1 | RO | See clause 9.6.1.3 in TS-0001. |
| descriptorRepresentation | 1 | RW | See clause 7.3.1. |
| semanticOpExec | 0..1 | RW | See clause 7.3.1 |
| descriptor | 1 | RW | See clause 7.3.1 |
| ontologyRef | 0..1 | WO | See clause 7.3.1 |
| relatedSemantics | 0..1(L) | WO | See clause 7.3.1 |
| semanticValidated | 0..1 | RW | A Boolean value representing the validation status of the triples in the descriptor attribute. The validation is against the referenced ontology as pointed by the ontologyRef attribute as well as other associated <semanticDescriptor> resources (and their referenced ontologies) linked by relatedSemantics attribute and triples in the descriptor attribute. | OA |
| validationEnable | 0..1 | RW | A Boolean value indicating whether the triples in the descriptor attribute needs to be validated by the hosting CSE | OA |

Editor’s note: reference to TS-0001 has to be added to References.

#### 7.3.4	Ontology Repository

An Ontology Repository is capable of storing multiple ontologies in the unified languages adopted by the M2M system, e.g. RDFS/OWL. For easy illustration of the examples, in this clause its is assumed that the M2M system adopts RDFS/OWL in describing ontologies. Figure 7.3.4-1 provides an example of Ontology Repository with the oneM2M Base Ontology, SSN and Saref ontologies represented by individual resources.

This structure provides support for re-use of existing ontologies, the ability to access both internal and external ones and for ontology import into the system. It also allows to fulfil the requirements for ontology discovery, as well as addition and updates, via CRUD operations.

Figure 7.3.4-1: Ontology Repository example

Resources of type <CSEBase> and <AE> optionally can have one Ontology Repository resource.The ontology resource is further described in clause 7.3.z.

Editor’s note: Contribution for adding clause 7.3.z in TR-0033 is needed.

The Ontology Repository resource may also contain a (virtual) sub-resource <semanticValidation> as the inferface to accept semantic validation requestion from an <AE> or a remote <CSE>. Upon receiving a Update request with <semanticDescriptor> resource representation addressing the <semanticValidation> sub-resource, the hosting CSE performs the semantic validation procedures as described in clause 8.3

## 7.4 	Implementation options

Editor’s Note: An example for such an implementation option is the use of a Semantic Repository, e.g. providing SPARQL support as part of a CSE implementation.

### 7.4.1	Introduction

The efficiency of queries, semantic resource discovery and access control for sematic information depend on the underlying implementation. In this clause architectural and implementation perspectives are presented.

### 7.4.2	The hierarchically layered architecture

While the current oneM2M architectural view is exclusively based on resources, these can be implemented in different ways. Especially for managing semantic triples, triple stores are the straightforward choice. This has implications for how the access control to resources and triples is handled. In this clause different implementation options are discussed assuming a hierarchical structuring into a semantic layer and a data layer.

As shown in figures 7.4.2.1-1and 7.4.2.2-1, data resources and semantic triples may be integrated in a hierarchically layered architecture. In the hierarchical model the Upper Layer provides an interface for RESTful operations, controls and manages the Access Control Policies (ACPs). The Lower Layer supports the upper layer with specific services.

From a functional perspective there are two layers: aData Layer containing the data resources and related functions and a Semantic Layer containing semantic triples and related semantic functions.  Each functional Layer may be used as either the Upper Layer or the Lower Layer  as detailed later in this clause.

The layers may reside on different CSEs, but integration on the same CSE may be more performance efficient.

#### 7.4.2.1	Data layer as upper layer

In figure 7.4.2.1-1 the Upper Layer is the Data Layer and the Lower Layer is the Semantic Layer which provides the Upper Layer with semantic information.

There are three alternatives for implementation of the Semantic Layer as the Lower Layer:

- Using Semantic Descriptors distributed in the oneM2M Resource Tree, which corresponds to the Release 2 data resource driven approach.

- Using permanent Sematic Graph Stores, which may be distributed or centralized.

- In a hybrid option, using temporary Semantic Graph Stores  together with the distributed resource model to provide support for semantic functionality e.g. in Release 2.

Figure 7.4.2.1-1 shows a typical data resource driven approach for M2M scenarios. Resource Discovery through the data resource tree may be supported by the semantic leaves (i.e. distributed graph stores) in the Semantic Layer. The ACPs are maintained under <semanticDescriptor> resources in the Data Layer. Further description for the Access Control methods in this architecture are provided in clause 7.5.

Figure 7.4.2.1-1: Hierarchically layered structure - controlled by the data layer

#### 7.4.2.2	Semantic layer as upper layer

In figure 7.4.2.2-1, the Upper Layer is the Semantic Layer and the Lower Layer is the Data Layer supporting the upper layer with raw data. The main implementation of the Sematic Layer as an Upper Layer is using Sematic Graph Stores. Further description for the Access Control methods in this architecture are provided in clause 7.5.

NOTE: In the following clauses the terms “Semantic Graph Stores” and “Triple Stores” are used interchangeably.

Figure 7.4.2.2-1: Hierarchically layered structure -
controlled by the semantic layer

Figure 7.4.2.2-1 shows a typical semantics driven scheme for Semantic Web scenarios. Semantic Query may be conducted in the Semantic Layer with the return of the URI or URL of the data resources in the Data Layer. Semantic Resource Discovery may also be realized with the return of the data resources in the Data Layer via proper mapping between these two layers. The triples in the Semantic Layer are associated with their specific ACPs. A data resource in the Data Layer is addressed by a triple (e.g. via its URI or URL) associated with the ACP.

### 7.4.3	The parallel architecture

Looking beyond the currently supported semantic functionality, a more advanced architecture may be needed. In the following clause the concepts of Data Entity and Semantic Entity are introduced. These concepts may be used in different configurations, supporting more advanced semantic functionality like semantic mash-up and the possible interaction with other semantic platforms like the semantic web.

Figure 7.4.3-1 shows a parallel architecture with distinct entities, i.e. a Data Entity and a Semantic Entity.

A Data Entity and/or a Semantic Entity may each have its own Access Control Policies (ACPs) for managing the access control within its scope.

The semantic triples or data resources in the Data Entity may be exposed to the Semantic Entity with specific ACPs associated. For example:

- a Semantic Publication function in the Data Entity may expose semantic triples to the Central Graph Store in Semantic Entity with the corresponding ACPs associated with the triples; or

- a Data Annotation function in the Data Entity may expose data and associated ACPs to the Central Graph Store via the local temporary or caching Relational Data Base Management System (RDBMS) and Semantic Reasoning and Mapping functions in Semantic Entity.

The data resources or semantic triples in the Semantic Entity may also be exposed to the Data Entity with specific ACPs associated. For example:

- a Semantic Mash-up function in the Semantic Entity may expose new data resources and related ACPs from the semantic mash-up to the Data Entity; or

- a Semantic Annotation function in the Semantic Entity may expose semantic triples and related ACPs to the <semanticDescriptor> resources in the Data Entity.

Figure 7.4.3-1: Access control in a parallel structure

Figure 7.4.3-1 shows that a Data Entity and a Semantic Entity may reside on different CSEs. But a Data Entity and a Semantic Entity may also reside on the same CSE. Figure 7.4.3-2 shows a logical resource tree with both a Data Entity and a Semantic Entity.

Figure 7.4.3-2: Logic resource tree with both a data entity and a semantic entity

## 7.5 	Approaches to Access Control

### 7.5.1	Access Control for semantic discovery, based on the ACPs in resource tree and triples in the graph store

#### 7.5.1.1	Introduction

Implementing access control for semantic related functionalities (e.g. semantic resource discovery, semantic query) based on the ACPs in resource tree can be seen as an attractive approach since the compatibility with existing resource tree ACPs will be kept.

#### 7.5.1.2	Solution A: Semantic filtering based on graph store

In the solution descriptions below, some assumptions are considered.

- There is a centralized graph store to store the triples in all <semanticDescriptor>s.

- Based on the query request with a target URL in the resource tree, the scope of the query is limited to the triples in both the <semanticDescriptor>s as child resources in the sub-tree under the target URL and the relevant <semanticDescriptor>s  linked to the <semanticDescriptor>s  under the target URL.

Editor’s note: the extensions of this solution for other cases (e.g. distributed graph stores) may be further considered.

In solution A, the triples in the <semanticDescriptor>s will be stored in one graph of a graph store. To retain the effect of ACPs in resource tree, the <semanticDescriptor>is used as the anchor to link the ACPs in resource tree and the access control during the query on semantic repository. The procedure of the solution A are described as follows.

- Pre-steps before semantic query process:

01) The CSE hosting the Graph store creates an internal ontology with class SemanticDescriptor and atomDescription, and the property describedIn, hasSubject   hasObject and hasProperty

02)  For each <semanticDescriptor>with ACP in resource tree(s), the CSE hosting the graph store creates corresponding semantic descriptor instances in the semantic graph store using IRI/URL of the respective <semantic Descriptor>.  The semantic descriptor instances are the instances of the predefined class SemanticDescriptor.

03)  The CSE hosting the graph store adds triples in semantic graph store to associate the semantic triples in the <semanticDescriptor>s in resource tree with the created semantic descriptor instances. The triples in the <semanticDescriptor>s in the resource tree(s) of other CSEs should be notified to the CSE hosting the graph store.

Considering that one subject can be described in multiple <semanticDescriptor>s with different ACPs, the association should be implemented  with each triple for classification, and  the association triples are added based on each triple described in the <semanticDescriptor>. Figure 7.5.1.2-1 shows the association between the triple and the semantic descriptor instance.

Figure 7.5.1.2-1: Association between the triple and the SemanticDescriptor instance

For example, for the triple in <semanticDescriptor> A as classX  property Y  classZ,  the following association triples are needed to be added. These association triples are termed “SD Relationship Triples”

atomDescriptionA   hasSubject   classX

atomDescriptionA   hasObject  classX

atomDescriptionA hasproperty classZ

atomDescriptionA  describedIn  SemanticDescriptorA

- The process after receiving the semantic query request with SPARQL statement.

- The receiver CSE finds the <semanticDescriptor>s where the Originator (AE ID or CSE ID) is allowed to use for querying based on the ACPs in resource tree and the target URL in the request.

- The receiver CSE identifies the corresponding SemanticDescriptor instances (same IRI/URL with the <semanticDescriptor>) in the semantic graph store.

- In the received original SPAQRL semantic query statements, the receiver CSE adds new sentences to indicate that the target variable triples are associated with the identified SemanticDescriptor (i.e. new SD Relationship Triples) instances as follows:

- find the variables and their relevant triples in the SPARQL query

- create atomdescription variables for each triple with variables in the query,

- associate the atomdescription variables  with each triple with variables in the query,

- add the sentence to associate the atomdescription variables and the identified SemanticDescriptor instances.

Figure 7.5.1.2-2 shows the association between the triple with variables and the SemanticDescriptor instances.

Figure 7.5.1.2-2: Association between the triple with variables in SPARQL query and the SemanticDescriptor instances

For example, for the original SPAQRL query

SELECT ?device ?operation

WHERE {

?device rdf:type m2m:WashMachine.

?device m2m:hasOperation ?operation.

}

If the allowed SemanticDescriptor  instance is SemanticDescriptorA,  then the modified SPAQRL query is given as

SELECT ?device ?operation

WHERE {

?device rdf:type m2m:WashMachine.

?device m2m:hasOperation ?operation.

?atom1 temp:hasSubject ?device.

?atom1 temp:hasObject ?operation

?atom1 temp:hasProperty m2m:hasOperation

?atom2 temp:hasSubject ?device

?atom2 temp:hasObject m2m:WashMachine

?atom2 temp:hasProperty rdf:type

?atom1  temp:desribedIn SemanticDescriptorA(IRI/URL).

?atom2  temp:desribedIn SemanticDescriptorA(IRI/URL).

}

- The receiver CSE sends the modified SPARQL semantic query statement to the CSE hosting the graph store for querying the graph store.

- The receiver CSE compose Response according to the semantic query results feedback from the CSE hosting the graph store.

In the following part, we give a complete example to explain solution A. The considered resource tree is shown in Figure 7.5.1.2-3 where three <semanticDescriptor> (SD) resources are involved.

Figure 7.5.1.2-1: Considered resource tree in the example

The triples in SD-1, SD-2 and SD-3 are assumed as follows.

SD-1

HomeA  rdf:type  ex:Home

HomeA  ex:hasLocation  LocationA

LocationA  ex:hasLatitude    “300”

LocationA  ex:hasLongitude  “200”

SD-2

DeviceA rdf:type  m2m:TemperatureSensor

DeviceA ex:hasLocation LocationA

There is a link to SD-1 in SD-2 that indicates Location(class) related information can be retrieved from SD-1.

SD-3

DeviceB rdf;type ex:DoorLock

DerviceB ex:hasLocation  LocationA

The CSEA hosts the graph store. The triples in the graph store will include all the triples in the<semanticDescriptor>, and there will be 4 additional triples (i.e. SD Relationship Triples) for each triple in the<semanticDescriptor>. The total additional triples are given as follows.

For SD-1

atom1 temp:hasSubject  HomeA

atom1 temp:hasObject  ex:Home

atom1 temp:hasProperty rdf:type

atom1 temp:describedIn SD-1

atom2 temp:hasSubject  HomeA

atom2 temp:hasObject  LocationA

atom2 temp:hasProperty ex:hasLocation

atom2 temp:describedIn SD-1

atom3 temp:hasSubject  LocationA

atom3 temp:hasObject  “300”

atom3 temp:hasProperty ex:Latitude

atom3 temp:describedIn SD-1

atom4 temp:hasSubject  LocationA

atom4 temp:hasObject  “200”

atom4 temp:hasProperty ex:hasLongtitude

atom4 temp:describedIn SD-1

For SD-2

atom5 temp:hasSubject  DeviceA

atom5 temp:hasObject  m2m:TemperatureSensor

atom5 temp:hasProperty rdf:type

atom5 temp:describedIn SD-2

atom6 temp:hasSubject  DeviceA

atom6 temp:hasObject  LocationA

atom6 temp:hasProperty ex:hasLocation

atom6 temp:describedIn SD-2

For SD-3

atom7 temp:hasSubject  DeviceB

atom7 temp:hasObject  m2m:DoorLock

atom7 temp:hasProperty rdf:type

atom7  temp:describedIn SD-3

atom8  temp:hasSubject  DeviceB

atom8  temp:hasObject  LocationA

atom8  temp:hasProperty ex:hasLocation

atom8  temp:describedIn SD-3

It is assumed that an originator sends the query request in which the target URL is the URL of AppA and SPARQL query filter is

SELECT ?device

WHERE {

?device ex:hasLocation ?Location.

?Location ex:hasLatitude ?val1.

?Location ex:hasLagitude ?val2.

FILTER(?val1==”300” && ?val2 ==”200”)

}

When receiving this query request, the CSEA will first identify the scope of the <semanticDescriptor>s related to the query as follows.

1)  find that there are  two SDs, i.e. SD-2 and SD-3, under the target URL, and then check the ACPs linked to these SDs and find that only SD-2 is allowed to be used by the originator in the query.

2)  find that there is a link (e.g. relatedSemantics attribute of  <semanticDescriptor>) in the SD-2 to SD-1 for the class Location, and then check the original SPARQL query and find that class Location is involved.

3)  check the ACP linked to SD-1 and find that SD-1 is not allowed to be used by the originator in the query.

After identifying the scope of the <semanticDescriptor>s (SD_2) related to the query, the CSEA revises the original SPARQL query as

SELECT ?device

WHERE {

?device ex:hasLocation ?Location.

?Location ex:hasLatitude ?val1.

?Location ex:hasLagitude ?val2.

?agtom1 temp:hasSubject ?device.

?atom1 temp:hasObject ?Location.

?atom1 temp:hasProperty ?hasLocation.

?atom2 temp:hasSubject ?Location.

?atom2 temp:hasObject ?val1.

?atom2 temp:hasProperty ex:hasLatitude.

?atom3 temp:hasSubject ?Location.

?atom3 temp:hasObject ?val2.

?atom3 temp:hasProperty ex:hasLongitude

?atom1 temp:describedIn SD-2

?atom2 temp:describedIn SD-2

?atom3 temp:describedIn SD-2

FILTER(?val1==”300” && ?val2 ==”200”)

}

The CSEA applies the revised SPARQL query to the graph store, and return the result.

The returned result is none device.

#### 7.5.1.3	Solution B: Graph division based semantic filtering

In the solution descriptions below, some assumptions are considered.

- There is a centralized graph store to store the triples in all <semanticDescriptor>s.

- The returned information for query request is in the scope of the triples in all possible <semanticDescriptor>s. The scope may contain more triples (i.e. from <semanticDescriptor>s  not explicitely linked to the  <semanticDescriptor>s under the original target URL) compared with solution A.

Editor’note: the extensions of this solution for other cases (e.g. distributed graph stores)  may be further considered.

In solution B,  the triples in the <semanticDescriptor>s will be stored in separated graphs in the graph store. There are two options for the graph division.

- Option 1

Store the triples in the same <semanticDescriptor> in a graph.

- Option 2

Store the triples in the semantic descriptors linked to the same ACP in a graph

For Option 1, there will be many graphs in the graph store and the query speed will be slow when the query across the union of a lot of graphs,  but each graph of Option 1 is not necessary to be updated with the update of ACPs. For Option 2, the number of graphs will be small but it needs the synchronization between the graphs and the ACPs.

The procedure of solution B is simple.

- Pre-step

- The CSE hosting the graph store stores the triples in the separated graphs of graph store as Option 1 or Option 2.

- The ACP information related to <semanticDescriptor>s in the resource tree(s) of other CSEs should be  notified to the CSE hosting the graph store.

- Query-step

The query request will be forwarded from the receiver CSE to the CSE hosting the graph store for query.

For Option 1:

After receiving the forwarded request, the CSE hosting the graph store will

- Find the  <semanticDescriptor> which is allowed to be used in the query according to the ACP.

- Identify the graphs that correspond to the found <semanticDescriptor> in the previous step.

- Apply the SPARQL query on the union of the identified graphs

- Return the query result

For Option 2:

After receiving the forwarded request, the CSE hosting the graph store will

- Identify the access permissions of the Originator of the original request before forwarding – according to ACPs, and find the relevant ACPs that includes the Originator to have discovery permissions.

- Identify the graphs that corresponds to the found ACPs in the previous step.

- Apply the SPARQL query on the union of the identified graphs.

- Return the query results

### 7.5.2	Direct access control of semantic graph store

#### 7.5.2.1	Introduction

As described in previous sub-clauses 7.5.1.2 and 7.5.1.3, <accessControlPolicy> specified by the accessControlPolicyIDs attribute of <semanticDescriptor> may be used for access control in the Semantic Graph Store when executing SPARQL operations as a part of semantic queries. One approach is to implement access control policies directly in the Semantic Graph Store, which makes it more efficient and scalable to control the access to a centralized Semantic Graph Store -. This approach may contain the following main steps with the following assumptions: 1) There is a centralized Semantic Graph Store; 2) The proposed approach will be used for semantic query over this centralized Semantic Graph Store; 3) Each semantic query matches all semanticDescriptors but not cross multiple semanticDescriptors; 4) There is a need for synchronization of access control policies between the CSE and the Semantic Graph Store.

- Construct Access Control Rules specified by <accessControlPolicy> in the Semantic Graph Store. Note that <accessControlPolicy> is specified by the accessControlPolicyIDs attribute of <semanticDescriptor> resource.

- Associate targeted Semantic Triples (i.e. RDF triples as described by the descriptor attribute of <semanticDescriptor> but stored in the Semantic Graph Store) with their accessControlPolicyIDs or <accessControlPolicy> with related Access Control Rules.

- Semantic triple operations are conducted with the selected semantic triples which are associated with the Access Control Rules allowing the Originator to operate.

Figure 7.5.2.1-1 below gives an example of access control policy for two <semanticDescriptor> resources, where there are two access control policies (i.e. <accessControlPolicy1> and <accessControlPolicy2>). The access to <semanticDescriptor1> is controlled by <accessControlPolicy1> and <accessControlPolicy2>, while the access to <semanticDescriptor2> is only controlled by <accessControlPolicy2>.

Figure 7.5.2.1-1: Example of access control policy for <semanticDescriptor>

#### 7.5.2.2	Access control modelling in semantic graph store

Examples for access control modelling in the Semantic Graph Store are shown in figure 7.5.2.2-1, figure 7.5.2.2-2, figure 7.5.2.2-3, and figure 7.5.2.2-4.

The Access Control Ontology shown in figure 7.5.2.2-1 defines two new classes: accessControlPolicy and accessControlRule. In addition, five new properties (i.e. hasACPRule, hasACOriginator, hasACOperations, hasACContexts and appliedTo) are defined. hasACPRule is used to link an accessControlPolicy instance with an accessControlRule instance. Properties hasACOriginator, hasACOperations and hasACContexts (optional) basically describe an accessControlRule instance and are used to specify who can issue what operations under which conditions. As these triples describe the ACP themselves, they are termed “ACP Triples”

Property appliedTo is used to describe which <semanticDescriptor> resource an accessControlPolicy instance can be applied to .As these triples bind <accessControlPolicy> and <semanticDescriptor> they are temed “ACP-SD Binding Triples”.

Note that this ontology is defined by following how oneM2M <accessControlPolicy> resource is specified in oneM2M TS-0001, where an access-control-rule-tuple consists of parameters such as accessControlOriginators, accessControlOperations, and accessControlContexts.

Figure 7.5.2.2-1: Access control ontology model

Figure 7.5.2.2-2 shows an example of the eHealth Ontology Reference Model, which will be used to develop the Semantic Graph Store example in figure 7.5.2.2-3 and SPARQL example in figure 7.5.2.2-4.

Figure 7.5.2.2-2: eHealth ontology reference model

Figure 7.5.2.2-3 describes an example of RDF triples in the Semantic Graph Store based on the example shown in figure 7.5.2.1-1 and the Access Control Ontology defined in figure 7.5.2.2-1. In this use case, there are two patients Jack and Alice; their doctors are John and Steve, respectively. There are three blood pressure meansurement samples (i.e. Sample1 for Jack, Sample2 and Sample3 for another patient3). Corresponding triples are shown in black text in figure 7.5.2.2-3, which are generated based on the eHealth Ontology Reference Model in figure 7.5.2.2-2.

The triples in red text in figure 7.5.2.2-3 are added for access control purpose according to the proposed Access Control Ontology model in figure 7.5.2.2-1, when new ACPs are created or updated. In this example, it is assumed two access control polices be created. First, two <semanticDescriptor> are described (i.e. semanticDescriptor1 contains Sample1 and Sample2, while semanticDescriptor2 contains Sample3. Then, two access control policies are defined (i.e. accessControlPolicy1 is applied to semanticDescriptor1, while accessControlPolicy2 is applied to both semanticDescriptor1 and semanticDescriptor2). Next, the detail Access Control Rules for accessControlPolicy1 and accessControlPolicy2 are described.

- accessControlPolicy1 has two accessControlRules, which states that 1) AE-ID-1, AE-ID-2, and AE-ID-3 can RETRIEVE and DISCOVER triples in the semanticDescriptor which accessControlPolicy1 is applied to (i.e. semanticDescriptor1); 2) AE-ID-1 and AE-ID-3 can CREATE, UPDATE, or DELETE triples in the semanticDescriptor which accessControlPolicy1 is applied to (i.e. semanticDescriptor1).

- For accessControlPolicy2, only one accessControlRule is defined; this accessControlRule states that AE-ID-1 and AE-ID-2 can DISCOVER triples in the semanticDescriptor which accessControlPolicy2 is applied to (i.e. semanticDescriptor1 and semanticDescriptor2).

Figure 7.5.2.2-3: eHealth triples in semantic graph store

#### 7.5.2.3	Examples of SPARQL query procedure

When the CSE receives SPARQL query from Originator, it will add the access control related patterns according to the ID of the Originator and the request operation of the query into the received SPARQL statement, and use the revised SPARQL statement to make query on the semantic graph store.

For example, in the scenario of the example in  figure 7.5.2.2-3, when AE-ID-3 sends the following SPARQL query request to the CSE,

select distinct ?sample ?sValue ?dValue

where

{

?sample rdf:type ex:BPMeasurementSample .

?sample ex:sValue ?sValue .

?sample ex:dValue ?dValue .

}

The CSE will add some access control related statements according to the ID (i.e. AE-ID-3) of the Originator and the request operation (i.e. DISCOVERY) of the query, the revised SPARQL query can be given as:

select distinct ?sample ?sValue ?dValue

where

{

?accessControlRule acp:hasACOriginator "AE-ID-3" .

?accessControlRule acp:hasACOperations "DISCOVERY" .

?accessControlPolicy acp:hasACPRule ?accessControlRule .

?accessControlPolicy acp:appliedTo ?semanticDescriptor .

?semanticDescriptor ex:containResource ?sample .

?sample rdf:type ex:BPMeasurementSample .

?sample ex:sValue ?sValue .

?sample ex:dValue ?dValue .

}

Alternatively, using the approach which is described in the sub-clause of 7.5.1 for the association between the semantic descriptor and semantic triples, the revised SPARQL query can be given as:

select distinct ?sample ?sValue ?dValue

where

{

?accessControlRule acp:hasACOriginator "AE-ID-3" .

?accessControlRule acp:hasACOperations "DISCOVERY" .

?accessControlPolicy acp:hasACPRule ?accessControlRule .

?accessControlPolicy acp:appliedTo ?semanticDescriptor .

?atom1 temp:describedIn ?semanticDescriptor.

?atom1 temp:hasSubject ?sample.

?atom1 temp:hasObject ?sValue.

?atom1 temp:hasProperty ex:sValue.

?atom2 temp:describedIn  ?semanticDescriptor.

?atom2 temp:hasSubject ?sample.

?atom2 temp:hasObject ?dValue.

?atom2 temp:hasProperty ex:dValue.

?atom3 temp:describedIn  ?semanticDescriptor.

?atom3 temp:hasSubject ?sample.

?atom3 temp:hasObject ex:BPMeasurementSample.

?atom3 temp:hasProperty rdf:type.

}

Figure 7.5.2.3-1 shows the SPARQL query result in the above example over the eHealth Semantic Graph Store in figure 7.5.2.2-3. According to the access control triples added to the Semantic Graph Store (i.e. red text in figure 7.5.2.2-3), AE-ID-3 is only allowed to DISCOVER samples included in semanticDescriptor1 (i.e. Sample1 and Sample2). As a result, the returned result for SPAQRL query in figure 7.5.2.3-1 presents the selected content of Sample1 and Sample2.

Figure 7.5.2.3-1: Example for eHealth semantic query result with access control

### 7.5.3	Access control using temporary semantic graph stores

This section describes an implementation approach that can be used for implementing the semantic features supported in Release 2 of oneM2M. <semanticDescriptor> resources have been introduced to be able to semantically annotate oneM2M resources of certain resource types, including AE, Container, ContentInstance, FlexContainer and more. Semantic functionalities have been added for filtering and selectively updating the semantic information stored in the descriptor attribute of the <semanticDescriptor> which is represented in the form of RDF triples. The SPARQL language has been selected as the most suitable for specifying the filter and selective update operations.

For implementing the SPARQL-based semantic functionality, a SPARQL-engine is needed and such engines are typically provided on top of semantic graph stores. Thus, it is a straight-forward implementation choice to use such a semantic graph store.

<semanticDescriptor> resources as any other oneM2M resources have associated access policies which determine whether a requester is allowed to access the content of the resource. These access policies also apply for the semantic description stored in a <semanticDescriptor> resource and have to be adhered to when executing SPARQL requests on and across semantic information contained in these <semanticDescriptor> resources. So even when storing the semantic information in semantic graph stores and accessing them using SPARQL requests, the access control policies have to be applied. Approaches for translating and applying access control policies within the semantic graph store are described in other sub-clauses of clause 7.5.

In this section, we show how the SPARQL-based functionality needed for oneM2M Release 2 can be implemented using temporary semantic graph stores. For an incoming SPARQL request, the access control policies are applied when accessing the relevant <semanticDescriptor> resource(s) for populating the temporary semantic graph store. Once this has happened, the SPARQL query can be executed without further access control checks.

Figure 7.5.3-1 shows the different steps in the case of a single <semanticDescriptor> resource being accessed to enable the execution of a SPARQL request on its semantic content.

Figure 7.5.3-1: Execute SPARQL request on single <semanticDescriptor>

When receiving the request with the SPARQL content, the Hosting CSE checks the access control policy applying to the <semanticDescriptor> resource. If the originator of the request is allowed to access it, it retrieves the semantic information from its descriptor attribute, initializes the Temporary Semantic Graph Store, and populates it with the semantic information. Then it forwards the SPARQL request to the Temporary Semantic Graph Store to be executed. Note that the Temporary Semantic Graph Store in this context is seen as an implementation component and not an architectural component according to the oneM2M architecture.

Figure 7.5.3-2 shows the case that, in addition to the targeted <semanticDescriptor> resource, a set of related <semanticDescriptor> resources needs to be included before executing the SPARQL request. This is described in Clause 8.4.x and TS-0001 [i.39] Section 10.2.35.2.2. The relevant <semanticDescriptor> resources are identified through the relatedSemantics attribute.

Figure 7.5.3-2: Execute SPARQL request on <semanticDescriptor> plus those identified through relatedSemantics attribute

In addition to the steps shown in figure 7.5.3-1, the Hosting CSE attempts to retrieve the semantic content of the <semanticDescriptor> resources identified by the relatedSemantics attribute and updates the Temporary Semantic Graph Store accordingly. The respective access control policies are checked as part of the retrieval as in any other resource access. Only once all the identified (and accessible) content has been added is complete, the SPARQL request is forwarded for execution.

Figure 7.5.3-3 shows the case that the semantic content of the targeted <semanticDescriptor> resource contains links to further <semanticDescriptor> resoruces identified by resourceDescriptorLink properties. This annotation-based approach is described in Section 8.4.x and in TS-0001 [i.39], Section 10.2.35.2.1.

Figure 7.5.3-3: Execute SPARQL request on <semanticDescriptor> plus those encountered during the execution in form of resourceDescriptorLink properties

In this case, the modified SPARQL engine of the Temporary Semantic Graph Store may encounter elements with resourceDescriptorLink properties when matching variables as part of the execution of the SPARQL request. In this case the execution will be halted and the engine requests the content of the <semanticDescriptor> resource identified by the resourceDescriptorLink property before continuing execution on the merged content. This can happen 0 to n times during the execution. Note that the Temporary Semantic Graph Store is not an architectural oneM2M component and logically should be seen as part of the Hosting CSE. The semantic content is requested on behalf of the original Originator with its access rights. The advantage of the implementation with the Temporary Semantic Graph Store is that no special care has to be taken with respect to access control policies. Access control policies are evaluated in the usual way when accessing the semantic content on which the SPARQL request is to be executed. The disadvantage is of course that a Temporary Semantic Graph store has to be initialized and populated each time a SPARQL request is to be executed.

# 8	Semantic functionalities

## 8.1	Introduction

<Text>

## 8.2	Semantic annotations

### 8.2.1	Overview

As identified in the requirements, Semantic Annotation within the oneM2M platform is of key importance for supporting semantic functionalities within the oneM2M platform.

### 8.2.2	Semantic instance management

#### 8.2.2.1	Overview

The management of semantic instances stored in the <semanticDescriptor> resource is one of key semantic functionalities , including the create, update and delete operations against semantic instances. A simple way to deal with the update of semantic instances is to overwrite the whole <semanticDescriptor> resource which might lead to data redundancy problems, but a more efficient approach is needed to handle the management of semantic instances. An approach using functions e.g SPARQL HTTP POST, SPARQL HTTP PUT etc provided by SPARQL to update or create semantic instances is proposed.

##### 8.2.2.2	Concrete example of managing semantic instance

In the oneM2M system, in order to change a semantic instances in the <semanticDescriptor> resources, the system has to change the whole semantic descriptor.

Figure 8.2.2.2-1: Concrete example of managing semantic instance in the oneM2M system

##### 8.2.2.3	Managing semantic instances using SPARQL update operation

A semantic description consisting of semantic instances is contained in the <semanticDescriptor> resource. In order to manage semantic instances using the SPARQL update operation, it is assumed that the semantic description is stored in the <semanticDescriptor> resource as depicted in figure 8.2.2.3-1.

Figure 8.2.2.3-1: Representation of a semantic description in a <semanticDescripor> resource

To manage the semantic instances, the SPARQL update operation has to be mapped to the oneM2M UPDATE (U) procedure. The UPDATE procedure can be used by an AE Originator to manage the semantic instances stored in the <semanticDescriptor> resource on a Receiver CSE (also called the Hosting CSE).

Originator is responsible for sending requests to update semantic instances stored in the <semanticDescriptor> resource by using the UPDATE method.

Hosting CSE processes the update procedures against the requested semantic instances if the originator is allowed to do the update operation. Figure 8.2.2.3-2 shows the interaction between Originator and Receiver and the procedures are processed as follows.

Figure 8.2.2.3-2: Procedure for managing the semantic instances
using oneM2M UPDATE operation

Step 001: The Originator can include mandatory parameters and partial or whole optional parameters in the Request message for UPDATE operation. In Step 001, different SPARQL statements can be used in order to update (i.e. add, delete, and modify) an existing semantic description in a target <semanticDescriptior> resource at the Receiver as shown in the following cases.

- Case 1: This case is to add semantic instances (e.g., RDF, triples) to an existing semantic description in a target <semanticDescriptor> resource in the Receiver. In this case, the Originator can include INSERT DATA or INSERT SPARQL statements in a Request as shown in the block below. The INSERT DATA statement can add semantic instances using the RDF PAYLOAD to the semantic description in a target <semanticDescriptor> resource. Thus, RDF PAYLOAD in an INSERT DATA SPARQL statement disallows blank nodes or variables. On the other hand, an INSERT SPARQL statement can add semantic instances corresponding to a template by copying semantic instances from a source <semanticDescriptor> resource to a target <semanticDescriptor> resource based on a pattern. Accordingly, a template in the INSERT statement allows blank nodes or variables with conditional SPARQL statements. Examples 1 and 2 give examples using INSERT DATA and INSERT SPARQL statements, respectively.

======================== INSERT DATA statement ========================= INSERT DATA {GRAPH <Target URI of <semanticDescriptor> resource> {RDF PAYLOAD} } ========================== INSERT statement ============================ INSERT { GRAPH <Target URI of <semanticDescriptor> resource 1> {template} } WHERE {GRPAH <Target URI of <semanticDescriptor> resource 2> {pattern} }

EXAMPLE 1:	Add semantic instance to a <semanticDescriptor> resource using INSERT DATA statement:

INSERT DATA { GRAPH <http://<Hosting CSE address>/<CSEBase>/<AE>/<semanticDescriptor>> {saref:WASH_LG_123 msm:hasOperation saref:WashingOperation_123} }

EXAMPLE 2:	Add semantic instance to a <semanticDescriptor> resource using INSERT statement:

INSERT { GRAPH <http://<Hosting CSE address>/<CSEBase>/<AE>/<semanticDescriptor1>> {?a saref:hasManufacturer ?c} } WHERE { GRAPH <http://<Hosting CSE address>/<CSEBase>/<AE>/<semanticDescriptor2>> {?a saref:hasManufacturer ?c} }

- Case 2: This case is to remove any of the semantic instances from an existing semantic description in a target <semanticDescriptor> resource in the Receiver. In this case, the Originator can include two different SPARQL statements including DELETE DATA statement or DELETE statement in the Request as shown in the block below. 
The DELETE DATA statement can remove specific semantic instances using RDF PAYLOAD from an existing semantic description in a target <semanticDescriptor> resource. Hence, the RDF PAYLOAD in the DELETE DATA SPARQL statement is not allowed to contain blank nodes or variables. However, the DELETE SPARQL  statement can remove semantic instances corresponding to the template through matching semantic instances based on a pattern. Accordingly, the template in the DELETE SPARQL statement is allowed to contain blank nodes or variables with conditional SPARQL statements. Examples 3 and 4 give examples using DELETE DATA and DELETE SPARQL statements, respectively.

======================== DELETE DATA statement ========================= DELETE DATA {GRAPH <Target URI of <semanticDescriptor> resource> {RDF PAYLOAD} } ========================== DELETE statement ============================ WITH <Target URI of <semanticDescriptor> resource> DELETE {template } WHERE {pattern}

EXAMPLE 3:	Remove semantic instances in the <semanticDescriptor> resource using DELETE DATA statement:

DELETE DATA { GRAPH <http://<Hosting CSE address/<CSEBase>/<AE>/<semanticDescriptor>> {saref:WASH_LG_123 msm:hasService saref:StateService_123} }

EXAMPLE 4:	Remove semantic instance in the <semanticDescriptor> resource using DELETE statement:

WITH <<http://<Hosting CSE address/<CSEBase>/<AE>/<semanticDescriptor>> DELETE {?a msm:hasService saref:StateService_123} WHERE {?a saref:hasManufacturer ‘LG'}

- Case 3: This case is to modify any of the semantic instances from the semantic description in a target <semanticDescriptor> resource in the Receiver. In this case, the Originator can include DELETE/INSERT SPARQL statements with template1 and template2 in the Request as shown in the block below. At this time, blank nodes or variables are allowed in each template.

WITH <Target URI of <semanticDescriptor> resource> DELETE {template1} INSERT {template2} WHERE {pattern}

EXAMPLE 5:	Modify semantic instances in a <semanticDescriptor> resource using DELETE/INSERT operation:

WITH http://<Hosting CSE address/<AE>/<semanticDescriptor> DELETE {?a saref:hasManufacturer ‘LG'} INSERT {?a saref:hasManufacturer ‘SAMSUNG'} WHERE {?a saref:hasManufacturer ‘LG'}

Step 002: The Receiver will verify the existence (including Filter Criteria checking, if it is given) of the requested resource first and whether the Originator has the appropriate privilege to update the requested resource. On successful validation, the Receiver can update the semantic instances according to the SPARQL statements in the Request message. The update procedures are processed as follows:

- According to Case 1: If the INSERT DATA SPARQL statement is included in Request message, the RDF PAYLOAD in the statement will be added to the target <semanticDescriptor> resource. However, if the RDF PAYLOAD already exists in the target <semanticDescriptor> resource, then the Receiver will return a failure request status with additional error information through Step 003. If the INSERT SPARQL statement included in the Request message, the Receiver adds semantic instances corresponding to template by copying semantic instances from the source <semanticDescripor> resource to the target <semanticDescriptor> resource based on the pattern. At this time, if there are no existing semantic instances corresponding to template or matched semantic instances based on pattern, the Receiver will return a failure request status with additional error information through Step 003. The blocks below show the processing result of Example 1 and Example 2 presented in Case 1.

Result of Examples 1 and 2 presented in Case 1 using semantic description in figure 8.2.2.3-1.

Description before:

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>LG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#StateService_123"/> </rdf:Description> </rdf:RDF>

Description after:

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>LG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#StateService_123"/> <msm:hasOperationrdf:resource="http://ontology.tno.nl/saref#WashingOperation_123"/> </rdf:Description> </rdf:RDF>

- According to Case 2: If the DELETE DATA SPARQL statement is included in Request message, then the RDF PAYLOAD in the statement will be removed from the target <semanticDescriptor> resource. At this time, if the RDF PALOAD does not exist in the resource, then the Receiver can return a failure request status with additional error information through Step 003. If the DELETE SPARQL statement is included in the Request message, the Receiver will remove all of semantic instances corresponding to the template based on a pattern. Accordingly, if there are no existing semantic instances corresponding to template or matched semantic instances base on pattern, then the Receiver will return a failure request status with additional error information through Step 003. The block below shows the processing result of Example 3 and Example 4 presented in Case 2.

Result of Example 2 presented in Case 2 using semantic description in figure 8.2.2.3-1.

Description before:

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>LG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#StateService_123"/> </rdf:Description> </rdf:RDF>

Description after:

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>LG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> </rdf:Description> </rdf:RDF>

- According to Case 3: If the target semantic instance included in the Request message exists in the <semanticDescriptor> resource, then the Receiver will remove all semantic instances corresponding to template1 from the <semanticDescriptor> resources, and then the Receiver will create new semantic instances corresponding to template2 in the <semanticDescriptor> resource base on pattern. In case that either the target semantic instance corresponding to template1 requested  to be removed does not exist in the  <semanticDescriptor> resource or the target semantic instance corresponding to template2 requested to be added to the <semanticDescriptor> resource already exists, the Receiver will return a failure request status with additional error information  through Step 003. The block below shows the processing result of Example 3 presented in Case 3.

Result of Example 3 presented in Case 3 using semantic description in figure 8.2.2.3-1.

Description before

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>LG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#StateService_123"/> </rdf:Description> </rdf:RDF>

Description after:

<rdf:RDF <rdf:Description rdf:about="http://ontology.tno.nl/saref#WASH_LG_123"> <rdf:type rdf:resource="http://ontology.tno.nl/saref#WashingMachine"/> <saref:hasManufacturer>SAMSUNG</saref:hasManufacturer> <saref:hasDescription>Very cool Washing Machine</saref:hasDescription> <saref:hasLocation rdf:resource="http://ontology.tno.nl/saref#Bathroom"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#WashingService_123"/> <msm:hasService rdf:resource="http://ontology.tno.nl/saref#StateService_123"/> </rdf:Description> </rdf:RDF>

Step 003: The Receiver will include all mandatory parameters and partial or whole optional parameters in the Response message for the UPDATE operation.

## 8.3 	Semantic validation

### 8.3.1	Problem statement

The <semanticDescriptor> resource contains a descriptor attribute which can store any RDF triples as the semantic description (i.e. annotation) of the associated resource (usually the parent resource of the <semanticDescriptor>). In the same time, <semanticDescriptor> resource contains a ontologyRef attribute, which is a reference (URI) of the ontology used to represent the information that is stored in the descriptor attribute.

Normally, the triples stored in the descriptor attribute should be compliant with the ontology referenced by the ontologyRef attribute. However, there is no guarantee that a issuer (e.g. a 3rd party AE) which creates or update the <semanticDescriptor> will always provide the consistent information. In case the semantic description (as triples in descriptor attribute) is not compliant with the referneced ontology, it basically means the <semanticDescriptor> is not valid and cannot be used by the AE and/or CSE properly. For example, it may cause a consumer application to mis-interpret the data semantics and types (e.g. termperature vs. humidity) so that lead to a wrong re-action (turn on/off a heater vs. a humidifier). This will undermine the benefits of semantic annotation for the IoT data and will hinder the usage of more advanced features of semantic enablement e.g. reasoning and mash-up.

Following are two detailed examples showing the potential inconsistency between the <semanticDescriptor> resources and the referenced ontology. Common assumption is described below:

The referenced ontology is called ‘OntologyH’, which represent the ontology of humidity sensor of domain X. The graphical representation of ‘OntologyH’ is show in figure 8.3.1-1. Besides that, OntologyH holds the following statement: “ controllingFunction ow:disjointwith measuringFunction”, meaning a ‘controllingFunction’ cannot be a ‘measuringFunction’ instance at the same time.

Figure 8.3.1-1: OntologyH (humidity sensor ontology of domain X)

A humidity sensor named ‘sensor12’ is reprented as an AE resource with its child resources as shown in figure 8.3.1-2. The semantic description of ‘sensor12’ is represented in the <semanticDescrptorX> child resource, where the ontologyRef attribute points to ‘OntologyH’.

Figure 8.3.1-2: oneM2M resource representation of humidity sensor ‘sensor12’

- Case 1: stand-alone <semanticDescriptor>

In this case, all semantic description about ‘sensor12’ is self-contained in the <semanticDescriptorX> resource.  Figure 8.3.1-3 further illustrate the RDF triples of the descriptor attribute of <semanticDescriptorX>.

Figure 8.3.1-3 RDF triples of <semanticDescriptorX> - case 1

Note that in the descriptor, it claims that ‘sensor12’ has the function ‘humidityContainer’ as an instance of class ‘controllingFunction’, while according to the renferece ‘OntologyH’, ‘humidityContainer’ can only be the instance of class ‘measuringFunction’. This causes the inconsistency issue.

- Case 2: linked <semanticDescriptors>

Case 2 has a similar setup as Case 1, the difference is that in Case 2, the descriptor attribute of <semanticDescriptorX> resource contains m2m:resourceDescriptorLink pointing to another <semanticDescriptorR> resource, which is the semantic description of a remote resource ‘roomA’. A similar case could be that the <semanticDescriptorR> resource is linked by the relatedSemantics attribute of <semanticDescriptorX> resource. The RDF triples of both resources are shown in figure 8.3.1-4 and 8.3.1-5 respectively.

Figure 8.3.1-4: RDF triples of <semanticDescriptorX> - case 2

Figure 8.3.1-5: RDF triples of <semanticDescriptorR> - case 2

Note that in <semanticDescriptorX>, ‘humidityContainer’ has ‘roomA/tempAspect’ as the quantified aspect and in < semanticDescriptorR> ‘roomA/tempAspect’ is claimed as an instance of class ‘TemperatureAspect’. However,  according to ‘OntologyH’, the measurement of ‘sensor12’ can only quantify instances of class ‘HumidityAspect’. This also causes the inconsistency issue.

### 8.3.2	Proposed solution

To solve the issues mentioned above, a semantic description validation common service function (CSF) is proposed to validate a <semanticDescriptor> resource against the referenced ontology. The end-to-end flow for semantic description validation is shown in figure 8.3.2-1. The extention to the resource structure is defined in clause 7.3.1 and 7.3.2.

Message flow

Figure 8.3.2-1: Message flow for semantic description validation

Step 1. The issuer (e.g. an AE or a CSE) sends to CSE-1 an operation request (CREATE, UPATE or RETRIEVE) pertaining to the <semanticDescriptor> resource hosted by CSE-1. In the case of CREATE or UPDATE, the request contains the <semanticDescriptor> resource representation, which includes the semantic description (triples in descriptor attribute), the URI to the referenced ontology (i.e. ontologyRef) and potential links to other <semanticDescriptor> resources (as in relatedSemantics attribute, or in the triples with m2m:resourceDescriptorLink in descriptor attribute). In the case of RETRIEVE, the request contains the URI of the <semanticDescriptor> resource.

Optionally, the request may contain a parameter (e.g. needValidation, which is to be specified) to indicate that the addressed <semanticDescriptor> needs to be validated before creation, update or retreival. Such indication may alternatively (e.g. in the case of CREAET and UPATE) be indicated by setting an extended attribute validationEnable of the <semanticDescriptor> resource as defined in clause 7.3.1.

Step 2. CSE-1 receives the operation request and check if the addressed <semanticDescriptor> resource is linked to any other remote <semanticDescriptor> resources (i.e. check if the addressed <semanticDescriptor> resource contains relatedSemantics attribute, or triples with m2m:resourceDescriptorLink in descriptor attribute). If no, the procedure goes to Case 1 (step 3a to 4a), otherwise, goes to Case 2 (step 3b to 6b). In the case of RETRIEVE, CSE-1 may only trigger the following steps if the addressed <semanticDescritpor> resource is not yet validated (by checking the semanticValidated attribute as defined in clause 7.3.1).

Case 1: stand-alone <semanticDescritpor> (see also clause 8.3.1 Case 1)

Step 3a. CSE-1 retrieves the ontology reprentation according to the URI in the ontologyRef attribute of the addressed <semanticDescriptor> resource from IN-CSE (which hosts the referenced ontology) . In case CES-1 cannot retrieve the ontology reprensentation (due to access right control or other exceptional reasons), skip Step 4a.

Step 4a. CSE-1 performs semantic validation of the semantic description (the triples in descriptor attribute) of the addressed <semanticDescriptor> resource against the retrieved ontology.

Case 2: linked <semanticDescritpor> (see also clause 8.3.1 Case 2)

Step 3b. CSE-1 sends a semantic validation request to IN-CSE (the hosting CSE of the referenced ontology according to ontologyRef) with the addressed <semanticDescriptor> resource representation (which includes descriptor, ontologyRef and URIs to other linked <semanticDescriptor> resources) to validate the semantic description of the addressed <semanticDescriptor> resource (together with the linked <semanticDescriptor> resources) against the referenced ontologies of the addressed and the linked <semanticDescriptor> resources.

The Ontology Repository resource on the IN-CSE may need to be extended with an additional attribute or sub-resource (e.g. <semanticValidation> as defined in clause 7.3.2) as the RESTful interface to accept the semantic validation request.

Step 4b. After receiving the semantic validation request from CSE-1, IN-CSE retrieves the linked <semanticDescriptor> resources (including the semantic description in descriptor attribute and the URI of the referenced Ontology in ontologyRef attribute). In case the linked <semanticDescriptor> resources also contain URIs linking to other <semanticDescriptor> resources, IN-CSE may repeat this step iteratively to retrieve all linked <semanticDescriptor> resources. In case IN-CSE cannot retrieve the linked <semanticDescriptor> resources (due to access right control or other exceptional reasons), skip Step 5b.

Step 5b. IN-CSE validates the semantic description of the addressed <semanticDescriptor> resource and the retrieved linked <semanticDescriptor> resources against the referenced ontologies of the addressed and the linked <semanticDescriptor> resources.

Step 6b. IN-CSE returns the validation response to CSE-1. In case Step 5b succeeds, the response code is successful, otherwise (including Step 5b is skipped due to Step 4b fails), the response code is failed.

Step 7. CSE-1 performs normal operation (CREATE, UPDATE or RETRIEVE) on the addressed <semanticDescriptor> resource according to the original request from the issuer following existing procedures. In addition, based on the validation result of Step 4a (in Case 1) or the validation response received in Step 6b (in Case 2), CSE-1 updates the validation status (validated or not) of the addressed <semanticDescriptor> resource accordingly. If Step 4a is skipped due to Step 3a fails, it’s also considered as not validated.

To do this, <semanticDescriptor> resource needs be extended with an additional attribute semanticValidated to represent the validation status as defined in clause 7.3.1.

Step 8. CSE-1 returns operation (CREATE, UPDATE or RETRIEVE) response to the issuer.

Note: Current assumption is that all referenced ontologies are hosted by the IN-CSE, no matter how the ontololgies are physicaly stored (in the IN-CSE, in a seperate database, or on an external website).

## 8.4	Semantic filtering and discovery

<Text>

## 8.5	General semantic queries

### 8.5.1	Semantic query vs. semantic resource discovery

In general, semantic queries enable the retrieval of both explicitly and implicitly derived information based on syntactic, semantic and structural information contained in data (such as RDF data). Currently oneM2M already supports semantic resource discovery through semantic filter. However, some essential differences between semantic query and semantic resource discovery need to be taken into consideration when realizing the semantic query feature, which is listed in table 8.5.1-1 from several aspects.

Table 8.5.1-1: Comparison semantic query and semantic resource discovery

| Aspects | Semantic Query | Semantic Resource Discovery |
| --- | --- | --- |
| Objective | The objective of Semantic Query is to extract “useful knowledge” over a set of “RDF data basis”. | Semantic resource discovery is mainly targeted for discovering resources for further resource accessing (e.g., CRUD operations). |
| Technical Focus | Semantic Query is a more advanced semantic-centric feature. For example, the query result can include any derived knowledge based on the query statement. | Semantic resource discovery is a more resource-oriented feature to leverage semantics to enable sophisticated resource discovery. |
| Processed Result | The semantic query result (in term of “knowledge”) can be returned as semantic information to answer the query, i.e., not just resources URIs. | The processed result of a semantic resource discovery is mainly to include a list of identified resource URIs. |

Below is an example from W3C (see https://www.w3.org/2009/Talks/0615-qbe/), which illustrates the above perspectives:

Query Example: Find me all the people in Tim Berners-Lee's FOAF (Friend of a friend) file that have names and email addresses. Return each person's URI, name, and email address.

PREFIX foaf:  <http://xmlns.com/foaf/0.1/>

SELECT *

WHERE {

?person foaf:name ?name .

?person foaf:mbox ?email .

}

Query Expected Results:

| Person | Name | Email |
| --- | --- | --- |
| <http://www.w3.org/People/karl/karl-foaf.xrdf#me> | "Karl Dubost" | <mailto:karl@w3.org> |
| <http://www.w3.org/People/Berners-Lee/card#amy> | "Amy van der Hiel" | <mailto:amy@w3.org> |
| <http://www.w3.org/People/Berners-Lee/card#edd> | "Edd Dumbill" | <mailto:edd@xmlhack.com> |

### 8.5.2	Introduction to semantic graph scoping (SGS)

To complete a given semantic query operation, two parts have to be in place:

- The Query Statement: A semantic query is normally initialized by a semantic query user based on his/her needs, which can be specified as a SPARQL query.

- The RDF Data Basis: This is the RDF triples where the semantic query is to be executed on, in order to yield the query result.

Given the oneM2M resource-oriented architecture, semantic query may need to be done directly over distributed semantic descriptors when there is no centralized Triple Store available. In particular, a unique situation is that the RDF data basis needed by a given semantic query may be dispersed in the resource tree and stored in different <semanticDescriptor> resources. Note that, those <semanticDescriptor> resources are often the child resources of normal oneM2M resources, and their major purpose currently is for semantic annotation and supporting semantic resource discovery, not directly for semantic query.

More importantly, a desirable query result for a given semantic query can be efficiently yielded only if the query is conducted over an “appropriate” RDF data basis, such a fundamental process for forming a RDF data basis is called a “Semantic Graph Scoping (SGS)” process. For example, as an illustration shown in figure 8.5.2-1., a given SPARQL query can be executed on a RDF data basis, which is formed through a SGS process and is constituted by the RDF triples from three <semanticDescriptor> resources, i.e., <SD_1>, <SD_2> and <SD_3>. It is worth noting that the query result in terms of derived knowledge of this query will be limited to the information included in those three <semanticDescriptor> resources.

Figure 8.5.2-1: Semantic descriptor discovery needed by semantic query over distributed semantic descriptors

Note that, SGS is an essential process for supporting semantic query feature over distributed semantic descriptors. For example, in the semantic resource discovery, semantic descriptors are mainly leveraged as “utilities” in order to identify normal oneM2M resources.  In comparison, SGS is to discover the semantic descriptor themselves such that they can form a RDF data basis for a given semantic query.

In addition, semantic query has more stringent requirements compared to the semantic resource discovery. For example, the originator of a semantic resource discovery can decide where the resource discovery starts by specifying a start point using the “To” parameter in an oneM2M request message, and the worst case is that the resource discovery cannot return any satisfied resource URI.  In comparison, for a given semantic query, the quality of the query result sometimes may be limited if it is not able to form an appropriate RDF data basis for this query by employing appropriate SGS.

For example, consider an example shown in figure 8.5.2-2 and the semantic query is formulated as “return me how many devices that their OperationA have the operation status larger than 60”. To answer this query (the desired answer is 3 since the operation status of all the Device12, Device34 and Device56 are larger than 60 now), ideally the SGS process should collect all of three involved <semanticDescriptor> child resources of Device12, Device34 and Device56 (assuming that the access control is not an issue), which forms the appropriate RDF data basis for answering this query. Otherwise, the quality of the query result may be limited to the RDF data basis formed by a SGS process if it does not include all of the three <semanticDescriptor> resources. Therefore, it can be seen that how SGS could potentially collect the involved <semanticDescriptor> resources needs to be specified, which is introduced in a later section.

Figure 8.5.2-2: A semantic query example over distributed semantic descriptors

### 8.5.3	Solutions to semantic graph scoping

In this section, several potential solutions are specified for the SGS process, and each of them has their own methodology, as well as pros/cons, which are discussed in details. Two major entities are involved, i.e., the originator (i.e., a semantic query user sending a query request message), and the receiver that is to conduct the semantic query processing and yield the query result.

Solution-1: Solution-1 is a straightforward solution in that the SGS is conducted at a local CSE. In particular, when an originator sends a semantic query to a receiver, it directly targets to the <CSEBase> resource. Accordingly, the SGS process at the receiver side will discover all the <semanticDescriptor> resources under <CSEBase> as the RDF data basis for this query as long as access control policy is allowed. Note that, this is a best-effort approach in the sense that the SGS will try to form a data basis as wide as possible, in which it is also possible that the triples from many <semanticDescriptor> resources may not be relevant to the query. In particular, such an SGS may also incur considerable processing cost when trying to traverse the whole resource tree.

By examining the working procedures of existing semantic resource discovery over distributed descriptors as specified in Sec. 8.5.5, the following two enhanced solutions are introduced:

Solution-2: Solution-2 highly follows the existing practice on semantic resource discovery in the sense that the SGS may still start with the URI as specified by the “To” parameter and how semantic descriptors can be collected is similar with the process as done in the semantic resource discovery as introduced in Sec. 8.5.5. During the SGS process, some existing practices adopted by the existing semantic resource discovery can also be leveraged. For example, when SGS discovers <semanticDescriptor> resources for forming a RDF data basis, the existing resourceDescriptorLink property (and other similar utilities) can also be leveraged. For example, similar to the semantic resource discovery, when a SGS discovers a specific <semanticDescriptor> resource, it is possible that this resource may be linked with other <semanticDescriptor> resources in the local or remote CSEs through the resourceDescriptorLink property. Accordingly, the SGS can also follow the resourceDescriptorLink in order to add other linked <semanticDescriptor> resources into the RDF data basis.

Regarding to another unique aspect related to query result quality, this solution allows for the case when the SGS cannot form an appropriate RDF data basis. Accordingly, the following mechanism can be adopted. For example, in order to enable the originator to tolerate or be aware of the quality of the query result, one thing at the receiver side could do is to not only return the query result, but also piggyback certain query summary information as a feedback in order to enable the originator to have some sense regarding how to interpret/evaluate the query result. For example, the summary information could explain how the query was processed, the overview of the RDF data basis used for this query, e.g., how many <semanticDescriptor> resources were involved in this query, etc.

Solution-3: In this approach, the semantic query process is decoupled with the SGS process. For example, without processing any semantic query, at the receiver side, it may proactively aggregate some related <semanticDescriptor> resources together by using existing <group> and/or < semanticGroup> resources (as defined in existing TS-0001 and TR-0007). Still taking the same example used previously, as shown in figure 8.5.3-1, the receiver or any other 3rd party entity may proactively create a <Group-1> resource, in which the members are the <semanticDescriptor> child resources of all the devices. The <semanticDescriptor> resource of the <Group-1> itself can be used to give the description about this group.

Figure 8.5.3-1: Use <group> resource for explicitly specifying an RDF data basis

For the originator, it may first discover various <group> resources to see which one have the most appropriate RDF data basis for the query to be launched. After such a <group> resource is selected, the originator may send its semantic query to the selected <group> resource. At the receiver side, the semantic query will be executed on the member resources of the selected <group> resource, which will be the data basis of this query (More general, it is also possible that the originator can form a RDF data basis by selecting more than one <group> resource). Last, the partial query results from each of member resources will be combined together as the final query result before being sent back to the originator. It is worth noting that the advantages for this approach include: 1) the receiver side can leverage its own knowledge on the resource tree to form some useful RDF data basis candidates; 2) the originator can have a clear understanding on the RDF data basis where the intended query is to be conducted. The disadvantage is that it is required that the receiver side needs to create different <group> or <semanticGroup> resources in order to form different RDF data basis candidates that may potentially be needed by various semantic queries.

It is worth noting that although this solution also proposes to leverage the <group> and/or <semanticGroup> resources for SGS, it has the fundamental differences compared to how those resources are used in the existing semantic resource discovery. For example, in semantic resource discovery, <group> resources are mainly used “internally” by the receiver when conducting a semantic resource discovery (i.e., the originator does not know any details regarding to how semantic descriptors are being organized/linked and collected, which is only known/used by the receiver side).  By comparison, in Solution-3, the <group> resources and its contents can be directly exposed to the originator as RDF data basis candidates. In other words, those <group> resources are representing RDF data basis candidates and are visible to the originator (i.e., not just being used internally by the receiver) such that the originator now is also involved in the SGS process, which is a different working procedure compared to the existing semantic resource discovery.

Overall, the table 8.5.3-1 has summarized the pros/cons for each of the proposed solutions as discussed above, respectively. As can be seen from the table that, Solution-2 and Solution-3 have their own advantages, and both of them outperform the native Solution-1.

Table 8.5.3-1: Pros/cons of solutions

| Solutions | Pros | Cons |
| --- | --- | --- |
| Solution-1 | Simple implementation Best effort discovery with wide search scope | Considerable discovery cost due to full-traversal of whole resource tree Considerable query processing due to a large data basis |
| Solution-2 | Follow the current practice on semantic resource discovery Less discovery cost due to a controllable discovery scope The originator may have some sense on the quality of the query result with the help of result summary | Relevantly more complex implementation is needed, compared to Solution-1. |
| Solution-3 | Fully decouple SGS with the query processing stage. The RDF data basis candidates can be proactively created at the receiver side. The originator has its own options to flexibly choose the appropriate RDF data basis candidate for its intended query, based on its subjective needs. The originator may have clear understanding what data basis the query is to be executed on. | Relevantly more complex implementation is needed, compared to Solution-1. |

## 8.6	Query scopes

## 8.7	Semantic reasoning

## 8.8	Semantic mash-up

### 8.8.1	Introduction

#### 8.8.1.1	Semantic mashup definition

Existing semantic resource discovery in oneM2M can help in discovering various IoT devices and their data. However, in many application scenarios, the discovered data needs to be further processed (e.g., integrated/orchestrated/combined) based on a certain application business logic. For example, users may just be interested in a metric called “weather comfortability index”, which cannot be directly provided by physical sensors, and in fact can be calculated based on the original sensory data collected from multiple types of physical sensors (e.g., temperature and humility sensors).

In general, the above process is called “Semantic Mashup”, which is defined as a process to discover and collect data from more than one source as inputs, conduct a kind of business logic-related mashup function over the collected data, and eventually generate meaningful mashup results. In particular, semantic mashup emphasizes on leveraging semantic-related technologies during the entire mashup process. For example, in the oneM2M context, an normal resource (e.g., a <AE> resource representing a temperature sensor) may be annotated by semantic descriptions and then they could be discovered and identified as a potential data source for a specific mashup application through the semantic resource discovery.

The above definition also indicates a fact that a complete semantic mashup process may involve multiple stages and multiple entities for each stage, which will be illustrated and discussed in details through the following sections.

#### 8.8.1.2	Semantic mashup example: smart parking application

Smart parking is one of the major applications in a smart city. In the smart city, each parking spot (e.g., inside parking buildings and any street parking spot) is equipped with a parking sensor. The parking sensor provides real-time parking spot information including the real-time status about its associated parking spot (i.e., occupied or not), the geographic location of the associated parking spot, as well as the real-time parking rate of the associated parking spot. All those information can be described in a semantic form, such as RDF triples. As shown in figure 8.8.1-1, there are some parking buildings (whose parking sensors are registered to Server-A) as well as street parking spots (whose parking sensors are registered to Server-B) around Building-A.

For a given user/client who wants to find a suitable parking spot near her/his destination (e.g., Building-A), she/he may send a parking request (indicating e.g., her/his destination and/or parking preference, etc.) to Server-C, which provides real-time parking assistance. In order to process this parking request, a mashup process will be triggered in Server-C. For example, by leveraging semantic-related technologies Server-C will first collect the needed information from multiple places, which include: 1) Real-time parking spot information from Server-A for the parking buildings; 2) Real-time parking spot information from Server B for the street parking spots. Then, Server-C will process and mashup all these collected information in order to find the most suitable parking spot according to a certain mashup function, which could have been provisioned to Server-C. For instance, the mashup function can define the most suitable parking spot as the one having the minimum parking rate or having the most convenient location (e.g., having the shortest walking distance to the elevator). Finally, the mashup result (i.e., the most suitable parking spot) will be returned to the user.

Figure 8.8.1-1: Smart Parking Assistance Realized Through Semantic Mashup

### 8.8.2	Problem statement

#### 8.8.2.1	Entities involved in sematic mashup

From the above smart parking example, it can be seen that multiple entities are involved in the mashup process, which include:

- Mashup Requestor (MR): The entity which initiates a mashup request to Semantic Mashup Function (as introduced next) for a certain need. For example, a client/user looking for the suitable parking spot is the mashup requestor in the smart parking use case. In the context of oneM2M, an AE or a CSE can be an MR.

- Resource Host (RH): The entity which hosts data source(s) for a given mashup process. For example, in the smart parking use case, Server-A and Server-B are RHs, which host data sources in terms of many parking sensors. In the context of oneM2M, a data source is typically represented by a oneM2M resource (e.g., a temperature <AE> resource) and a RH will be a CSE that hosts oneM2M resources.

- Semantic Mashup Function (SMF): The entity which is responsible for collecting the data inputs from data sources hosted on RHs and mashing them up to generate the mashup result based on a certain business logic. For example, in the smart parking use case, Server-C provides an SMF and one of mashup applications run by the SMF is the smart parking assistance. In the context of oneM2M, SMF is a Common Service Function.

#### 8.8.2.2	Technical analysis of semantic mashup

It is worth noting that there are many-to-many relationships between different MRs, RHs and SMFs in reality. Typically, a RH may provide the same data inputs for different mashup applications. For example, the same outdoor temperature sensors can not only provide inputs for a weather reporting mashup application, but also for a travel planning mashup application. Similarly, a single SMF may provide and support various mashup applications. For example, in the smart parking use case, the SMF hosted by Server-C may also support the shopping guidance mashup application besides the smart parking assistance; accordingly, an MR may resort to Server-C in order to not only find the most suitable parking spot near Building-A (supported by smart parking assistance mashup application) but also get the most recent coupons provided by the shops in Building-A (supported by the shopping guidance mashup application). In addition, for a given mashup application, different MRs may trigger individual mashup processes/instances to be conducted by SMF. For example, in the smart parking use case, different users as MRs may resort to Server-C for finding their respective parking spots given their different destinations, and each of their requests may trigger an individual mashup process for the same smart parking assistance mashup application.

Considering the multiple entities involved in a mashup process as well as their potential many-to-many relationships as discussed above, a common SMF needs to be included in a service layer in order to provide generic semantic mashup support for various application scenarios. In particular, in the context of oneM2M service layer, this SMF could be a CSF since data inputs mainly come from oneM2M resources and MRs mainly refer to service layer entities such as AEs/CSEs. In comparison, when there is no such a common SMF in the system, alternative ways to realize semantic mashup likely will be inefficient/non-optimal. For example, all mashup-related tasks could be handled by MRs themselves (i.e., MRs need to fully understand business logics, identify the qualified data sources, collect data inputs, and mashup those data inputs in order to derive the mashup result), which may have the following potential issues:

- An MR has to collect data inputs from original resources. However, in most of cases, an MR does not really care about original resources and it is only interested in the mashup result. Furthermore, the MR needs to have various domain knowledge if data inputs to be collected are from different domains. Accordingly, all the mashup-related processing needs to be handled by the MR itself, which increases the implementation complexity for the MR.

- Some resources (as data sources) hosted by RHs may be sensitive due to various access control policies. In other words, certain resources may not be exposable to an MR or not allowed to be retrieved directly by an MR. In comparison, a common SMF may have more privileges for collecting and accessing data inputs.

- Different MRs may conduct mashup operations individually without any collaboration, which may lead to considerable/unnecessary overhead (e.g., repetitive data retrieval from the same data source). In comparison, a common SMF could retrieve and feed a data input to multiple mashup processes if they need the same data input(s), which can significantly reduce the related overhead.

### 8.8.3	Semantic Mashup Function (SMF)

#### 8.8.3.1	High-level architecture

This section describes the high-level architecture of Semantic Mashup Function (SMF) and the high-level operations of SMF that are needed during the execution of a semantic mashup process. In the meantime, this section also introduces various semantic mashup paradigms in the real world and the details on how this SMF can be tailored in order to support those different paradigms, which demonstrates the improved flexibility, reusability, and system efficiency of SMF.

Figure 8.8.3-1: High-level architecture of Semantic Mashup Function

The high-level architecture of an SMF is shown in figure 8.8.3-1, In general, the SMF is designed in a modular way and mainly includes the following components:

- Semantic Mashup Job Profile (SMJP): Each specific semantic mashup application has a corresponding SMJP, which not only provides functionality/interaction details for external entities to discover (e.g., MRs), but also defines the internal working details regarding how to realize this mashup application (e.g., the criteria of how to select the qualified data sources as well as the definition of mashup function). To be more specifically, an SMJP includes the following parts:

  - SMJP Semantic Description: In general, an MR first needs to discover a desired SMJP based on its need before sending a request to an SMF for triggering a real mashup process for this SMJP. Since there could be various mashup applications supported by an SMF, the mashup applications’ corresponding SMJPs could be stored in a repository called SMJP Library for MRs to browse and discover. An MR can evaluate the semantic descriptions (e.g., RDF triples) of an SMJP in order to identify whether an SMJP meets its need.

The semantic descriptions can include the information regarding to what is the functionality that can be realized by executing this SMJP, how to interact with or run this SMJP, e.g., what inputs are needed from MR side and what is the expected mashup result (as output) of this SMJP, etc. Taking the example shown in figure 8.8.3-1, the semantic descriptions of the SMJP (which has the smjpID of SMJP-001) indicate that: 1) this is a “smart parking assistance mashup application”; 2) an MR needs to provide its current location, destination and/or parking preference as user inputs in order to trigger a real mashup process for applying this SMJP; and 3) the mashup result will be a suitable parking spot (including the spot’s ID/name and location).The semantic descriptions can also specifies the “internal” operation details regarding to how to execute and realize a semantic mashup process, which defines the following aspects:

    - Data Sources Criteria: The potential data sources for an SMJP are described through some criteria filter(s), which defines what types of data sources are eligible or qualified to provide data inputs for this specific mashup application. Taking the smart parking example shown in figure 8.8.3-1, Two types of data sources are desired, i.e., the parking spots in any parking buildings near the destination, and the parking spots in any street parking near the destination. Note that, an SMJP only defines the “criteria” for identifying the qualified data sources, which means that it does not refer to any specific data sources. Typically, when a real mashup process of an SMJP is triggered in SMF, SMF will then identify the specific qualified data sources according to the criteria as defined in the SMJP (the details will be discussed later).

    - Mashup Function: For a given semantic mashup process, after the SMF collects data inputs from the qualified data sources, the next step is to mashup those inputs and derive the mashup result, which is described by the mashup function. Taking the smart parking example shown in figure 8.8.3-1, after identifying all the parking spots near the destination, various spot selection algorithms can be used as mashup functions in order to determine the best suitable one. For example, the default one is to find the parking spot having the minimum cost.

  - Utility or Runnable Code Block: This part mainly stores the related utilities or code blocks for realizing the SMJP. For example, it could include specific mathematical formulas to be used by the parking spot selection algorithms, and the runnable code blocks for realizing the mashup functions as mentioned earlier. Note that, this part is optional in the sense that the implementations of SMJP could be stored separately or just internally hosted by SMF.

- Semantic Mashup Instance (SMI): Once an MR identifies a desired SMJP (which can be analogous to a “job description”, but not a real job), it can ask SMF to initialize a real mashup process (which corresponds to a “working instance” of this SMJP and is called Semantic Mashup Instance, or SMI). In order to do so, the SMF will inject the corresponding SMJP into the Mashup Engine of SMF for the SMI instantiation, during which the engine may be involved in:

  - Identifying the qualified data sources according to the data source criteria as defined in the SMJP;

  - Collecting data inputs from those identified data sources;

  - Mashing up the collected inputs by applying mashup functions as defined in the SMJP, and finally deriving the mashup result;

Typically, an SMI has the following three parts as shown in figure 8.8.3-1:

- the smjpID, which is the reference to the applied SMJP;

- The identified data sources, which indicate where the data inputs can be collected and optionally can also contain the data inputs collected from those data sources; To consider an SMI as a whole, the identified data sources in a SMI can be regarded as the “Mashup Members” of this SMI and accordingly the data source criteria as defined in SMJP is in fact a member filter for determining how to select qualified mashup members for a given SMI. The term “data source” and “mashup member” will be used interchangeably in the rest of sections.

- The mashup result derived by this SMI.

Taking the smart parking example shown in figure 8.8.3-1, SMI-1 is an SMI for smart parking assistance mashup application, which is created by MR-1. As can be seen, based on MR-1’s inputs (e.g., current location and destination, etc.), the parking spots in parking buildings, i.e., XX and YY, as well as street parking spots on Main Street and 5th Avenue are identified as “qualified data sources”. By applying the parking slot selection algorithm, the final mashup result in terms of the suitable parking spot is parking spot -16, which is located in 1st floor, 3rd row of the parking building XX.  It can also be seen that, besides the smart parking assistance mashup application, MR-1 may need a shopping guidance mashup result as well, which will trigger another SMI-2 referring to a different SMJP (i.e., SMJP-002, which specifies shopping guidance mashup application). In addition, another MR-2 (having a different destination) may also ask the SMF for its own parking need, which will trigger another SMI-3 (note that, SMI-3 applies the same SMJP as SMI-1, i.e., SMJP-001).

#### 8.8.3.2	High-level operations

With the high-level architecture of an SMF as introduced in clause 8.8.3.1, the next question is how those components should work together and how an SMF should interact with other entities, such as RHs (providing potential data sources), and MRs (having various semantic mashup needs). It is worth noting that an SMF may involve in different tasks/operations for realizing a complete semantic mashup process. This clause is to introduce those major SMF operations, and particularly discuss the possible solutions for implementing those operations in the context of oneM2M.

Figure 8.8.3-2: High-level operations for Semantic Mashup Function

The high-level SMF operations are shown in figure 8.8.3-2, which is discussed in details as follows:

- Operation 1 - SMJP Discovery: This process is needed when an MR (e.g., MR-1 in figure 8.8.3-2) tries to discover a desired SMJP for its need. Since operations in oneM2M context is resource-oriented, an SMJP can be exposed as a oneM2M resource (e.g., <SMJP>) and the semantic descriptions of the SMJP can be put into the <semanticDescriptor> child resource of <SMJP>. Accordingly, the SMJP Discovery can be implemented by leveraging the existing semantic resource discovery mechanism.

- Operation 2 - SMI Creation: This process is needed when an MR already identified a desired SMJP, but there is no corresponding SMI available for use. To implement this operation, an MR can send an SMI creation request targeted to the CSE hosting SMF in order to instantiate a new SMI for the desired SMJP. Alternatively, the SMF can also create a new SMI by itself instead of being triggered by the SMI creation request from MR.

- Operation 3 – Mashup Member Identification: This process is needed when an SMF tries to identify the qualified mashup members (i.e., data sources) for a given SMI, by referring to the criteria as defined in the corresponding SMJP of this SMI. Since in the oneM2M context, data sources (such as sensors) are normally represented as oneM2M resources hosted by RHs, this operation can also be implemented through the existing semantic resource discovery mechanism.

- Operation 4 – Mashup Result Retrieval: This process is needed when an MR tries to retrieve the mashup result from a specific SMI. It is worth noting that for a given SMI, it may involve in multiple rounds for mashup result generation especially when the mashup result needs to be refreshed periodically. For example, an SMI of a weather reporting mashup application for a given area (e.g., New York City Area) may need to re-calculate the mashup result every certain minutes due to real-time weather changes. In order to do so, this SMI first needs to re-collect new data inputs from its identified mashup members (note that, the SMI is not necessary to re-identify the qualified mashup members for every round of mashup result generation if the existing identified mashup members are still qualified). Accordingly, there could be several alternative mechaniSMF for the mashup result generation, e.g.:

  - Option 1: The SMF proactively and periodically runs the mashup result generation and as long as the newly mashup result becomes available, it will be exposed as a oneM2M resource for MRs to access. In this approach, Operation 4 is only involved with a normal oneM2M resource retrieval. The benefit of this approach is that the MRs can obtain the mashup results with minimum delay but the overhead is that the SMF needs to proactively and periodically run the mashup result generation no matter whether there is a need.

  - Option 2: The SMF will work in a reactive way to generate the mashup result. In this approach, only after receiving a mashup result retrieval request from an MR, SMF will just start to re-collect new data inputs and re-calculate the mashup result (which corresponds to Operation 5 as introduced next). In other words, Operation 4 in this approach will further trigger Operation 5. The benefit of this approach is that SMF will work in an on-demand way, which may reduce overhead as compared to Option 1. However, the downside is that it leads to longer waiting time for an MR before the up-to-date mashup result becomes available because data re-collection and mashup result generation will not be triggered until the SMF receives a request from the MR.

- Operation 5 – Data Input Collection and Mashup Result Generation: This process is needed when an SMF tries to generate a mashup result for a given SMI. Note that, Operation 3 focuses on how to identify the mashup members while Operation 5 focuses on how to collect data inputs from those identified/qualified mashup members, which can be implemented through the normal resource retrieval. In addition, the working mechanism used for Operation 4 as mentioned above will affect how Operation 5 is used by the SMF.

- Operation 6 – SMI Discovery and Re-use: As mentioned earlier, in some scenarios, an SMI can be re-used and shared among different MRs. For example, the same SMI of a weather reporting mashup application for New York City Area can be shared by different users asking weather information for this area. Accordingly, this process is needed when an MR (e.g., MR-2 in figure 8.8.3-2) tries to discover whether there is already an available/desired SMI ready for use. Similarly, in the oneM2M context, a given SMI can also be exposed as a resource (i.e., each SMI has a corresponding Semantic Mashup Resource, or called <SMR>), in which the essential parts for describing this SMI can be included, such as the referred smjpID, the identified mashup member list, and/or the mashup result yielded by this SMI. Accordingly, taking the example shown in figure 8.8.3-2, MR-2 can find a desired SMI (which is available and was created by MR-1) through an SMI discovery process, which can also be realized by using the existing semantic resource discovery mechanism. After that, MR-2 can ask the discovered SMI for the mashup result, and the SMI will directly leverage the already-identified mashup members. This approach leads to less processing overhead, since MR-2 does not have to require the SMF to generate a new SMI (therefore Operation 2 and 3 are not needed).

#### 8.8.3.3	Functional paradigms

It is worth noting that although the smart parking mashup application was used in the previous sections for illustrating the details of an SMF, the smart parking assistance is just one of the possible semantic mashup paradigms. This section is to explore the two major semantic mashup paradigms in real world, and to show how an SMF can be tailored in order to well support each of those paradigms.

Paradigm 1: Short-lived Semantic Mashup: Short-lived semantic mashup application basically refers to as the application in which a mashup process will be completed once the corresponding mashup result is produced. The previous smart parking assistance mashup application falls into this paradigm. For example, once a user gets a suitable parking spot from SMF, the whole mashup process is completed. In the meantime, since different users may be towards different destinations and have different parking preferences, the same SMI for serving user A may not be re-used for serving user B. Accordingly, every time when a user needs to find a suitable parking spot for its own use, the SMF may probably need to instantiate a new SMI. With the proposed SMF in clauses 8.8.3.1 and 8.8.3.2, the Operations 1-5 could be adopted as the solution to Paradigm 1.

Paradigm 2: Long-lived Semantic Mashup: Long-lived semantic mashup application basically refers to the application in which a mashup process will last for a relatively long time, during which the corresponding SMI may generate the mashup result for multiple times and the SMI can also be re-used/shared among different MRs. The previous weather reporting mashup application falls into this paradigm. For example, once an SMI has been created for reporting weather information of New York City Area, the mashup result of this SMI will be refreshed by the SMF periodically due to real-time weather changes. In the meantime, the same SMI can be shared and re-used in this paradigm by different MRs, e.g., the users from New York City Area can ask the same SMI for the real-time weather information in the area. With the SMF, the Operations 1-6 could be adopted as the solution to Paradigm 2.

## 8.9	Semantics-based data analytics

## 8.10	Ontology management

## 8.11	Semantic Access Control

### 8.11.1	Synchronizing ACP information between the Resource Tree and the Semantic Graph Store.

As described earlier, the Direct Access Control of Semantic Graph Store approach requires synchronization between <accessControlPolicy> resources at the Hosting CSE and ACP Triples at the Semantic Graph Store. In order to maintain such synchronization, the Hosting CSE needs to perform the following tasks:

- When a new <accessControlPolicy> resource is created, the Hosting CSE will generate new ACP Triples according to the ACP ontology (see TBD) and stores these new ACP Triples in the  Semantic Graph Store

- When the privileges attribute of an existing <accessControlPolicy> resource is updated, the Hosting CSE will also generate new ACP Triples and update corresponding old ACP Triples at the Semantic Graph Store accordingly

- When an existing <accessControlPolicy> resource is deleted, the Hosting CSE will need to remove the corresponding ACP Triples at the Semantic Graph Store.

Figure 8.11.1-1 illustrates the procedure for creating ACP Triples in Semantic Graph Store, which is triggered when an Originator requests to create an <accessControlPolicy> resource at the Hosting CSE.

Figure 8.11.1-1: Procedure for creating ACP triples in the Semantic Graph Store

- Step 1: The Originator sends a request to create an <accessControlPolicy> resource to the Hosting CSE. This message contains the representation of <accessControlPolicy> to be created (e.g. the value of privileges attribute).

- Step 2: The Hosting CSE receives the request in Step 1 and, subject the Originator access rights verification, will create the requested <accessControlPolicy> resource.

Example: Assume <acp1> to be the newly created ACP resource and its URI “acp1URI”. Assuming <acp1> has one access control rule (e.g. acr11) and the URI of the corresponding privileges attribute is “acr11URI”. For exemplification, assume also that acr11 allows an AE (“AE-ID-1”) to perform DISCOVERY operations.

- Step 3: The Hosting CSE sends a response to the Originator.

Example: If Step 1 was successful, “acp1URI” will be contained in this response message.

- Step 4: The Hosting CSE generates corresponding ACP Triples based on the content of <acp1>  and the ACP ontology,

Example: An example of ACP Triples for <acp1> resource created in Step 1 is illustrated in figure 8.11.1-2.

Figure 8.11.1-2: Example ACP triples corresponding to <acp1> resource

  - In figure 8.11.1-2:

    - line#1 defines prefix “acp” which will used in lines #2-#6.

    - line#2 defines a new acp:accessControlPolicy class instance for <acp1> resource. The subject value of this triple (i.e. acp:acp1) is “acp1URI”, therefore the subject value of this triple makes it possible to locate the corresponding resource <acp1>. The Hosting CSE can also use “acp1URI” to locate corresponding triples in the Semantic Graph Store (e.g. when updating existing ACP Triples).

    - line#3 defines that acp:acp1 instance has an associated access control rule acr11. The object value of this triple (i.e. acp:acr11) is “acr11URI”, therefore the object value of this triple, makes it possible to locate the corresponding privileges attribute of <acp1> resource. The Hosting CSE can use “acr11URI” to locate the corresponding triples in the Semantic Graph Store (e.g. when updating existing ACP Triples).

    - line#4 defines that acp:acr11 (i.e. the object on line#3) is an acp:accessControlRule class instance.

    - line#5 and line#6 give the values of two properties of acp:acr11 based on the assumptions in this example.

Note: The triples on lines #4-#6 define the access control rule acr11. If <acp1> has more access control rules, additional access control rules will be defined similarly to those on lines #4-#6.

  - Optionally: The Hosting CSE may add the address of the Semantic Graph Store to the <accessControlPolicy> resource created in Step 2 in a new attribute, to enable direct addressing of the triples.

- Step 5: The Hosting CSE sends a SPARQL request to store the ACP Triples created in Step 4 to the selected Semantic Graph Store.

Example: The ACP Triples shown in figure 8.11.1-2 will be contained in the SPARQL request.

- Step 6: The Semantic Graph Store receives the SPARQL request, processes it and saves the ACP Triples into its graph store.

- Step 7: The Semantic Graph Store sends a response back to the Hosting CSE to confirm the request in Step 6 is successfully executed.

The procedure for updating ACP Triples in a Semantic Graph Store follows a similar flow to the procedure used when a new <accessControlPolicy> resource is created. In this case the Originator requests to update the privileges attribute of an existing <accessControlPolicy> resource, as shown in figure 8.11.1-3.

Note: This procedure applies also for updates of the accessControlPolicyIDs attribute of the <semanticDecriptor> resource.

Figure 8.11.1-3: Procedure for updating ACP triples in Semantic Graph Store

- Steps 1- 3: Similar to those describing figure 8.11.1-1, but reflecting normal processing of an UPDATE operation. In this case the Originator triggers an update of the privileges attribute of an existing <accessControlPolicy>

- Step 4: Based on the new value of the privileges attribute the Hosting CSE generates new ACP Triples

  - Example:  Assume the Originator aims to update the privileges attribute of <acp1> resource from “DISCOVERY” to “DISCOVERY” and “RETRIEVE” as the new accessControlOperations.  To implement these changes in figure 8.11.1-3 the Hosting CSE can simply add a new triple e.g. “acp:acr11  acp:hasACOperations  “RETRIEVE”.  Alternatively, the Hosting CSE can replace the triple on Line#6 to the new triple “acp:acr11  acp:hasACOperations  “DISCOVERY”, “RETRIEVE”.”.

- Step 5: The Hosting CSE sends a SPARQL request to the Semantic Graph Store to update existing ACP Triples related to <acp1> resource to reflect the update being requested.

Example: As described in Step 4, there are two options to implement this.

  - The Hosting CSE adds a new triple with the following SPARQL request:

  - The Hosting CSE replaces Line#6 in figure 8.11.1-3 with the SPARQL request:

- Step 6: The Semantic Graph Store processes the received SPARQL request and updates the corresponding ACP Triples.

- Step 7: The Semantic Graph Store sends a response to the Hosting CSE to inform it whether the request has successfully executed.

The procedure for deleting ACP Triples in a Semantic Graph Store follows a similar flow to the procedure. In this case the Originator requests to delete an existing <accessControlPolicy> resource, as shown in figure 8.11.1-4.

- Steps 1- 3: Similar to those describing figure 8.11.1-1, but reflecting normal processing of a DELETE operation. In this case the Originator triggers the deletion of an existing <accessControlPolicy> resource.

Figure 8.11.1-4: Procedure for Deleting ACP Triples in the Semantic Graph Store

- Step 4: The Hosting CSE sends a SPARQL request to the Semantic Graph Store to delete existing ACP Triples

  - Example: The following SPARQL request implements this request:

- Step 5: The Semantic Graph Store processes the received SPARQL request and removes all requested ACP Triples.

- Step 6: The Semantic Graph Store sends a response to the Hosting CSE to inform it whether the request was successfully executed.

### 8.11.2	Synchronizing SD-related triples between the Resource Tree and the Semantic Graph Store

#### 8.11.2.1	Introduction

Functionality such as Direct Access Control of the Semantic Graph Store require synchronization between information the resources at the Hosting CSE and the Semantic Graph Store. In addition to ACP Triples, others such as SD Original Triples, ACP-SD Binding Triples and SD relationship triples need to be synchronized.

Several use cases are envisioned:

- When a <semanticDescriptor> is created:

  - In this case the Hosting CSE will generate SD Relationship Triples and ACP-SD Binding Triples and then store them in the SGS

- When the accessControlPolicyIDs attribute of a <semanticDescriptor> resource changes

  - In this case the Hosting CSE will generate new ACP-SD Binding Triples and use them to update corresponding old ACP-SD Binding Triples in the SGS. This case may apply also when the accessControlPolicyIDs attribute of the parent changes.

- When the descriptor attribute of a <semanticDescriptor> resource changes:

  - In this case the Hosting CSE will generate new SD Relationship Triples and use them to update old SD Relationship Triples in the SGS

- When a <semanticDescriptor> resource is deleted:

  - In this case the Hosting CSE will delete all corresponding SD Original Triples, SD Relationship Triples and ACP-SD Binding Triples from the SGS

#### 8.11.2.2	Procedure for Creating ACP-SD binding triples and SD relationship triples in SGS

Figure 8.11.2.2-1 illustrates the procedure for creating ACP-SD Binding Triples and SD Relationship Triples in SGS, which is triggered when an Originator requests to create a new <semanticDescriptor> resource.

After checking the access rights and other related security functions, the Hosting CSE creates the <semanticDescriptor> resource locally (referred to as SD1 and its URI assumed to be sd1URI). Then, the Hosting CSE will store all semantic triples as described in the descriptor attribute of SD1 resource to the SGS. More importantly, the Hosting CSE will generate new SD Relationship Triples and ACP-SD Binding Triples and store them to the SGS as well. Note that if SD1 has no accessControlPolicyIDs attribute, ACP-SD Binding Triples will not be generated.

The following steps are performed.

- Step 1: The Originator sends “Create <semanticDescriptor> Resource” request to the Hosting CSE. It is assumed that the value of descriptor attribute and accessControlPolicyIDs attribute of <semanticDescriptor> resource will be given in this request message.

  - Assume the descriptor attribute contains only one SD Original Triple “S1  P1  O1 .”

  - Assume the value of accessControlPolicyIDs is “acp1URI” i.e. the access control policy acp1 will be applied.

- Step 2: The Hosting CSE accordingly creates the <semanticDescriptor> resource (referred to as sd1).

  - Assume its URI is sd1URI.

- Step 3: The Hosting CSE sends a response to Originator to inform it if Step 2 is successfully completed.

- Step 4: Bases don the SD Original Triple contained in the descriptor attribute of sd1, the Hosting CSE generates SD Relationship Triples.

  - In our example, there is only one SD Original Triple, as shown below:

- Step 5:, The Hosting CSE will generate the ACP-SD Binding Triples

  - In our example, since sd1’s accessControlPolicyIDs attribute points to acp1 resource as shown below:

- Step 6: The Hosting CSE sends a SPARQL request to the SGS to store these SD Relationship Triples and ACP-SD Binding Triples to the SGS.

- Step 7: The SGS processes the SPARQL request and store corresponding SD Relationship Triples and ACP-SD Binding Triples in the SGS.

- Step 8: The SGS sends a response message to the Hosting CSE to inform it if the SPARQL request in Step 6 is successfully executed.

Note:

If the <semanticDescriptor> resource being created in Step 2 does not have accessControlPolicyIDs attribute, the accessControlPolicyIDs attribute of the parent resource may be used or system default access privileges may be applied. The new ACP-SD Binding Triples will also be generated using either the parent resource’s accessControlPolicyIDs attribute or based on the default privileges.

Figure 8.11.2.2-1: Procedure for creating SD relationship triples and ACP-SD binding triples

#### 8.11.2.3	Procedure for updating ACP-SD binding triples in SGS

Figure 8.11.2.3-1 shows the procedure for updating ACP-SD Binding Triples when the accessControlPolicyIDs attribute of a <semanticDescriptor> resource is updated.

For example, the sd1 resource created earlier has accessControlPolicyIDs changed from acp1 to acp2; with the ACP Triples for the resource acp2 as follows:

@PREFIX	acp:			<http://accessControlPolicy.org>.

acp:acp2 	rdf:type 		acp:accessControlPolicy .

acp:acp2 	acp:hasACPRule 	acp:acr21 .

acp:acr21 	rdf:type 		acp:accessControlRule .

acp:acr21 	acp:hasACOriginator 	"AE-ID-2" .

acp:acr21 	acp:hasACOperations 	"RETRIEVE" .

The following steps are performed:

- Step 1: The Originator sends a request to update the resource sd1’s accessControlPolicyIDs from the URI of the resource acp1 to the URI of the resource acp2. The URI of the resource acp2 (i.e. acp2URI) is contained in this request. The URI of the resource sd1 (i.e. sd1URI) is also contained in this request.

- Step 2: The Hosting CSE checks access rights. If it is allowed, the Hosting CSE updates sd1’s accessControlPolicyIDs with acp2’s URI given in Step 1.

- Step 3: The Hosting CSE sends a response back to the Originator to inform it if the request in Step 1 is successful or not.

- Step 4: Since the sd1’s accessControlPolicyIDs is changed, the Hosting CSE generates a new ACP-SD Binding Triple (“acp:acp2  acp:appliedTo  sd:sd1”) to reflect this change. This new ACP-SD Binding Triple will replace the old ACP-SD Binding Triple (i.e. “acp:acp1  acp:appliedTo  sd:sd1”)

(new ACP-SD Binding Triple) acp:acp2	acp:appliedTo		sd:sd1

(old ACP-SD Binding Triple)  acp:acp1	acp:appliedTo		sd:sd1

- Step 5: The Hosting CSE sends an SPARQL request to replace the old ACP-SD Binding Triple in the SGS with the new ACP-SD Binding Triple as shown in above Step 4. This SPARQL request for this example is shown below:

@PREFIX 	acp: 	<http://accessControlPolicy.org> .

@PREFIX	sd:	<http:semanticDescriptor.org> .

DELETE

{ ?acp	acp:appliedTo   sd:sd1 }

WHERE

{

?acp	acp:appliedTo   sd:sd1

}

INSERT DATA

{ acp:acp2    acp:appliedTo	sd:sd1 . }

- Step 6: The SGS processes the SPARQL request and updates the specified ACP-SD Binding Triples in Step 5.

- Step 7: The SGS sends a response to the Hosting CSE to inform it if the SPARQL request in Step 5 is successfully performed.

Note:

If the accessControlPolicyIDs attribute of the <semanticDescriptor> resource was empty to start with, its parent resource’s accessControlPolicyIDs may be enforced. The hosting CSE will apply this step based on updates to the accessControlPolicyIDs attribute of the parent resource.

Figure 8.11.2.3-1: Procedure for updating ACP-SD binding triples in the SGS

#### 8.11.2.4	Procedure for updating SD relationship triples in SGS

Figure 8.11.2.4-1 shows the procedure for updating SD Relationship Triples when the descriptor attribute of a <semanticDescriptor> resource is changed.

For example, the descriptor of the sd1 resource created earlier is changed to have two SD Original Triples (Old one – “S1  P1  O1”; New one – “S2  P2  O2”).

The following steps are performed:

- Step 1: The Originator sends a request to update the resource sd1’s descriptor to include one new SD Original Triple (i.e. “S2  P2  O2”). The URI of the resource sd1 (i.e. sd1URI) is also contained in this request.

- Step 2: The Hosting CSE checks access rights. If it is allowed, the Hosting CSE updates sd1’s descriptor attribute by adding one new SD Original Triple (i.e. “S2  P2  O2”).

- Step 3: The Hosting CSE sends a response back to the Originator to inform it if the request in Step 1 is successful or not.

- Step 4: The Hosting CSE generates new SD Relationship Triples below to reflect this change.

  - In our example:

sd:tripleInstance12 	rdf:type		sd:sdOriginalTriple .

sd:tripleInstance12	sd:describedIn		sd:sd1 .

sd:tripleInstance12	sd:hasSubject		sd:S2 .

sd:tripleInstance12	sd:hasProperty	sd:P2 .

sd:tripleInstance12	sd:hasObject		sd:O2 .

- Step 5: The Hosting CSE sends an SPARQL request to replace old SD Relationship Triples and/or add new SD Relationship Triple in the SGS with the new SD Relationship Triple generated in above Step 4. This SPARQL request for this example is shown below:

@PREFIX 	acp: 	<http://accessControlPolicy.org> .

@PREFIX 	sd: 	<http://semanticDescriptor.org> .

INSERT DATA

{ sd:tripleInstance12 	rdf:type		sd:sdOriginalTriple .

sd:tripleInstance12	sd:describedIn		sd:sd1 .

sd:tripleInstance12	sd:hasSubject		sd:S2 .

sd:tripleInstance12	sd:hasProperty	sd:P2 .

sd:tripleInstance12	sd:hasObject		sd:O2 .

}

- Step 6: The SGS processes the SPARQL request and adds new SD Relationship Triples

- Step 7: The SGS sends a response to the Hosting CSE to inform it if the SPARQL request in Step 5 is successfully performed.

Notes:

If an old SD Original Triple is removed or updated by a new SD Original Triple, the corresponding SD Relationship Triples related to this old SD Original Triple will be removed from the SGS.

The update of triples in the descriptor attribute may be performed also by targeting the  semanticOpExec attribute of the <semanticDescriptor> parent resource  with a SPARQL query;  when this SPARQL query is executed, new SD Original Triples may be added to the descriptor attribute of the <semanticDescriptor> resource. In this case Steps 4 – 7 will be performed. More specifically, SPARQL Update consists of DELETE and ADD operations, so the SD relationship triples associated with the old original triples will be deleted, and the new ones stored.

Figure 8.11.2.4-1: Procedure for updating SD relationship triples in the SGS

#### 8.11.2.5	Procedure for deleting SD relationship triples and ACP-SD binding triples in SGS

Figure 8.11.2.5-1 shows a procedure for deleting SD Relationship Triples and ACP-SD Binding Triples from the SGS, which could be triggered by the Initiating AE/CSE or the Hosting CSE to delete a <semanticDescriptor> resource.

For example, the sd1 resource created earlier is removed.

The following steps are performed.

- Step 1: The Originator sends “Delete <semanticDescriptor> Resource” to the Hosting CSE to delete sd1 resource. The URI of sd1 resource (i.e. sd1URI) is contained in this request.

- Step 2: The Hosting CSE deletes sd1 resource locally.

- Step 3: The Hosting CSE sends a response to the Originator to inform it if the deletion request in Step 1 is successful.

- Step 4: The Hosting CSE sends an SPARQL request to the SGS to remove SD Relationship Triples and ACP-SD Binding Triples related to sd1 resource. The SPARQL will look like:

@PREFIX   	acp: 	<http://accessControlPolicy.org>.

@PREFIX	sd:	<http:semanticDescriptor.org> .

DELETE

{ ?sd	?p	?o

?tripleInstance	  ?p1	?o1

?acp	acp:AppliedTo	?sd

}

WHERE

{

?sd	?p	?o.

?tripleInstance	  ?p1	?o1.

?tripleInstance	sd:describedIn	?sd .

?acp	acp:AppliedTo	?sd

FILTER ( ?sd = sd:sd1)

}

- Step 5: The SGS processes the SPARQL request in Step 4 and removes corresponding SD Relationship Triples and ACP-SD Binding Triples.

- Step 6: The SGS sends a response to the Hosting CSE to inform it if the SPARQL request in Step 4 is successfully performed.

Note:

Steps 4 – 6 will also be performed if a SPARQL query targeting the semanticOpExec attribute of a <semanticDescriptor> resource results in the deletion of existing SD Original Triples.

Figure 8.11.2.5-1: Procedure for deleting SD relationship triples and ACP-SD binding triples from the SGS

# 9	Conclusions

The following text is to be used when appropriate:

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex A:
Use Cases

Editor’s Note: Updated and new use cases related to semantics can be added in this Annex.

A.1	Introduction

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V.1.1.1 | <dd Mmm yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 14-Oct-2016 | Created first draft |
| V.0.1.0 | 28-Oct-2016 | Included TP25 contributions: MAS-2016-0224R01-ACP_Synchronization_for_TR-0007 MAS-2016-0228R01-TR-0007_semanticDescriptor_validation |
| V.0.2.0 | 31-Dec-2016 | Included missing TP25 contribution: MAS-2016-0229R02-Semantic_Graph_Scoping Included TP26 contributions: MAS-2016-0265R01-Semantic_Mashup_Function MAS-2016-0266-Access_Control_section_move_TR-0033 MAS-2016-0267-Sync_SD_related_triples MAS-2016-0268R01-SemanticDescription_section_move_TR-0033 MAS-2016-0281-Requirements_move_TR-0033 |

# Text boxes

Access Control Ontology

@

prefix rdf

:

<

http

://

www

.

w

3

.

org

/

1999

/

02

/

22

-

rdf

-

syntax

-

ns

#>

.

@

prefix rdfs

:

<

http

://

www

.

w

3

.

org

/

2000

/

01

/

rdf

-

schema

#>

.

@

prefix xsd

:

<

http

://

www

.

w

3

.

org

/

2001

/

XMLSchema

#>

.

@

prefix acp

:

<

http

://

accessControlPolicy

.

org

/

>

.

@

prefix ex

:

<

http

://

example

.

org

/

>

.

@

prefix m

2

m

:

<

http

://

oneM

2

M

.

org

/

>

.

acp

:

accessControlPolicy rdf

:

type rdfs

:

Class

.

acp

:

accessControlRule rdf

:

type rdfs

:

Class

.

acp

:

hasACPRule

rdf

:

type

rdf

:

Property

;

rdfs

:

domain

acp

:

accessControlPolicy

;

rdfs

:

range

acp

:

accessControlRule

.

acp

:

hasACOriginator

rdf

:

type

rdf

:

Property

;

rdfs

:

domain

acp

:

accessControlRule

;

rdfs

:

range

m

2

m

:

AE

_

ID

,

m

2

m

:

CSE

_

ID

,

xsd

:

anyURI

.

acp

:

hasACContexts

rdf

:

type

rdf

:

Property

;

rdfs

:

domain

acp

:

accessControlRule

;

rdfs

:

range

m

2

m

:

ipv

4

,

m

2

m

:

ipv

6

,

m

2

m

:

contryCode

,

rdfs

:

Literal

.

acp

:

hasACOperations

rdf

:

type

rdf

:

Property

;

rdfs

:

domain

acp

:

accessControlRule

;

rdfs

:

range

m

2

m

:

accessControlOperations

,

rdfs

:

Literal

.

acp

:

appliedTo

rdf

:

type

rdf

:

property

;

rdfs

:

domain

acp

:

accessControlPolicy

;

rdfs

:

range

xsd

:

anyURI

,

rdfs

:

Literal

,

m

2

m

:

ID

,

ex

:

resourceGroup

.

Access Control Triples

ontologyRef=’OntologyH’

sensor12-AE

semanticDescriptorX

descriptor

humidityContainer

…

<rdf:Description rdf:about= “…/sensor12”

<rdf: type ont:humiditySensor/>

< ont:hasfunction rdf:resource=“…/humidityContainer” />

…

</rdf:Description>

…

< rdf:Description rdf:about=“…/humidityContainer”

<rdf:type ont:controllingFunction/>

…

</rdf:Description>

…

<rdf:Description rdf:about= “…/sensor12”

<rdf: type ont:humiditySensor/>

< ont:hasfunction rdf:resource=“…/humidityContainer” />

…

</rdf:Description>

…

< rdf:Description rdf:about=“…/humidityContainer”

<on:quantifies rdf:resource=“…/roomA/tempAspect”/>

…

</rdf:Description>

< rdf:Description rdf:about =“…/roomA/tempAspect”/>”

< m2m:resourceDescriptorLink rdf:resource=“…/semanticDescriptorR”/>

…

</rdf:Description>

…

< rdf:Description rdf:about =“…/tempAspect”/>”

<rdf:type rdf:resource=“ont:TemperatureAspect”/>

…

</rdf:Description>

linked <semanticDescriptor> hosting CSE

Issuer

CSE-1

IN-CSE

CSE-2

1. Create/Update/Retrieve <semanticDescriptor>

ontology hosting CSE

<semanticDescriptor> hosting CSE

3b. request to validate <semanticDescriptor>

4b. retrieve linked <semanticDescriptor>

5b. validate <semanticDescription> against referenced  ontology

6b. validation response

7. <semanticDescription>

validation status update

8. response

3a. retrieve referenced ontology

4a. validate <semanticDescription> against referenced  ontology

2. check linked <semanticDescriptor>

CASE1

CASE2