| oneM2M Technical Report |
| --- |
| Document Number | oneM2M-TR-0057-V-0.2.0 |
| Document Name: | Getting Started with oneM2M |
| Date: | 2019-02-26 |
| Abstract: |  |
| Template Version: January 2017 (Do not modify) |

The present document is provided for future development work within oneM2M only. The Partners accept no liability for any use of this report.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2019, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright and the foregoing restriction extend to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	5

2	References	5

2.1	Normative references	5

2.2	Informative references	5

3	Definitions of terms, symbols and abbreviations	5

3.1	Terms	5

3.2	Symbols	6

3.3	Abbreviations	6

4	Conventions,	6

5	oneM2M Overview	6

5.1	Introduction	6

5.1.1	oneM2M Service Layer	6

5.1.2	Functional Architecture description	9

5.1.3	Common Service functions	13

5.1.4	Benefits of using oneM2M	13

5.2	REST Architecture	15

5.3	Application Program Interfaces (API)	16

5.3.1	Introduction	16

5.3.2	oneM2M Primitives	16

5.3.2.1	Overview	16

5.3.2.2	Primitive structure	17

5.3.3	oneM2M Resources	19

5.3.3.1	Resource template	19

5.3.3.2	Resource structure	20

5.3.3.3	Resource attributes	21

5.3.3.4	Resource Schema	22

5.3.4	oneM2M Procedures	24

5.3.4.1	Access Resources in Local CSE	24

5.3.4.2	Access Resources in Remote CSE	24

5.3.4.3	CREATE operation	25

5.3.4.4	RETRIEVE operation	26

5.3.4.5	UPDATE operation	26

5.3.4.6	DELETE operation	27

5.2.4.7	NOTIFY operation	27

5.4	Data collection principles	27

5.4.1	Container	27

5.4.2	Access Control Policy	28

5.4.3	Subscription and Notification	30

5.4.4	Discovery	31

5.5	Data collection example	31

6	Core Functionalities	31

6.1	Introduction	31

6.x	Addressing modes	31

6.x	Retargeting	32

6.x	Access Control Policy	32

6.x	Subscription and Notification	32

6.x	Announcement	32

6.x	Block/NB sync/async modes	32

6.x	Long polling Channel	32

6.x	IPE	32

6.x	Group management	32

6.x	App-ID	32

7	Main feature descriptions	32

7.1	Introduction	32

7.2	3GPP Interworking	32

7.2.1	MTC	32

7.2.2	Cellular IoT	32

7.3	FlexContainer	33

7.4	Semantics	33

7.5	Industrial Domain	33

7.5.1	Time Series	33

7.5.2	Transaction	33

7.x	Security	33

7.x 	SDT	33

Proforma copyright release text block	33

Annexes	34

Annex <y>: Bibliography	34

History	35

# 1	Scope

The present document …

EXAMPLE:	The present document provides the necessary adaptions to the endorsed document.

The Scope shall not contain requirements.

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

As a Technical Report (TR) is entirely informative it shall not list normative references.

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions of terms, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Terms

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

If a definition is taken from an external source, use the format below where [N] identifies the external document which must be listed in Section 2 References.

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Abbreviation format

<ABBREVIATION1>	<Explanation>

<ABBREVIATION2>	<Explanation>

<ABBREVIATION3>	<Explanation>

# 4	Conventions,

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	oneM2M Overview

## 5.1	Introduction

### 5.1.1	oneM2M Service Layer

The architecture standardized by oneM2M defines an IoT Service Layer, i.e. a software Middleware sitting between processing / communication hardware and IoT applications providing a rich set of functions needed by many IoT applications.

It supports among others:

- secure end-to-end data/control exchange between IoT devices and custom applications by providing functions for proper identification

- authentication, authorization, encryption

- remote provisioning & activation

- connectivity setup

- buffering

- scheduling

- synchronization

- aggregation

- group communication

- device management

- etc…

oneM2M’s Service Layer is typically implemented as a software layer and sits between IoT applications and processing or communication hardware and operating system elements that provide data storage, processing and transport, normally riding on top of IP. However, non-IP transports are also supported via interworking proxies. The oneM2M Service Layer provides commonly needed functions for IoT applications across different industry segments.

- oneM2M defines a horizontal architecture providing common services functions that enable applications  in multiple domains, using a common framework and uniform APIs.

Using these standardized APIs make it much simpler for M2M/IoT solution providers to cope with complex and heterogeneous connectivity choices by abstracting out the details of using underlying network technologies, underlying transport protocols and data serialization. This is all handled by the oneM2M Service Layer without a need for the programmer to become an expert in each of these layers. Therefore, the application developer can focus on the process / business logic of the use case to be implemented and does not need to worry about how exactly the underlying layers work. This is very much like writing a file to a file system without worrying how hard disks and their interfaces actually work.

Therefore, the IoT Service Layer specified in oneM2M can be understood as a distributed operating system for IoT providing uniform APIs to IoT applications in a similar way as a mobile OS does for the smart phone eco system.

Figure 5.1.1-1: IoT Service layer

For example, the following “vertical” domains are isolated silos which makes it difficult to exchange data between each other. Using  a “horizontal” architecture allows the providion of a seamless interaction between applications and devices. In the below use case, a security application detects that when noboby is in the building, it triggers the switching off of the light and it stops the air conditioning.

Figure 5.1.1-2: IoT Cross-domain interoperability

- Cloud provider independent: From Fragmentation to Standards ( decoupling device, cloud, and application by open interfaces

Figure 5.1.1-3: Cloud provider independent

- Common IoT key problems solved by oneM2M

Figure 5.1.1-4: Common IoT key problems

- oneM2M in a nutshell:

oneM2M’s Service Layer corresponds to a software “framework”, located between the IoT applications and communication HW/SW that provide storage/connectivity/data transport.

It provides functions that IoT applications across different industry segments commonly need (eg. data transport, security/encryption, scheduling, event notifications, remote software update...)

It supports cooperative intelligence in distributed applications i.e. in devices, gateways and back-end/cloud applications

It supports a selection of underlying transport protocols and serialization formats

It is like an Operating System for the Internet of Things, sitting on field devices/sensors, gateways and in servers.

And, it is a standard – not controlled by a single private company.

### 5.1.2	Functional Architecture description

oneM2M Layered Model comprises three layers:

- the Application Layer,

- the Common Services Layer

- the underlying Network Services Layer.

Figure 5.1.2-1: oneM2M Layered Model

oneM2M entities:

The oneM2M functional architecture comprises the following functions:

Application Entity (AE): The Application Entity is an entity in the application layer that implements an M2M application service logic. Each application service logic can be resident in a number of M2M nodes and/or more than once on a single M2M node. Each execution instance of an application service logic is termed an "Application Entity" (AE) and is identified with a unique AE-ID.

Examples of the AEs include an instance of a fleet tracking application, a remote blood sugar measuring application, a power metering application or a pump controlling application.

Common Services Entity (CSE): A Common Services Entity represents an instantiation of a set of "common service functions" of the oneM2M Service Layer. A CSE is actually the entity that contains the collection of oneM2M-specified common service functions that AEs are able to use. Such service functions are exposed to other entities through the Mca (exposure to AEs) and Mcc (exposure to other CSEs) reference points. Reference point Mcn is used for accessing services provided by the underlying Network Service Entities such as waking up a sleeping device. Each CSE is identified with a unique CSE-ID.

Examples of service functions offered by the CSE include: data storage & sharing with access control and authorization, event detection and notification, group communication, scheduling of data exchanges, device management, and location services.

Underlying Network Services Entity (NSE): A Network Services Entity provides services from the underlying network to the CSEs.

Examples of such services include location services, device triggering, certain sleep modes like PSM in 3GPP based networks or long sleep cycles.

oneM2M Reference Points:

Figure 5.1.2-2: oneM2M Functional Architecture

The oneM2M functional architecture defines the following reference points:

- Mca: Reference point for the communication flows between an Application Entity (AE) and a Common Services Entity (CSE). These flows enable the AE to use the services supported by the CSE, and for the CSE to communicate with the AE. The AE and the CSE may or may not be co-located within the same physical entity.

- Mcc: Reference point for the communication flows between two Common Services Entities (CSEs). These flows enable a CSE to use the services supported by another CSE.

- Mcn: Reference point for the communication flows between a Common Services Entity (CSE) and the Network Services Entity (NSE). These flows enable a CSE to use the supported services provided by the NSE. While the oneM2M Service Layer is, usually independent of the underlying network – as long as it supports IP transport – it leverages specific M2M/IoT optimization such as 3GPP’s eMTC features (e.g. device triggering, power saving mode, long sleep cycles, etc).

- Mcc’: Reference point for the communication flows between two Common Services Entities (CSEs) in Infrastructure Nodes (IN) that are oneM2M compliant and that reside in different M2M Service Provider domains.

- Additional reference points are defined in oneM2M for specific purposes such as enrolment functions etc. and are not detailed in this overview.

oneM2M Nodes:

oneM2M has defined a set of Nodes that are logical entities identifiable in the oneM2M System. oneM2M Nodes typically contain CSEs and/or AEs. For the definition of Node types, oneM2M distinguishes between Nodes in the “Field Domain” – i.e. the domain in which sensors / actors / aggregators / gateways are deployed – and the “Infrastructure Domain” – i.e. the domain in which servers and applications on larger computers reside.

Figure 5.1.2-3: oneM2M node topology

Nodes can be of the following types:

- Application Dedicated Node (ADN): a Node that contains at least one AE and does not contain a CSE. It is located in the Field Domain. An ADN would typically be implemented on a resource constraint device that may not have access to rich storage or processing resources and – therefore – may be limited to only host a oneM2M AE and not a CSE. Examples for devices that would be represented by ADNs: simple sensor or actor devices.

- Application Service Node (ASN):  a Node that contains one CSE and contains at least one Application Entity (AE), located in the Field Domain. An ASN could be implemented on a range of different devices ranging from resource constraint devices up to much richer HW. Examples for devices that would be represented by ASNs: data collection devices, more capable sensors and actors including simple server functions.

- Middle Node (MN):  a Node that contains one CSE and could contain AEs. MNs are located in the Field Domain. There could be several MNs in the Field Domain of the oneM2M System. Typically an MN would reside in an M2M Gateway. MNs would be used to establish a logical tree structure of oneM2M nodes, e.g. to hierarchically aggregate data of buildings / neighborhoods / cities / counties / states etc.

- Infrastructure Node (IN):  a Node that contains one CSE and could contain AEs. There is exactly one IN in the Infrastructure Domain per oneM2M Service Provider. An example of physical mapping,  an IN could reside in an M2M Service Enablement Infrastructure.

- Non-oneM2M Node (NoDN): This Node type is not shown in the figure above. oneM2M specifications also define a Node Type for non-oneM2M Nodes which are Nodes that do not contain oneM2M Entities (neither AEs nor CSEs). Typically such Nodes would host some non-oneM2M IoT implementations or legacy technology which can be connected to the oneM2M system via interworking proxies.

### 5.1.3	Common Service functions

As a horizontal architecture providing a common framework for IoT, oneM2M has identified a set of common functionnalities, that are applicable to all the IoT domains. Think of these functions as a large toolbox with special tools to solve a number of IoT problems across many different domains. Very much like a screw driver can be used to fasten screws in a car as well as in a plane, the oneM2M CSFs are applicable to different IoT use cases in different industry domains.

In its first phase, oneM2M went through a large number of IoT use cases and identified a set of common requirements which resulted in the design of this set of tools termed Common Service Functions. Furthermore, oneM2M has standardized how these functions are being executed, i.e. is has defined uniform APIs to access these functions. Figure 5.3.1-1 shows a grouping of these functions into a few different scopes.

Figure 5.1.3-1: Common Service Functions

The services above reside within a CSE and are referred to as Common Services Functions (CSFs). The CSFs provide services to the AEs via the Mca reference point and to other CSEs via the Mcc reference point.

All these services are not specific to any IoT domain in particular. It enables each domain to build on the top of this service layer and really focus on its specific industrial needs. This is similar to functions of a generic operating system (OS) exposed to applications running on that OS. For instance, many applications read and write to files. File I/O is typically provided by the OS. oneM2M’s Service Layer provides similar functions in a generic way to many different IoT Applications.

### 5.1.4	Benefits of using oneM2M

- Service Layer on top of transport network  supporting a choice of transport protocols and serializations of data/messages

- Flexibility: it can be deployed on all domains, not tied to a particular protocol technology.

- IP based:  relies on known existing APIs to handle IP communications.

- Aware of optimizations if underlying network is 3GPP-based: can make use of policy-based scheduling, power saving mode, triggering /wakeup of devices, non-IP data transport, etc without the need for the developer to be aware of these terms.

- Enhances data sharing efficiency: communications over an underlying network are policed by provisioned policies that govern the use of network resources based on configurable categories of events/messages. Avoids storm of low-value messages in netoworks with costly resources. Lowers Opex.

- For example, in use cases with a need for fast & compact message exchanges one may want to rely on TCP sockets (opened via web sockets) and use binary serialization (e.g. CBOR) whereas in other cases a combination of HTTPS/JSON may be preferable for simpler debugging.

- Evolution: supported transport protocols and/or message serialization can evolve while the oneM2M code will not change. This allows for easy adaptation to future transport technologies.

- Horizontal platform provides common service functions that enable multiple IoT domains

- One investment/deployment serves multiple domains, does not re-invent the wheel. Lowers Capex.

- No need to maintain domain-specific platforms, reduction in Capex

- Cross-domain service/application innovation with a common framework and uniform APIs, allows for sharing of information and processes across domains that were isolated thus far (e.g. home security system versus heating system), Supports new business opportunities.

- Re-use of the code whatever the domain was. Increases reusability / lowers Capex.

- Easy interworking/integration with existing & evolving deployments paves the way to long term evolution and sustainable economy.

- Does not disrupt existing “vertical deployment”, but evolves it. Supports interworking with legacy technology.

- Interworking with a rich set of proximal IoT technologies, embracing different ecosystems.

- Takes advantage of the operators’ network capabilities and existing management technologies.

- Data sharing and semantic interoperability brings the real value.

- Data oriented RESTful API design.

- Semantic data annotation, discover and reasoning facilitates intelligent analytics and service mashups.

- Security protection at both channel and object level, with static and dynamic access control.

- Open standards to avoid lock-in to a platform or a cloud provider.

- No single party or company controls the technology / features.

- Several open source implementations available (CSE or AE).

- oneM2M is an international standard.

- Developed using standardization methodology that has insured successful interoperability in many technical domains, using the same process as in 3GPP.

- Developed by many companies based on consensus: it does not depend on a single or a small number of companies; not using a closed proprietary technology.

- It is an open standard: transparent development process & open access to all deliverables; all the specifications, even the drafts are available at http://www.onem2m.org/technical/latest-drafts

In summary, the oneM2M initiative can remove fragmentation of the IoT world. Because it is independent of the access or protocol technology that is used for transport, it is designed to be a long term solution for IoT deployment.

## 5.2	REST Architecture

Representational State Transfer (REST) is a software architectural style that defines a set of constraints to be used for creating web services.

RESTful services allow the requesting systems to access and manipulate textual representations of resources by using a uniform and predefined set of stateless operations. A stateless protocol operation does not require the server to retain session information or status about each communicating partner for the duration of multiple requests.

REST is not a protocol. It is about manipulating resources, uniquely identified by URIs. A resource is stateful and contains a link pointing to another resource. All the actions on resources are done through a Uniform Interface.

As REST is an architecture style, it can be mapped to multiple protocols such as HTTP, CoAP, etc…

Six guiding constraints define a RESTful system. These constraints restrict the ways in which the server can process and respond to client requests

- Client-server: separation of concerns is the principle behind the client-server constraints.

- Stateless server: request from client to server contains all of the information necessary to understand the request, and cannot take advantage of any stored context on the server.

- Cache: the client can reuse response data, sent by the server, by storing it in a local cache.

- Layered system: allows an architecture to be composed of hierarchical layers. It enables the addition of features like a gateway, a load balancer, or a firewall to accommodate system scaling.

- Code-on-demand: (optional) REST allows client functionality to be extended by downloading and executing code in the form of scripts (e.g. JavaScript).

- Uniform interface

  - Identification of resources:  resource identifier enables the identification of the particular resource involved in an interaction between components.

  - Manipulation of resources through representations: resource representations are the state of a resource that is transferred between components.

  - Self-descriptive messages: contain metadata to describe the meaning of the message.

  - Hypermedia as the engine of application state or HATEOAS: Clients find their way through the API by following links available in the resource representations.

## 5.3	Application Program Interfaces (API)

### 5.3.1	Introduction

The oneM2M REST APIs are used to manipulate data generated by the Application Entity (AE) to the oneM2M Service platform (CSE) as well as data retrieve services. The oneM2M REST APIs are developed for handling CRUD+N (Create, Retrieve, Update, Delete and Notification) operations for oneM2M resources specified in oneM2M standards.

The oneM2M API includes the following components:

- Primitives.

- Resources + Attributes.

- Data Types.

- Protocol Bindings .

- Procedures (CRUD+N).

The oneM2M API is used by CSEs and AEs to communicate with one another. The communication can be originated from an AE or CSE depending on the operation.

Communication is done via the exchange of oneM2M primitives across the oneM2M defined reference points (Mca/Mcc/Mcc’).

Primitives are used to perform CRUD+N operations on resources hosted by CSEs or to send notifications to AEs. Each CRUD+N operation is comprised of a pair of Request and Response primitives.

Access and manipulation of the resources is subject to access control privileges.

### oneM2M Primitives

#### 5.3.2.1	Overview

Primitives are service layer messages transmitted over the Mca/Mcc/Mcc’ reference points.

Originators send requests to Receivers via primitives. Originator and Receiver can be an AE or a CSE.

Each CRUD+N operation consists of one request and one response primitive.

Figure 5.3.2.1-1: General primitives flow

Primitives are binded to underlying transport layer protocols such as HTTP, CoAP , MQTT or WebSocket. Primitives are generic with respect to underlying network transport protocols. Each primitive is binded to zero or more messages in the transport layer.

Figure 5.3.2.1-2: oneM2M Communications

#### 5.3.2.2	Primitive structure

A primitive consists of two parts; control and content.

- The control part: contains parameters required for the processing of the primitive itself (e.g. request or response parameters).

- The content part is optional based on the type of primitive and contains the representation of the resource consisting of all or a subset of the resource attributes.

Figure 5.3.2.2-1: Primitive structure

Primitives are encoded and serialized based on the particular oneM2M protocol binding being used.

The originator and receiver of each primitive use the same binding, and thus use compatible forms of encoding/ decoding and serialization/de-serialization.

During transfer, the control part is encoded based on the protocol binding being used and the content portion is serialized using XML, JSON and CBOR.

oneM2M Request Primitive: oneM2M short names HTTP/1.1 Method: POST ( op : Operation URI: m2msp1.com/CSE01Base ( to : To URI Query String: ?rcn=1 ( rcn : Result content From: ae01.com ( fr : From X-M2M-RI:0001 ( rqi : Request identifier X-M2M-RVI: 2a ( rvi : Release Version Indicator Content: <AE> representation ( pc: primitive content oneM2M Response Primitive: Status: Created ( rsc :Response Status Code Location: http//m2msp1.com/CSE01Base/ae01 ( uri : URI X-M2M-RI:0001 ( rqi : Request identifier Content: <AE> representation created ( pc: primitive content

Figure 5.3.2.2-2: Example of Control part binded to HTTP

The Content part of a primitive contains serialized representation of a resource. oneM2M supports XML, JSON or CBOR serializations of resources.

This is an example of a oneM2M <container> resource representation in JSON format.

This is an example of a oneM2M <container> resource representation in XML format.

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cont_temp">

<ty>3</ty>

<ri>server/cnt-2951972863155866584</ri>

<pi>server</pi>

<ct>20181114T145000</ct>

<lt>20181114T145000</lt>

<et>20181114T145000</et>

<st>0</st>

<mni>10000</mni>

<mbs>0</mbs>

<mia>0</mia>

<cni>0</cni>

<cbs>0</cbs>

</m2m:cnt>

### oneM2M Resources

#### Resource template

All entities in the oneM2M System, such as AEs, CSEs, application data representing sensors, commands, etc. are represented as resources in the CSE.  Each resource has its own specific type.

Each resource type has a defined set of mandatory and optional attributes as well as child resources.

A resource can contain child resources.

Each resource is addressable and can be the target of CRUD operations specified in oneM2M primitives.

Figure 5.3.3.1-1 : Resource template

| Resource Type | Short Description |
| --- | --- |
| accessControlPolicy | Controls "who" is allowed to do "what" and the context in which it can be used for accessing the resources |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE |
| container | Used to shares data instances among entities |
| contentInstance | Represents a data instance in the <container> resource. |
| CSEBase | The structural root for all the resources that are residing on a CSE. It stores information about the CSE itself |
| delivery | Forwards requests from CSE to CSE |
| eventConfig | Defines events that trigger statistics collection |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd |
| fanOutPoint | Used for addressing bulk operations to all the resources that belong to a group. |
| group | Stores information about resources of the same type that need to be addressed as a Group. |
| locationPolicy | Includes information to obtain and manage geographical location. |
| mgmtCmd | Represents a method to execute management procedures required by existing management protocols |
| mgmtObj | Represents management functions that provides an abstraction to be mapped to external management technology. |
| node | Represents specific Node information |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE |
| schedule | Contains scheduling information for delivery of messages |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications |
| statsConfig | Stores configuration of statistics for applications |
| subscription | Represents subscription information related to a resource. |

Table 5.3.3.1-1 : Resource type examples

#### 5.3.3.2	Resource structure

The root of the oneM2M resource structure is <CSEBase>.

The <CSEBase> is assigned an absolute address.  All other child resources are addressed relative to <CSEBase>.

Depending on the type of child resource it is instantiated 0..n times.

Figure 5.3.3.2-1 : <CSEBase> Resource example

#### 5.3.3.3	Resource attributes

Each resource contains attributes that store information pertaining to the resource itself.

The attributes are :

- Universal Attributes : which appear in all resources

- Common Attributes : which appear in more than one resource and have the same meaning whenever they do appear.

- Resource-specific attributes

Figure 5.3.3.3-1: <AE> Resource example

| Universal Attribute | Description |
| --- | --- |
| resourceType | Identifies the type of resource |
| parentID | resourceID of the parent of this resource. |
| creationTime | Time/date of creation of the resource. |
| lastModifiedTime | Last modification time/date of the resource. |
| resourceID | Identifier for resource. |
| resourceName | Name of the resource |

Table 5.3.3.3-1 : Universal resource attributes

#### 5.3.3.4	Resource Schema

oneM2M defines XML, JSON and CBOR schemas which define the attributes of each resource type.

Schemas bind oneM2M attributes to well-known data types defined by XML Schema definitions (e.g. xs:string, xs:anyURI, etc …).

Schemas also bind oneM2M attributes to oneM2M defined  data types (e.g. m2m:id, m2m:stringList, etc ...).

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:include schemaLocation="CDT-commonTypes-v3_8_0.xsd" />

<xs:include schemaLocation="CDT-subscription-v3_8_0.xsd" />

<xs:element name="request" substitutionGroup="m2m:sg_regularResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes -->

<xs:extension base="m2m:regularResource">

<xs:sequence>

<!-- Common Attribute, specific to <container>, <contentInstance>, <request> and <delivery> resources -->

<xs:element name="stateTag" type="xs:nonNegativeInteger" />

<!-- Resource Specific Attributes -->

<xs:element name="operation" type="m2m:operation" />

<xs:element name="target" type="xs:anyURI" />

<xs:element name="originator" type="m2m:ID" />

<xs:element name="requestID" type="m2m:requestID" />

<xs:element name="metaInformation" type="m2m:metaInformation" />

<xs:element name="primitiveContent" type="m2m:primitiveContent" minOccurs="0" />

<xs:element name="requestStatus" type="m2m:requestStatus" />

<xs:element name="operationResult" type="m2m:operationResult" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:subscription"></xs:element>

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

</xs:schema>

Figure 5.3.3.4-1: Example of schema

### 5.3.4	oneM2M Procedures

#### 5.3.4.1	Access Resources in Local CSE

Figure 5.3.4.1-1 : Access Resources in Local CSE

#### 5.3.4.2	Access Resources in Remote CSE

Figure 5.3.4.2-1 : Access Resources in Remote CSE

#### 5.3.4.3	CREATE operation

Figure 5.3.4.3-1 : CREATE operation

#### 5.3.4.4	RETRIEVE operation

Figure 5.3.4.4-1 : RETRIEVE operation

#### 5.3.4.5	UPDATE operation

Figure 5.3.4.5-1 : UPDATE operation

#### 5.3.4.6	DELETE operation

Figure 5.3.4.6-1 : DELETE operation

#### 5.2.4.7	NOTIFY operation

Figure 5.3.4.7-1 : NOTIFY operation

## 5.4	Data collection principles

### 5.4.1	Container

- Container for data instances is represented by the <container> resource.

  - Data storage used to share information with other entities and track data.

- <container> resource has no associated content.

  - Only attributes and child resources are available.

  - Actual data/content is stored in <contentInstance> child resource.

- <container>  is the only resource allowed to have recursive child resources.

  - <container> resource can have other <container> as  child resources.

  - useful for representing hierarchical data structure.

Figure 5.4.1-1: Example of resources tree

### 5.4.2	Access Control Policy

- Access Control Policies (ACPs) are used by the CSE to control access to the resources.

- The resources are always linked to Access Control Policies. ACPs are shared between several resources

- Access Control Policies contain the rules (Privileges) defining:

  - WHO can access the Resource (e.g. Identifiers of authorized AE/CSE).

  - For WHAT operation (CREATE / RETRIEVE / UPDATE / DELETE…).

  - Under WHICH contextual circumstances (Time, Location, IP address).

- ACPs are represented by <accessControlPolicy> resources.

  - Comprised of attributes privileges and selfPrivileges that represent a set of access control rules for entities.

<accessControlPolicy> resource content:

<m2m:acp xmlns:m2m="…" rn="">

<pv>

<acr>

<acor></acor>

<acop></acop>

</acr>

</pv>

<pvs>

<acr>

<acor></acor>

<acop></acop>

</acr>

</pvs>

</m2m:acp>

Signification

- acr = « Access Control Rule »

- acor = « Access Control Originators »

- acop = « Access Control Operations »

Operation Code

- CREATE 			1

- RETRIEVE 		2

- UPDATE 			4

- DELETE 			8

- NOTIFY 			16

- DISCOVERY 	32

Example:

<pv>

<acr>

<acor>admin</acor>

<acop>63</acop>

</acr>

</pv>

<pvs>

<acr>

<acor>guest</acor>

<acop>34</acop>

</acr>

<pvs>

- Common attribute accessControlPolicyIDs link resources that are not <accessControlPolicy> resources to <accessControlPolicy> resources.

  - All resources are accessible only if the privileges from the ACP grants it.

  - All resources have an associated accessControlPolicyIDs attribute, either explicitly or implicitly.

Figure 5.4.2-1 : Access control policy verification example

### 5.4.3	Subscription and Notification

- Events generated by resources can be received using the <subscription> resource.

- The <subscription> resource contains subscription information for its "subscribed-to" resource.

  - <subscription> resource is a child resource of the "subscribed-to" resource.

- The originator (resource subscriber) has RETRIEVE privileges to the "subscribed-to" resource in order to create the <subscription> resource.

- Notification policies specified in the attributes can be applied to the <subscription>.

  - Specify which, when, and how notifications are sent.

  - Example: batchNotify – receive batches of notification rather than one at a time.

Figure 5.4.3-1 : Subcription and notification example

### 5.4.4	Discovery

- Resource Discovery Capabilities

  - Under the RESTful architecture, Resource Discovery can be accomplished using RETRIEVE operation by an Originator.

  - The use of the filterCriteria parameter allows limiting the scope of the results.

    - Type, Labels, Content Size and so on can be configured in the parameter.

Figure 5.4.4-1 : Discovery example

## 5.5	Data collection example

Editor note: to provide a basic example scenario using data collection + Subscription/Notification

# 6	Core Functionalities

## 6.1	Introduction

Editor notes: here are examples clauses that could be addressed to simply describe Core Fonctionalities. It is here for information and the list could be revised.

## 6.x	Addressing modes

## 6.x	Retargeting

## 6.x	Access Control Policy

## 6.x	Subscription and Notification

## 6.x	Announcement

## 6.x	Block/NB sync/async modes

## 6.x	Long polling Channel

## 6.x	IPE

## 6.x	Group management

## 6.x	App-ID

# 7	Main feature descriptions

## 7.1	Introduction

## 7.2	3GPP Interworking

### 7.2.1	MTC

### 7.2.2	Cellular IoT

## 7.3	FlexContainer

## 7.4	Semantics

## 7.5	Industrial Domain

### 7.5.1	Time Series

### 7.5.2	Transaction

## 7.x	Security

- 7.x.1 Introduction

- Dynamic Authorization

- Distributed Authorization

- End to end

## 7.x 	SDT

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A>:
Title of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>:
Title of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself.

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <yyyy-mm-dd> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V0.0.1 | 2018-11-10 | Initial draft |
| V0.1.0 | 2018-12-10 | Implemented contribution agreed at ARC#38 ARC-2018-0317R01-TR-0057-oneM2M-overview_clause_5 |
| V0.2.0 | 2019-02-26 | Implemented contribution agreed at SDS#39 SDS-2019-0110R03-TR-0057_oneM2M_overview |

# Text boxes

Application
Service
Node

Application
Dedicated
Node

Application
Dedicated
Node

Application
Dedicated
Node

Middle Node

Middle Node

Middle Node

Infrastructure Node

AE

AE

AE

AE

AE

CSE

CSE

CSE

AE

CSE

AE

AE

CSE

CSE

{

"m2m:cnt": {

"cbs": 0,

"cni": 0,

"ct": "20180406T085712",

"et": "99991231T235959",

"lt": "20180406T085712",

"mbs": 60000000,

"mia": 1600,

"mni": 10000,

"pi": "CAE0120180406T084680_cse01",

ri": "cnt20180406T08571214_cse01",

"rn": "cont_temp",

"st": 0,

"ty": 3

}

}

cnt : container

cbs : currentByteSize

cni : currentNrOfInstances

ct : creationTime

et : expirationTime

lt : lastModifiedTime

mbs : maxByteSize

mia : maxInstanceAge

mni : maxNrOfInstance

pi : parentID

ri : resourceID

rn :resourceName

st : stateTag

ty : resourceType

Privileges:

Manage the right for resources of this ACP

Self-privileges:

Manage the right to access or modify this resource. It defines who can set an Access Control Policy

Combinations of these values are specified by adding them together. For example the value 5 is interpreted as "CREATE and UPDATE".

63 grants all rights

34 grants Retrieve and Discovery rights