| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | Mapping between Requirements TS and CSF’s |
| Source:* | Laurent Laporte, Sprint, laurent.laporte@sprint.com Rajesh Bhalla, ZTE, rabhalla@ztetx.com Omar Elloumi, Alcatel-Lucent, omar.elloumi@alcatel-lucent.com |
| Contact: |  |
| Date:* | 2013-09-03 |
| Abstract:* | This document presents the output of an action item assigned to Laurent Laporte, Rajesh Bhalla, and Omar Elloumi as a result of the discussion of document oneM2M-ARC-2013-0320R01 |
| Agenda Item:* | tbd |
| Work item(s): | WI-0001, WI-0002 |
| Document(s) Impacted* | Requirements TS, Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | tbd |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

This contribution presents the output of an action item that was assigned to Laurent Laporte, Rajesh Bhalla, and Omar Elloumi as a result of discussion regarding document oneM2M-ARC-2013-0320R01 during the September 12th meeting.  Specifically, the thirty two identified requirements that were identified as not mapped to a CSF were examined and discussed.  These requirements are:

- OSR-1, OSR-009, OSR-015, OSR-022, OSR-028, OSR-034, OSR-041, OSR-057, OSR-058

- MGR-003, MGR-010, MGR-016

- ABR-001, ABR-002, ABR-003

- SMR-001, SMR-002, SMR-003, SMR-005, SMR-007

- SER-004. SER-005, SER-006, SER-007, SER-011, SER-013, SER-015, SER-018, SER-019, SER-020, SER-023, SER-024

Results and Discussion

Almost every remaining requirement in the above list was mapped to a CSF either in whole or in part.  The need for two additional CSFs was identified. The results are shown below:

- New CSFs recommended:

  - “Semantics/Abstraction” CSF:

    - ABR-002

    - ABR-003

    - SMR-001

    - SMR-002

    - SMR-003

    - SMR-005

    - SMR-007

  - “Interworking” CSF:

    - OSR-028

- Mapping between existing CSF and requirement:

  - DMR

    - OSR-034

    - OSR-058

    - SER-015

  - DMG

    - MGR-003

  - CMDH

    - MGR-016

  - SEC

    - SER-004 – SER-006

    - SER-011

    - SER-018 – SER-020

    - SER-023,-024

- Mapping to two or more CSF:

  - OSR-001 – CMDH and DMR

  - OSR-009 – CMDH, DMR, and SMG

  - MGR-010 – REG and SEC

  - SER-007 – SEC and SMG

  - SER-013 – DMG and SEC

  - OSR-015 – CMDH and/or DMR (enhanced CSF description will be needed)

- Enabler Functions:

  - OSR-022

  - OSR-041

- Applicable to protocol design:

  - OSR-041

  - OSR-057

- Should be re-examined by WG1 since it appears to specify a solution:

  - ABR-001

Proposal

The following paths forward are proposed:

- Modify descriptions of existing CSFs as needed based upon the above mappings;

- Draft sections for new CSFs based upon the requirements identified in the first bullet as needed for the initial release;

- Enhance Enabler Functions to include requirements OSR-022 and -041;

- Work with WG3 to resolve the disposition of requirements OSR-041 and -057;

- Remand the issue of ABR-001 to WG1 for further discussion and evaluation;

- Incorporate the table from this document into an Appendix to the TS xyz.

Proposed informative Annex to  TS-0001:

CSF Name: Long form name of the CSF in question

Supported Sub-functions: list of  sub-functions taken from the associated CSF description for a CSF name

Requirements: Requirements that map in whole or in part to the CSF

Notes: field for any pertinent comments, including identified overlap for requirements

| CSF Name | Supported Sub-functions | Requirements | Notes |
| --- | --- | --- | --- |
| Addressing and Identification (AID) | Management of identifiers | OSR-026, -023, -024, -025 | Overlap w/: DSC for OSR-023,-024, and -025 |
| Security (SEC) | Sensitive Data Handling Secure storage Secure execution Independent environments Security administration Pre-provisioning Dynamic bootstrap Network bootstrap Security association Link level Object level Authorization and access Identity protection | SER-001,-002, -003, -004, -005, -006, -007, -008, -009, -010, -011, -012, -013, -016, -017, -018, -019, -020, -021, -022, -023, -024, -025 MGR-010 | Overlap w/: DMG for SER-013 REG for MGR-010 SMG for SER-007 |
| Session management (SMG) | Session management (CSE to CSE, Application to CSE, and Application to Application) Session persistence over link outage Session context handling Assignment of session ID Session routing Multi-hop session management Session policy management | OSR-003, -004, -009, -045 SER-007 | Overlap w/: CMDH and DMR for OSR-009 SEC for SER-007 |
| Service Charging and Accounting (SCA) | Charging enablers Sending charging information to charging server Subscription-based charging Event-based charging Session-based charging Service-based charging Correlation with Underlying Network Charging management Offline charging Online charging | CHG-001, -002a, -002b, -003, -004, -005 |  |
| Data Management and Repository (DMR) | Data storage and management Semantic support Data aggregation Data analytics Device data backup and recovery | OSR-001, -007, -009, -016, -020, -021, -032, -034, -036, -058 SMR-006 SER-015 | Overlap w/: CMDH for OSR-001, -009, -021, -032 SUB for OSR-016 GMG for OSR-020 . |
| Communication Management / Delivery Handling (CMDH) | Providing communications with other CSE’s, AE’s, and NSE’s Communications management: best effort Communications policy management Underlying Network connectivity management Communications management: data store and forward Ability to trigger off-line device | OSR-001,-002, -005, -006, -008, -009, -012, -013, -014, -015, -018, -019, -021, -027, -032, -035, -038, -039, -040, -048, -049, -050, -053, -062, -063, -064, -065, -066, -067, -068 CRPR-001, -002, -003 MGR-016 | Overlap w/: DMR for OSR-001, -009, -021, -032 SMG for OSR-009 LOC for OSR-006 GMG for OSR-006 NSE for OSR-006, -027 SMG for OSR-009 |
| Device Management (DMG) | Configuration Management Diagnostics and Monitoring Firmware management Software management Device Area Network topology management | OSR-017,-069,-070,-071 OPR-001, -002, -003 MGR-001, -003, -004, -006, -007, -008, -009, -011, -012, -013, -014, -015, -019, -020, -021 SER-013, -014 | Overlaps w/: GMG for OSR-017 SEC for SER-013 |
| Discovery (DIS) | Discover resource Local discovery (within CSE) Directed remote discovery | OSR-023, -024, -025, -059, -060, -061 MGR-002 SMR-004 | Overlaps w/: AID for OSR-023, -024, -025 |
| Location (LOC) | Location management Network-provided GPS-provided Confidentiality enforcement as it relates to location | OSR-006, -051, -052 SER-026 |  |
| Registration (REG) | CSE registration Application registration Device registration ID correlation | MGR-010 | Overlaps w/: SEC |
| Subscription/Notification Support (SUB) | Subscribe (CS, Application) Local Remote Subscription to a group Notification Synchronous asynchronous | OSR-010, -016, -033 | Overlaps w/: DMR for OSR-016 |
| Network Service Exposure / Service execution and triggering (NSE) | Access Underlying Network service Location Device triggering Small data Policy and charging Support multiple Underlying Network functions | OSR-006, -011, -027, -037, -054, -055, -056 MGR-017, -018 OPR-004, -005, -006 | Overlaps w/: CMDH for OSR-027 GMG for OSR-006, -037 LOC for OSR-006 |
| Group Management (GMG) | Management of a group and its membership CRUD Use Underlying Network group capabilities Bulk operations Access control | OSR-006, -017, -020, -029, -030, -031, -037, -047 MGR-005 | Overlaps w/: CMDH for OSR-006 LOC for OSR-006 GMG for OSR-006 NSE for OSR-006, -037 DMR for OSR-020 DMG for OSR-017 |