| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2(ARC) |
| Title:* | Usage patterns |
| Source:* | FUJITSU(TTC) |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2013-10-03 |
| Abstract:* | Adding sage patterns as appendix part of TS |
| Agenda Item:* | Detail consideration on CSF functionalities |
| Work item(s): | WI- |
| Document(s) Impacted* | TS- |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG member should agree on inclusion of proposed texts. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

WG member realized some needs to share the understandings regarding interaction between CSF, which was proposed as oneM2M-ARC-2013-0383.

This contributions proposed to add new Appendix part on Architecture-TS to describe possible Usage Scenarios for typical usage of M2M Platform system.

=== PROPOSED TEXTS STARTS HERE ===

Ax		Usage Scenarios

These sections describe typical interactions between CSFs. Since actual interactions between CSFs are up to implementation, these usage scenarios are informative.

Ax.1	Storing data to M2M Platform from M2M Device

Ax.1.1	Basic scenario

[Scenario]

- M2M Device measures the resource value, and it upload the measured value to URI to post.

- M2M Platform System provides API to accept request to store the data sent by M2M Device

- When data is successfully updated, URI to access the stored data will be issued.

[Involved CSFs]

- Communication Management and Delivery Handling CSF: CMDH

- Security: SEC

- Addressing and Identification  CSF: AID

- Data Management and Repository CSF: DMR

[Pre condition]

- M2M Device is configured to update data on the M2M Platform System periodically.

- M2M Device has authentication credential to be authenticated by M2M Platform

- M2M Device has a URI to store the uploading data

[Trigger Event]

Scheduled timer managed by CMDH[D] is fired

[Interactions]

- CMDH[D] triggers scheduled data update to store data (described as policy).

- CMDH[D] resolves the address of M2M System from URI to store the data.

- CMDH[D] establishes the connection to M2M System along with URI for storing data.

- DMR[P] asks SEC[P] to check whether CMDH[D] is allowed to update the resource specified by URI.

- SEC[P] returns the result of check.

- DMR[P] stores received data, and asks Identification  and AID [P] to assign new ID.

- DMR[P] notify the ID to CMDH[D].

[Post condition]

- New URI to refer stored data is assigned

- M2M Device and M2M Platform shares assigned URI

Ax.1.2	Alternate scenario 1

[Scenario]

- When size of updating data is large, M2M System may provide alternate path to transfer the data

[Involved CSFs]

- Communication Management and Delivery Handling CSF: CMDH

- Security: SEC

- Addressing and Identification  CSF: AID

- Data Management and Repository CSF: DMR

[Pre condition] (Added)

- M2M Device is configured to transfer the data in two step procedure

[Trigger Event]

Scheduled timer managed by CMDH[D] is fired

[Interactions]

- CMDH[D] triggers scheduled data update to store data (described as policy).

- CMDH[D] resolves the address of M2M System from URI to store the data.

- CMDH[D] establishes the connection to M2M System along with URI for storing data.

- DMR[P] asks SEC[P] to check whether CMDH[D] is allowed to update the resource specified by URI.

- SEC [P] returns the result of check.

- DMR[P] asks CMDH[P] to handle large data transfer

- CMDH[P] returns new URI to accept large data from M2M Device to DMR[P].

- DMR[P] returns URI to accept data to CMDH[D]

- CMDH[D] establishes the connection to  URI to transfer large data

- CMDH[P] handles transferred data to store the data from CMDH[D]

- CMDH[P] asks AID[P] to issue new ID for stored data.

- CMDH[P] notify assigned URI for stored data to CMDH[D]

[Post condition]

- New URI to refer stored data is assigned

- M2M Device and M2M Platform shares assigned URI

Ax.1.3	Alternate scenario 2

Ax.2	Retrieving data from M2M Platform System

Ax.1.1	Basic scenario

### Ax.1.2	Alternate scenario 1

### Ax.1.3	Alternate scenario 2

Ax.3	Subscribing changes of data on M2M Platform System

Ax.4	Notifying change of data on M2M Platform System

Ax.5	Authorizing M2M Application to refer the data on behalf of User

Ax.6	Changing device settings of M2M Device

Ax.7	Updating firmware on M2M Device

Ax.8	Triggering data upload to M2M Platform from M2M Device