| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 - Architecture |
| Title:* | Clarify Description of Reference Points, and add Y’ - R03 |
| Source:* | Richard Brennan, Telxxis LLC (TIA) rbrennan@telxxis.com |
| Contact: |  |
| Date:* | 2013--10-14 |
| Abstract:* | Provides clarifications to Clause 5.2.2 - Reference Points; a. R01: proposed text changes R02: renaming in alignment with oneM2M-ARC-2013-0388-Renaming_reference_pointsand additional text changes. Split into two proposed Changes R03: Change 1 as agreed at ARC #7 |
| Agenda Item:* | 6 |
| Work item(s): | oneM2M-WI-0002-Architecture-V1.1 |
| Document(s) Impacted* | oneM2M-TS-0001-Functional_Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agreement for inclusion in the output draft |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement..

Change 1: Existing text from: oneM2M-TS-0001 oneM2M Functional Architecture-V-0.1.1 Including re-naming from: oneM2M-ARC-2013-0388-Renaming_reference_points

### 5.2.2	Reference Points

The following reference points are supported by the Common Services Entity (CSE). The “Mc(-) nomenclature is based on the mnemonic “M2M communications”.

#### 5.2.2.1	Mca Reference Point

The Mca reference point designates communication flows between an Application Entity (AE) and a Common Services Entity (CSE). The Mca reference point shall allow an AE to use the services provided by the CSE, and for the CSE to communicate with the AE. The services offered via the Mca reference point are dependent on the functionality supported by the CSE.

NOTE: The AE and the CSE it invokes may or may not be co-located within the same node.

#### 5.2.2.2	Mcc Reference Point

The Mcc reference point designates communication flows between two Common Services Entities (CSEs). The Mcc reference point shall allow a CSE to use the services of another CSE in order to provide needed functionality. The services offered via the Mcc reference point are dependent on the functionality supported by the CSEs.

NOTE: The Mcc reference point between two CSEs may be supported between different M2M nodes.

Editor’s Note: In the event oneM2M develops specifications for more than one CSE implementation, the use of the Mcc reference point between them (for both intra-domain and inter-domain instances) would need elaboration, and is FFS. This requires coordination between the ARC and PRO working groups.

#### 5.2.2.3	Mcn Reference Point

The Mcn reference point designates communication flows between a Common Services Entity (CSE) and the Underlying Network Services Entity (NSE). The Mcn reference point shall allow a CSE to use the services (other than transport and connectivity services) provided by the Underlying NSE in order to provide needed functionality. The services offered via the Mcnreference point are dependent on the services provided by the Underlying NSE.

Editor’s Note: The following “NOTE” should be moved into clause 6.x

NOTE: Information exchange between two M2M nodes assumes the usage of the transport and connectivity services of the Underlying Network Services Entity, which are considered to be the basic services.

Editor's Note: While allowing for different instantiations of the CS Function into different functional Entities, this specification follows the following guidelines/principles while specifying the interfaces on the Mc(-) reference points:

•	Specification of the interfaces on reference points Mca and Mcc are independent of the functionality provided by the CSE.

•	Specification of the interfaces on reference point Mcn may take into account the functionality provided by the CSE.