| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | High Level Flow for M2M Service Connection |
| Source:* | LG Electronics |
| Contact: | Seungkyu Park, seungk.park@lge.com |
| Date:* | 2013-10-07 |
| Abstract:* | This contribution provides the high level flow for the M2M service connection. |
| Agenda Item:* | Tbd |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

In the current specification, the M2M bootstrapping, registration and M2M service connection are mentioned or implied. Although they are relying on each other, the relationship between them is not clearly described. This contribution tries to address the relationship and the prerequisites on each procedure.

## Beginning of Text ##

## 6.2 	High Level Flow for Service Connection

This section provides the description of the high level flow for the service connection between an Application and a CSE, or between CSEs.

Figure 6.2-x High Level Flow for Service Connection

M2M bootstrapping is the procedure to provision essential information (e.g., credentials) into the Application or to the CSE to enable the registration to the corresponding CSE. The Security CSF is involved in the M2M bootstrapping providing the credentials such as the root secret. The M2M bootstrapping might require the Application or the CSE uses the Underlying Network services such as transport and connectivity that is assured by the network connection. The network connection might be progressed by the network bootstrap and the network registration, but they are outside the scope of this specification.

After the successful M2M bootstrapping, the Application or the CSE is ready for the registration to the corresponding CSE, and the Registration CSF will perform the registration. During the registration, the context information regarding the Application or the CSE can be delivered to the corresponding CSE, and the credentials provisioned during the M2M bootstrap can be used.

Once the Application or the CSE is registered to the local CSE, the Application or the CSE can use the services offered by the local CSE through the M2M service connection. The M2M service connection can be made either in the session-oriented or session-less manner. For the secure M2M service connection, the Security CSF shall provide the security functions such as the authentication, the authorization and the confidentiality. Especially, the session-oriented M2M service connection is managed by the Session Management CSF.

In case of the multi-hop M2M service connection, every Application or CSE involved in the multi-hop M2M service connection shall be registered to the corresponding CSE for the request forwarding. However, the registration order does not matter.

For example, the Application Entity (AE) in the Application Service Node (ASN) can have the M2M service connection with the Application Entity in the Infrastructure Node (IN) through the CSE in the Middle Node (MN) if the followings are met:

- The AEs in the ASN and in the IN are bootstrapped

- The CSEs in the ASN and in the MN are bootstrapped

- The AE in the ASN is registered to the CSE in the ASN

- The CSE in the ASN is registered to the CSE in the MN

- The CSE in the MN is registered to the CSE in the IN

- The AE in the IN is registered to the CSE in the IN.

## End of Text ##