| CHANGE REQUEST |
| --- |
| Group Name:* | ARC WG |
| Source:* | NEC Corporation |
| Format:* | Plenary |
| Date:* | 2013-10-05 |
| Contact:* | Takanori Iwai, NEC, t-iwai@hx.jp.nec.com, Norio Uchida, NEC, n-uchida@cq.jp.nec.com, Ataru Kobayashi, NEC, a-kobayashi@df.jp.nec.com, JaeSeung Song, NEC Lab Europe, JaeSeung.Song@neclab.eu, Joerg Swetina, NEC Lab Europe, Joerg.Swetina@neclab.eu |
| Reason for Change/s:* | This contribution provides new resources for NSE-CSF. |
| Clause/Sub Clause Affected* |  |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | <A list of the designation of the relevant work item(s)> |
| Document(s) Impacted* | oneM2M-TS-0001-Functional_Architecture-V0_0_7- |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The group is kindly requested to review and agree the proposed changes. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Change 1: Define new resource types to leverage broadcasting/multicasting capability of Underlying Networks, in accordance with the resource template (oneM2M-ARC-2013-0036R04).

### 9.5.x	Resource bcastRequest

This resource represents a request to Underlying Networks of broadcasting / multicasting data to a group of M2M Devices in a specific area.

Figure 9.5.x-1: Structure of broadcastRequest resource 
(only child resources and specific resource attributes are shown)

The resource shall contain at least the following data elements.				(Mandatory)

Note: The representation of the resource is to be specified in Stage 3 documents or left to implementation.   Hypermedia formats such as HTML, microformat, ATOM or JSON may be used to represent a resource.  The applicability of Resource Description Framework (RDF) is a subject for a future study.

- Message Body: a datum to be sent to M2M Devices.  A string is expected in many cases, but any other format may be specified.

- Geographic Area: a set of values to specify a geographic area in which the Underlying Network broadcasts/multicasts the data.  
e.g. a circle (center, radius), ellipse (two focuses, long radius, short radius), rectangle (four points), polygon (multiple points), belt (center, width, length) with latitudes and longitudes, or Area ID pre-shared between the hosting CSE and the ASE.

- Duration Parameters: a set of values to specify how many times, how long the Underlying Network repeats broadcasting/multicasting the data.  Since broadcasting/multicasting is usually one-way communication, it should be repeated a few times.
e.g. the number of times, interval, delay tolerance, expiration timer, and misc.

The resource may as well contain the following data elements.				(Optional)

- Priority: a value to specify how fast the hosting CSE (and the NSE) should process the request.
e.g. 0: Urgent, 1: High, 2: Normal, 3: Low

- Method: a value/string to specify which mechanism/technology is to be used in the Underlying Network to broadcast/multicast the data.
e.g.  CBS, MBMS, or any others

- Radio Bearer: a value/string to specify which radio bearer is to be used in the Underlying Network to broadcast/multicast the data.
e.g.  UMTS, GMS, etc.

- NSE: a list of NSEs which the hosting CSE should request to broadcast/multicast the data.

Depending on the features supported in the Underlying Network, the resource may contain the following data elements.									(Optional)

- Message Category: a hinting value to specify which kind of content is stored in the Message Body.
e.g. 1: Disaster, 2: Security, 3: Medical affairs, 4: Transportation, 5: Energy, 6: Weather, 7: Advertising

- Acknowledgement: a binary flag (TRUE of FALSE) to specify if the M2M Device have to acknowledge the received data.

- Device Action: a value to specify the action of M2M Devices when they received the Message Body.
e.g. Beep, pop-up a message, etc.

The above contents of the resource are supposed to be given by the Application Service Entity (ASE) with a CREATE request.

The resource shall contain the child resources according to their multiplicitly in Table 9.5.y-1 (0 indicated the optionality of the child resource).

Table 9.5.y-1: Child resources of bcastRequest resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <bcastResult> | 0..1 | See section 9.5.y |

<Additional information about subResources (if needed)>

The resource shall have the attributes according to their multiplicitly in Table 9.5.y-2 (0 indicated the optionality of the attribute).  The resource has no resource-specific attribute.

Table 9.5.y-2: Attribute of container resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime | 1 | RW | XRef <section> where the common attribute is described. |
| accessRightID | 1..n | RW | XRef <section> where the common attribute is described. |
| creationTime | 1 | RO | XRef <section> where the common attribute is described. |
| lastModifiedTime | 1 | RO | XRef <section> where the common attribute is described. |

The values of above attributes are set by the hosting CSE when the resource is created.

- The value of expirationTime SHALL be later than the value specified in the contents of the resource.

- The default value of accessRightID is the identifier of the entity who request to create the resource (=the originator of the CREATE request).

<Additional information about subResources (if needed)>

# Comments

This table contains  a list and a short description of all the attributes. Common attributes definition may be relocate dto a common section and referenced

It clarify if the attribute is:

- Read/Write (RW ), i.e.it can be set by an update or a create,

- Rread Only (RO), i.e. it is set by the CSE and it can only be read,

- Write Once (WO), i.e. it is set by at the creation and then it can only be read.

Could there be multiple occurrences of this attribute (pointing to multiple accessRights)? That could mean that the sum of the accessRights are valid? Not important for the Template… but may need to be considered.

# Text boxes

<bcastRequest>

0..1

<bcastResult>