| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Device management resource |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin (yinjiaxin@huawei.com) |
| Date:* | 2013-09-25 |
| Abstract:* | The contribution provides description to management object resource. |
| Agenda Item:* | Tbd |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the texts into the TS if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information diCSEosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

#### 9.X	Resource <mgmtObj>

The mgmtObj resource contains management data which represents individual M2M management functions. It represents a structured Management Object.

Figure 9.x.1: Structure of <mgmtObj>

The <mgmtObj> resource shall contain the sub resources with the indicated multiplicity in Table 9.x.1.

Table 9.x.1

| subResource | Multiplicity | Description |
| --- | --- | --- |
| <parameters> | 0..unbounded | Collects multiple parameters or attributes for management purpose. A <parameters> can have zero or more other <parameters> so as to form hierarchical structure, i.e. the management data for this specific <mgmtObj>. Such structure helps to import existing management objects as defined in OMA DM, BBF TR-069, or any other DM technology. |

The <mgmtObj> resource shall contain the attributes with the indicated multiplicity in Table 9.x.2.

Table 9.x.2

| AttributeName | Multiplicity | Type | Description |
| --- | --- | --- | --- |
| expirationTime | 1 | RW | See clause 9.x.x Common attributes. |
| accessRightID | 1 | RW | See clause 9.x.x Common attributes. |
| creationTime | 1 | RO | See clause 9.x.x Common attributes. |
| lastModifiedTime | 1 | RO | See clause 9.x.x Common attributes. |
| moID | 1 | WO | Contains a URN that uniquely identifies the MO data model used for this <mgmtObj> resource as well as the manage function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> and shall not be modifiable afterwards. It is mandatory for the <mgmtObj>, of which the data model is not specified by oneM2M but mapped from underlying existing data model specified in other device management protocols (e.g. OMA-DM, BBF TR-069). For oneM2M specific <mgmtObj> resource, this attribute is also mandatory, but the provided value may be ignored, since the MO data model and the management function /version can be determined by its reserved resource name. |
| originalMO | 1 | WO | Contains the local path of the original MO instance on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the original MO instance on the remote entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local MO path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM, "Device.USBHosts.Host.3." in BBF TR-069). |
| <moAttribute> | 0…1 | RW | Each <moAttribute> is mapped from a leaf node of a MO tree (including oneM2M data mode and the existing management data models) based on the mapping rules below the table. |
| description | 0…1 | RW | Text format description of mgmtObj. |

When mapping an MO tree to a corresponding M2M <mgmtObj>, the follow rules shall apply:

- The root node of original MO tree (or sub-tree) maps to <mgmtObj>:

- The leaf nodes, if any, of the root node, maps to as the<moAttribute> attribute of the<mgmtObj> resource with the same name as the leaf node.

- An interior node of original MO tree maps to a <parameters> with the same name as the interior node.

- A leaf node of an interior node on the original MO tree maps to a<moAttribute> attribute with the same name as the leaf node.

#### 9.y	Resource <parameters>

Figure 9.28: Structure of <parameters>

The <parameters> resource shall contain the child resources with the indicated multiplicity in Table 9.y.1.

Table 9.y.1

| subResource | Multiplicity | Description |
| --- | --- | --- |
| <parameters> | 0..unbounded | See clause 9.y |

The <parameters> resource shall contain the attributes with the indicated multiplicity in Table 9.y.2.

Table 9.y.2

| AttributeName | Mandatory/Optional | Type | Description |
| --- | --- | --- | --- |
| originalMO | O | WO | See clause 9.x |
| accessRightID | M | RW | See clause 9.x.x Common attributes. |
| creationTime | M | RO | See clause 9.x.x Common attributes. |
| lastModifiedTime | M | RO | See clause 9.x.x Common attributes. |
| <moAttribute> | O | RW | See clause 9.x |

# Text boxes

*

<parameters>

n

”attribute”

<parameters>

1

*

<parameters>

n

”attribute”

<mgmtObj>

1