| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Device management resource message flows |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin (yinjiaxin@huawei.com) |
| Date:* | 2013-09-25 |
| Abstract:* | The contribution provides description to management object resource message flow. |
| Agenda Item:* | Tbd |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the texts into the TS if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information diCSEosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

#### 10.2.x	External management object management through <mgmtObj>

##### 10.2.x.1	Introduction

This clause describes the management procedures over X and Y reference points. Different RESTful requests addressing an <mgmtObj> resource (or its attributes or child resources) shall be translated into existing management commands and procedures performed on the mapped external management object data on the manageable entity, based on the converting mechanism described in the following clauses.

##### 10.2.x.2	Create <mgmtObj>

The procedure is used to create a specific <mgmtObj> resource in the hosting CSE to expose at run-time the corresponding management function of a manageable entity (i.e. M2M Device/Gateway) over X reference point. Depending on the data model being used, the created <mgmtObj> resource may be a partial or complete mapping from the external management object on the manageable entity. If such external management object is missing from the manageable entity, it shall be added to the manageable entity. Further RESTful operations performed on the created <mgmtObj> resource shall be converted by the hosting CSE into a corresponding device management action performed on the mapped external management object on the manageable entity over Y reference point using existing device management protocols (e.g. OMA-DM or BBF TR-069).

Editor’s Note: Whether existing device management protocols are part of the Y reference point is FFS.

Originator: shall request to create a new <mgmtObj> resource to be named as <mgmtObj> by using a CREATE verb. The request shall address baseURI resource of the hosting CSE. The request may also provide the attributes as described in clause 9.x.1. If the <mgmtObj> resource contains one or more <parameters> child resources which may also contains <parameters> child resources recursively, the originator may create each of the <parameters> child resource step by step as needed by sending the CREATE request addressing the parent resource of <parameters> the child resource.

The originator may be:

- The CSE on the manageable entity: In this case, the CSE first collects the original external management object data (the management tree structure or also the value of the tree nodes if needed) of the local device and transforms the data into the <mgmtObj> resource representation, then requests the hosting CSE to create the corresponding <mgmtObj> resource.

- An AE registered to the N-CSE: In this case, the AE requests the hosting CSE to add the corresponding external management object data to the manageable entity by creating an <mgmtObj> resource in the hosting CSE.

NOTE 1:	The hosting CSE in the network domain may also create the <mgmtObj> resource locally by itself. The details are out of scope. In this case, the hosting CSE first collects the original external management object data on the manageable entity via Y reference point following existing (e.g. OMA-DM or BBF TR-069) device management protocols, then transforms the data into the <mgmtObj> resource representation and create the <mgmtObj> resource locally in the hosting CSE.

NOTE 2:	The <mgmtObj> resource may also be created in the hosting CSE by other offline provisioning means which are out of scope.

Hosting CSE: shall check if the originator has the CREATE permission on the addressed baseURI resource (or the parent <mgmtObj> or <parameters> resource in the case of child resource creation). The hosting CSE shall also check the validity of provided attributes. Upon successful validation, a new <mgmtObj> resource with name "<mgmtObj>" is created in the hosting CSE with the provided attributes. If the originator is an AE, the hosting CSE shall also send the management request over Y reference point to add the corresponding external management object data to the manageable entity based on existing management protocol. The hosting CSE shall maintain the mapping relationship between the created <mgmtObj> resource and the original external management object data on the manageable entity. Then the hosting CSE shall respond to the originator with the appropriate generic responses. It shall also provide in the response the URL of the created new resource.

The hosting CSE shall be:

- An N-CSE.

Figure 10.2.x.1: Illustration of procedures to create an <mgmtObj> resource by D/G-CSE

Step 001:	D/G-CSE shall first collect local external management object data to be exposed by the <mgmtObj> resource.

Step 002:	To create an <mgmtObj> resource, D/G-CSE shall issue a CREATE request with the collected external management object data to the N-CSE.

Step 003:	If the creation is allowed, an <mgmtObj> resource shall be created in the N-CSE with the provided external management object data and other required attributes (e.g. "originalMO", "external management objectID").

Step 004:	A response shall be returned to D/G-CSE.

List of procedure specific exceptions:

Step 003:	If the creation is not allowed, the <mgmtObj> resource shall not be created, and a proper error code shall be returned to D/G-CSE in step 004.

Figure 10.2.x.2: Illustration of procedures to create an <mgmtObj> resource by N-AE

Step 001:	To add a new external management object to a manageable entity (D/G-CSE), N-AE shall issue a CREATE request with the external management object data to the N-CSE to create an <mgmtObj> resource.

Editor’s Note: Where in the resource structure to create the <mgmtObj> is FFS.

Step 002:	If the creation is allowed, N-CSE shall trigger existing (OMA-DM or BBF TR-069) device management procedures to add a corresponding new external management object to the manageable entity.

Step 003:	An <mgmtObj> resource shall be created in the N-CSE with the provided external management object data and other required attributes (e.g. "originalMO", "moID").

Step 004:	A response shall be returned to N-AE.

List of procedure specific exceptions:

Step 002:	If the creation is not allowed, steps 002-003 shall be skipped and a proper error code shall be returned to N-AE in step 004.

Step 002:	If the corresponding external management object cannot be added to the manageable entity due to some reason (e.g. not reachable, memory shortage), step 003 shall be skipped and a proper error code shall be returned to N-AE in step 004.

Step 002:	If the corresponding external management object exists already on the manageable entity and it is not multi-instance external management object, then no new external management object is added to the manageable entity. Step 003 shall still be performed and a successful response shall be returned to N-AE in step 004.

Table 10.2.x.1: mgmtObj Create

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | none |
| Information on Request message | op: C fr: Identifier of the AE or CSE that intiates the request. to: The URI of the baseURI where the <mgmtObj> resource is intend to be created. cn: The representation of the <mgmtObj> resource in which the attributes described in clause 9 |
| Local processing on Hosting CSE | New external management object created on the manageable entity using external management technologies in case the originator is N-AE. |
| Information on Response message | Proper error code if the new external management object is not created. |
| Post-condition | none |
| Exceptions | The creation of the external management object is not allowed. The created external management object already exists. Corresponding external management object cannot be added to the manageable entity due to some reason (e.g. not reachable, memory shortage) |

##### 10.2.x.3	Retrieve <mgmtObj>

The procedure is used to retrieve information from an existing <mgmtObj> resource or its <parameters> child resource.

Originator: shall request to retrieve an existing <mgmtObj> resource by using a RETRIEVE verb. The request shall address a specific "<mgmtObj>" resource of a CSE or a specific <parameters> child resource of the <mgmtObj> resource to retrieve all attributes of the <mgmtObj> resource or the <parameters> child resource.

The originator may be:

- An N-AE.

- A D/G-CSE on the manageable entity.

Hosting CSE: shall check if the originator has the READ permission on the addressed <mgmtObj> resource (or the <parameters> child resource in the case of child resource retrieval). Upon successful validation, the hosting CSE shall retrieve the corresponding <mgmtObj> resource or the <parameters> child resource including all attributes and references to all its child resources from its repository and shall respond to the originator with the appropriate generic responses. If the originator is an M2M N-AE and if the requested information of the <mgmtObj> or <parameters> resource is not available on the hosting CSE, the hosting CSE shall identify the corresponding external management object data on the manageable entity according to the mapping relationship it maintains, and send the management request over mId reference point to get the corresponding external management object data from the manageable entity based on existing device management protocol (e.g. OMA-DM, BBF TR-069), then return the result to the originator.

The hosting CSE shall be:

- An N-CSE.

Figure 10.2.x.3: Illustration of procedures to retrieve an <mgmtObj> resource by a D/G-CSE

Step 001:	To retrieve an <mgmtObj> resource, D/G-CSE shall issue a RETRIEVE request to the N-CSE.

Step 002:	If the retrieval is allowed, an <mgmtObj> resource shall be retrieved from the repository of
N-CSE.

Step 003:	A response shall be returned to D/G-CSE.

List of procedure specific exceptions:

Step 002:	If the retrieval is not allowed or the specific <mgmtObj> resource does not exist in the N-CSE, the retrieval shall be failed and a proper error code shall be returned to D/G-CSE in step 003.

Figure 10.2.x.4: Illustration of procedures to retrieve an <mgmtObj> resource by an M2M N-AE

Step 001:	To retrieve external management object data from a manageable entity (D/G-CSE), N-AE shall issue a RETRIEVE request to the N-CSE to retrieve the corresponding <mgmtObj> resource.

Step 002:	If the retrieval is allowed, the addressed attributes of the <mgmtObj> resource or its child resource shall be retrieved from the repository of the N-CSE.

Step 003	If the requested information is not available or expired in the <mgmtObj> resource, N-CSE shall trigger existing (OMA DM or BBF TR-069) device management procedures to get the latest information of the corresponding external management object from the manageable entity.

Step 004:	A response shall be returned to N-AE.

List of procedure specific exceptions:

Step 002:	If the retrieval is not allowed or the specific <mgmtObj> resource does not exist in the N-CSE, step 003 shall be skipped and a proper error code shall be returned to N-AE in step 004.

Step 003:	If the corresponding external management object data cannot be retrieved from manageable entity due to some reason (e.g. external management object not found), a proper error code shall be returned to N-AE in step 004.

Table 10.2.x.2: mgmtObj Retrieve

|  | Description |
| --- | --- |
| Call flow type | RETRIEVE |
| Pre-conditions | none |
| Information on Request message | op: R fr: Identifier of the AE or CSE that intiates the request. to: The URI of the <mgmtObj> resource. |
| Local processing on Hosting CSE | Get corresponding external management object data from manageable entity by existing management procedures |
| Information on Response message | Proper error code if the external management object can not be retrieved. |
| Post-condition | None |
| Exceptions | Corresponding external management object data cannot be retrieved from manageable entity due to some reason (e.g. external management object not found) |

##### 10.2.x.4	Update <mgmtObj>

The procedure is used to update information of an existing <mgmtObj> resource or its <parameters>child resource.

Originator: shall request to update information of an existing <mgmtObj> resource by using a UPDATE, CREATE or DELETE verb. The request shall address:

- a specific <mgmtObj> resource or a specific <parameters> child resource of the <mgmtObj> resource on the hosting CSE to update the all attributes of the <mgmtObj> resource or the <parameters> child resource with new values when using UPDATE verb; or

- a specific <mgmtObj> resource or a specific <parameters> child resource of the <mgmtObj> resource on the hosting CSE to add an attribute to the <mgmtObj> resource or the <parameters> child resource when using CREATE verb.

The originator may be:

- An M2M N-AE.

- A D/G-CSE on the manageable entity.

Hosting CSE: shall check if the originator has the WRITE permission on the address <mgmtObj> resource (or the <parameters> child resource in the case of child resource update). The hosting CSE shall also check the validity of provided attributes if any. Upon successful validation, the hosting CSE shall update, add or delete the corresponding attribute(s) of the <mgmtObj> resource or the <parameters> child resource accordingly. If the originator is an M2M N-AE, the hosting CSE shall also identify the corresponding external management object data on the manageable entity according to the mapping relationship it maintains, and send the management request over Y reference point to update, add or delete the corresponding external management object in the manageable entity accordingly based on existing device management protocol (e.g. OMA DM or BBF TR-069). The hosting CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An N-CSE.

Figure 10.2.x.5: Illustration of procedures to update an <mgmtObj> resource by a D/G-CSE

Step 001:	To update an <mgmtObj> resource, D/G-CSE shall issue a UPDATE/CREATE/DELETE request to the N-CSE with the provided new value.

Step 002:	If the update is allowed, an <mgmtObj> resource shall be updated from the repository of N-CSE.

Step 003:	A response shall be returned to D/G-CSE.

List of procedure specific exceptions:

Step 002:	If the update is not allowed or the specific <mgmtObj> resource does not exist in the N-CSE, the deletion shall be failed and a proper error code shall be returned to D/G-CSE in step 003.

Figure 10.2.x.6: Illustration of procedures to update an <mgmtObj> resource
or its child resource by an M2M N-AE

Step 001:	To update external management object data in a manageable entity (D/G-CSE), N-AE shall issue a UPDATE/ CREATE/ DELETE request to the N-CSE to update the corresponding <mgmtObj> resource or its child resource.

Step 002:	If the update is allowed, N-CSE shall trigger existing (OMA DM or BBF TR-069) device management procedures to override/ add/ delete the corresponding external management object data in the manageable entity accordingly.

Step 003: 	The addressed attribute(s) of the <mgmtObj> resource or its child resource shall be updated accordingly.

Step 004:	A response shall be returned to N-AE.

List of procedure specific exceptions:

Step 002:	If the update is not allowed or the specific <mgmtObj> resource (or its child resource) does not exist in the N-CSE, steps 002-003 shall be skipped and a proper error code shall be returned to N-AE in step 004.

Step 002:	If the corresponding external management object data cannot be updated to manageable entity due to some reason (e.g. not reachable, external management object not found), step 003 shall be skipped and a proper error code shall be returned to N-AE in step 004.

Step 002:	If the corresponding external management object data cannot be deleted from manageable entity due to some reason (e.g. not reachable, memory shortage or external management object not found), step 003 shall still be performed and a successful response with the proper indication shall be returned to N-AE in step 004.

Table 10.2.x.3: <mgmtObj> Update

|  | Description |
| --- | --- |
| Call flow type | UPDATE |
| Pre-conditions | none |
| Information on Request message | op: U fr: Identifier of the AE or CSE that intiates the request. to: The URI of the <mgmtObj> resource. cn: The representation of the <mgmtObj> resource in which the attributes described in clause 9 |
| Local processing on Hosting CSE | Override/add/delete corresponding external management object data in manageable entity by existing management procedures |
| Information on Response message | Proper error code if the external management object can not be updated. |
| Post-condition | none |
| Exceptions | Corresponding external management object data cannot be updated to manageable entity due to some reason (e.g. not reachable, external management object not found). Corresponding external management object data cannot be deleted from manageable entity due to some reason (e.g. not reachable, memory shortage or external management object not found). |

##### 10.2.x.5	Delete <mgmtObj>

The procedure is used to delete an existing <mgmtObj> resource or its <parameters> child resource so as to hide the management function of a manageable entity (i.e. M2M Device/Gateway) from being exposed via X reference point. An M2M N-AE uses this procedure to remove the corresponding external management object data (e.g. an obsolete software package) from the manageable entity.

Originator: shall request to delete an existing <mgmtObj> resource or its <parameters> child resource by using a DELETE verb. The request shall address the specific <mgmtObj> resource or a specific <parameters> child resource of the <mgmtObj> resource on the hosting CSE.

The originator may be:

- The D/G-CSE on the manageable entity: In this case, the D/G-CSE issues the request to the hosting CSE to hide the corresponding remote management function from being exposed by the <mgmtObj> resource.

- An M2M N-AE: In this case, the N-AE requests the hosting CSE to delete the <mgmtObj> resource from the hosting CSE and to remove the corresponding external management object data from the manageable entity.

NOTE 1:	The hosting CSE in the network domain may also delete the <mgmtObj> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <mgmtObj> resource may also be deleted in the hosting CSE by other offline provisioning means which are out of scope.

Hosting CSE: shall check if the originator has the DELETE permission on the addressed <mgmtObj> resource (or the <parameters> child resource in the case of child resource deletion). Upon successful validation, the hosting CSE shall remove the addressed resource from its repository. If the originator is an N-AE, the hosting CSE shall also identify the corresponding external management object data on the manageable entity according to the mapping relationship it maintains, and send the management request over Y reference point to remove the corresponding external management object data from the manageable entity based on existing management protocol. Then the CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An N-CSE.

Figure 10.2.x.7: Illustration of procedures to delete
an <mgmtObj> resource by D/G-CSE

Step 001:	To delete an <mgmtObj> resource, D/G-CSE shall issue a DELETE request to the N-CSE.

Step 002:	If the deletion is allowed, an <mgmtObj> resource shall be removed from the repository of
N-CSE.

Step 003:	A response shall be returned to D/G-CSE.

List of procedure specific exceptions:

Step 002:	If the deletion is not allowed or the specific <mgmtObj> resource does not exist in the N-CSE, the deletion shall be failed and a proper error code shall be returned to D/G-CSE in step 003.

Figure 10.2.x.8: Illustration of procedures to delete an <mgmtObj> resource by N-AE

Step 001:	To delete an existing external management object from a manageable entity (D/G-CSE), N-AE shall issue a DELETE request to the N-CSE to delete the corresponding <mgmtObj> resource.

Step 002:	If the deletion is allowed, N-CSE shall trigger existing (OMA-DM or BBF TR-069) device management procedures to delete the corresponding external management object from the manageable entity.

Step 003:	The <mgmtObj> resource shall be deleted from the repository of the N-CSE.

Step 004:	A response shall be returned to N-AE.

List of procedure specific exceptions:

Step 002:	If the deletion is not allowed or the specific <mgmtObj> resource does not exist in the N-CSE, steps 002-003 shall be skipped and a proper error code shall be returned to N-AE in step 004.

Step 002:	If the corresponding external management object cannot be deleted from manageable entity due to some reason (e.g. not reachable, external management object not found), step 003 shall still be performed and a successful response with the proper indication shall be returned to N-AE in step 004.

Table 10.2.x.3: <mgmtObj> Delete

|  | Description |
| --- | --- |
| Call flow type | DELETE |
| Pre-conditions | none |
| Information on Request message | op: D fr: Identifier of the AE or CSE that intiates the request. to: The URI of the <mgmtObj> resource. |
| Local processing on Hosting CSE | Trigger existing (OMA-DM or BBF TR-069) management procedures to delete the corresponding external management object from the manageable entity. |
| Information on Response message | Proper error code if the external management object can not be deleted. |
| Post-condition | none |
| Exceptions | Corresponding external management object cannot be deleted from manageable entity due to some reason (e.g. not reachable, external management object not found). |

##### 10.2.x.6	Execute <mgmtObj>

The procedure is used for executing a specific management command on a manageable entity through an existing <mgmtObj> resource on the hosting CSE.

Originator: shall request to execute a specific management command which is represented by an existing <mgmtObj> resource or its attribute/child resource by using an UPDATE verb. The request shall address the specific executable <mgmtObj> resource or its attribute/child resource and shall contain an empty body. In the case that the management command is represented by an attribute of a <mgmtObj> resource, such attribute shall contain a URI that the request may also address to trigger the command execution alternatively.

After the execution request, the originator may request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute/child resource by using a RETRIEVE method as described in clause 10.2.x.3.

The originator shall be:

- An M2M N-AE.

Hosting CSE: shall check if the originator has the WRITE permission on the addressed <mgmtObj> resource or its attribute/child resource. Upon successful validation, the hosting CSE shall send the management request over Y reference point to execute the corresponding management command (e.g. "Exec" in OMA DM) on the manageable entity based on existing device management protocol. And the hosting CSE shall respond to the originator with the appropriate generic responses. The response may also contain execution results.

Upon receiving a RETRIEVE request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute/child resource, the hosting CSE shall perform the procedures as described in clause 10.2.x.3.

Upon receiving from manageable entity a management notification (e.g. OMA-DM "Generic Alert" message or
BBF TR-069 "Inform" message) regarding the execution result or status, the hosting CSE may actively send the management request over Y reference point to retrieve the execution result or status external management object information from the manageable entity and update the corresponding <mgmtObj> resource or its attribute/child resource locally.

The hosting CSE shall be:

- An N-CSE.

Figure 10.2.x.9: Illustration of procedures to execute an <mgmtObj> resource

Step 001:	To execute a management command on a manageable entity (D/G-CSE), N-AE shall issue an UPDATE request to the N-CSE to execute the corresponding executable <mgmtObj> resource or its attribute/child resource.

Step 002:	If the execution is allowed, N-CSE shall trigger existing (OMA DM, BBF TR-069) device management procedures to execute the corresponding management command on the manageable entity.

Step 003:	A response shall be returned to N-AE.

Steps 004-007:	N-AE issues RETRIEVE request to retrieve execution result or status from the executable <mgmtObj> resource or its attribute/child resource as described in clause 10.2.x.3.

List of procedure specific exceptions:

Step 002:	If the execution is not allowed or the specified <mgmtObj> resource or its attribute/child resource does not exist in the N-CSE, step 002 shall be skipped and a proper error code shall be returned to N-AE in step 003.

Step 002:	If the corresponding external management object operation cannot be executed in manageable entity due to some reason (e.g. not reachable, external management object not found), a proper error code shall be returned to N-AE in step 003.

Table 10.2.x.3: <mgmtObj> Execute

|  | Description |
| --- | --- |
| Call flow type | UPDATE |
| Pre-conditions | none |
| Information on Request message | op: U fr: Identifier of the AE or CSE that intiates the request. to: The URI of the <mgmtObj> resource. cn: none |
| Local processing on Hosting CSE | Trigger existing (OMA DM, BBF TR-069) device management procedures to execute the corresponding management command on the manageable entity. |
| Information on Response message | Proper error code if the external management object can not be executed. |
| Post-condition | none |
| Exceptions | Corresponding external management object operation cannot be executed in manageable entity due to some reason (e.g. not reachable, external management object not found) |

##### 10.2.x.7	Manage a group of <mgmtObj> resources on different managed entities

In order to manage a group of <mgmtObj> resources (or <parameters> child resources) on different managed entities in a batch mode, a <group> resource shall be created in prior with the members as the list of target <mgmtObj> resources on different managed entities.

Originator: sends a request (CREATE/ RETRIEVE/ UPDATE/ DELETE) to the group hosting CSE, addressing the bulk child resource of the <group> resource that represents the group of <mgmtObj> resources to be managed on different managed entities.

Group Hosting CSE: shall fan out the request to each of the member resource hosting CSE that hosts a <mgmtObj> resource of the group.

Member Hosting CSE: shall perform the corresponding management procedures as described in clauses 10.2.x.1 to 10.2.x.7 based on the received request.

Note that the <mgmtObj> resources in the same group are recommended to be homogeneous, i.e. using the same data model and representing the same management function. Otherwise, the fan out requests may result in errors or meaningless response.