| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | CR against TS0001v0.1.2 including change marks |
| Date:* | 2013-10-05 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) |
| Reason for Change/s:* | This CR is proposing changes to clarify and refine the interpretation of ‘rt’: response type as an optional parameter of a request and suggests the addition of a result content ‘rc’ parameter. |
| Clause/Sub Clause Affected* | 8.1.2 |
| Agenda Item:* |  |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | Architecture TS 0001v0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Rationale

When requesting an operation to be executed on a Hosting CSE, it needs to be clear what the expected components of the result of the requested operation are.

In some cases the Originator wants the Hosting CSE to just perform the requested operation and is not interested in getting any feedback on the outcome of the operation. In other cases the originator may actually need to hear back about the outcome of the operation.

What exactly makes sense to define as possible components in the result of an operation depends on the operation itself, so whether it was a Create, Retrieve, Update or Delete operation. It is important to express what is expected by the Originator as otherwise, the Hosting CSE may not provide the expected information or it may provide information that the Originator cannot handle.

In the CR below, the following possible result content components are suggested as a function of the requested operation:

- In case of op=C (Create):

  - ‘None’: No result is expected, i.e. the hosting CSE does not need to feedback the outcome of the Create operation.

  - ‘Status only’: Result of Create operation should only contain indication on successful/unsuccessful completion of the operation.

  - ‘URI’: Result of a Create operation should contain the URI of the created resource if the operation was successful or an indication of unsuccessful completion otherwise.

  - ‘URI and Content’: Result of a Create operation should contain the URI of the created resource and the content of the created resource if the operation was successful or an indication of unsuccessful completion otherwise.

- In case of op=R (Retrieve): 

The result of a Retrieve operation should be the content of the resource to be retrieved if the operation was successful or an indication of unsuccessful completion otherwise.

- In case of op=U (Update)

  - ‘None’: No result is expected, i.e. the hosting CSE does not need to feedback the outcome of the Update operation.

  - ‘Status only’: Result of an Update operation should only contain indication on successful/unsuccessful completion of the operation.

  - ‘Replaced Content’: Result of an Update operation should contain the replaced content of the updated resource if the operation was successful or an indication of unsuccessful completion otherwise.

- In case of op=D (Delete)

  - ‘None’: No result is expected, i.e. the hosting CSE does not need to feedback the outcome of the Delete operation.

  - ‘Status only’: Result of a Delete operation should only contain indication on successful/unsuccessful completion of the operation.

  - ‘Deleted Content’: Result of a Delete operation should contain the deleted content of the target  resource if the operation was successful or an indication of unsuccessful completion otherwise.

Furthermore, the attached CR provides a clarification of the ‘rt’ response type, since it makes sense to always include a reference that can be used to retrieve request results. It is also suggested to select a response type that is sent to the originator by notification.

### ==================== Start Text Proposal ===================

### 8.1.2	Request

Request from an Originator to a Receiver includes the following information:

op:  operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D),

to:  address of target resource, e.g. /m2m.provider1.com/netBase/temp1,

fr:  address of the resource representing the Originator. Used for access control, e.g., /m2m.provider2.com/remBase/app1,

mi:  meta-information about the Request,

- Editor's Note: Defaults for meta-information are FFS.

cn:  resource content to be transferred.

Note: The to target resource needs to be known by the Originator. It can be known either by pre-provisioning or by discovery.

- Editor’s Note: How pre-provisioning and discovery are performed is FFS.

The op information shall indicate the operation to be executed at the Receiver:

Create (C):  a new resource addressable with to parameter is created,

Retrieve (R):  an existing to addressable resource is read and provided back to the Originator,

Update (U):  the content of an existing to addressable resource is replaced with cn new content,

Delete (D):  an existing to addressable resource and all its sub-resources are deleted from the Resource Storage.

- Editor’s Note: This is an initial list of the verbs. The need for more verbs is anticipated to cover all use cases, configuration and functions.

The to information shall address the target resource in the Receiver.

The fr information shall be used by the Receiver to check the Originator identity for access permission verification.

The cn information shall be present in a Request for the following operations:

Create:  cn is the content of the new resource,

Update:  cn is the content to be replaced in an existing resource,

Retrieve:  cn is the filter to be applied for discovery purposes.

Note that the cn information can also be empty.

The mi information shall be as follows:

ot:  optional originating timestamp of when the message was built,

Example usage of the originating timestamp includes: to measure and enable operation (e.g. message logging, correlation, message prioritisation/scheduling, accept performance requests, charging, etc.) and to measure performance (distribution and processing latency, closed loop latency, SLAs, analytics, etc.)

et:  optional expiration timestamp,

Example usage of the expiration timestamp includes to indicate when messages (including delay-tolerant) should expire due to the freshness of the responses being no longer of value, and to inform message scheduling/prioritisation.

rt:  optional response type: indicates whether the response to the issued request shall contain

- ‘reference only’: Only a reference that can be used to access the result of the requested operation at a later time

- ‘reference and result’: In addition to the reference explained under ‘reference only’ also the results of the requested operation

- ‘reference and result notification to {notificationReference}’: In addition to the reference explained under ‘reference only’ also the results of the requested operation shall be returned. The results need to be sent as a notification to the Originator using the {notificationReference}

Example usage of the response type set to " reference only " includes when the response content is extremely large, or when multiple response content from a target group are to be aggregated asynchronously over time

rc: optional result content: Indicates what are the expected components of the result of the requested operation:

- In case of op=C (Create):

  - ‘None’: No result is expected, i.e. the hosting CSE does not need to feedback the outcome of the Create operation.

  - ‘Status only’: Result of Create operation should only contain indication on successful/unsuccessful completion of the operation.

  - ‘URI’: Result of a Create operation should contain the URI of the created resource if the operation was successful or an indication of unsuccessful completion otherwise.

  - ‘URI and Content’: Result of a Create operation should contain the URI of the created resource and the content of the created resource if the operation was successful or an indication of unsuccessful completion otherwise.

- In case of op=R (Retrieve): 

The result of a Retrieve operation should be the content of the resource to be retrieved if the operation was successful or an indication of unsuccessful completion otherwise.

- In case of op=U (Update)

  - ‘None’: No result is expected, i.e. the hosting CSE does not need to feedback the outcome of the Update operation.

  - ‘Status only’: Result of an Update operation should only contain indication on successful/unsuccessful completion of the operation.

  - ‘Replaced Content’: Result of an Update operation should contain the replaced content of the updated resource if the operation was successful or an indication of unsuccessful completion otherwise.

- In case of op=D (Delete)

  - ‘None’: No result is expected, i.e. the hosting CSE does not need to feedback the outcome of the Delete operation.

  - ‘Status only’: Result of a Delete operation should only contain indication on successful/unsuccessful completion of the operation.

  - ‘Deleted Content’: Result of a Delete operation should contain the deleted content of the target  resource if the operation was successful or an indication of unsuccessful completion otherwise.

rp:  optional response persistence: indicates the duration for which the reference  containing the responses is to persist.

Example usage of response persistence includes requesting sufficient persistence for analytics to process the response content aggregated asynchronously over time. If an expiration timestamp is specified then the response persistence should last beyond the Request expiry time.

Once the Request is delivered, the Receiver shall analyze the Request to determine the target resource.

If the target resource is addressing another M2M node, the Receiver shall route the request appropriately by use of the CMDH CSF.

If the target resource is addressing the Receiver, it shall:

- Check the existence of to addressed resource,

- Identify the resource type,

- Check the permission for fr Originator to perform the requested operation,

- Perform the requested operation (using cn content when provided),

- Depending on the requested result content, respond to the Originator with indication of successful or unsuccessful operation results. In some specific cases (e.g. limitation in the binding protocol or based on application indications), the Response could be avoided.

The message flow procedure started with an Originator Request shall be considered closed when either:

- A Request is received with an expired et (expiration timestamp),

- A Response is delivered to the Originator,

- The requested operation at the Receiver is successfully completed and no Response is needed.