| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | NOTIFY call flow template |
| Source:* | LG Electronics |
| Contact: | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Date:* | 2013-10-07 |
| Abstract:* | The call flow template for NOTIFY request/response. |
| Agenda Item:* | TBD |
| Work item(s): | WI-0002 oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text1 into the TS and text2 into the working assumption. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

In general, notification can be used in the subscription/notification mechanism. It can also be used in other purposes, for example a local CSE sends a notification to an AE to make AE generate/write a new data into a container.

For various usages of notification, this contribution proposes NOTIFY request/response call flow template.

Difference between this NOTIFY and CRUD operation is that NOTIFY does not request to manipulate the target URI (to parameter in request). Therefore there’s no local processing at the Receiver, but at the Originator side to handle a notification trigger.

*********************** Beginning of Text1 ***********************

## 10.1.5	NOTIFY (N)

The NOTIFY operation shall be used for notifying information which does not have a resource representation.

Originator: requests to notify information by using NOTIFY method. See clause 8.1.2 for the information to be included in a Request message.

Receiver: responses to the Originator with the operation results as specified in clause 8.1.3.

Figure 10.1.5-1: Procedures for NOTIFYing information

Step 001: A notification to be sent to the Receiver is triggered in the Originator.

Step 002: The Originator shall send the following information in the NOTIFY Request message:

op:	N (Notify)

to: 	address that the Receiver can receive the notification data from

fr:	address of the resource representing the Originator

cn:	URI of the <subscription> resource as a reference to the notification, and the content of the resource to be notified

Step 003: The Receiver responds with a Response message that shall contain the following information:

rs: 	operation result

General Exceptions:

- The Receiver cannot receive information from URI of to in the request. The Receiver responds with an Error.

*********************** End of Text1 ***********************

*********************** Beginning of Text2 ***********************

The highlighted part should be replaced with flow specific information.

<Name of the call flow>

Brief introductory text explaining what the flow is about, specify if originator can be an AE, Middle Node, Infra-Node etc

Originator: <text describing anything specific to the Originator in this call flow (if applicable)>

Receiver: <text describing anything specific to the Receiver in this call flow (if applicable)>

Table

This table should be used as a template to generate specific call flow descriptions. What already covered by the generic call flow and descriptions in the textt part should not be repeated.

Editor’s note: this call flow template will be evolving as we handle more examples..

Table x.y <Name of the call flow>

|  | Description |
| --- | --- |
| Call flow type | NOTIFY |
| Pre-conditions | <Pre-conditions> |
| Local processing on Originator CSE | < specific local processing on Receiver CSE> |
| Information on Request message | <cn: data representation to be Notified > <specific information elements to be included in the Request message> |
| Generic Information on Response message | <specific information elements to be included in the Response message> |
| Post-conditions | <Post-condition> |
| Exceptions | <Exceptions if different from general exceptions, specify in which procedure step the exceptions apply to> |

*********************** End of Text2 ***********************