| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Call flow of notification for subscription |
| Source:* | LG Electronics |
| Contact: | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Date:* | 2013-10-07 |
| Abstract:* | The call flow template for NOTIFY request/response. |
| Agenda Item:* | TBD |
| Work item(s): | WI-0002 oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text1 into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

As a response to the subscription, notification is sent to the owner of <subscription> resource.

This contribution proposes to incorporate 10.2.x notification into <subscription> management clause since this notification flow is associated with subscription resource.

*********************** Beginning of Text1 ***********************

## 10.2.X	Notification

This procedure shall be used to notify modifications of a subscribed-to resource as specified in an associated <subscription> resource.

Originator: shall request to send modification information when a change of a subscribed-to resource only if conditions meet specified in the criteria of the <subscription> resource. In case of deletion of a subscribed-to resource, the Originator which is the subscription hosting CSE shall notify the deletion regardless of the criteria.

Receiver: shall response to the Originator with the operation results. If the notificationURI targets a <container> resource in the Receiver, the Receiver shall store the notification data to the container as a new instance with the subscription reference.

Table 10.2.x.1 Notification for subscription flow

|  | Description |
| --- | --- |
| Call flow type | NOTIFY |
| Pre-conditions | Notification is triggered regarding subscription information in a <subscription> resource. |
| Local processing on Originator CSE | Generate data representation for the notification. |
| Information on Request message | to: notificationURI of the corresponding <subscription> resource cn: URI of the <subscription> resource as a reference to the notification, and the content of the resource to be notified. |
| Generic Information on Response message | No change from the basic procedure. [clause 10.1.5 NOTIFY (C)] |
| Post-conditions | If to in the request message addresses a container resource, the Receiver shall store the notification data to the container; otherwise, the Receiver processes the notification data. |
| Exceptions | No change from the basic procedure. [clause 10.1.5 NOTIFY (C)] |

*********************** End of Text1 ***********************