| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#7 |
| Title:* | Session Management CSF Resources |
| Source:* | Session management CSF group (ZTE, LG, InterDigital) |
| Contact: |  |
| Date:* | <2013-10-06> |
| Abstract:* | This contribution proposes Session Management CSF resources |
| Agenda Item:* | CSF Resource Descriptions |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Rationale

This contribution provides resources to support service layer sessions.

2	Proposal

### 9.5.q	Resource sessions

The <sessions> resource shall represent a collection of <session> resources.

Figure	9.5.q.1: Structure of sessions resource

Editor’s Note: There is currently some discussion/debate on-going in the ARC group as to the pros/cons of collections.   Supporting a sessions collection can provide value-add functionality such as subscriptions to session collection events (e.g. notification of when a new session is created).  Alternatively, <session> resources could be instantiated independent a sessions collection.

This resource shall contain the child resources according to their multiplicity in Table 9.5.q-1 (0 indicated the optionality of the child resource).

Table 9.5.q-1: Child resources of sessions resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| <session> | <session> resource | 0..n | <session> resources that support attributes and child resources used by the SMG CSF to manage M2M service sessions. |

The sessions resource shall contain the attributes according to their multiplicity in Table 9.5.q-2 (0 indicated the optionality of the attribute).

Table 9.5.q-2: Attributes of sessions resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.r	Resource <session>

A <session> resource contains information for managing an individual M2M service session between M2M Application Entities, between an M2M Application Entity and a CSE, or between CSEs.

Editor’s Note: There is currently some discussion/debate on-going in the ARC group as to the pros/cons of collections.   The below figure proposes collections.  Alternatively, this hierarchy could be flattened by removing the collections and instead instantiated the child resources directly under the <session> resource.

Figure	9.5.r.1: Structure of <session> resource

Editor’s Note: It may make sense for oneM2M to define a more generic <policy> resource rather than a <sessionPolicy> resource in which case a sessionPolicy collection under  <session> would not be needed.  Instead a <session> could reference (i.e. link to) <policy> resources similar to the way it links to <accessRight> resources.

This resource shall contain the child resources according to their multiplicity in Table 9.5.r-1 (0 indicated the optionality of the child resource).

Table 9.5.r-1: Child resources of <session> resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| sessionEndpoints | Collection of <sessionEndpoint> resources | 1 | Collection of M2M service session endpoint resources that support endpoint specific attributes |
| sessionPolicies | Collection of <sessionPolicy> resources | 0..1 | Collection of M2M service session policy resources that are used by the SMG to manage the M2M service session in a policy based manner |
| sessionContext | Collection of <sessionContextInstance> resources | 0..1 | Collection of M2M service session context instance resources which store context information related to M2M service session activity and events. |

The resource shall contain the attributes according to their multiplicity in Table 9.5.r-2 (0 indicated the optionality of the attribute).

Table 9.5.r-2: Attributes of <session> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | Time of creation of the resource |
| expirationTime | 1 | RW | Absolute time after which the resource will be deleted by the hosting CSE. This attribute can be provided by the issuer upon resource creation, and in such a case it will be regarded as a hint to the hosting SCL on the lifetime of the resource. This attribute can also be updated by the issuer (before time expires) to extend and renew the lifetime of the resource. |
| accessRightID | 1..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |
| sessionID | 1 | RO | A unique ID is assigned by Session Management CSF when M2M service session is established (i.e. when <session> resource is created). |
| sessionState | 1 | RW | The state information of a <session> resource, indicates one of values below: ONLINE: the M2M service session is in progress. PAUSE: the M2M service session is alive, but no transfer actual data during the sessionPauseTimer or AE can set this attribute. RESET: if this value is set, the whole information of the M2M service session is reset and the state information is to be ONLINE. |
| sessionDescriptor | 1 | WO | Information (e.g. a string) describing the session. This description can be used to discover an existing session via the CSE resource discovery mechanisms (e.g. by perspective session endpoints). |
| allEndpoints | 1 | RO | Requests targeting this attribute will be considered candidates for forwarding to all endpoints of this session by the SMG CSF. Whether or not the request is forwarded to a particular session endpoint is determined by the SMG CSF checking the trailing portion of the URI that follows “allEndpoints”. This portion of the URI path will be compared against each session endpoint’s endptPaths attribute. If a match is found, then the request is forwarded towards the session endpoint. Otherwise, the request is not forwarded towards a session endpoint. |
| sessionPauseTimer | 0..1 | RW | Time value that the session state is going to be PAUSE state. This timer starts the latest data has been transferred between session endpoints. |

### 9.5.s	Resource sessionEndpoints

The sessionEndpoints resource shall represent a collection of <sessionEndpoint> resources.

Figure	9.5.s.1: Structure of sessionEndpoints resource

This resource shall contain the child resources according to their multiplicity in Table 9.5.s-1 (0 indicated the optionality of the child resource).

Table 9.5.s-1: Child resources of sessionEndpoints resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| <sessionEndpoint> | M2M service session endpoint resource | n | M2M service session endpoint resources that support attributes used by the SMG CSF to manage M2M service sessions. |

This resource shall contain the attributes according to their multiplicity in Table 9.5.s-2 (0 indicated the optionality of the attribute).

Table 9.5.s-2: Attributes of sessionEndpoints resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.t	Resource <sessionEndpoint>

The <sessionEndpoint> resource contains attributes and child resources applicable to a particular M2M service session endpoint.

Figure	9.5.t.1: Structure of <sessionEndpoint> resource

This resource can contain the child resources according to their multiplicity in Table 9.5.t-1 (0 indicates the optionality of the child resource).

Table 9.5.t-1: Child resources of <sessionEndpoint> resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| nextHops | Collection of M2M service session next hop resources | n | M2M service session next hop resources support attributes used by the SMG CSF to manage M2M service session hops. |

This resource shall contain the attributes according to their multiplicity in Table 9.5.t-2 (0 indicated the optionality of the attribute).

Table 9.5.t-2: Attributes of <sessionEndpoint> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| endptNodeID | 1 | RO | Identifier of M2M node (M2M-Node-ID) hosting M2M service session endpoint |
| endptID | 1 | RO | Identifier of M2M service session endpoint. Configured with an application identifier (App-Inst-ID) if session endpoint is an M2M Application. Configured with a CSE identifier (CSE-ID) if session endpoint is a CSE. |
| endptSubID | 1 | RO | Identifier of M2M Service Provider’s service subscription (M2M-Sub-ID) associated with M2M service session endpoint |
| endptPaths | 0..n | RW | A session endpoint may publish a list of resource paths to restrict the scope of a M2M service session to a particular set of endpoint resources. For example, a M2M service session can be created to only allow session-based communication with a subset of M2M application entity resources. When present, a SMG CSF can compare the URI specified in session-based requests against the URI paths specified in this attribute. If a match is found, then the SMG CSF forwards the request towards the session endpoint. Otherwise, the SMG CSF does not. In the absence of this attribute, the scope of M2M service session endpoint shall not be restricted. Note, accessRights take precedence over this attribute. |
| endptDescription | 1 | RW | Information describing the session endpoint that can be used by perspective session participants to discover session endpoint via CSE resource discovery mechanisms |
| endptPolicies | 0..n | RW | List of URIs of <sessionPolicy> resources applicable to this session endpoint. |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.u	Resource nextHops

The nextHops resource can represent a collection of <nextHop> resources.

Figure	9.5.u.1: Structure of nextHops resource

This resource shall contain the child resources according to their multiplicity in Table 9.5.u-1 (0 indicated the optionality of the child resource).

Table 9.5.u-1: Child resources of sessionPolicies resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| <nextHop> | M2M service session next hop resource | n | M2M service session next hop resource that supports attributes used by the SMG CSF to keep track of the next hop used to forward session messages to for a particular session endpoint. |

This resource shall contain the attributes according to their multiplicity in Table 9.5.u-2 (0 indicated the optionality of the attribute).

Table 9.5.u-2: Attributes of sessionPolicies resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.v	Resource <nextHop>

The <nextHop> resource contains information regarding the next hop CSE that a Session Management CSF forwards messages to for a specific session endpoint. When a M2M session consists of multiple CSE hops in between session endpoints, the the SMG CSF uses <nextHop> resources to maintain state of the next hop CSEs that session-based requests are forwarded to for a given session and/or session endpoint. Maintaining this information is used by the SMG CSF for tearing down multi-hop M2M sessions spanning across multiple CSEs as well as sharing session context between SMG CSFs hosted on different CSEs.

Figure	9.5.v.1: Structure of <nextHop> resource

This resource shall contain the attributes according to their multiplicity in Table 9.5.v-1 (0 indicated the optionality of the attribute).

Table 9.5.v-1: Attributes of <nextHop> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| nextHopNodeID | 1 | RW | Identifier of a next hop M2M node (oneM2M defined M2M-Node-ID) for targeted M2M service session endpoint |
| nextHopID | 1 | RW | Identifier of the next M2M service session hop. Configured with an application identifier (oneM2M defined App-Inst-ID) if next hop is an M2M Application. Configured with a CSE identifier (oneM2M defined CSE-ID) if next hop is a CSE. |
| nextHopSubID | 1 | RW | Identifier of M2M Service Provider’s service subscription (oneM2M defined M2M-Sub-ID) associated with M2M service session next hop. |
| nextHopDescription | 1 | RW | Information describing the session endpoint that can be used by perspective session participants to discover session endpoint via CSE resource discovery mechanisms |
| nextHopState | 0..1 | RW | Indicates if next hop is currently reachable or not. Next hop’s SMG can set this attribute to OFFLINE or ONLINE. Additionally, a CSE can set this attribute to NOT_REACHABLE if it detects a next hop CSE cannot be reached and ONLINE if it detects next hop CSE can be reached. |
| nextHopPolicies | 0..n | RW | List of URIs of <sessionPolicy> resources applicable to next hop (e.g. policies controlling when SMG CSF selects next hop to forward session messages to) |
| creationTime | 1 | RO | Time of creation of the M2M service session endpoint’s next hop resource |
| lastModifiedTime | 1 | RO | Last modification time of M2M service session endpoint’s next hop resource |
| accessRightID | 0..1 | RW | URI of an access rights resource associated with M2M service session endpoint’s next hop resource |

### 9.5.w	Resource sessionPolicies

The sessionPolicies resource shall represent a collection of <sessionPolicy> resources.

Figure	9.5.w.1: Structure of sessionPolicies resource

Editor’s Note: It may make sense for oneM2M to define a more generic <policy> resource rather than a <sessionPolicy> resource in which case a sessionPolicy collection under  <session> would not be needed.  Instead a <session> could reference (i.e. link to) <policy> resources similar to the way it links to <accessRight> resources.

This resource shall contain the child resources according to their multiplicity in Table 9.5.w-1 (0 indicated the optionality of the child resource).

Table 9.5.w-1: Child resources of sessionPolicies resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| <sessionPolicy> | M2M service session policy resource | n | M2M service session policy resource that supports policy related attributes |

This resource shall contain the attributes according to their multiplicity in Table 9.5.w-2 (0 indicated the optionality of the attribute).

Table 9.5.w-2: Attributes of sessionPolicies resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.x	Resource <sessionPolicy>

The <sessionPolicy> resource contains attributes applicable to a particular M2M service session policy.

Figure	9.5.x.1: Structure of sessionPolicies resource

Editor’s Note: It may make sense for oneM2M to define a more generic <policy> resource rather than a <sessionPolicy> resource.

The resource shall contain the attributes according to their multiplicity in Table 9.5.x-1 (0 indicated the optionality of the attribute).

Table 9.5.x-1: Attributes of sessionPolicy resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| policyType | 1 | RW | The type of policy syntax/language/semantics used to specify the session policy definition. |
| policy | 1 | RW | Session policy definition |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.y	Resource sessionContext

The sessionContext resource shall represent a collection of <sessionContextInstance> resources.

Figure	9.5.y.1: Structure of sessionContext resource

This resource shall contain the child resources according to their multiplicity in Table 9.5.y-1 (0 indicated the optionality of the child resource).

Table 9.5.y-1: Child resources of sessionContext resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| <sessionContextInstance> | M2M service session context instance resource | n | Resource that is used to store context information pertaining to M2M service session |

This resource shall contain the attributes according to their multiplicity in Table 9.5.y-2 (0 indicated the optionality of the attribute).

Table 9.5.y-2: Attributes of sessionContext resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | Time of creation of the resource |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |

### 9.5.z	Resource <sessionContextInstance>

The <sessionContextInstance> resource contains attributes applicable to a particular type of M2M service session context that is collected and maintained by a SMG CSF.

Figure	9.5.z.1: Structure of <sessionContextInstance> resource

The resource shall contain the attributes according to their multiplicity in Table 9.5.z-1 (0 indicated the optionality of the attribute).

Table 9.5.z-1: Attribute of <sessionContextInstance> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| sessionContextType | 1 | RO | Describe the type of sessionContext information such as the number of transferred data, size, and etc. |
| sessionContext | 1 | RW | URI of resource where context information for this session context instance is stored by SMG CSF (i.e. container resource - session context Information can be stored within a container’s content instance resources). Information related to M2M service session activity and events in terms of the defined type that have occurred. |
| creationTime | 1 | RO | Time of creation of the resource |
| maxNrInstances | 1 | RW | Maximum number of instances of this type of session context that are stored by SMG (i.e. max number of container content instances used by SMG CSF) |
| maxByteSize | 1 | RW | Maximum number of bytes allocated for storage of this type of session context. |
| maxAge | 1 | RW | Maximum age of this type of session context stored by SMG CSF. |
| applicableEndpts | 0..n | RW | List of session endpoints that this context shall be collected for. If not specified, than context shall be collected for all session endpoints |
| contextPolicy | 0..n | RW | List of session endpoints that this context shall be collected for. If not specified, than context shall be collected for all session endpoints |
| accessRightID | 0..n | RW | URI of an access rights resource. Must refer to the access right resource. |
| lastModifiedTime | 1 | RO | Last modification time of a resource |