| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2013-10-08 |
| Contact:* | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* | Reword “owner of the subscription” as “resource subscriber”. |
| Clause/Sub Clause Affected* | 6.2.13 Subscription and Notification |
| Agenda Item:* |  |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | oneM2M Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

“owner of the subscription” was brought to mean an entity that created a subscription to a resource during the draft session at TP#6. However, the concept of ownership might bring unwanted confusion. This contribution propose to replace “owner of the subscription” with “resource subscriber”, which seems different from “M2M Service Subscriber” by the name.

************************* START OF CHANGE 1  *************************

### 6.2.13	Subscription and Notification

#### 6.2.13.1	General Concepts

The Subscription and Notification (SUB) CSF is responsible for providing notifications pertaining to a subscription that tracks changes on a resource (e.g., deletion of a resource). A subscription to a resource is initiated by an AE or a CSE, and is granted by the Hosting CSE subject to access rights. During an active subscription, the Hosting CSE sends a notification per modification of the resource to the address where the resource subscriber wants to receive.

Editor’s Note: Determining subscribe-able resources is FFS.

#### 6.2.13.2	Detailed Descriptions

The SUB CSF shall manage subscriptions to resources, subject to access rights, and send corresponding notifications. An AE or a CSE shall be subscription resource subscriber. An AE shall be able to subscribe to resources on a local CSE or on a remote CSEs. A CSE shall be able to subscribe to resources on multiple CSEs. A subscription Hosting CSE shall send a notification to the address where the resource subscriber specified per modification on a resource.

A subscription request shall include the resource subscriber ID, the hosting CSE-ID and subscribed-to resource address. It may also include a criteria to specify the interested modifications and the address where to send the notifications.

A single subscription can subscribe to a single resource. Multiple resources shall be able to be subscribed via a single subscription when they are grouped and represented as a single group resource. However, there may be resources that cannot be subscribed to.

A subscription is represented as "subscription resource" in CSE resource structure.

Editor’s Note: The resource structure is yet to be agreed to. How Subscription resource is represented is FFS.

************************* END OF CHANGE 1  *************************