| INPUT CONTRIBUTION |
| --- |
| Group Name:* | [ARC/SEC/MAS Access Control Adhoc 7.1] @TP#7 |
| Title:* | Suggested Access Control Terminology |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com |
| Contact: | As above |
| Date:* | 2013-10-17 |
| Abstract:* | This contribution is intended for the ARC/SEC/MAS Access Control Adhoc 7.1 during TP#7. This document points out some unfortunately terminology confusion in the Access Control discussions, and suggests some terminology to alleviate the confusion. |
| Agenda Item:* | TBD |
| Work item(s): | TBD |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Adopt the proposed terminology for the Access Control Ad Hoc discussions, with the understanding that the definitions may need further refining before being included in a TS or TR. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This document points out some unfortunately terminology confusion in the Access Control discussions, and suggests some changes in terminology.

2	Rationale

A term that is causing confusing in the Access Control discussions is “user”.

- In the early discussion in oneM2M we were not even able to arrive at a definition of what a user is. It seems the term “user” is most commonly associated with a person – but this was not always the case.

- In some access control discussions and literature, the term “user” refers to a person. In other access control discussions and literature, the term “user” can be associated with either a person or an “automated agent”. In the scope of oneM2M and automated agent would be a Node (ADN, ASN, MN or IN), a CSE, or an AE – or possibly smaller functional units such as CSFs.

I had been working on the assumption that (in the scope of access control discussions in oneM2M)

- The term “user” could be associated with either a person or an automated agent, and

- RBAC could map both of these types of users (persons and automated agents) to roles.

However, as I read contributions from other participants, it is clear that some participants are working under the assumption that

- The term “user” could be associated only with a person, and

- RBAC maps only persons to roles, and automated agents are not assigned roles.

In order for the discussions to progress smoothly, it is important that we are using the same terminology.

Section 3 below proposes some terminology and some possible definitions. I think there are great advantages to allowing automated agents (e.g. CSE, AE) to be assigned roles. For example, there may be advantages to assigning Air-conditioner AEs to a “AirConditioner” role while assigning temperature sensor AEs to a “tempSensor” role, since those groupings of automated agents will need similar permissions. This has been the motivation for some of the terminology.

The requested decision is

Accept the proposed terminology for the Access Control Ad Hoc discussions, with the understanding that the definitions may need further refining before being included in a TS or TR.

3	Proposal

I propose using the following terminology in the scope of access control discussions:

Generic Access Control Terminology

- Controlled Activity: An activity (combination of operation and object) where the system may decide to decline performing that activity.

- Subject: A person or automated agent associated with a request that requires a Controlled Activity, where a decision to serve the request may depend on this association.

Note: An automated agent is a functional entity, e.g. ADN, ASN, MN, IN, CSE, AE, CSF…

Note: There are a variety of ways that a Subject may be associated with the request, including (but possibly not limited to):

  - The Subject sending the request,

  - The Subject forwarding the request, or

  - The Subject delegating authority to the sender of the request.

[Editor’s note: this is a difficult concept to define – so I expect that a formal definition might require some work. The important thing about this definition is that a Subject can be a “person or automated agent”]

- Subject Session: set of requests from a Subject.

- Note: There are many ways to scope a Subject Session. Examples include (but are not limited to): the set of requests within a particular time interval, the set of requests within a particular “Secure session” [to be defined elsewhere], and the set of requests associated with a particular type of activity.

- Subject Identity: An identity that can be “bound to” (that is, associated with) a Subject for the purpose of making decisions on Controlled Activities. A Subject Identity could be unique to the Subject (e.g. person’s name/account, CSE-ID), or a Subject Identity could be assigned to multiple Subjects (e.g. person’s department, identifier assigned to a group of CSEs). A Subject Identity can be permanently bound to the Subject or can be temporarily bound to the Subject for one or more Subject Sessions.

- Permission: A pairing of a Subject Identity with a Controlled Activity, which has the following interpretation at a CSE:

If

    - A request requires the Controlled Activity, and

    - The CSE can verify that a Subject associated with the request is bound to the Subject Identity,

Then the Controlled Activity is allowed in response to the request.

Note: A wildcard identity may be defined for use in case where the activity is to be allowed for all Subjects.

[Editor’s Note: this approach assumes that a Permission requires only one condition to be satisfied. This definition might need revisiting if multiple conditions need to be satisfied.]

A CSE makes decisions using the Permissions configured to the CSE prior to the decision being made.

The following process by a CSE in deciding to allow a Controlled Activity in response to a request):

- The CSE determines the set of Subject Identities bound to Subjects associated with a request. The set of Subject Identities can depend on the Subject Sessions within which the request was made.

- The CSE examines the set of configured Permissions associated with this set of Subject Identities

- If any of these Permissions includes the Controlled Activity, then the CSE allows the Controlled Activity.

[Editor’s Note: this approach assumes that a Permission requires only one condition to be satisfied. This process might need revisiting if multiple conditions need to be satisfied.]

Note any variation that has equivalent outcome is acceptable, for example:

- The CSE examines the set of preauthorized Permissions associated with the Controlled Activity.

- The CSE determines the set of Subject Identities bound to Subjects to be associated with those permissions. The set of Subject Identities can depend on the Subject Sessions within which the request was made.

- If any of the Subjects associated with a request is bound to one of these Subject Identities, then the CSE allows the Controlled Activity.

Role-Related Terminology

- Role: A category of Subject Identity such that the Permissions including that Subject Identity will not alter when there are changes to the set of Subjects bound to that Subject Identity.  A Role is typically bound to a Subject within Subject Sessions related to a type of activity being requested. Roles are used to simplify management of permissions.

- [Editor’s Note: This definition is not intended to provide a complete description of how Roles work. This definition is intended for the purpose of distinguishing when something is a Role].