| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* | CR against TS0001v0.1.2 including change marks |
| Date:* | 2013-10-16 |
| Contact:* | Hongbeom Ahn (hongbeom.ahn@lge.com) |
| Reason for Change/s:* | Based on the WG’s opinion, add more detail information. |
| Clause/Sub Clause Affected* | 6.2.7 |
| Agenda Item:* | 6 – Contributions |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | Architecture TS 0001v0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

2	Proposal

# Start of proposed text #

### 6.2.7	Location

#### 6.2.7.1	General Concepts

The Location (LOC) CSF allows M2M AEs to obtain geographical location information of M2M Nodes (e.g., ASN, MN) for location-based services. Such location information requests may be from an M2M AE residing on either a local Node or a remote Node.

Note: Geographical location information can be more than simply the longitude and the latitude information.

#### 6.2.7.2	Detailed Descriptions

LOC CSF shall obtain and manage geographical location information based on the requests from an M2M AE residing on either a local Node or a remote Node. In order to obtain geographical location of an M2M Node, the LOC CSF shall interact with any of the following: a location server in the Underlying Network; a GPS module in the M2M Node; or, information for inferring location stored in other M2M Nodes.

In order to update the location information, an M2M AE shall be able to configure an attribute (e.g., update period) in this case based on the defined the attribute, the LOC CSF shall update the location information using one of interaction defined above.

Editor’s Note: Updating mechanism needs to be provided.

Note: The location technology (e.g., Cell-ID, Assistant-GPS, and Fingerprint) used by the Underlying Network depends on the capabilities of the Underlying Network.

The LOC CSF shall be able to request M2M Nodes to share and report their own or other M2M Nodes’ geographical location information with the requesting M2M Applications.

The LOC CSF shall be able to provide means for protecting the confidentiality of geographical location information.

Editor’s Note:  Details of the protection of privacy (e.g. obtaining the consent) is FFS.

# End of proposed text #