| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | subscription resource |
| Source:* | LG Electronics, CATT, HTC, Huawei, ALU, Cisco |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com Wei Zhou, zhouwei@catt.cn Den Yu, den_yu@htc.com Yuan Tao, taoyuan.tao@huawei.com Omar Elloumi, omar.elloumi@alcatel-lucent.com Philip Jacobs, phjacobs@cisco.com |
| Date:* | 2013-10-30 |
| Abstract:* | This contribution proposes subscriptions collection resource and <subscription> resource. |
| Agenda Item:* | Tbd |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

### 9.5.y	Resource <subscription>

The <subscription> resource contains subscription information for its subscribed-to resource.

The list of subscribable resources are as follows.

- <entity> resource (see clause TBD)

- <application> resource (see clause TBD)

- <accessRight> resource (see clause 9.6.2)

- <container> resource (see clause 9.6.3)

- <group> resource (see clause 9.6.5)

Editor’s Note: New subscribable resources can be added to the above list as new resource type definitions are agreed.

The <subscription> resource shall represent a subscription to a subscribed-to resource. An Originator shall be able to create a <subscription> resource when the originator has RETRIEVE permission to the subscribable resource. The Originator of a <subscription> resource becomes a resource subscriber.

When a modification to the subscribed-to resource occurs, that modification is compared to the criteria attribute to determine whether a notification is to be sent to the resource subscriber.

Editor’s Note: The access rights of the <subscription> resource is FFS. It may need <accessRight> and/or creator attributes to be added.

Figure 9.5.y-1: Structure of <subscription> resource

Editor’s Note: criteria is shown as an attribute, however whether we need a separate attribute or child resource for notification policy is FFS.

The <subscription> resource shall contain the attributes described in Table 9.5.y-1

Table 9.5.y-1: Attributes of <subscription>

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| ExpirationTime (common) | 1 | RW | See Table 9.6.1-1 |
| creationTime (common) | 1 | WO | See Table 9.6.1-1 |
| lastModifiedTime (common) | 1 | RO | See Table 9.6.1-1 |
| expirationCounter | 0..1 | RW | When the number of notification becomes the same as this counter, the <subscription> resource shall be deleted. |
| notificationURI | 1..n | RW | URI where the resource subscriber will receive notifications. |
| aggregationURI | 0..1 | RW | URI to aggregate notifications from group members of a group resource. |
| criteria | 0..1 | RW | Criteria to filter modifications to be sent to the resource subscriber (e.g., interested modification or notification policy). Editor’s Note: Defining criteria is FFS |

## End of Text ##

# Comments

we don’t know the parent-child relationship yet

since this contribution removed all about the collection resource, this should be removed too

as Josef commented before, active/inactive would be indicated maybe by an attribute later

as I commented ealier, this default criteria can be discussed later. BTW, this statement is false, when subscribed-to resource is deleted, it can be notified. Still this is also one of criteria we can deal with later.

# Text boxes

0..n

1

<subscription>

subscriptions

1..n

0..1

0..1

notificationURI

aggregationURI

0..1

criteria

<subscription>

expirationCounter