| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* | CR against TS0001v0.1.2 including change marks |
| Date:* | 2013-11-08 |
| Contact:* | Hongbeom Ahn (hongbeom.ahn@lge.com) |
| Reason for Change/s:* | Changes the locationPolicy attributes and resource description. |
| Clause/Sub Clause Affected* | 9.6.7 |
| Agenda Item:* |  |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | Architecture TS 0001v0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

Since TP#7 we agreed the concept this <locationPolicy> resource represents the method for obtaining and managing location information and actual location information shall be stored in a <container> resource, some attributes needs to be included such as locationContainerID (for cross reference)and locationContainerName.

Further, the other attributes, requestorID and locationReqPolicy are added. These attributes are used when the location information is obtained by location server in the underlying network. For example, the hosting CSE can use OMA MLP (mobile location protocol) over Mcn reference point between the CSE and the location server, in this case the requestorID can be used for privacy control, and locationReqPolicy can be used for specifying the required parameters (e.g. location accuracy).

2	Proposal

# Start of proposed text #

### 9.6.7		Resource Type locationPolicy

<locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node.

The actual location information shall be stored in the <instance> resource, a child resource of <container> resource and the <container> resource has the locationID attribute which holds the URI of this <locationPolicy> resource as a linkage. The LOC CSF can obtain location information based on the defined attributes under <locationPolicy> resource, and store the location information in the target <container>.

NOTE: Geographical location information is more than longitude and latitude.

Editor’s Note: The specific information where this resource is created is FFS.

Figure	9.6.7-1:  Structure of <locationPolicy> resource

The resource shall contain the attributes according to their multiplicity in Table 9.6.7-1 (0 indicates the optionality of the attribute).

Table 9.6.7-1:  Attributes of <locationPolicy> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchStrings | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| locationSource | 1 | RWO | Indicates the source of location information Network-Based GPS-Based Sharing-Based |
| locationUpdatePeriod | 0..1 | RW | Indicates the period for updating location information. If the value is marked ‘0’ or not defined, location information is updated only when a retrieval request is triggered. |
| locationTargetID | 0..1 | WO | The identifier to be used for retrieving the location information of a remote Node and this attribute is only used in case the locationSource attribute indicates Network-based. |
| locationServer | 0..1 | WO | Indicates the identity of the location server. This attribute is only used in case the locationSource attribute indicates Network-based. |
| locationContainerID | 0..1 | RO | URI of the <container> resource where the actual location information of a M2M Node is stored. |
| locationContainerName | 0..1 | WO | Name of the <container> resource where the actual location information of a M2M Node is store. If it is not assigned, the Hosting CSE automatically assigns a name of the resource. |
| requestorID | 0..1 | WO | Indicates ID and its type of ID that describes the originator which has requested the location information of the target M2M Node for privacy control. This attribute is only used in case the locationSource attributes indicates Network-based. |
| locationReqPolicy | 0..1 | RW | Indicate required parameters (e.g. location accuracy) between the Hosting CSE and the location Server. This attribute is only used in case the locationSource attribute indicates Network-based. The parameters can be different based on the interface which is used for location server connection. |

# End of proposed text #

# Text boxes

1

<locationPolicy

locationSource

locationUpdatePeriod

locationTargetID

locationServer

0..1

0..1

locationContainerID

locationServer

requestorID

locationReqPolicy

0..1

0..1

0..1

0..1

0..1