| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC |
| Title:* | Supported Resource Type Discovery Procedure |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2013-11-20 |
| Abstract:* | This contribution proposes supported resource type discovery. |
| Agenda Item:* | ARC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

oneM2M specification defines many “optional” resource types and attributes of each resource type, which means some of resource types and attributes are really implemented in CSE; Originator doesn’t have any knowledge which resource types and attributes are really implemented in Receiver CSE.

Since Originator (e.g., AE, CSE) doesn’t know which resource types the Resource Hosting CSE supports a priori, Originator may perform the operations (e.g., Create, Update) multiple times with trial and error. It’s also applied to attributes; Originator doesn’t know which attributes the Resource Hosting CSE supports prior to the real operation (Create, Update, Retrieve).

For example, Originator tries to create resource type 1, 2, 3, 4, and 5 in Receiver’s CSE but Receiver only supports resource type 1 and 3 so Originator fails to create resource type 2, 4, and 5.

To be able to minimize communication and computational burdens of both Originator and Resource Hosting CSE, this contribution proposes discovery process to recognize which resource types and attributes of the resource are supported in Resource Hosting CSE.

For example, Originator discovers capabilities of Receiver so Originator recognizes Receiver supports resource type 1 and 3. Then Originator just tries to create resource type 1 and 3 and doesn’t try to create resource type 2, 4, and 5.

Based on the result of this discovery process, Originator can access resources or attributes without any errors.

============================Start of 1st Change=============================

### 10.3.X 	Supported Resource Type Discovery Procedure

#### 10.3.X.1	Introduction

The supported resource type discovery procedures allow discovering of resource types and attributes of the resource types supported by a CSE. This procedure shall be applied when the Originator is either an AE or a CSE and the Receiver is a CSE. This specification defines multiple optional resource types and attributes for each resource type, which means that Originator can suffer multiple times of try and error for accessing (e.g., creating or updating) resource or attributes if the Originator doesn’t know which resource types or attributes of each resource type are supported by the Receiver. This supported resource type discovery procedure helps reduce unnecessary try and error by discovering which resource types or attributes are supported in the target Receiver. After this procedure, the Originator should send requests to the Receiver only including the supported resource types and/or attributes confirmed by the Receiver with this procedure.

Supported resource type discovery shall be done using the RETRIEVE request with the parameter indicating supported resource type discovery by the Originator to distinguish from discovery of resource and retrieval of resource. this discovery supports retrieving all the resource types or list of attributes and child resource types of a certain resource type, or informing whether the resource type or attribute is supported or not.

#### 10.3.X.2	Supported Resource type Discovery procedure via Retrieve Operation

This procedure shall be used for discovering capabilities of a CSE. The discovery result shall be returned to the Originator using a successful message.

Originator:  The Originator shall be either an AE or a CSE. The Originator shall provide the baseURI of the Receiver and the parameter indicating supported resource type discovery in the request. Resource type and/or attribute may be included in the request.

Receiver or Hosting CSE:  The Receiver shall be a CSE. If the Originator sends Retrieve operation with supported resource type discovery indicator, the Receiver shall perform the following procedures based on parameters of Originator’s request.

- If the request addresses baseURI without any resource type and attribute, the Receiver shall respond to the Originator with the list of all the resource types the Receiver supports.

- If the request addresses baseURI with a resource type, the Receiver shall respond to the Originator with the list of all the attributes and child resource types the Receiver supports for that resource type if the Receiver supports the resource type. 
If the Receiver doesn’t support the resource type the Originator indicated in the request, the Receiver informs the Originator the resource type is not supported.

- If the request addresses baseURI with resource type and attribute, the Receiver shall respond to the Originator whether the attribute of the resource type is supported or not by the Receiver if the Receiver supports the resource type.

- If the request addresses baseURI with attribute only, the Receiver shall respond to the Originator with format error.

Table 10.3.X.2-1 Supported Resource Type Discovery procedure via Retrieve Operation

| Description |
| --- |
| Call Flow Yype | RETRIEVE |
| Pre-Conditions | Originator needs to discover capabilities in the Hosting CSE. |
| Information on Request message | To: baseURI of Receiver. Cn: Resource type discovery indicator to determine this request is supported resource type discovery. Resource type and/or attribute the Originator needs to discover capabilities. |
| Local processing on Hosting CSE | Procedures described for the Receiver of the Retrieve Request as described above. |
| Information on Response message | Contains the URI list of name of resource types and attributes. Contains indicator whether resource type or attribute is supported or not. |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The request contains invalid parameters (e.g., only attribute parameter is specified.). |

============================End of 1st Change==============================

============================Start of 2nd Change=============================

### 6.2.5	Discovery

#### 6.2.5.1	General Concepts

Discovery (DIS) CSF is responsible for searching information (e.g., supported resource types/attribute) and resources according to a "request" from an Originator within a given scope and subject to permissions, including those allowed by M2M service subscription. An Originator could be an Application or another CSE. The scope of the search could be in one CSE, or in more than one CSE. The discovery results are returned back to the Originator.

#### 6.2.5.2	Detailed Descriptions

DIS CSF shall provide discovery of information/resources residing in its own CSE subject to permissions including the M2M service subscription. The DIS CSF shall be able to support various discovery methods through the use of "filter criteria" that can limit the scope of information/resources that are returned based on various filters (e.g. keyword, identifiers, location, semantic information) or a combination of such filters.

The DIS CSF shall be triggered by sending a "request" to the address (e.g., URI) of the discovery resource. Upon receiving such request, the DIS CSF shall identify and return the matching information/resources. A successful response may include the actual discovered information or address(es) (e.g., URI(s)) pertaining to the discovered resources. In addition, based on the policies or Originator request, the CSE which received the Discovery request may forward the request to other CSEs on its registered Middle/Infrastructure Node.

============================End of 2nd Change==============================