| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Multi-Protocol Information Elements and Subscription Notification Policy |
| Source:* | Cisco, LG Electronics, |
| Contact: | Philip Jacobs, phjacobs@cisco.com Seungmyeong Jeong, seungmyeong.jeong@lge.com Heedong Choi, heedong.choi@lge.com |
| Date:* | 2013-12-10 |
| Abstract:* | This contribution proposes a design principle and information elements - subscription notify policy - that exemplifies this principle. This revision adds more description to the subscription notification policy attibutes in the table, improves the name of two attributes, and adds an editor’s note pointing out the problem that intermediate nodes may pose. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Introduction

Some of the intended outcomes of the WG3 Work Item WI 0008 are to make oneM2M protocol interworking easier with other protocols and to generate a more inclusive set of oneM2M specifications, which are more likely/easier for industry, segments to adopt. Having started to analysis deployed protocols, we see that some have similar functions but use different mechanisms or different ways of expressing a mechanism. By including deployed protocol mechanisms and/or expressions inter-working between oneM2M will be easier. Conceptually an information element (maybe a resource) can be considered to be multi-protocol when viewed per the figure 1 below.

Figure 1 - Contents of a multi-protocol information element

As an example, consider what policies may be desirable for subscribers to have to about being notified. For scenarios where less message chattiness is desirable, aggregation of notifications into batches, sent when the subscriber wants notifications could be one native oneM2M policy. For scenarios where a constrained node is the subscriber is used, which may be unable to function properly if it were to receive too many notifications per unit time, a rate limiting policy could be applied. So we could have two native oneM2M subscription notification policies within a subscription resource.

- Batch notification: if set, accumulate notifications to be sent per “schedule”. E.g. 3-5am, 4-6pm, daily. If not set then send notifications immediately.

- Rate limiting: if set, then drop pending notifications after “count” notifications have been sent within each “duration” time. E.g. count =1,000, duration = 1 minute.

Subscription notification is a fairly common function across deployed protocols. Looking at two protocols from WG3 Work Item WI 0008, (TR-0009) MQTT and XMPP.

We could take from both the MQTT “Retained message” function and XEP-0163 “sending the last published item”:

- New subscription: if set, then notify the new resource subscriber of the subscribed resource event prior to their subscription becoming active, (if available). We could choose to make this default behaviour or to set the behaviour in an attribute.

We could derive from XEP-0163 “sending the last published item” (for MQTT this would assume “durable” sessions)

- Reachability notification: following a period of unreachability, when the resource subscriber becomes reachable, we could either send no prior notifications, send all pending notifications, or just the last pending notification. E.g. reconnectNotify = none, reconnectNotify = last, reconnectNotify = all, etc.

By including inputs derived from XMPP and MQTT in information elements, we should find that interworking translation will be easier. This is what is proposed below.

It is for further study in conjunction with current Ad hoc ARC discussions whether additional benefits of this principle might accrue in the future, for example:

- deployed protocols augmentation by native oneM2M functions within multiprotocol information elements e.g. add oneM2M charging to MQTT

- deployed protocol augmentation by other deployed ptotocols functions within multiprotocol information elements

- (or even further in the future) easier migration from deployed protocol to native oneM2M protocol

This contribution proposes to add policies to clause 9.6.9.

Some of those policies lead to storage of notification events, e.g. batch policy, therefore to indicate the relative priority to retain certain notification events over others belonging to the same subscriber in the case of storage congestion, a priority for these notification events is specified.

Depending upon how subscriber identity is tracked we may need to add subscriberID into <subscription>, it is FFS.

Also, a notificationCongestionPolicy will be needed at the CSE level, which would indicate what action to take when there is storage congestion. It is FFS, but could for example, specify:

- Immediately send (if possible) enough of the oldest notification events to free up sufficient storage, and if send fails then

- Drop enough of the lowest priority notifications to free sufficient space for new higher priority notification events. The age of lowest priority events is to be used as a tie-breaking criteria,

------------------------------------------------------START OF FIRST CHANGE--------------------------------------------------

### 9.6.9	Resource Type subscription

The <subscription> resource contains subscription information for its subscribed-to resource.

The list of subscribable resources is as follows.

- <entity> resource (see clause TBD)

- <application> resource (see clause TBD)

- <accessRight> resource (see clause 9.6.2)

- <container> resource (see clause 9.6.3)

- <group> resource (see clause 9.6.5)

Editor’s Note: It is not yet clear how or where to best to explain the applicability of the resource <subscription>. Subscribable resources can be added to the list above, Non-subscribable resources can also be added to the list above, and/or we could ensure that the applicability of the resource <subscription> is clearly described with each resource, removing or keeping the list here.

The <subscription> resource shall represent a subscription to a subscribed-to resource. An Originator shall be able to create a <subscription> resource when the originator has RETRIEVE permission to the subscribable resource. The Originator of a <subscription> resource becomes a resource subscriber.

When a modification to the subscribed-to resource occurs, that modification is compared to the criteria attribute to determine whether a notification is to be sent to the resource subscriber.

Editor’s Note: The access rights of the <subscription> resource is FFS. It may need <accessRight> and/or creator attributes to be added.

Figure 9.6.9-1: Structure of <subscription> resource 
(only resource specific attributes are shown)

Table 9.6.9-1: Child resources of <subscription> resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| notificationSchedule | <schedule> | 0..1 | See clause 9.6.x |

The <subscription> resource shall contain the attributes described in Table 9.6.9-2

Table 9.6.9-2: Attributes of <subscription> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| filtercriteria | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| expirationCounter | 0..1 | RW | When the number of notifications becomes the same as this counter, the <subscription> resource shall be deleted. |
| notificationURI | 1..n | RW | URI where the resource subscriber will receive notifications. |
| aggregationURI | 0..1 | RW | URI to aggregate notifications from group members of a <group> resource. |
| batchNotify | 0..1 | RW | Indicates that notifications should be batched for delivery. When set, notification events are temporarily stored until either a specified number is ready to send or until a duration after the first noticifaction event has expired. |
| rateLimit | 0..1 | RW | Indicates that notifications should be rate-limited. When set, notification events that exceed a specified number within a specified time are temporarily stored then sent when the number of events sent per specified time falls below the limit. |
| priorSubscriptionNotify | 0..1 | WO | Indicates that when this subscription is created, whether notification events prior to subscription should be sent, e.g. send prior “n” notifications, if available. |
| interimEventsNotify | 0..1 | RW | Indicates the notification action to be taken following a period of unreachability, when the resource subscriber becomes reachable (e.g. send “n” iterim notificiations, if available.) |
| notificationStoragePriority | 0..1 | RW | Indicates a priority for this subscription relative to other subscriptions belonging to this same subscriber for retention of notification events when storage is congested. The storage congestion policy which uses this attribute as input is specified in clause TBD. |

Editor’s Note: In the case when there are intermediate nodes between the Originator and a Receiver, the intermediate nodes may not act in accordance with the subscription notification policy. Examples include: a policy of batching subscribed events for up to 30 seconds then deliver immediately, but an intermediate node may decide to delay or further aggregate the subscription notifications. The solution to this problem is FFS, but may include sending a representation of policy with the subscription notifications, which is to be considered by intermediate nodes (e.g. Request Expiration Time).

------------------------------------------------------END OF FIRST CHANGE--------------------------------------------------