| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Correction on section 9.6.7 |
| Source:* | NEC |
| Contact: | Barbara Pareglio, Barbara.pareglio@neclab.eu |
| Date:* | 2013-11-28 |
| Abstract:* | This contribution correct some inconsistency between figure 9.6.7.-1 and table 9.6.7-1 |
| Agenda Item:* | Contribution |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 V. 0.2.2, Technical Specification - M2M Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Introduction

The contributions correct a mistake in figure 9.6.7-1, since the multiplicity of the attributes does not reflect the information in table 9.6.7-1. In the figure, the attributes: locationUpdatePeriod, locationTargeId and locationServer are depicted as mandatory, while they are all optional attributes.

---------------------------------------------------------------START OF 1st CHANGES-------------------------------------------------

### Resource Type locationPolicy

<locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M entity by the LOC CSF.

The actual location information shall be stored in the <instance> resource, a child resource of <container> resource.  The <container> resource has the locationId attribute which holds the URI of this <locationPolicy> resource as a linkage. The LOC CSF can obtain location information based on the attributes defined under <locationPolicy> resource, and store the location information in the target <container> resource.

NOTE: Geographical location information is more than longitude and latitude.

Editor’s Note: The specific information where this resource is created is FFS.

Figure 9.6.7-1:  Structure of <locationPolicy> resource
(only resource specific attributes are shown)

This resource shall contain the attributes according to their multiplicity in Table 9.6.7-1 (0 indicates the optionality of the attribute).

Table 9.6.7-1:  Attributes of <locationPolicy> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchStrings | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| maxNumOfInstances | 0..1 | RW | Maximum number of bytes that are allocated for a <locationContainer> resource for the overall instances. |
| maxByteSize | 0..1 | RW | Maximum number of instances of a <locationContainer> resource. Editor's Note: This does not seem to be correct discription. The original contributor needs to provide new description. |
| locationSource | 1 | RW | Indicates the source of location information Network Based GPS Based Sharing Based |
| locationUpdatePeriod | 0..1 | RW | Indicates the period for updating location information. If the value is marked ‘0’ or not defined, location information is updated only when a retrieval request is triggered. |
| locationTargetId | 0..1 | RW | The identifier to be used for retrieving the location information of a remote Node and this attribute is only used in the case that location information is provided by a location server. |
| locationServer | 0..1 | RW | Indicates the identity of the location server. This attribute is only used in that case location information is provided by a location server. |

---------------------------------------------------------------END OF 1st CHANGES--------------------------------------------------