| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP8 |
| Title:* | Functional architecture in oneM2M-TS-0001 oneM2M Functional Architecture-V-0.2.2 |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2013-11-30 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes additions to the functional architecture

* * * Start of 1st Change * * *

#### 5.2.2.4 Mcc’ Reference Point

The Mcc’ reference point designates communication flows between two Common Service Entities (CSEs) in infrastructure nodes that are oneM2M compliant and that resides in different M2M SP domains. Hence, it allows a CSE of an infrastructure node residing in the Network Domain of an M2M Service Provider to communicate with a CSE of another infrastructure node residing in the Network Domain of another M2M Service Provider to use its services,  and vice versa.

The actual trigger for this communication could be initiated elsewhere in the oneM2M network. Hence, Mcc’ extends the reachability of services offered over the Mcc reference point, or a subset thereof.

Note that the services offered via the Mcc reference point are dependent on the functionality supported by the CSEs.

* * * End of 1st Change * * *

* * * Start of 2nd Change * * *

#### Resource Addressing

Resources shall be uniquely addressable via URI. The following are examples of addressable resources.

/baseRoot/Entity Instance 1

/baseRoot/Entity Instance n

/baseRoot/Application Instance 1

/baseRoot/Application Instance n

/baseRootContainer1/Container2

Resources may be associated by using a link with reference to another resource.

The baseRoot shall contain all resources of the hosting node. A baseRoot is the root of all other resources it contains. The baseRoot shall represent the first element of the path representing a resource in an absolute URI, as per [F]. All other resources hosted in the CSE shall also be identified by an absolute URI.

The authority part of the absolute URI, as per [E] and [F] shall be either an infrastructure service node public domain name, a middle service node public domain name or an application service node public domain name and shall conform to the naming convention depicted in section 6.5.1.1.1:

example of a URI identifier of a container resource hosted by a CSE could be "http://IntermediatenodeCSEID.infrastructurenodeCSEID.m2m.myoperator.org/baseRoot/containers/myExampleContainer"

* * * End of 2nd Change * * *