| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | mgmtObj resource |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin (yinjiaxin@huawei.com) |
| Date:* | 2013-11-28 |
| Abstract:* | The contribution provides description to management object resource. |
| Agenda Item:* | Tbd |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the texts into the TS if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

#### 9.X	Resource Type MgmtObj

The mgmtObj resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology (e.g. OMA DM, BBF TR-069 and LWM2M) data models.

Figure 9.x.1: Structure of <mgmtObj>

The <mgmtObj> resource shall contain the sub resources with the indicated multiplicity in Table 9.x.1.

Table 9.x.1: Child Resource of <mgmtObj>

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <parameters> | 0..n | Collects multiple parameters or attributes for management purpose. A <parameters> can have zero or more other <parameters> so as to form hierarchical structure, i.e. the management data for this specific <mgmtObj>. Such structure helps to import existing management objects as defined in OMA DM, BBF TR-069, LWM2M, or any other technology. |

The <mgmtObj> resource shall contain the attributes with the indicated multiplicity in Table 9.x.2.

Table 9.x.2: Attributes of <mgmtObj>

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType(rT) | 1 | WO | See clause 9.6.1 Common attributes. |
| mgmtDefinition | 1 | WO | Indicates specific device management functionalities. Editor’s note: Description needed. |
| expirationTime | 1 | RW | See clause 9.6.1 Common attributes. |
| accessRightID | 1 | RW | See clause 9.6.1 Common attributes. |
| creationTime | 1 | RO | See clause 9.6.1 Common attributes. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 Common attributes. |
| objectID | 0…1 | WO | Contains a URN that uniquely identifies the external management technology data model used for this <mgmtObj> resource as well as the manage function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> and shall not be modifiable afterwards. It is mandatory for the <mgmtObj>, of which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols (e.g. OMA-DM, BBF TR-069 and LWM2M). |
| objectPath | 0…1 | WO | Contains the local path of the external management object instance on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM, "Device.USBHosts.Host.3." in BBF TR-069). |
| <moAttribute> | 0…n | RW | Each <moAttribute> is mapped from a leaf node of a hierarchical structured management objects (including oneM2M data model and the existing management data models) based on the mapping rules below the table. |
| description | 0…1 | RW | Text format description of mgmtObj. |

When mapping resources from management technologies to a corresponding <mgmtObj> resource, the follow rules shall apply:

- The root resource of external management objects maps to the <mgmtObj> resource:

- For child resource of the root resource of specific technology:

- Rule1) If the child external management object cannot have child external management object, the external management object maps to the <moAttribute> attribute of the <mgmtObj> resource with the same resource name

- Rule2) If the child external management object can have another child external management object, the external management object maps to the <parameters> resource with the same resource name

- For the external management object that is mapped to the <parameters> resource, the child external management object of the external management object are mapped to the <moAttribute> attribute or to the <parameter> resource according to the Rule1 and Rule2.

#### 9.y	Resource Type Parameters

Figure 9.28: Structure of <parameters>

The <parameters> resource shall contain the child resources with the indicated multiplicity in Table 9.y.1.

Table 9.y.1: Child Resource of <parameters>

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <parameters> | 0..n | See clause 9.y |

The <parameters> resource shall contain the attributes with the indicated multiplicity in Table 9.y.2.

Table 9.y.2: Attributes of <parameters>

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| accessRightID | 1 | RW | See clause 9.x.x Common attributes. |
| creationTime | 1 | RO | See clause 9.x.x Common attributes. |
| lastModifiedTime | 1 | RO | See clause 9.x.x Common attributes. |
| objectID | 0…1 | WO | See table 9.x.2 |
| objectPath | 0…1 | WO | See table 9.x.2 |
| <moAttribute> | 0…1 | RW | See table 9.x.2 |
| description | 0…1 | RW | Text format description of mgmtObj. |

# Text boxes

1

<mgmtObj>

objectID

0…1

<parameters>

objectPath

<moAttribute>

description

0…1

0…n

0…1

0…n

1

<parameters>

0…1

<parameters>

0…n

objectID

objectPath

<moAttribute>

description

0…1

0…n

0…1