| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#8 |
| Title:* | Service Session Management (SSM) CSF Resources |
| Source:* | Session management CSF group (ZTE, LGE, InterDigital) |
| Contact: |  |
| Date:* | <2013-11-13> |
| Abstract:* | This contribution proposes Service Session Management (SSM) CSF resources |
| Agenda Item:* | CSF Resource Descriptions |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Rationale

This contribution provides resources to support M2M Service Session Management (SSM).

At TP7, an initial version of the SSM resources was proposed in contribution oneM2M-ARC-2013-0454R02.  Based on the feedback received from TP7 and the Nov 7th ARC call, the following is a summary of the modifications provided in this contribution.

- Simplified SSM resource structure

  - Removed use of collection resources

  - Replaced  <sessionParticipant> resource functionality with sessionParticipants attribute

  - Simplified attributes in <session>, <sessionPolicy>, and <sessionContext> resources

- To allow re-used and sharing of <sessionPolicy> resources, added a ‘policies’ attribute to <session> resource to link by reference to <sessionPolicy> resources.

- Added sessionCredential attribute to <session> resource

- Added sessionCapable and sessionInvite attributes to <application> resource to support service session.

2	Proposal

### 9.6.w	Resource Type session

The M2M Service Session Management resource structure consists of <session>, <sessionContext>, and <sessionPolicy> resources. A <session> resource contains information for managing an individual M2M service session. The <sessionContext> resources are child resources of a <session> resource since they are used to maintain context information for a particular service session. The <sessionPolicy> resources are not child resources of a <session> since multiple <session> resources may use the same <sessionPolicy>. For this reason, a <session> resource links by reference to <sessionPolicy> resources.

Figure	9.6.w.1: Structure of <session> resource

This resource shall contain the child resource according to their multiplicity in the Table 9.6.w-1 (0 indicates the optionality of the child resource).

Table 9.6.w-1: Child resources of <accessRight> resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <sessionPolicy> | 0..n | See section 9.6.y. |

The <session> resource shall contain the attributes according to their multiplicity in Table 9.6.w-2 (0 indicates the optionality of the attribute).

Table 9.6.w-2: Attributes of <session> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchString | 1 | RW | See section 9.6.1 where this common attribute is described. |
| sessionID | 1 | RO | A unique ID is assigned by SSM CSF when M2M service session is established (i.e. when <session> resource is created). |
| credentials | 0..1 | RO | Credentials used by the session participants (e.g. to perform E2E security (e.g. authentication, encryption/decryption of service session data, etc). Editor’s note: Need to further discuss viability of CSE managing service session credentials and storage within <session> resource with SEC WG. |
| state | 1 | RW | Used to observe and control the operational state of M2M service session (e.g. ONLINE, PAUSED, RESET, etc) Editor’s note: Supported session states is FFS. |
| participants | 1 | RW | List of identifiers of M2M service session participants. For participants that are AEs, application identifier (App-ID) is used. For participants that are CSEs, CSE identifier (CSE-ID) is used. |
| policyLinks | 0..1 | RW | List of URIs of M2M service session policy resources associated with this service session |

### 9.6.x	Resource <sessionContext>

The <sessionContext> resource contains attributes applicable to a particular type of M2M service session context that is collected and maintained by a M2M service session.

Figure	9.6.x.1: Structure of <sessionContext> resource

The <sessionContext> resource shall contain the attributes according to their multiplicity in Table 9.6.x-1 (0 indicated the optionality of the attribute).

Table 9.6.x-1: Attribute of <sessionContext> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchString | 1 | RW | See section 9.6.1 where this common attribute is described. |
| type | 1 | RW | Used to select the type of service session context that the SSM stores within the ‘context’ attribute. SSM supports policy-based context collection by configuring this attribute with a URI that references a <sessionPolicy> resource defining a set of context collection rules. SSM also supports natively collecting certain types of session content (e.g. total number of requests, rate of request, total bytes consumed, etc) Editor’s Note: Supported set of native context types is FFS. |
| context | 1 | RO | Service session context information collected by SSM. Type of collected context is defined by ‘type’ attribute. |

### 9.6.y	Resource <sessionPolicy>

A <sessionPolicy> resource contains a description of an individual M2M service session policy.

Figure	9.6.y.1: Structure of sessionPolicies resource

Editor’s Note: It may make sense for oneM2M to define a more generic <policy> resource rather than a <sessionPolicy> resource.

The <sessionPolicy> resource shall contain the attributes according to their multiplicity in Table 9.6.y-1 (0 indicated the optionality of the attribute).

Table 9.6.y-1: Attributes of sessionPolicy resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchString | 1 | RW | See section 9.6.1 where this common attribute is described. |
| rules | 1 | RW | Defines rules for service session management. E.g. Service session context collection rules Service session request processing rules CMDH delivery parameter configuration rules. Rules for SSM CSF interaction with underlying network Editor’s Note: Supported set of native rules is FFS. |

### 9.x.y	Service Session Attributes for <application>

Editor’s note –  To support M2M service sessions, sessionCapable and sessionInvite attributes have been defined for the <application> resource.   The latest version of the TS however does not yet include a section for the <application> resource.  Once it does, these attributes should be included.

Figure	9.x.y.1: Service Session attributes of application resource

Table 9.x.y-1: Session Attributes of application resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| sessionCapable | 0..1 | RO | Defines whether AE is capable of service-session based communication (TRUE or FALSE) |
| sessionInvite | 0..1 | RW | Used to invite an AE to join a service session. To invite a AE to join a service session, this attribute is updated with the URI of a <session> resource which the AE is invited to join. An AE can subscribe to updates to this attribute and in turn receive notifications for each service session invitation. |