| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP#8 |
| Title:* | CSE Resource Description |
| Source:* | Telecom Italia, CATT, ZTE |
| Contact: | Lupano Michele, michele.lupano@telecomitalia.it Wei Zhou, zhouwei@catt.cn Hao Wu, wu.hao18@zte.com.cn |
| Date:* | 2013-12-09 |
| Abstract:* | This contribution proposes resource description for <CSE> resources. |
| Agenda Item:* | To be defined |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this text into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution proposes resource description for <CSE> resources.

- Proposal

### ===================== 1st Change =========================

### 9.6.x		Resource <remoteCse>

A <remoteCse> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <baseURI> resource.

Conversely each registered CSE shall also be represented as a sub-set <remoteCse> resource in the registering CSE's <baseURI> resource.

For example, when CSE1 registers with CSE2, there will be two <remoteCse> resources created: one in CSE1 <baseURI1>/<remoteCse2> and one in CSE2 <baseURI2>/<remoteCse1>.

Figure 9.6.x-1: Structure of <remoteCse> resource
(only child resources and specific resource attributes are shown)

The <remoteCse> resource shall contain the child resources according to their multiplicitly in Table 9.6.x-1 (0 indicated the optionality of the child resource).

Table 9.6.x-1: Child resources of <remoteCse> resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <ae> | 0..n | See section 9.6.x. |
| [variable] | <container> | 0..n | See section 9.6.x. |
| [variable] | <group> | 0..n | See section 9.6.x. |
| [variable] | <accessRight> | 0..n | See section 9.6.x. |
| [variable] | <subscription> | 0..n | See section 9.6.x. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.x. |

This resource shall contain the attributes according to their multiplicitly in Table 9.6.x-2 (0 indicates the optionality of the attribute).

Table 9.6.x-2: Attributes of <remoteCse> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID(aRI) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| searchStrings (sS) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| pointOfAccess (poA) | 0..n | RW | For server capable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not server capable. |
| baseURI (bUr) | 1 | RW | The URI of the <baseURI> resource of the remote CSE. |
| announceTo (aT) | 0..1 | RW | A list of remote CSEs to which the registered remote CSE could be announced. The attribute is absent in case of announced <remoteCse> resource. |
| link (lk) | 0..1 | RW | The URI address of the <remoteCse> resource being announced. The attribute is present only in the announced <remoteCse> resource. |

<remoteCse> and announced <remoteCse> shall have different resourceType coding.

Editor’s note: the CSE information to be exposed strictly dependens by the <baseURI> resource information that must be specified.

Editor’s note: announcement attributes and refercences must be alined with agreed resource announcement contributions when available.

================== End of 1st Change ======================