| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP#8 (Mizazaki, Japan) |
| Title:* | Application Resource Type |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com |
| Contact: | See source |
| Date:* | <2013-12-02> |
| Abstract:* | This contribution introduces the notion of an Application resource that represents, in a Common Services Entity, an Application Entity known to the CSE. |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 – Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To adopt the suggested modification for inclusion into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

In its current version, the Architecture Technical Specification introduces in the section 9.2 the concept of a resource type “Application”. This resource is succinctly described to store information related to an application, without being completely specified.

As a result, this present contribution proposes to specify the resource type Application, and to extend its scope to other means deemed useful.

- Proposal

# Start of proposed new text #

### 9.6.X		Resource Type Application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

The <application> resource shall contain the following attributes.

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime | 1 | RW | See sectioin 9.6.1 where this common attribute is described. |
| accessRightID | 0..1 | RW | See sectioin 9.6.1 where this common attribute is described. |
| creationTime | 1 | RW | See sectioin 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See sectioin 9.6.1 where this common attribute is described. |
| creator | 1 | RW | See sectioin 9.6.1 where this common attribute is described. |
| searchStrings | 0..1 | RO | See sectioin 9.6.1 where this common attribute is described. |
| type | 1 | RO | The type of the application. Typically, the type could be something like FIRMWARE or SOFTWARE. |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (eg. “HeatingMonitoring”) |
| version | 1 | RO | The version number of the application (eg 3.4 or Saucy Salamander or 4.4-KitKat) |
| releaseDate | 1 | RO | The release date of the application |
| state | 1 | RW | The current state of the application (deployed, installed, started, stopped, …) |

# End of proposed text #