| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP#8 (Mizazaki, Japan) |
| Title:* | Application Resource Type |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com Yonglae Cho, KT, yonglae.cho@kt.com |
| Contact: | See source |
| Date:* | <2013-12-02> |
| Abstract:* | This contribution introduces the notion of an Application resource that represents, in a Common Services Entity, an Application Entity known to the CSE. |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 – Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To adopt the suggested modification for inclusion into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

In its current version, the Architecture Technical Specification introduces in the section 9.2 the concept of a resource type “Application”. This resource is succinctly described to store information related to an application, without being completely specified.

As a result, this present contribution proposes to specify the resource type Application, and to extend its scope to other means deemed useful.

- Proposal

# Start of proposed new text #

### 9.6.X		Resource Type Application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

The <application> resource shall contain the following attributes.

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType |  |  |  |
| expirationTime | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
|  |  |  | See section 9.6.1 where this common attribute is described. |
| searchStrings | 0..1 | RO | See section 9.6.1 where this common attribute is described. |
| type | 1 | RO | The type of the application. It is either FIRMWARE (for an operating system/runtime environment supporting/including the CSE) or SOFTWARE(eg. Application entity or part of AE). |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (eg. “HeatingMonitoring”) |
| status | 1 | RW | The current state of the application (deployed, installed, started, stopped, …) |
| appId | 1 | RO | Application Identifier |
| App-Inst-Id | 0..1 | RO | When the application resource refers to an actual application instance in the executing environment. |
| reachabilityStatus | 1 | RW |  |

The <application> resource shall contain the following sub resources.

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| firmware | <mgmtObj> | 0..n | This resource is only present if the “type” attribute is set to FIRMWARE. It represents the firmware component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its “parameters” subresource: name (multiplicity 1) version (multiplicity 1) state (multiplicity 1) |
| software | <mgmtObj> | 0..n | This resource is only present if the “type” attribute is set to SOFTWARE. It represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its “parameters” subresource: name (multiplicity 1) version (multiplicity 1) state (multiplicity 1) |
| [variable] | <commCapabilities> | 1..n | This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. |
| [variable] | <dataModel> | 1 | This resource describes the data model of the application, i.e. the data (variables, commands, events) that is exchanged and used by this application. M2M The data model shall include variables (readable and/or writable from the perspective of the application), events (sent by the application) and commands (understood by the application), even if these may be then mapped in a similar or even the same way on underlying protocols. |

# End of proposed text #