| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Summary Tables |
| Source:* | Cisco Systems Inc |
| Contact: | Philip Jacobs, phjacobs@cisco.com |
| Date:* | 2013-12-11 |
| Abstract:* | This editorial contribution proposes to add summary tables for the parameters of the General Flow in Clause 8.1. This version incorporates feedback from TP8. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Introduction

The current text description of clauses 8.1.2 Request, 8.1.3 Successful Operation and 8.1.4 Unsuccessful Operation, contains many information elements in list form without any unified view of how then are applied for CRUD operations. Therefore it is proposed to add tabular summaries for the Request and Response information elements including CRUD operations, for easier understanding.

It is proposed that the first “Request Summary” table would be added as a new subclause of 8.1.2 as 8.1.2.1.

It is proposed that the “Response Summary” table would be added as new clause 8.1.5

Note that this table is based upon the baseline ARC TS v_0_2_2, and may need to be revised as clauses 8.1.2, 8.1.3, and 8.1.4 are revised.

------------------------------------------------------START OF FIRST ADDITION --------------------------------------------------

### 8.1.2.1	Summary of Request Message Parameters

Table x summarises the parameters specified in clause 8.1.2 for the Request message, showing any differences as applied to C, R, U or D operations. “M” indicates mandatory, “O” indicates optional, “N/A” indicates “not applicable”.

Table x - Summary of Request message parameters

| Request message parameter \ Operation | Create: a new resource is created | Retrieve: an existing resource is read and the result is provided | Update: the content of an existing resource is replaced with new content | Delete: an existing resource and all its sub-resources are deleted |
| --- | --- | --- | --- | --- |
| To (to) – the address of the target resource on the target CSE | M | M | M | M |
| From (fr) – the identifier of the message Originator | M | M | M | M |
| Request Identifier (ri) – uniquely identifies a Request message | M | M | M | M |
| Resource Type (rt) - of resource to be created | M | N/A | N/A | N/A |
| Content (cn) - to be transferred | O | O | M | N/A |
| Originating Timestamp (ot) - when the message was built | O | O | O | O |
| Request Expiration Timestamp (rqet) – when the request message expires | O | O | O | O |
| Result Expiration Timestamp (rset) -when the result message expires | O | O | O | O |
| Operational Execution Time (oet) - the time when the specified operation is to be executed by the target CSE. | O | O | O | O |
| Response Type (rt) – local CSE response shall either indicate that the Request was accepted, or include the operation result | O | O | O | O |
| Result Destination (rd) – either a reference to where the result is stored, or the result is sent to the Originator | O | O | O | O |
| Result Persistence (rp) - the duration for which the reference containing the responses is to persist | O | O | O | O |
| Result Content (rc) – the expected components of the result | O | O | O | O |
| Lifespan (ls) - time after which the system should not deliver the message | O | O | O | O |
| Event Category (ec) – indicates how and when the system should deliver the message | O | O | O | O |
| Delivery Aggregation (da) - aggregation of requests to the same target CSE is to be used | O | O | O | O |

------------------------------------------------------END OF FIRST ADDITION ------------------------------------------------------

---------------------------------------------------START OF SECOND ADDITION --------------------------------------------------

### 8.1.5	Summary of Response Message Parameters

Table y summarises the parameters specified in clauses 8.1.3 and 8.1.1 for the Response messages, showing any differences as applied to successful C, R, U or D operations, and unsuccessful operations. “M” indicates mandatory, “O” indicates optional, “N/A” indicates “not applicable”.

Table y - Summary of Response Message Parameters

| Response message parameter \ success or not | Successful operation: Create: a new resource is created | Successful operation: Retrieve: an existing resource is read and the result is provided | Successful operation: Update: the content of an existing resource is replaced with new content | Successful operation: Delete: an existing resource and all its sub-resources are deleted | Unsuccessful Operation |
| --- | --- | --- | --- | --- | --- |
| Request Identifier (ri) – uniquely identifies a Request message | M | M | M | M | M |
| Result (rs) - operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., | M | M | M | M | M |
| Status codes (cs) - (e.g., authorization timeout, etc.) | O | O | O | O | O |
| Response Address (ra) - address for the temporary storage of end node Responses. | O | O | O | O | N/A |
| Content (cn) - to be transferred | O (The address and/or the content of the created resource) | M (the retrieved resource content or aggregated contents of discovered resources) | O (The content replaced in an existing resource) | O (The content actually deleted) | N/A |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O |
| Result Expiration Timestamp (rset) – when the result message expires | O | O | O | O | O |

------------------------------------------------------END OF SECOND ADDITION--------------------------------------------------