| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC#8 |
| Title:* | M2M Service Subscription Management |
| Source:* | Omar Elloumi, Tim Carey Alcatel-Lucent, omar.elloumi@alcatel-lucent.com |
| Contact: |  |
| Date:* | 2013-12-2 |
| Abstract:* | Rationale and addition of M2M Service Subscription management |
| Agenda Item:* |  |
| Work item(s): | ARC TS |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add normative text in ARC TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Rationale

The requirements TS identifies several M2M Service Subscription related requirements. Those are depicted below:

OSR-023

The M2M System shall be able to identify the M2M Services to be used by M2M Service Subscriptions.

Note: M2M Service Subscriptions are not Application subscriptions (e.g., Home Energy Management).

OSR-024

The M2M System shall be able to identify the M2M Devices used by M2M Service Subscriptions.

OSR-025

The M2M System shall be able to identify the M2M Applications used by M2M Service Subscriptions.

OSR-026

If provided by the Underlying Network, the M2M System shall be able to  associate the M2M Device used by M2M Service Subscriptions with the device identifiers offered by the Underlying Network and the device.

Typically the M2M Service Subscription is created following a business agreement between an M2M Application Provider and an M2M Service provider. However during the lifetime of the M2M Service Subscription it should be possible for the application provider to use the Mca reference point to manage (add/delete/update):

- Devices pertaining to a M2M Service Subscription

- Applications  instances pertaining to a M2M Service Subscription

- Services pertaining to a M2M Service Subscription.

- M2M Service Subscription

While this contribution presents a resource for a M2M Service Subscription per se (and sub resources or attributes for devices, applications and services) typically a M2M Service Subscription is created by on offline provisioning tool of the M2M SP.

The use of roles in the context of M2M service subscription is FFS.

The M2M Service Provider provides a set of M2M services. The M2M Service has a unique and is associated with a set of M2M Service Capabilities.  The mechanism by which M2M Services are defined is FFS.

When an application provisions a M2M service subscription it needs to select a set of M2M services by providing the identifier of the M2M Service.

The M2M Service Subscription is defined to be an agreement between a provider and a subscriber for consumption of M2M Services for a period of time.

The following description depicts the list of service capabilities pertaining to the M2M Service Susbscription:

- Add/Update/Delete/Retrieve  a M2M Service Subscription

- Update the list of devices pertaining the M2M Service Subscription

  - Add or delete devices

  - Add, delete and update a range of device based upon external IDs

  - Update device attributes

- Update the list of applications pertaining the M2M Service Subscription

  - Add or delete applications

  - Update application attributes

- Update the list of M2M Services pertaining to the M2M Service Subscription

  - Add or delete M2M Services

Editor’s note: The list above only indicates the list of service capabilities exposed across the Mca reference point. There are additional service capabilities (e.g., validateM2MServiceSubscription) that would be provided by the M2M Service Subscription and consumed by other CSFs. These service capabilities are FFS.

- Proposal

Add the following section to 9.6

### 9.6.X Resource Type <m2mSeviceSubscription>

This resource represents a M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription (the technical part of the contract between an M2M Application provider and an M2M Service Provider).

Figure 9.6.x.x: Structure of <m2mServiceSubscription> resource
(only child resources and resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.x-x  (0 indicates the optionality of the child resource).

Table 9.6.x-x: Child resources of <m2mServiceSubscription> resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <device> | 0..n | A resource representing a device under this service subscription. The same device can belong to multiple M2M service subscriptions. |
| [variable] | <service> | 0..n | A resource that represents a subscribed service, identified by a service identifier. |
| [variable] | <application> | 0..n | A resource that represents an application under this service subscription. The same application can belong to multiple M2M service subscriptions. |

This resource shall contain the attributes according to their multiplicitly in Table 9.6.3-2 (0 indicates the optionality of the attribute).

Table 9.6.3-2: Attribute of <m2mServiceSubscription> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (st) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |

### 9.6.X Resource Type <device>

This resource is a representation of a device that is a part of an M2M Service Subscription.

Figure 9.6.x.x: Structure of <device> resource 
(only child resources and resource specific attributes are shown)

This resource shall contain the attributes according to their multiplicitly in Table 9.6.3-2 (0 indicates the optionality of the attribute).

Table 9.6.3-2: Attribute of <device> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (st) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| deviceIDTypeList | 1 | RW | A list if deviceID and type pairs. |
| profile | 1 | RW | Device profile |
| extIdList | 0..1 | RW | Represent a list of external identifiers used for the purpose of control plane interactions with the underlying network. For more information on this ID, see 7.1.8 (M2M-Ext-ID) |
| appInstIdList | 0..1 | RW | Represents a list of application instance identifiers pertaining to applications running on this device. |

### 9.6.X Resource Type <service>

This resource points to a service identifier requested for the M2M Service Subscription.

Figure 9.6.x.x: Structure of <service> resource 
(only child resources and resource specific attributes are shown)

This resource shall contain the attributes according to their multiplicitly in Table 9.6.3-2 (0 indicates the optionality of the attribute).

Table 9.6.3-2: Attribute of <service> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (st) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| serviceID | 1 | RW | Contains the identifier of the subscribed service |

### 9.6.X Resource Type <application>

This resource points to an application that is part of the M2M Service Subscription.

Figure 9.6.x.x: Structure of <application> resource 
(only child resources and resource specific attributes are shown)

This resource shall contain the attributes according to their multiplicitly in Table 9.6.3-2 (0 indicates the optionality of the attribute).

Table 9.6.3-2: Attribute of <application> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (st) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| appInstID | 1 | RW | Contains the identifier of an application instance. See 7.1.2 |