| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2/WG5 |
| Title:* | Management Adapter in MN |
| Source:* | Masaharu Hattori, KDDI, ma-hattori@kddi.com |
| Contact: | Masaharu Hattori, KDDI, ma-hattori@kddi.com |
| Date:* | 2013-12-09 |
| Abstract:* | Function of Management Adapter in MN (related with oneM2M-MAS-2013-0133) |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | If oneM2M-MAS-2013-0133 is agreed, this contribution will be discussed in joint session of Architecture WG and MAS WG for inclusion in the Functional Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution is related to clarify the role of the Management Adapter in MN.

According to “Requirement TS”, there is a MGR-012 requirement which sentence is described below.

“Upon detection of a new device the M2M Gateway shall be able to be provisioned by the M2M Service Infrastructure with an appropriate configuration which is required to handle the detected device.”

And according to “Study of Management Capability Enablement TR”, the M2M Gateway needs to have LWM2M Server feature in OMA DM LWM2M deployment scenario, so as to meet the requirement.

However, the present management architecture is assumed below.

- Proxy function is needed in order to manage the device in M2M Area Network.

- The device in M2M Area Network is required to implement proxy client (e.g. OMA-DM 1.3, 2.0 and TR-069)

Figure 6.2.4.1.1-1  Device Management Architecture

Therefore, it seems not to consider that management protocol in Device in M2M Area Network is OMA LWM2M protocol, meanwhile more lightweight protocol is preferable for the device.

- Proposal

The proposal of this contribution is that Management Adapter in MN adds function so as to utilize management protocols which doesn’t have proxy function.

Typically, the sentence below describe in Architecture TS ver. 0.2.2 chapter 6.2.4.1.1

## Beginning of Text ##

##### 6.2.4.1.1	Device Management Architecture

*****

In the case of the Middle and Device Nodes, the DMG in the CSE of the Middle Node has the same functionality as the DMG in the CSE of the Device Node. In addition, the DMG in the Middle Node can be used to manage devices in the M2M Area Network. In this case, the DMG is deployed with Proxy functionality that interacts with the Proxy Management Client using the "mp" interface. The "mp" interface represented by a gray dashed line is technology dependent and is outside the scope of this specification.

If the proxy function of management protocol cannot be utilized, the Management Adapter in MN provide function below.

- Bridging between Management Server and Client in the same DMG

If Management protocol doesn’t has proxy function, the Management Adapter can bridge between Management Server and Client in the same DMG of MN.

Figure 6.2.4.1.1-1  Device Management Architecture

*****

## End of Text ##