| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP8 |
| Title:* | Functional architecture in oneM2M-TS-0001 oneM2M Functional Architecture-V-0.2.2 |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2013-11-30 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes additions to the functional architecture

* * * Start of 1st Change * * *

## 6.5. 	Other Aspects

### 6.5.1 Inter M2M SP communication for oneM2M compliant nodes

Communication between different M2M SPs which occurs over the reference point Mcc’, is subject to business agreements. The offered functionality is typically a subset of the functionality offered over the Mcc reference point.

Any interM2M SP communication in support of any request originating from one M2M SP domain shall be routed through the infrastructure node of the originating M2M domain towards the infrastructure node of the target M2M SP domain and finally routed to its target CSE, if different from the infrastructure node. Hence the infrastructure node in both M2M domains shall be the exit and entry points, respectively, for all inter M2P SP communication traffic.

Public DNS shall be used to support traffic routing for inter M2M SP communication in accordance with [C]. This relies on public domain names being allocated to communicating CSE entities within the oneM2M architecture, and to whom access across domains is permitted through policies.  To that effect, an M2M SP supporting inter- M2M SP communication shall ensure that the public domain names for the CSEs whose functionality is available across domains are held in its public  DNS and shall always point to the IP address associated with the infrastructure node  for the domain  (being the entry point) for accessibility purposes.

The M2M SP could also have additional policies that govern accessibility from other domains to CSE functionality located within its own domain and that is out of scope. Additionally, the M2M SP shall be able to install policies in the infrastructure node, being the entry point for all inter-M2M SP communication traffic that includes white list and black list capabilities for access to public CSEs defined in its DNS. These policies are however out of scope. Note that access rights are not impacted as these are applied to the actual target resource associated with the final destination of a request.

The public domain names of CSEs to whom access from other domains is allowed by policies, shall be created in the DNS of the M2M SP by the infrastructure node at registration time of these CSEs, and shall be removed at de-registration. DNS entries for CSEs can also be created/removed for registered CSEs at any time by the M2M SP through administrative means to handle dynamic policies.

#### 6.5.1.1 Public Domain Names and CSEs

To enable the usage of public DNSs as depicted above, there is need for a naming convention for public names for CSEs.  This naming convention facilitates the creation of the necessary entries of the public domain names of CSEs in the DNS by the infrastructure node.

CSEs public domain names shall be a sub-domain of the infrastructure node public domain name. This naming convention allows the infrastructure node to include the needed DNS entry corresponding to the CSE to whom access from other domains is allowed. This would typically occur when the CSE registers with the infrastructure node, subject to policies, or administratively. The infrastructure node shall also have a public domain name.

Accordingly, the structure of the public domain of the CSEs in any node (middle service node/Application service node) shall follow the following naming convention, which relies on the CSE identifier (CSE-ID) as part of the naming convention to facilitate the entry creation:

- Infrastructure Service Node public domain name: <infrastructure node CSE Identifier>.<M2M Service provider domain name>

- CSE middle service Node public domain name: <middle Node CSE Identifier>.<Infrastructure node identifier public domain name>

- CSE Application  Service Node  public domain name: <Application Node CSE Identifier>.<Infrastructure public domain name>

The A/AAAA records in the DNS, as per [A], [B], and [D] shall consist of the public domain name of the CSE and the IP address of the M2M infrastructure service node, since the M2M infrastructure service node is the entry point of the M2M service Provider domain name where it belongs to.

* * * End of 1st Change * * *

* * * Start of 2nd Change * * *

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.x]	oneM2M TR-0008, "Security Analysis:

[A] 	IETF RFC 1035 “Domain names – Implementation and specification”

[B]	IETF RFC 3596 “DNS Extensions to Support IP Version 6”

[C]	GSMA-IR.67 DNS/ENU Guidelines for Service Providers & GRX/IPX Providers

[D]	IETF RFC 2929 DNS IANA Considerations September 2000

[E]	IETF RFC 6874 “Representing IPV6 Zone Identifiers in Address Literals and Uniform Resources Identifiers

[F]	IETF RFC 3986: Uniform Resource Identifier (URI): Generic Syntax

* * * End of 2nd Change * * *